This  driver  is  designed  to  support  a DR-11W under
RSX-11M+ version 3.0 and later interfaced to an  ACROAMATICS
2110  Telemetry  data processor (TDP) system.  The design of
this driver follows the VAX/VMS XA driver in  direct  memory
access  (DMA) mode as closely as possible.  This was done to
ease compatibility of software access to the telemetry  sys-
tem, and its always nice to have a structure to follow.  

     The  driver  accepts  4 general functions, read logical
block, write logical block, set characteristics,  and  sense
characteristics.   In  addition,  the  read and write accept
subfunction codes reset, set function  bits,  and  set  time
out.   The  device is flagged as a record structured sequen-
tial device in the driver unit control  block  (UCB).   This
has  the  side effect of allowing use of read/write virtual,
but the operating system will  convert  this  to  read/write
logical and strip off all subfunction bits.  

     The  read  and  write  logical  functions  are  used to
transfer data via a dma channel between the external  device
and  the host PDP-11.  The transfers can have either a reset
or set function subfunction as required, and a new time  out
set if required.  The processing of the subfunctions is per-
formed prior to setting up the DMA channel, which would  al-
low  for  most hardware handshake protocols to be fulfilled.
The time out processing is performed just before setting the
go bit to start the transfer.  The transfer complete is sig-
nalled by an interrupt, which can come from  either  a  word
count  register overflow or any of the exception interrupts.
The transfer complete is signalled by placing the number  of
bytes  transferred  in  the  second word of the input output
status block (IOSB) and success (is.suc) in the  first  word
of  the IOSB.  A device time out will place a time out error
code (ie.tmo) in the frist word of the IOSB and the  CSR  in
the second word.  

     The driver allocates and releases unibus mapping regis-
ters (UMR's) for each data  transfer.   If  a  higher  speed
transfer is required, the driver could be modified to accept
device allocation and permanently  allocate  UMR's  at  that
time.  The interface to the TDP has a 4K word first in first
out (FIFO) buffer which allows extra processing time between
transfers before a data overrun will occur.  

     Since  is  is  possible  for  rogue devices to generate
spurious  interrupts,  or  as  in  this  device's  case,  to
generate  a  DMA done interrupt coincident with a frame done
interrupt when the requested transfer count exactly equals a
telemetry  frame.   In this case, a hardware race will occur
in which the ATTENTION interrupt and the DMA done  interrupt
will both be pending.  To assure correct handling of all in-
terrupts, all transfers are flagged with  an  interrupt  ex-
pected in the UCB and the interrupt handler clears the flag.
If an interrupt occurs when the flag is clear, the interrupt
is  dismissed.  All access to the interrupt expected flag is
done at hardware priority (PR5) to assure proper  synchroni-
zation.   All  setting  of  the  CSR  is also done at device
priority to assure stability.  

DR-11W DRIVER FOR RSX-11M+ version 3.0 OR LATER       Page 2



     For  non-DMA operations, the sense and set characteris-
tics functions are  available.   For  a  Set  characteristic
(io.stc) function, the user parameter (first word of the I/O
parameter block) has all but the lower three  bits  cleared,
and  these  bits  are  then  left shifted to the control bit
positions and or'ed into the CSR.  For a sense  characteris-
tics,  the CSR is merely read.  In both cases the entire CSR
is returned in the second word of the  IOSB.   No  interrupt
processing  is expected with these functions, and should one
occur, it would be dismissed as an unexpected interrupt.  

     The  following  code fragments shows a typical MACRO-11
interface to the QA driver.  The setting up of the  subfunc-
tion codes is as follows:  

     1.  IO.SFT=2       ;set function subfunction 

     2.  IO.RES=4       ;reset subfunction 

     3.  IO.STO=10      ;set time out subfunction 

The access to the driver is shown as follows:  

     1.  Assign logical unit:  
                alun$s  #tdplun,#"QA,0  ;
                 bcc    setasn            ;ok ?
                 mov    $dsw,r0           ;get status return
                 return

     2.  Sense characteristics 
                qiow$s  #io.sec,#tdplun,#tdpflg,,#driosb,,
                 bcc    15$               ;ok?
                 mov    $dsw,r0
                return
         15$:    tstb   driosb+1          ;check i/o
                 bpl    20$               ;if plus, no error
                 mov    driosb,r0         ;and io status
                 return

     3.  Write logical block, set function:  
         wrset:  mov    r2,incnt          ;set character
         count
                qiow$s
         
         #io.wlb!io.sft,#tdplun,#tdpflg,,#driosb,,<#inbuf,in
         cnt,#wrsetup>
                 bcc    10$               ;ok ?
                mov     $dsw,ro
                return
         10$:   tstb    driosb+1          ;transfer ok?
                bmi     20$               ;minus, no
                cmp     driosb+2,incnt    ;how many bytes



DR-11W DRIVER FOR RSX-11M+ version 3.0 OR LATER       Page 3



     The  read  logical and set characteristics are are very
similar to the write logical and sense characteristic  exam-
ples.  The use of a new time out would be similar to the set
function subfunction, being or'ed into  the  function  code,
and  the  new time out (in seconds) as the fourth element of
the device dependant parameters.  

     Two command files (asm.cmd and bld.cmd) are used to as-
semble and build the driver.  These files assume the  source
code  is  in the named directory [qadrv].  The driver map is
placed in UIC [1,34] and the driver and symbol table in  UIC
[1,54].  The command file QA.CMD will load the driver at the
top of the GEN partition and configure online the controller
(QAA) and the unit (QA0).