SRD - Sorted Directory Utility
                          ==============================






                                   User's Guide
                                   ============



                                    Version 6.6
                                    ===========



   SRD - Sorted Directory Utility                                    Page 2
   Version 6.6  12-Jun-85









        1.0  INTRODUCTION


        SRD is a utility that produces sorted directory listings and
        performs some useful directory manipulation that is absent from
        PIP.  In addition it produces an output file that can be edited by
        the standard RSX Editor (EDI) [which PIP does not] and provides a
        wildcard facility in specifying file names so that, for instance,
        all files beginning with the letters RSX could be listed.

        SRD has to read the entire directory into memory before sorting it.
        The size of SRD's buffer can be increased by installing it with an
        increment.  On an RSX-11M system, SRD will try expand itself
        dynamically.  If it cannot fit the entire directory in memory, SRD
        will give a warning message and do the directory in chunks.  Each
        chunk will be sorted separately.  A write-back will be cancelled in
        this case.



        2.0  INVOKING SRD


        SRD can be invoked by any of the standard RSX-11M invocation
        methods, i.e.

                        RUN $SRD
                    or  SRD
                    or  SRD command-line


        In either of the first two cases, SRD prompts for further commands
        with:

                    SRD>


        A CTRL-Z will terminate SRD in this mode.



        2.1  Indirect command files.

        SRD will accept an Indirect Command File as input, or SRD may be
        invoked by an Indirect Command File if it is an installed task.



   SRD - Sorted Directory Utility                                    Page 3
   Version 6.6  12-Jun-85


        3.0  SRD COMMAND LINE.


        The format of the command line is similar to PIP's directory
        operations, i.e.

                    SRD>[output filespec=][input filespec][/switches]




        3.1  Output Filespec


        Output Filespec defines the output specification for the listing.
        This may be a file (e.g.  DIR.LST), a device (e.g.  LP:) or omitted
        all together, in which case TI: is used.  If any part of the output
        file specification is omitted that part defaults to the
        corresponding part of SY:[current UIC]DIRECTORY.LST.

        The /AP switch may be used to append the listing to an existing
        file.  A later section describes the use of the /AP switch.



        3.2  Input Filespec


        Input Filespec defines the input specification defining the files
        on which the switches are to act.  SRD can work on a 'partial file
        specification' basis for each of the filename, extension and
        version number fields so that:

                    SRD SU/LI/WI


        not only lists out the latest file called SU (as PIP would), but
        fills in wildcards for any part of the filespec you left out and
        lists out all files whose filename starts with the two letters SU,
        for all extensions and all versions.

        To emphasize this, note that S.M;1/LI/WI would list out all the
        following:

                    S.M;1
                    SYSTEM.MAC;1
                    SYS.MAP;1
                    START.MY;13
                    and so on.


        If the Input Filespec is omitted, *.*;* is assumed.



   SRD - Sorted Directory Utility                                    Page 4
   Version 6.6  12-Jun-85


        Note that the system manager may select certain options and your
        site may have /WI and/or /LI as defaults.  HELP SRD SWITCH DEFAULTS
        should tell you the default switch settings.



        3.3  Command Line Switches


        Any valid combination of switches described in the next section may
        be used.  (See Switch Combinations.)

        Defaults for the various switches will be discussed later.  These
        may differ at your site.  HELP SRD SWITCH DEFAULTS should tell you
        the default switch settings.



        3.4  SRD will accept an Indirect Command File as input,

        or may be invoked by an Indirect Command File.



        4.0  SRD SWITCHES




        4.1  Switch summary

        /00  -  Include [0,0] in wildcarded directory search.
        /AE  -  After & Equal to specified date and time.
        /AF  -  AFter specified date and time.
        /AP  -  APpend listing to a file.
        /AT  -  ATtach output device.
        /BE  -  Before & Equal to specified date and time.
        /BF  -  BeFore specified date and time.
        /BK  -  BlanK spaces before each file name in list.
        /CM  -  CoMmand file format in listing.
        /CO  -  Select COntiguous files.
        /DA  -  Select file on the DAte specified.
        /DE  -  DElete specified files and confirm by listing them.
        /ER  -  ERror producing files.
        /FI  -  Find file by File Ident without sequence number.
        /FO  -  File Owner selection by UIC.
        /FU  -  FUll listing of attributes.
        /GT  -  Files Greater Than specified blocks allocated.
        /HD  -  Echo command line in HeaDer of listing.
        /HE  -  HElp.
        /HV  -  Higher Version listing - defaults to 2.
        /ID  -  IDentify current version of SRD.
        /LI  -  LIst.
        /LO  -  LOcked files listing.
        /M2  -  Middle listing type 2.



   SRD - Sorted Directory Utility                                    Page 5
   Version 6.6  12-Jun-85


        /MI  -  MIddle listing.
        /MU  -  MUltiple header files.
        /NA  -  NAme sort.
        /NE  -  List file Not Equal to specification.
        /NV  -  New Version of files, same as /SV
        /OV  -  Obsolete Versions.
        /PA  -  PAck file listings. Remove blanks.
        /PU  -  PUrge.
        /RD  -  Revision Date.
        /SD  -  Selective Delete.
        /SE  -  SElect by wildcard specification.
        /SI  -  SIze of SRD's buffer area.
        /SM  -  SuMmary lines in listing.
        /SP  -  SPool.
        /SR  -  Specify SoRt order listing.
        /SV  -  Select highest Version - default = 1.
        /SY  -  Include SYstem UFD's.
        /TB  -  Show Total Blocks used/allocated.
        /WB  -  Write Back the directory file.
        /WD  -  Wildcard the specification for Delete operations.
        /WI  -  WIldcard the specification.
        /ZE  -  List files with ZEro blocks used.

        See appendix for some examples.



        4.2  Switch Actions




        4.2.1  Produce a Directory Listing (/LI) - This just lists the
        filename, extension and version of the files that meet the
        specification given.  The output is sorted, by default, into the
        order:

                    first       Ascending on File Extension
                    then        Ascending on File Name
                    then        Descending on File Version


        In addition a header and trailer line are output for each UFD.  The
        header line contains the name of the UFD, the current date and
        time, and the command line that was originally used.  The trailer
        line contains the number of files selected and the total number of
        files in the directory.  If one of the switches /MI, /FU, /AE, /AF,
        /BE, /BF, /DA, /CO, /LO, /MU, /ZE, /GT, /ER, /FO, or /TB is
        specified the total number of blocks used/allocated for the
        selected files is also listed.



   SRD - Sorted Directory Utility                                    Page 6
   Version 6.6  12-Jun-85


        4.2.1.1  /-LI - The /LI switch can be negated to suppress the
        listing which usually accompanies some of the other switches (e.g.
        /WB or /PU).  Just the header and trailer lines are printed.



        4.2.2  'Middle' Directory Listing (/MI[:n], /M2) - These switches
        act similarly to the /LI switch, except that they produce
        additional information about the selected files.  The extra
        information listed out depends on the setting of the /M2 switch and
        is either (/M2 not specified):

                    Creation Date and Time
                    Revision Date and Time
                    Revision Number

                    or (/M2 specified):

                    Number of Blocks Allocated to File
                    End of File Block Number
                    Contiguous/Locked/Multiheader Flags
                    File ID
                    Creation Date and Time (Revision Date if /RD spec'd)




        4.2.3  Produce a Full Directory Listing (/FU[:n]) - This acts
        similarly to the /LI switch, except that it lists out yet more
        information, i.e.

                    Number of Blocks allocated to File
                    End of File Block Number
                    Contiguous/Locked/Multiheader Flags
                    File ID
                    Owner UIC
                    Protection Codes
                    Creation Date and Time
                    Revision Date and Time
                    Revision Number


        If n is specified, it defines the width of the listing (72 to 132).
        If n is not defined it defaults to the device buffer size.



        4.2.4  Append listing to a file (/AP) - If this switch is specified
        the generated listing is appended to the specified output file.  If
        the specified output file does not exist or can not be opened
        (locked or privilege violation), the result depends upon whether a
        non-zero version number is specified for the listing file.  If so,
        and there is an error opening the file for append, SRD will issue a
        fatal error message.  If no version number is specified (or version
        zero), and there is an open error, SRD will issue a warning message



   SRD - Sorted Directory Utility                                    Page 7
   Version 6.6  12-Jun-85


        and then attempt to create a new file version.  For convenience /AP
        may be specified with either the output file specification or input
        file specification.



        4.2.5  Change the Sort Order (/NA) - If this switch is specified
        the output sort order is altered to be:

                    first       Ascending on File Name
                    then        Ascending on File Extension
                    then        Descending on File Version




        4.2.6  Select Files not Specified (/NE) - If this switch is
        specified then all files that do not meet the given specification
        are listed out.



        4.2.7  Select Files by Version Number (/HV[:n]) - This switch lists
        out all files which meet the given specification whose version
        number is greater than or equal to n.  If not specified, n defaults
        to 2.



        4.2.8  Latest Versions of Files (/SV[:n] & /NV[:n]) - These
        switches list out the latest n versions of all files that meet the
        given specification.  If not given, n defaults to 1.  If n is
        specified as -1 the oldest version of the selected files are
        listed.



        4.2.9  Select Obsolete Versions of Files (/OV:n) - This switch
        restricts the listing of file names to all versions except the "n"
        highest versions.  The default value for "n" is 1.  

        For a given "n", /OV:n lists file names not listed by /SV:n, and
        the files listed are those that would be deleted if /PU:n were
        specified.

        For example, /OV:14/LI would only list files which had more than
        14(8) versions and list the lowest versions.  As indicated by the
        definition, if n is -1 then all but the oldest version are listed
        out.



   SRD - Sorted Directory Utility                                    Page 8
   Version 6.6  12-Jun-85


        4.2.10  Select Files by Date (/AE,/AF,/BE,/BF,/DA) - Each of these
        switches takes an optional date and/or time as parameter, in the
        form dd-mmm-yy hh:mm, or hh:mm dd-mmm-yy, etc.  e.g.:

        /DA:03-DEC-83 10:30

        In fact the date may be specified as ddmmmyy if desired:

        /DA:3DEC83 10:30

        If no date is specified, today's date is assumed.  If no time is
        specified, time checks are ignored.

             1.  /AE lists all files created on or after the given date
                 (and time).

             2.  /AF lists all files created after (but not on) the given
                 date (and time).

             3.  /BE lists all files created on or before the given date
                 (and time).

             4.  /BF lists all files created before (but not on) the given
                 date (and time).

             5.  /DA lists all files created on the given date (and time).


        For these switches the listing includes the creation date and time.
        If the /RD switch is specified then the Revision Date is used for
        the checks and the listing includes the Revision Date and Time.



        4.2.11  Use wildcards in filename (/SE:filespec) - Because of the
        parsing structure in RSX (before V4.0 & V2.0M+), it was impossible
        to have wildcards for letters in the Input Filespec, and so this
        switch was included to allow the facility.


                                       NOTE


             If your system is RSX-11M V4.0  or  RSX-11M+  V2.0  or  a
             higher  version  of these systems, the /SE switch is only
             necessary if you want to wildcard the file version field.



        The filespec argument it takes is identical to that defining the
        Input Filespec with the following additional features:

                    % (or ?) matches one wildcard character.



   SRD - Sorted Directory Utility                                    Page 9
   Version 6.6  12-Jun-85


                    * matches any number (including zero) of wildcard
        characters.


        Any combination of these characters may be used in any of the
        filename, extension or version number fields.  Note that within
        each field, if an * is specified somewhere, and the final character
        is not an * then that final character is assumed to be required as
        the last character of the field.  "*D" will match FRED but not
        FREDA and "*D*" will match both FRED and FREDA.

        Suppose we have the files:

        FRED, FREDA, FREDERIK, FEED, FILD, FEEDER, FRIED, FD

        then

        /SE:F%%D* will match FRED, FREDA, FREDERIK, FEED, FILD,FEEDER

        /SE:F%%D will match FRED, FEED, FILD

        /SE:F*D will match FRED, FEED, FILD, FRIED, FD

        /SE:F*D* will match everything.

        Note that /SE cannot be used in combination with a standard Input
        Filespec.



        4.2.12  List by file ID (/FI:n) - This switch will list a file with
        the specified identification number.  A handy switch when you have
        an error message which doesn't tell the file name but gives the ID.
        Note that only the file identification number should be specified,
        not the sequence number.



        4.2.13  File owner (/FO:[ggg,mmm]) - List files by the owner of the
        file or if negated all files not owned by the specified UIC.
        Either of the UIC fields may be wildcarded, e.g., /FO:[*,54] for
        all files owned by any group number and a member number of 54(8).
        the form "/-FO" will list all the files in the current UFD not
        owned by the current UIC.

        An alternate form of this switch is supported for compatibility.
        "/FO:g:m" is valid.



        4.2.14  Selection by block size (/GT:n) - This switch list files
        which have at least n blocks allocated.  It is very useful for
        locating where all the storage has gone!



   SRD - Sorted Directory Utility                                   Page 10
   Version 6.6  12-Jun-85


        4.2.15  Blocks used/allocated (/TB) - This will ensure that SRD
        summarizes the blocks used and allocated for the selected files.



        4.2.16  Delete Files (/DE) - This switch deletes all files which
        meet the given specification and lists the deleted files for
        confirmation.



        4.2.17  Purge the directory (/PU:n) - This switches purges all but
        the highest n versions of all files meeting the Input File
        Specification and lists those purged.  If not specified, n defaults
        to 1.  If n is -1 then all but the oldest version of the specified
        files are purged.



        4.2.18  Selectively Delete Files (/SD:filespec) - This switch lists
        all the files that meet the given specification, and SRD prompts
        the user to see if the file should be deleted.  There are five
        allowable replies:

                    Y = Delete this file
                    N = Do Not Delete This File
                    G = Delete the rest of the specified files
                    Q = Exit without deleting any more files
                    CTRL-Z = Terminate selective delete sequence.


        Any other response is interpreted as "N" (NO).  If "G" (GO) is
        entered, the question "ARE YOU SURE?" is asked to be certain you
        wish to delete the remaining files.

        The filespec, if given, follows the same rules as for /SE.



        4.2.19  Write Back the Directory File (/WB) - If this switch is
        specified then as well as producing a listing, SRD writes the file
        headers back to the UFD in the order of the listing.  This means
        both that the UFD is compressed (which could speed up FCS
        operations) and that future PIP operations will proceed in the
        sorted order given.  A particularly useful application of this is

                    SRD [0,0]/WB
                    or
                    SRD [0,0]/WB/NA

        which will sort the UFD files, so that SRD [*,*]/LI will then list
        files in numeric order of directories as well as sorted on
        filename, etc.



   SRD - Sorted Directory Utility                                   Page 11
   Version 6.6  12-Jun-85


        Write Access to the directory is required and Write Failure is
        usually due to a protection violation.  In the event of a
        write-back failure, the operation is attempted several times.



        4.2.20  Use Revision Date (/RD) - On the date selection, use the
        revision date (if any).  In addition, if this is used for a /MI
        (/M2) listing the Revision Date will be listed instead of the
        Creation Date.  This switch is installation selectable and may have
        a default set by your system manager.



        4.2.21  Sort the Directory (/SR) - Sort the file names.  This
        option is turned off if the files are not being listed or written
        back.  You can also say /-SR to get the files listed in the order
        they are in the directory.  This is the same order that PIP lists
        them.

        Using the key arguments on the /SR switch specifies the order in
        which SRD will sort the files.  The key argument consists of one or
        two characters.  The first character specifies the field of the
        file specification on which to sort and the second character
        specifies the sort order, ascending or descending.

        The file specification field characters are:
                    N - file name
                    T - file type
                    V - file version
                    D - file date


        The second character is either an A or a D for Ascending or
        Descending

        SRD's default sorting order is:
             1.  Ascending by file type
             2.  Ascending by file name
             3.  Descending by version number

        This default sorting order is specified by /SR:T:N:VD or
        /SR:TA:NA:VD.  If any or all or the optional key arguments are
        omitted the default order is used.



        4.2.22  Include System UFD's in Wildcard Searches (/SY) - If this
        switch is specified then all system UFD's (i.e.  those with a group
        code between 0 and 10 inclusive) will be included in [*,*] or [*,n]
        searches.  If it is switched off (/-SY) then such UFD's will be
        ignored.  This switch (or it's negation) has no effect unless the
        group code of the specified UFD is wild.  This switch is
        installation dependent and may have a default set by your system
        manager.



   SRD - Sorted Directory Utility                                   Page 12
   Version 6.6  12-Jun-85


        4.2.23  Include [0,0] in Wildcard Searches (/00) - If this switch
        is specified then [0,0] will be included in [*,*], [0,*] or [*,0]
        searches.  If the switch is negated (/-00) then the [0,0] directory
        will be ignored during the search.  Directory [0,0] can always be
        listed by specifying it directly.



        4.2.24  Treat all specifications as 'wildcarded' (/WI, /WD) - One
        of the great powers of SRD is the ability to specify just, say, S
        as a filename and get a listing of all files with a filename
        beginning with S.  It is, however, also desirable at times to be
        able to specify that you want only files with a filename of S on
        its own.  The switch /WI controls this with 'implicit wildcarding'
        assumed if it is specified, but not if it is negated (see /SE for
        an example).  In addition /WD specifies whether the 'implicit
        wildcarding' indicated by /WI also applies during delete/purge
        operations (yes if specified, no if negated).  Both are ignored if
        /SE or /SD is given.


                                       NOTE

             If /-WI is  specified,  "FRED"  will  still  be  read  as
             FRED.*,  but "FRED." will only look for files with a file
             name of FRED and with a null extension.





        4.2.25  Select only Contiguous Files (/CO) - This switch causes SRD
        to select only files which are contiguous.



        4.2.26  Select only Locked Files (/LO) - This switch causes SRD to
        list only files which are locked.



        4.2.27  Select only Zero-Blocks-Used Files (/ZE) - This switch
        causes SRD to list only files which have zero blocks used.



        4.2.28  Select only Multi-Header Files (/MU) - This switch causes
        SRD to list only files which have multiple headers.



   SRD - Sorted Directory Utility                                   Page 13
   Version 6.6  12-Jun-85


        4.2.29  Print out the current Version of SRD (/ID) - This option
        will display the current version of SRD.



        4.2.30  Print out the available Buffer Size (/SI) - This option
        will display the size of SRD's buffer which it uses to read the
        directory files into memory.  This switch is for diagnostic
        purposes only, and can be used to determine how large a directory
        file can be processed by SRD.



        4.2.31  Attach output device if terminal (/AT) - If this switch is
        specified then the output device (if it is a terminal) will be
        attached during the operation.  This has the advantage of allowing
        CTRL-O to be used to suppress any listing, and the disadvantage of
        tying up the terminal during what could be a long search.  If the
        switch is negated (-/AT) the terminal will not be attached.  This
        switch is installation dependent and may have a default set by your
        system manager.



        4.2.32  Give brief help (/HE) - Typing /HE will print out a brief
        summary of the SRD switches.  For this to function properly, the
        HELP facility must be present on your system.  /HE will cause a
        command "HELP SRD" to be issued to the operating system.



        4.2.33  Spool the Output File (/SP) - If this switch is specified
        then the output file (if one was specified) is spooled to the Print
        Spooler (PRT...).  In addition, if a multiple-UIC search is being
        done, SRD inserts a form feed before each new UIC.



        4.2.34  Command file format (/CM:xxx:fffff) - This switch is used
        to generate an indirect command file which will invoke a processor
        such as a compiler.  For each file selected by the SRD command
        line, SRD's output file may contain a line like:

        xxx outfile,listfile=infile.typ;ver,infile

        The field "xxx" represents the processor name, as specified by the
        first /CM switch argument.  The "outfile", "listfile", and "infile"
        are all made from the selected file name for each file selected.

        The second switch value controls the actual format of the output
        line.  This switch value can contain any of the letters "O", "L",
        "T", "V", and "S", in any order.  The meaning of these letters is
        as follows:

                   letter      meaning



   SRD - Sorted Directory Utility                                   Page 14
   Version 6.6  12-Jun-85


            
                      O     provide "outfile" field
                      L     provide "listfile" field
                      T     provide type for first "infile"
                      V     provide version number in first "infile" field
                      S     provide second "infile" field (always with
            version ";0")

        If the second switch value is not specified, then the default form
        for each output line is "infile" only.

        For example, if a user account contains only the files MAIN.MAC;10,
        SUB1.MAC;7, SUB2.MAC;2, SUB2.MAC;3, and SUB3.FOR;6, then the
        command


        >SRD MAINBLD.CMD=/SV/CM:MAC

        would produce file MAINBLD.CMD containing only the lines
           MAC MAIN
           MAC SUB1
           MAC SUB2
           MAC SUB3

           and the command

           >SRD SUBASM.CMD=S*.MAC/SV/CM::TVLO

           produces SUBASM.CMD containing:

           SUB1,SUB1=SUB1.MAC;7
           SUB2,SUB2=SUB2.MAC;3


        Any string not containing "/", ":", or "=" can be used for the
        processor name argument or it may be null.

        Note that if /NV (or /SV) is not specified then the "V" should be
        used in the second switch value to avoid duplicate lines.

        The /PA switch is implicit in the /CM switch.



        4.2.35  Print command line in header (/HD) - This switch causes SRD
        to print the command line issued in the header following the line
        showing the UIC.  The command echoed in the header is the line the
        user typed before any wildcard substitutions were made.  This
        switch may be negated to suppress the command line echo.  This
        switch is installation dependent and may have a default set by your
        system manager.



   SRD - Sorted Directory Utility                                   Page 15
   Version 6.6  12-Jun-85


        4.2.36  Print summary lines (/SM) - This switch causes SRD to print
        a summary line following the files listed for each directory
        stating the number of files selected and the total number of files
        in the directory.  If switch /FU, /MI, /DA, /AF, /AE, /BF, /BE,
        /CO, /LO, /MU, /ZE, /GT, /ER, /FO, or /TB is specified, then an
        additional summary line will give the number of blocks used and
        allocated for the files selected.  This switch is installation
        dependent and may have a default set by your system manager.



        4.2.37  Place two spaces before each file name (/BK) - This switch
        causes SRD to insert two blank characters ahead of the file name on
        each file listing line.  (Some widely used previous versions of SRD
        inserted these two blanks, while others did not.  This switch gives
        you a choice.) This switch is installation dependent and may have a
        default set by your system manager.



        4.2.38  Pack file listings (/PA) - The pack switch removes all
        spaces from the file listing.  FILE     .Q  ;21 becomes FILE.Q;21.



        4.3  Switch Combinations


        All switch combinations work as would seem logical.  For example,

                    SRD /AF:7-DEC-83 10:30/BE:7-DEC-83 14:44


        would list out all files created on 7th December 1983 between 10:30
        and 14:44.

                    SRD *.*/PU/SD


        will list out the files to be purged and allow you to selectively
        delete them.



        4.3.1  Restrictions to Switch Combinations - 
             1.  /DA cannot be used with /AE, /AF, /BE or /BF.
             2.  /DE cannot be used without /SE or a file name specified.
             3.  Only one of /NV, /SV, /OV, /PU may be used at once.
             4.  Only one of /LI, /MI, /FU should be used at once.  SRD
                 will use the switch requesting the most listing
                 information.
             5.  /ID, /SI and /HE cannot be used with other switches.
             6.  And other nonsensical combinations (like /NA/-SR).
             7.  It is not meaningful to negate the switches /NE, /HV, /SV,
                 /OV, /AE, /AF, /BE, /BF, /DA, /SE, /PU, /SD, /ID, /SI and



   SRD - Sorted Directory Utility                                   Page 16
   Version 6.6  12-Jun-85


                 /HE.




        4.4  Switch Defaults


        Default values for the switches are set at Task-Build time, and may
        vary from installation to installation.  Any of the switches may be
        preset in this way, but usually the only ones affected are /LI,
        /NA, /RD, /SR, /SY, /AT, /00, /WI, /WD, /M2, /HD, /SM, and /BK.
        HELP SRD SWITCH DEFAULTS or HELP SRD DEFAULTS should display a list
        of the switch defaults at your site.



        5.0  ERROR MESSAGES


             1.  SRD -- Directory too big.  Doing in pieces.

                 SRD was unable to expand its buffer sufficiently to hold
                 the whole directory at once.

             2.  SRD -- Command read error

                 Either an error occurred in reading the command line, or a
                 comma was specified other than in the UIC of the Input or
                 Output Filespec.

             3.  SRD -- Command syntax error

                 The command line failed to parse correctly, and is
                 therefore invalid.

             4.  SRD -- Error in input spec

                 An invalid input filespec was given.

             5.  SRD -- Error in output spec

                 An invalid output filespec was given.

             6.  SRD -- Error reading MFD

                 An error occurred while SRD was trying to read the Master
                 File Directory.

             7.  SRD -- Parse error

                 The output filespec could not be parsed correctly.

             8.  SRD -- Open error on input



   SRD - Sorted Directory Utility                                   Page 17
   Version 6.6  12-Jun-85


                 SRD detected an error opening an input file.

             9.  SRD -- Open error on output

                 SRD detected an error opening the output file.

             10. SRD -- Directory find error

                 A directory was specified which does not exist.

             11. SRD -- No such file(s)

                 No files were found to match the input specification.

             12. SRD -- Invalid date format.  Enter DD-MMM-YY HH:MM
                 (1-SEP-83 10:30)

                 Dates must be entered in the form DD-MMM-YY HH:MM (or vice
                 versa) or DDMMMYY HH:MM (or vice versa) with the single
                 exception that the date may be abbreviated to one
                 character.

             13. SRD -- Error reading file header for [g,m]name.typ;ver

                 SRD detected an error while trying to read a file header.

             14. SRD -- Put error

                 An error occurred while trying to output a record to the
                 output device.

             15. SRD -- Write error

                 An error occurred while trying to write back a directory.

             16. SRD -- Read error

                 An error occurred while trying to read a directory.

             17. SRD -- Error deleting file

                 An error occurred while trying to delete a file.

             18. SRD -- Directory privilege violation

                 The user does not have the required read or write access
                 to the given directory.

             19. SRD -- Directory open error

                 An error occurred while trying to open a directory file.

             20. SRD -- Directory write-back error for [g,m]



   SRD - Sorted Directory Utility                                   Page 18
   Version 6.6  12-Jun-85


                 An error occurred while trying to write a directory back
                 into the directory file.

             21. SRD -- Write-back cancelled.  Can't fit entire directory
                 in memory:  [g,m]

                 A write back was requested (/WB) but cannot be performed
                 as the directory has only been sorted in chunks.

             22. SRD -- File ID-Sequence number mis-match for
                 [g,m]name.typ;ver

                 An attempt to read a file header failed because of a file
                 ID and sequence number mismatch.

             23. SRD -- Header-read privilege violation for
                 [g,m]name.typ;ver

                 The user did not have valid access rights to read the file
                 header for the specified file.

             24. SRD -- File date corrupt in file header for
                 [g,m]name.typ;ver

                 The date stored in the file header is corrupt.

             25. SRD -- Error reading extension header --

                 SRD detected an error while trying to read an extension
                 file header.   

             26. SRD -- Invalid or duplicate /SR: sort key values

                 The sort key values may not be repeated.  The valid keys
                 are T (file type), N (file name), V (file version), and D
                 (file date).  Examples:  /SR:N:T:V (all ascending);
                 /SR:N:DD (name ascending, date descending).

             27. SRD -- Sort key combination invalid for /SV, /NV, /OV, /PU

                 In order to get version selection, name and type must be
                 the first two sort keys (either order), and version must
                 be the third sort key.

             28. SRD -- Some file dates can not be read for sort by date

                 Dates in some file headers are corrupt.  If these files
                 are selected for listing, they will be listed first.

             29. SRD -- Char. other than O,L,T,V,S found in /CM switch -
                 ignored



   SRD - Sorted Directory Utility                                   Page 19
   Version 6.6  12-Jun-85


                 The only options accepted in the second /CM switch value
                 are O, L, T, V, and S.

             30. SRD -- Unable to open specified output file for append

                 The output file specification included a specific version
                 number.  The file did not exist or could not be opened for
                 append (for example, file locked or file protection
                 violation).

             31. SRD -- Output file append error - attempting to open new
                 file version

                 The output file specification was for a highest version.
                 The file did not exist or could not be opened for append
                 (for example, file locked or file protection violation).
                 SRD will create a new file version if possible.




   SRD - Sorted Directory Utility                                   Page 20
   Version 6.6  12-Jun-85


        6.0  SRD SYSTEM MANAGER'S GUIDE




        6.1  Task Structure


        SRD consists of fifteen modules, in the following structure:


                                     SRDROT
                                       !
                                     SRDATA
                                       !
                                     SRDSUB
                                       !
                                     SRDTRP
                                       !
             -----------------------------------------------------------
             !           !           !           !          !          !
          SRDINI      SRDNUD      SRDOPR      SRDSRT     SRDDBF     SRDLST
             !                       !           !                     !
          SRDREP                  SRDXX1      SRDXX2                SRDTST
                                                                       !
                                                                    SRDXX3

        (Note that some routines from SYSLIB are also overlaid).



        6.1.1  SRDROT - SRDROT is the high-level module that controls all
        the others.  It first calculates the top of the re-usable task
        space (see write-up on SRDXXn) and the minimum size of buffer
        required (the difference between that and the top of the code).  It
        then calls SRDINI to get a command.  If the request was /ID it
        outputs the Version Number message and returns to call SRDINI for
        another input line.  If the request was /SI it calls SRDDBF to
        calculate the current buffer size and returns to call SRDINI for
        another input line.  In all other cases it calls SRDOPR and SRDSRT
        to access each directory, SRDLST to output any listing and SRDNUD
        to access the next UIC (if a wildcard was specified).  It is also
        responsible for spooling the output file if required.



        6.1.2  SRDATA - SRDATA merely contains all the global data used by
        the task.



   SRD - Sorted Directory Utility                                   Page 21
   Version 6.6  12-Jun-85


        6.1.3  SRDSUB - SRDSUB contains four commonly used subroutines:
             1.  ATTDET - which attaches to or detaches from a given
                 device.
             2.  CNVDAT - which converts an ASCII date and time into an
                 internal format.  Note that CNVDAT has two subsidiary
                 entry points (CVDATE and CVTIME) if only the date or time
                 on their own are to be converted.
             3.  SRDCOM - which compresses a directory in the input buffer
             4.  ALERR - which is called by various routines (including
                 $AUTO) when an Executive Directive fails.  Currently it
                 simply puts the return address in R0 and the contents of
                 the DSW in R1 and issues a HALT (which will terminate the
                 program with a register dump) but should really be made
                 rather more intelligent.




        6.1.4  SRDTRP - All errors are logged by executing a TRAP
        instruction.  These are trapped by SRDTRP which formats and outputs
        the relevant error message and then exits.  While very easy to
        implement this is a rather noddy method of error reporting and
        should really be improved.



        6.1.5  SRDINI - SRDINI first shrinks the task back to its basic
        size (this is not really necessary as SRDOPR will do it if
        necessary).  It then sets the default values for the switch masks,
        zeroes all the valid data areas and gets the next command line from
        the user (via GCML$), calls SRDREP to replace any illegal
        characters and then parses it via CSI.  If the user requested help
        (/HE) it supplies it (via a spawn to MCR) and prompts for another
        line.  It opens the output file (if any were given), interprets and
        sets up dates for the /DA, /AE, /AF, /BE and /BF switches and then
        sets up the filename block for the (first) required directory.



        6.1.6  SRDREP - SRDREP simply checks the command string for
        characters that CSI will object to, and replaces them.  Otherwise,
        expressions like:

                        SRD /DA:10:30
                    or  SRD /SE:;1


        would be truncated.



   SRD - Sorted Directory Utility                                   Page 22
   Version 6.6  12-Jun-85


        6.1.7  SRDOPR - SRDOPR opens the current directory file, unless it
        is already open, and finds out how large it is (or how much more
        there is to be read into memory).  It then attempts to
        extend/contract SRD until the buffer is the same size as that
        required for the directory (or what remains of it).  [Note that it
        must ensure that SRD maintains at least the minimum buffer
        calculated in SRDROT, or the next attempt to load in the SRDINI
        overlay will fail.] If that fails it merely extends SRD as far as
        it can.  It then attempts to read in as much of the directory as it
        has found room for.  It then compresses the buffer and, if more
        directory was needed, tries to read in some more until it either
        has all of the directory in memory, or can compress the existing
        buffer no further.



        6.1.8  SRDSRT - SRDSRT first compresses the directory, by moving
        the entries up over unused slots.  It then sorts the entire
        directory (by using a modified Shell sort followed by a shuttle
        sort).  If /WB was specified and the whole directory is in memory,
        it is written back into the directory file.



        6.1.9  SRDNUD - SRDNUD reads the MFD to find the next directory
        that matches the wildcard search requested.



        6.1.10  SRDLST - SRDLST examines each entry in the directory in the
        buffer in turn.  First it checks the version number, if /HV was
        specified.  If that qualifies, it converts the directory name to
        ASCII in the output buffer and, if a filename was specified
        (directly or via /SE or /SD), calls SRDTST to check it.  If the
        match fails and /NE was not specified (or vice versa) the name is
        ignored.  Otherwise it checks the current (and adjacent) version to
        see if the filename qualifies under any /SV, /OV or /PU switches.
        If it does, it checks to see if it qualifies under any /CO, /LO or
        /MU switches.  If that matches it checks to see if it qualifies
        under any /AE, /AF, /BE, /BF or /DA switches.  Once it has been
        determined that the given file specification matches that
        requested, the module formats the output line(s) according to the
        type of listing requested.  If /SD was specified it then prompts
        the user to see if he wants the file deleted.  If /DE or /PU was
        specified, or /SD and the user answered Y this time, or G
        previously, the file is deleted.  The routine then returns to check
        the next entry.  When all the entries have been checked the routine
        outputs the trailer line for the directory.



   SRD - Sorted Directory Utility                                   Page 23
   Version 6.6  12-Jun-85


        6.1.11  SRDTST - SRDTST checks an individual filename to see if it
        matches up to the selection criteria laid down by a specified input
        filename, or a /SE switch (q.v.).



        6.1.12  SRDDBF - SRDDBF merely calculates the amount of space in
        the buffer and outputs a message accordingly.



        6.1.13  SRDXX1/2/3 - SRDXX1, SRDXX2 and SRDXX3 are used to enable
        SRD to reclaim some space.  Each defines a PSECT that will follow
        all others in a segment ($$$XXn) and a global symbol to locate that
        PSECT (XXn).  One is attached at the end of each of the three
        longest segments, not counting SRDINI.  The idea is that once
        SRDINI (which is the longest path in the task) has parsed the
        command line, the later modules can reclaim the extra space it
        required as buffer space, and they do this by SRDROT working out
        from the SRDXXn modules, segment (of the others) ends.  This is a
        potentially tricky method, but appears to work at the moment in
        overlaid or non-overlaid versions of SRD.  If SRD starts crashing
        with errors from $AUTO it is probably something to do with these.



        6.1.14  SRDSYS/SRDPRE - These are two prefix files used in
        assembling the SRD modules.  SRDSYS simply contains the
        system-specific definitions (such as Operating System, existence of
        EIS and such-like) and is created by SRD.CMD.  SRDPRE contains
        definitions of all the local symbols (such as the switch bit
        settings) and macros used in SRD.



        6.2  Assembling and Building SRD


        SRD is assembled and built by means of the command file SRD.CMD.
        On the first time through SRD.CMD it will ask questions relating to
        what system you are running on (to create SRDSYS.MAC) and to what
        default switch settings you want for SRD (and will create SRD.BLD
        and SRD.ODL).  In future invocations you can use these files
        without having to create new copies each time.  SRD is a
        non-privileged task, with 5 units and a task name of ...SRD.  It
        should be task-built with the following options:

                    TSKV    =SSTVC$:7
                    STACK   =128
                    ASG     =TI:1
                    ASG     =SY:2:3:4
                    ASG     =TI:5
                    UNITS   =5



   SRD - Sorted Directory Utility                                   Page 24
   Version 6.6  12-Jun-85


                    GBLDEF  =..RWLG:1
                    GBLDEF  =SWINI:n
                    GBLDEF  =SW2INI:n
                    GBLDEF  =SW3INI:n
                    TASK    =...SRD




        6.2.1  SWINI - defines the initial switch settings of the first
        mask:

                         2 = /LI - List the directory
                    100000 = /NA - Sort by Name first




        6.2.2  SW2INI  - defines the initial switch settings of the second
        mask:

                        40 = /RD - Use Revision Date for date checks
                       100 = /SR - Sort the directory
                       400 = /SY - Include system accounts in [*,*]
                      1000 = /AT - Attach output device if terminal
                     10000 = /WD - Implicit wildcarding in delete
                     20000 = /WI - Implicit wildcarding in listing
                    100000 = /M2 - Type 2 Middle Size Listing



        6.2.3  SW3INI  - defines the initial switch settings of the third
        mask:

                         1 = /00 - Include [0,0] in [*,*]
                         2 = /SM - Include summary lines in listing
                         4 = /HD - Include command line in listing
                        10 = /BK - Put in 2 blanks ahead of file names




        6.3  SRD RSX-11M Overlay


        The overlay used currently except for RSX-11M V4/FCSRES is:  (Check
        the ODL file if FCSRES used in versions prior to V4, some SYSLIB
        references are deleted from the ODL below)

 .NAME  OV1INI
 .NAME  OPNFNB
 .NAME  PRSFNB
 .NAME  CSI12
 .ROOT  SRDR-*(O1,O2A,O2B,O2C,O4,O5)
 SRDR:  .FCTR SRDROT-SRDATA-SRDSUB-SRDTRP-LIBR



   SRD - Sorted Directory Utility                                   Page 25
   Version 6.6  12-Jun-85


 LIBR:  .FCTR LB:[1,1]SYSLIB/LB:ASSLUN:ARITH:CBTA:DIRECT:DEL:EOFCHK-LIBR2
 LIBR2: .FCTR LB:[1,1]SYSLIB/LB:MKDL:MOVREC:PGCS:RDWAIT:RETADR:WATSET
 O1:    .FCTR SRDINI-SRDREP-*(O11)
 O2A:   .FCTR SRDNUD
 O2B:   .FCTR SRDOPR-SRDXX1
 O2C:   .FCTR SRDSRT-SRDXX2
 O5:    .FCTR SRDDBF
 O4:    .FCTR SRDLST-SRDTST-LB:[1,1]SYSLIB/LB:PUTSQ-SRDXX3
 O11:   .FCTR OV1INI-*(OP1,PRS1,CSI1)
 OP1:   .FCTR OPNFNB-LB:[1,1]SYSLIB/LB:OPFNB:$PRINT
 PRS1:  .FCTR PRSFNB-LB:[1,1]SYSLIB/LB:PARSE
 CSI1:  .FCTR CSI12-LB:[1,1]SYSLIB/LB:.CSI1:.CSI2
 .END



6.3.1  SRD RSX-11M FCSRES Overlay - The overlay used on RSX-11M mapped
Version 4.0 with FCSRES is:

 .ROOT  OSRDR-*(O1,O2A,O2B,O2C,O4,O5)
 SRDR:  .FCTR SRDROT-SRDATA-SRDSUB-SRDTRP
 O1:    .FCTR SRDINI-SRDREP
 O2A:   .FCTR SRDNUD
 O2B:   .FCTR SRDOPR-SRDXX1
 O2C:   .FCTR SRDSRT-SRDXX2
 O4:    .FCTR SRDLST-SRDTST-SRDXX3
 O5:    .FCTR SRDDBF
 .END














                                APPENDIX A

                                 EXAMPLES




ALL examples are from the same directory.   The  first  example  shows  the
directory  as PIP would list it.  The /-SR switch tells SRD not to sort the
directory.


 ** DR2:[352,352] 20-OCT-83 01:45
>SRD /LI/-SR
SAVIT    .CMD;1
CASHFLOW .FTN;13
CHAR170  .SEQ;1
C        .FTN;27
EBCDIC   .B2S;3
EDTINI   .EDT;1
FIXUIC   .PRO;22
LOGIN    .CMD;3
MTDRV    .MAC;2
QFORMS   .CMD;34
CALC     .FTN;1
REPAIR   .PRO;13
TOOLS    .CMD;14
TVI      .CMD;2
CASHFLOW .CMD;5


 ** DR2:[352,352] 20-OCT-83 01:45
>SRD *.CMD/MI
CASHFLOW .CMD;5       17-MAY-83 13:46  20-OCT-83 01:02 (2.)
LOGIN    .CMD;3       19-MAY-83 19:14  20-OCT-83 01:02 (2.)
QFORMS   .CMD;34      21-JUL-83 11:50  20-OCT-83 01:02 (2.)
SAVIT    .CMD;1       09-JUL-83 19:24  20-OCT-83 01:02 (2.)
TOOLS    .CMD;14      08-AUG-83 11:19  20-OCT-83 01:02 (2.)
TVI      .CMD;2       29-JUL-83 07:41  20-OCT-83 01:02 (2.)





EXAMPLES                                                           Page A-2



 ** DR2:[352,352] 20-OCT-83 01:45
>SRD /NA
C        .FTN;27
CALC     .FTN;1
CASHFLOW .CMD;5
CASHFLOW .FTN;13
CHAR170  .SEQ;1
EBCDIC   .B2S;3
EDTINI   .EDT;1
FIXUIC   .PRO;22
LOGIN    .CMD;3
MTDRV    .MAC;2
QFORMS   .CMD;34
REPAIR   .PRO;13
SAVIT    .CMD;1
TOOLS    .CMD;14
TVI      .CMD;2


 (EXCLUDE all .CMD files and sort by name)
 ** DR2:[352,352] 20-OCT-83 01:45
>SRD *.CMD/NA/NE
C        .FTN;27
CALC     .FTN;1
CASHFLOW .FTN;13
CHAR170  .SEQ;1
EBCDIC   .B2S;3
EDTINI   .EDT;1
FIXUIC   .PRO;22
MTDRV    .MAC;2
REPAIR   .PRO;13


 (All files starting with "C" and sort them by version in
  descending order.)
 ** DR2:[352,352] 20-OCT-83 01:45
>SRD C*./SR:VD
C        .FTN;27
CASHFLOW .FTN;13
CASHFLOW .CMD;5
CALC     .FTN;1
CHAR170  .SEQ;1


 (Full listing of all files starting with "CA" then
  any two characters and any type.
  Must have four character file name.)
 ** DR2:[352,352] 20-OCT-83 01:45
>SRD /SE:CA%%.*/FU
CALC     .FTN;1      13./13.             [352,352] (14152,3)
   [RWED,RWED,RWED,R]     17-MAY-83 13:46  20-OCT-83 01:02 (2.)





EXAMPLES                                                           Page A-3



 ** DR2:[352,352] 20-OCT-83 01:45
>SRD /SE:*OW.*
CASHFLOW .CMD;5
CASHFLOW .FTN;13



SRD V6.6 INDEX                                                     Page A-4




            /-LI  . . . . . . . 6
            /-SR  . . . . . . . 11
            /00 . . . . . . . . 12
            /AE . . . . . . . . 5, 8, 21
            /AF . . . . . . . . 5, 8
            /AP . . . . . . . . 6
            /AT . . . . . . . . 13
            /BE . . . . . . . . 5, 8, 21
            /BF . . . . . . . . 5, 8
            /BK . . . . . . . . 15
            /CM . . . . . . . . 13
            /CO . . . . . . . . 5, 12
            /DA . . . . . . . . 5, 8, 15, 21
            /DE . . . . . . . . 10, 15
            /ER . . . . . . . . 5
            /FO . . . . . . . . 5, 9
            /FU . . . . . . . . 5, 6, 15
            /GT . . . . . . . . 5, 9
            /HD . . . . . . . . 14
            /HE . . . . . . . . 13, 15, 21
            /HV . . . . . . . . 7, 22
            /ID . . . . . . . . 9, 13, 15, 20
            /LI . . . . . . . . 5
            /LO . . . . . . . . 5, 12, 22
            /M2 . . . . . . . . 6, 11
            /MI . . . . . . . . 5, 6, 11, 15
            /MU . . . . . . . . 5, 12
            /NA . . . . . . . . 7
            /NE . . . . . . . . 7
            /NV . . . . . . . . 7
            /OV . . . . . . . . 7, 15
            /PA . . . . . . . . 15
            /PU . . . . . . . . 6, 10, 15
            /RD . . . . . . . . 6, 11
            /SD . . . . . . . . 10
            /SE . . . . . . . . 8, 9, 21, 22
            /SI . . . . . . . . 13, 15, 20
            /SM . . . . . . . . 15
            /SP . . . . . . . . 13
            /SR[:key1...] . . . 11
            /SV . . . . . . . . 7, 15, 22
            /SY . . . . . . . . 11
            /TB . . . . . . . . 5, 10
            /WB . . . . . . . . 6, 10, 22
            /WD . . . . . . . . 12
            /WI . . . . . . . . 12
            /ZE . . . . . . . . 5, 12

            ALERR . . . . . . . 21
            Allocation  . . . . 9
            Append  . . . . . . 6
            Attach terminal . . 13
            ATTDET  . . . . . . 21




SRD V6.6 INDEX                                                     Page A-5



            Blanks  . . . . . . 15
            Block size  . . . . 9
            Buffer Size (/SI) . 13
            Building SRD  . . . 23

            CNVDAT  . . . . . . 21
            Combining switches  . 15
            COMMAND LINE  . . . 3, 14
            Command Line Switches 4
            Contiguous  . . . . 12
            Creation Date . . . 6
            CVDATE  . . . . . . 21
            CVTIME  . . . . . . 21

            Date  . . . . . . . 8
            Default output file 3
            Delete  . . . . . . 10
            Directory Listing . 5
            DIRECTORY.LST . . . 3

            Error messages  . . 16
            Exclude files . . . 7

            FCSRES  . . . . . . 25
            File format . . . . 13
            File ID . . . . . . 6, 9
            File owner  . . . . 9
            Filespec  . . . . . 3
            Full listing  . . . 6

            Header  . . . . . . 14
            Help  . . . . . . . 13
            Highest versions  . 7

            Indirect command  . 2, 4, 13
            INVOKING SRD  . . . 2

            Keys  . . . . . . . 11

            Locked Files  . . . 12

            MFD . . . . . . . . 12
            Middle listing  . . 6
            Modules . . . . . . 20
            Multi-Header Files  . 12

            Name sort   . . . . 7
            No sort . . . . . . 11

            Obsolete  . . . . . 7
            Output  . . . . . . 3, 11, 13, 15, A-2
            Overlay . . . . . . 24

            PIP . . . . . . . . 2
            Purge files . . . . 10



SRD V6.6 INDEX                                                     Page A-6




            Quick reference . . 4

            Restrictions  . . . 15
            Revision Date . . . 6, 11
            Rewrite directory . 10

            Selective delete  . 10
            Sort  . . . . . . . 11
            Sort keys . . . . . 11
            Spaces  . . . . . . 15
            Spool files . . . . 13
            SRD version . . . . 13
            SRDATA  . . . . . . 20
            SRDCOM  . . . . . . 21
            SRDDBF  . . . . . . 23
            SRDINI  . . . . . . 21
            SRDLST  . . . . . . 22
            SRDNUD  . . . . . . 22
            SRDOPR  . . . . . . 22
            SRDPRE  . . . . . . 23
            SRDREP  . . . . . . 21
            SRDROT  . . . . . . 20
            SRDSRT  . . . . . . 22
            SRDSUB  . . . . . . 21
            SRDSYS  . . . . . . 23
            SRDTRP  . . . . . . 21
            SRDTST  . . . . . . 23
            SRDXX1/2/3  . . . . 23
            Summary lines . . . 15
            SW2INI  . . . . . . 24
            SW3INI  . . . . . . 24
            SWINI . . . . . . . 24
            Switch Actions  . . 5
            Switch Combinations 15
            Switch Defaults . . 16
            Switch summary  . . 4
            Switches  . . . . . 4
            SYSLIB  . . . . . . 20
            System manager  . . 20
            System UFD's  . . . 11, 12

            Task Structure  . . 20
            Total blocks  . . . 10
            Two spaces  . . . . 15

            UIC . . . . . . . . 9
            Usage . . . . . . . 5

            Version . . . . . . 7

            Wildcards . . . . . 8, 12
            Write back  . . . . 10

            Zero-Length Files . 12