ALEDA User Documentation



                      Aleda was written by Dennis V.  Jensen
                      of  the  Ames Laboratory at Iowa State
                      University as part of U.S.  Department
                      of Energy contract W-7405-ENG-82.  The
                      right to use this software release  is
                      allowed  in  the  public  domain.  The
                      author,  Ames  Laboratory,  and  USDOE
                      assume  no  responsibility  as  to the
                      correctness  of  the  code   nor   the
                      appropriateness for such use as it may
                      be applied.  Any  comments  about  the
                      Aleda  Library  may be directed to the
                      author  at  258H   Development,   Ames
                      Laboratory, Ames, Iowa  50011.








          1.0   Introduction                ____________

          Aleda is designed for the Fortran programmer to gain access to
          serial  ports for device interfacing and for user interaction.
          This library of  subroutines  provides  defaults  for  missing
          parameters   wherever   possible  yet  maintains  a  versatile
          programmable approach to interfacing.  The  nucleus  of  Aleda
          will   detect  the  operating  system  environment  (RT-11  or
          TSX-Plus) and adapt appropriately.  This is based  on  options
          configured  in  a  device  table and possibly overriden by the
          user's  program  at  run  time.   The  ability  to   implement
          overlapped  I/O  and  computation (asynchronous processing) is
          included.  Response to error conditions is also programmable.

          An Aleda routine is invoked with any of the following forms:

               Call Lprog ( ...  )

               Ierror = Lprog ( ...  )

               If ( Lprog( ...  ) ) goto <error processing>

          1.1   The Functional Value of Aleda subroutines                ___ __________ _____ __ _____ ___________

          All Aleda routines  are  setup  as  function  subprograms  and
          return  an  integer  as the functional value of the call.  The
          values returned indicate the result of  processing  the  call.
          These  routines  may  also  be accessed using the FORTRAN CALL
          statement.  When using the CALL statement it would be wise  to
          always  include  the  optional Return Code parameter to verify
          that the routine terminated with no errors.


                         ALEDA User Documentation                 PAGE 2
                         Aleda Conventions


          1.2   Required and Optional Parameters                ________ ___ ________ __________

          Aleda subprogram parameters are classified as either  required
          or  optional.   Required  parameters  are  necessary  for  the
          routines to carry out their specified task.  An error code  is
          returned  if  a required parameter is not provided.  Generally
          the required parameters are at the beginning of the  parameter
          list and optional parameters are at the end.

          Optional parameters are those that need not be provided in the
          call  list.   They  are  optional  because  they  have default
          values, or they return supplemental information  that  is  not
          necessary to complete the specified operation.  

          Parameters are positional;  they must always occupy  the  same
          position  in the call list.  Null parameters are those that do
          not specify a variable or constant at  an  optional  parameter
          position  in  the  list;  the delimiting commas are present or
          less than the maximum number of parameters are specified.  

          Note:  One restriction currently exists for LGETI2 and LGETR4.
          They  currently  require  that  trailing  commas exist for all
          non-specified optional parameters.  This is because  they  are
          written  in  Fortran  and  cannot  correctly  determine if the
          parameters exist unless an actual null entry is in the  user's
          call  list.   This  restriction  will be corrected in the near
          future.

          1.3   Return Code Parameters                ______ ____ __________

          Return codes are associated with most Aleda routines.  If  the
          return code is NEGATIVE then this code is an Aleda ERROR CODE.
          The return code value will be the same as the functional value
          of  an  Aleda  routine  when  an error has occured.  After the
          SUCCESSFUL COMPLETION of an Aleda  routine,  the  return  code
          will   typically  be  ZERO.   For  some  Aleda  routines,  the
          successful  return  code  will  be  a  count   of   characters
          transfered.   For  routines  which  interact  with the user, a
          return code value of ONE indicates a processing BREAK REQUEST.
          For   this  case,  the  functional  value  of  an  Aleda  user
          interaction routine can be non-zero without  being  an  actual
          error.   (Refer to the description of each routine to know how
          to interpret specific return codes.)

          1.4   Error Codes                _____ _____

          Aleda  indicates  that  processing  errors  have  occurred  by
          returning  a  negative  functional  value  for  the  call that
          detected an error.  In addition, if an  optional  Return  Code
          parameter  was  provided,  it  too  will  be assigned the same
          negative value.  A list of the defined error codes and a brief
          description of their meaning is provided in a table at the end
          of this document.  


                         ALEDA User Documentation                 PAGE 3
                         Aleda Conventions


          The routine LERROR will evaluate an Aleda error code and  list
          at   the   console   the   error  number  and  the  associated
          description.  Using optional  LERROR  parameters  a  user  can
          include  in  the  error  message  text  additional information
          specific to the program to help locate the exact point  and/or
          cause of the error.

          1.5   Control Word Parameters                _______ ____ __________

          Some Aleda routines have an optional control  word  parameter.
          The  value  of this parameter specifies variations in the type
          of processing a particular routine will do.   To  enable  more
          than  one  optional processing function it is necessary to sum
          the individual control word values of each  desired  function.
          (Refer to the description of each routine to know what control
          word options are available.)

          1.6   Logical Unit Numbers                _______ ____ _______

          A connection to a serial port is established through a logical
          unit  number.   Each  logical  unit  number  associates with a
          device descriptor that provides all  information  and  working
          storage  for  correctly  interfacing with a device or terminal
          port.  There is a logical unit for each input and each  output
          stream.   For  example,  the console keyboard is unit zero (0)
          and the console display is unit one (1)  by  convention.   All
          other  units  can  be  defined in addition to these to be such
          things  as  a  device  supported  under  RT-11  using   direct
          interrupts   (DLv11-types   of   interfaces),  as  a  TSX-Plus
          Communication  Line  (CL)  type  of  device,  and/or   dynamic
          configuration  to  adapt to either of these depending on which
          system is being run.  

          The device table is configured in Macro-11.  The  details  for
          configuring  these  tables  are  documented in the Macro files
          *dev*.mac .  Typically, this can be configured for your system
          once  and  used thereafter.  Some modifications can be applied
          from the Aleda call list for simple changes to the  table.   A
          typical  device  table  is included in the library and will be
          linked  into  an  Aleda  program  if  another  table  is   not
          explicitly  included in the link input files.  (See CLTABL.MAC
          which  is  the  distributed  device  table  included  in   the
          library.)

          For  interfacing  to  devices,  the  unit  number  is   always
          required.   For  interfacing  to  the user, the unit number is
          never specified because units 0 and 1 are always used to  talk
          to  the user's terminal.  Units 2 and 3 would typically be the
          input stream and output  stream  of  the  first  device  being
          interfaced.   The maximum unit number is configured internally
          as  24  but  can  be  easily  changed  in  the  ALV51C  module
          (DEVICES==24.).


                         ALEDA User Documentation                 PAGE 4
                         Aleda Conventions


          1.7   The Macro Call Conventions                ___ _____ ____ ___________

          Aleda provides access  to  facilities  which  were  originally
          developed in Macro-11.  Within the source files these routines
          are known as Alvin.  Alvin  provides  more  capabilities  than
          available   at   the   Fortran   level   but  with  associated
          complexities in their use.  The source for these routines  are
          well  documented.   For  brevity,  many of the details are not
          included here and the user will for now have to refer  to  the
          source  to  gain more information.  To aid in using Alvin, the
          $Alvin macro  is  defined  in  the  Alvin.MLB  macro  library.
          $Alvin defines table offsets of relevant descriptors and other
          structures which are used internally.  

          In a future release more documentation  will  be  included  on
          these extended features.  

          1.8   RT-11 Interrupt Considerations                _____ _________ ______________

          When running under RT-11, the interrupts will be processed  by
          inline service routines.  To be generally executable under all
          monitors and to avoid interference with the user's program, no
          .DEVICE  protection is provided automatically within Aleda.  A
          device can be dynamically enabled and then disabled  when  not
          in  use,  though.   And  NOABORT  can  be added to the console
          device definition (see DLTDEV) to prevent control-C aborts and
          to  allow  soft  error reporting.  For example, an LBREAK will
          detect a control-C, then a call to  ALVEXI  will  disable  all
          active  devices,  after  which  a  program  can  STOP  with no
          repercussions.   Of  course,  under  the  SJ  monitor   active
          interrupts  are  not an issue as a bus reset will be issued on
          abort.

          When an interrupt is enabled, the exact contents of the vector
          and  CSR  are retained.  These are restored when the device is
          disabled.  Therefore, what Aleda taketh, it giveth back to  be
          as it was before the enable.


                         ALEDA User Documentation                 PAGE 5
          Detailed Description of Aleda Device Interfacing Routines


          LENABL

          2.0   Description                ___________

          Fortran callable subroutine to enable  the  specified  logical
          unit number for the transfer of characters.

          2.1   Calling Sequence                _______ ________

               Ierror = LENABL ( Unitnumber, [Buffer], [BufferSize],
                                 [ReturnCode], [ControlWord], [CSR],
                                 [Vector], [AssociatedUnit]        )

          2.2   Parameter Description                _________ ___________

          Unitnumber:         Required parameter.  Logical  unit  number
                              of device to be enabled.
          Buffer:             Optional parameter.  Array which  will  be
                              used  as  the  circular  Buffer into which
                              data will  be  written  by  the  specified
                              logical unit.
          BufferSize:         Optional parameter.  Size in bytes of  the
                              buffer  mentioned  above.  Buffers must be
                              at least 20 bytes long.
          ReturnCode:         Optional parameter.  Variable which, after
                              the  call,  will  contain  a numeric value
                              indicating  the  success  or  reason   for
                              failure of a particular call.
          ControlWord:        Optional   parameter.    Value   indicates
                              certain  optional processing functions are
                              to be performed.   No  optional  functions
                              are currently defined for this routine.
          CSR:                Optional  parameter.    Address   of   the
                              Control  Status  Register of the device to
                              be  enabled.   (Applicable  to  RT  direct
                              interrupt support only.)
          Vector:             Optional parameter.  Interrupt  vector  of
                              device  to  be enabled.  (Applicable to RT
                              direct interrupt support only.)
          AssociatedUnit:     Currently not used.


                         ALEDA User Documentation                 PAGE 6
          Detailed Description of Aleda Device Interfacing Routines


          LDSABL

          3.0   Description                ___________

          Fortran callable subroutine to disable the  specified  logical
          unit  number.   I/O  will  be prohibited on the unit after the
          disable.  All interrupt linkage will be reverted to the  state
          prior to enable.

          3.1   Calling Sequence                _______ ________

               Ierror = LDSABL ( UnitNumber, [ReturnCode] )

          3.2   Parameter Description                _________ ___________

          UnitNumber:         Required parameter.  Logical  unit  number
                              of device to be disabled.
          ReturnCode:         Optional parameter.  Variable which, after
                              the  call,  will  contain  a numeric value
                              indicating  the  success  or  reason   for
                              failure of a particular call.



                         ALEDA User Documentation                 PAGE 7
          Detailed Description of Aleda Device Interfacing Routines


          LGETLN

          4.0   Description                ___________

          Fortran callable subroutine to access  the  specified  logical
          unit  number  for transfer of characters to the user specified
          buffer.

          4.1   Calling Sequence                _______ ________

               Ierror = LGETLN ( UnitNumber, Line, LineSize,
                                 [ReturnCode], [ControlWord],
                                 [TerminatorArray]           )

          4.2   Parameter Description                _________ ___________

          UnitNumber:         Required parameter.  Logical  unit  number
                              of the device from which characters are to
                              be transferred.
          Line:               Required  parameter.   Array  into   which
                              characters from the specified logical unit
                              will be transferred.
          LineSize:           Required parameter.  Size in bytes of  the
                              buffer LINE mentioned above.
          ReturnCode:        Optional parameter.  If positive- number of
                              characters  transferred  into  LINE on the
                              current call.  Else- error code.
          ControlWord:        Optional   parameter.    Value   indicates
                              certain  optional processing functions are
                              to be performed.
                  0           Do not perform any special processing.
                  1           Interpret  the  characters  in  the   user
                              specified  TerminatorArray  as end-of-line
                              characters.
                  2           Include  the   parity   bit   when   doing
                              character transfer.
          TerminatorArray:    Optional parameter.  String of  characters
                              which  will  be interpreted as end-of-line
                              characters.  The  first  byte  of  a  this
                              array  is  the  number of characters which
                              are terminators, then each terminator byte
                              follows immediately in the array.


                         ALEDA User Documentation                 PAGE 8
          Detailed Description of Aleda Device Interfacing Routines


          LPUTLN

          5.0   Description                ___________

          Fortran callable subroutine to output characters from  a  user
          specified line buffer to a specified logical unit number.

          5.1   Calling Sequence                _______ ________

               Ierror = LPUTLN ( Unitnumber, Line, LineSize,
                                 [ReturnCode], [ControlWord],
                                 [TerminatorArray]           )

          5.2   Parameter Description                _________ ___________

          UnitNumber:         Required parameter.  Logical  unit  number
                              of the device to be written to.
          Line:               Required parameter.   Array  to  hold  the
                              characters  which  will  be  output to the
                              device specified by the unit number.
          LineSize:           Required parameter.  Size  of  the  buffer
                              array LINE in bytes.
          ReturnCode:         Optional parameter.  Number of  characters
                              actually   transferred  to  the  specified
                              device on the current call.
          ControlWord:        Optional   parameter.    Value   indicates
                              certain  optional processing functions are
                              to be performed.
          TerminatorArray:    Optional parameter.  String of  characters
                              which  will  be interpreted as end-of-line
                              characters.  The  first  byte  of  a  this
                              array  is  the  number of characters which
                              are terminators, then each terminator byte
                              follows immediately in the array.

          5.3   Control Word Value Description                _______ ____ _____ ___________

                  0           Do not perform any special processing.
                  1           Interpret  the  characters  in  the   user
                              specified  TerminatorArray  as end-of-line
                              characters.
                  2           Include  the   parity   bit   when   doing
                              character transfer.
                  8           Output any  terminator  encountered  along
                              with the other characters.


                         ALEDA User Documentation                 PAGE 9
          Detailed Description of Aleda Device Interfacing Routines


          LRECEV

          6.0   Description                ___________

          Fortran  callable  subroutine  to  initiate  the  transfer  of
          characters  from  the specified logical unit number to an user
          specified circular buffer.  An LRecev is required  before  the
          first LGetLN to a specified logical unit.  Subsequent LRecev's
          are optional and can be used  to  accomplish  such  things  as
          flushing  the current contents of the circular buffer (control
          option RESET).

          6.1   Calling Sequence                _______ ________

               Ierror = LRECEV ( UnitNumber, [Buffer], [BufferSize],
                                 [ReturnCode], [ControlWord]       )

          6.2   Parameter Description                _________ ___________

          UnitNumber:         Required parameter.  Logical  unit  number
                              of  the  device  on  which  the  character
                              transfer is to be initiated.
          Buffer:             Optional parameter.  Array which  will  be
                              used  as  the  circular  buffer into which
                              data  will  be  written  by   the   device
                              specified by UnitNumber.
          BufferSize:         Size of the circular buffer in bytes.   If
                              size  =  0, then the buffer is presumed to
                              already be initialized
          ReturnCode:         Optional parameter.  Variable which, after
                              the  call,  will  contain a numberic value
                              indicating  the  success  or  reason   for
                              failure of a particular call.
          ControlWord:        Optional   parameter.    Value   indicates
                              certain  optional processing functions are
                              to be performed.  Alvin receive  functions
                              PARON,   PAROFF,  SILENT,  and  RESET  are
                              available.   (No  echo   is   SILENT=10000
                              octal, buffer RESET=1000 octal)


                         ALEDA User Documentation                PAGE 10
          Detailed Description of Aleda Device Interfacing Routines


          LERROR

          7.0   Description                ___________

          Fortran callable subroutine to output to the console a message
          associated with ALEDA error return codes.

          7.1   Calling Sequence                _______ ________

               Ierror = LERROR ( ErrorCode, [Value], [UserLine, Count] )

          7.2   Parameter Description                _________ ___________

          ErrorCode:          Required parameter.   Numeric  error  code
                              value  returned  by one of the other ALEDA
                              routines.
          Value:              Optional   parameter.     Numeric    value
                              supplied by the user which will be printed
                              at the console along with  the  associated
                              ALEDA error message.
          UserLine:           Optional  parameter.    Character   string
                              supplied by the user which will be printed
                              at the console along with  the  associated
                              ALEDA error message.
          Count:              Required parameter if  parameter  UserLine
                              specified,  otherwise  ignored.  Number of
                              characters in character string UserLine.


                         ALEDA User Documentation                PAGE 11
          Detailed Description of Aleda Device Interfacing Routines


          LCNVTD

          8.0   Description                ___________

          Fortran callable subroutine to  convert  a  two  byte  integer
          value   to   a   character  string  representing  the  decimal
          equivalent of that value.  The value of the optional parameter
          CONTROL WORD determines the format of the string returned.

          8.1   Calling Sequence                _______ ________

               Ierror = LCNVTD ( Value, Stringbuffer, [Returncode],
                                 [ControlWord]                     )

          8.2   Parameter Description                _________ ___________

          Value:              Required parameter.  Integer*2 value which
                              the   character   string   returned   will
                              represent.
          StringBuffer:       Required parameter.  Area into  which  the
                              character  string  representation of value
                              will be placed.   This  buffer  should  be
                              seven bytes long.
          ReturnCode:         Optional  parameter.   Number   of   valid
                              characters  in the converted string.  This
                              value  should  be  used  in  printing  the
                              string   returned  because,  with  certain
                              formatting   options,   StringBuffer   may
                              contain   garbage  characters  beyond  the
                              first ReturnCode number of characters.  
          ControlWord:        Optional parameter.  Value determines  the
                              format of the string returned.

          8.3   Control Word Values and Associated Formats                _______ ____ ______ ___ __________ _______

               0 (default)    Left justify  string  in  buffer  with  no
                              trailing decimal point.
               1,3            Right justify string in first 5  positions
                              of  buffer if value was positive, or first
                              6 positions if string has  a  minus  sign.
                              The string will contain leading zeroes and
                              will not include a decimal point.
               2              Same format as ControlWord = 1, except any
                              leading zeroes will become blanks.
               4              Left justify string and  include  trailing
                              decimal point.
               5,7            Right justify string in first 6  positions
                              of  buffer if value was positive, or first
                              7 positions if value  was  negative.   The
                              last  valid character in StringBuffer will
                              be a decimal point  and  the  string  will
                              include leading zeroes.
               6              Same format as ControlWord = 5, except any


                         ALEDA User Documentation                PAGE 12
          Detailed Description of Aleda Device Interfacing Routines


                              leading   zeroes  in  string  will  become
                              blanks.



                         ALEDA User Documentation                PAGE 13
          Detailed Description of Aleda User Interfacing Routines


          LPUTST

          9.0   Description                ___________

          Fortran callable subroutine to output a string to the  console
          listing device.  This routine expects strings to be terminated
          with a zero byte (null) or a backslash (\).  If the string  is
          terminated with a backslash, LPUTST will add a carriage return
          and a linefeed after the message has  been  transmitted.   The
          current maximum string length is 256 characters.

          9.1   Calling Sequence                _______ ________

               Ierror = LPUTST ( String, [ReturnCode] )

          9.2   Parameter Description                _________ ___________

          String:             Required parameter.  Character  string  to
                              be  output  to the console listing device.
                              String must be less  than  256  characters
                              long  and  terminate with a null byte or a
                              backslash.
          ReturnCode          Optional parameter.  Value  returned  will
                              be  the  number of characters transmitted,
                              if positive, or a negative error code.



                         ALEDA User Documentation                PAGE 14
          Detailed Description of Aleda User Interfacing Routines


          LGETI2

          10.0  Description                ___________

          Fortran callable subroutine to prompt for and accept, from the
          console  keyboard,  an  ascii string representing an Integer*2
          value,  convert   the   value   to   its   internal   16   bit
          representation,  and return the value to the caller.  Optional
          default, minimum, and maximum values may be  provided.   If  a
          default value is provided, it will be displayed along with the
          caller supplied Prompt.  If minimum and/or maximum values  are
          provided,  they will be displayed when keyboard input can't be
          converted to  a  valid  value,  eg.   entering  an  alphabetic
          character  in  response  to  the  prompt  will  cause an error
          message and the minimum and maximum values  to  be  displayed.
          Prompting  will  continue  until  a  valid  Integer*2 value is
          provided.

          10.1  Calling Sequence                _______ ________

               Ierror = LGETI2 ( Prompt, Var, [ReturnCode], [Default],
                                 [Minimum], [Maximum]                )

          10.2   Parameter Description                 _________ ___________

          Prompt:             Required parameter.  User supplied  string
                              which   will  be  output  to  the  console
                              listing device to prompt of input.
          Var:                Required  parameter.   Integer*2  variable
                              which    will    contain    the   internal
                              representation of  value  input  from  the
                              keyboard.
          ReturnCode:         Optional parameter.   Value  will  be  the
                              number   of   characters  input  from  the
                              keyboard  if  there  was   no   error   in
                              processing,  otherwise  it will contain an
                              error code value.
          Default:            Optional parameter.  Value  that  will  be
                              returned  if  a carriage return is entered
                              in response to the prompt for input.
          Minimum:            Optional parameter.  Minimum  valid  input
                              value.   Entering  a valued less than this
                              will cause an error message and the  valid
                              range of input values to be displayed, and
                              the user will be prompted to enter another
                              value.
          Maximum:            Optional parameter.  Maximum  valid  input
                              value.  Entering a value greater than this
                              will cause an error message and the  valid
                              range of input values to be displayed, and
                              the user will be prompted to enter another
                              value.


                         ALEDA User Documentation                PAGE 15
          Detailed Description of Aleda User Interfacing Routines


          LGETR4

          11.0  Description                ___________

          Fortran callable subroutine to prompt for and accept, from the
          console keyboard, an ascii string representing a Real*4 value,
          convert the value to its internal 4 byte  representation,  and
          return  the  value  to the caller.  Optional default, minimum,
          and maximum values may be provided.  If  a  default  value  is
          provided,  it will be displayed along with the caller supplied
          Prompt.  If minimum and/or maximum values are  provided,  they
          will  be displayed when keyboard input can't be converted to a
          valid value, eg.  entering an alphabetic character in response
          to  the prompt will cause an error message and the minimum and
          maximum values to be displayed.  Prompting will continue until
          a valid Real*4 value is provided.  Values may be in decimal or
          scientific notation, but, either way, input values and  values
          for parameters Default, Minimum and Maximum should all contain
          a decimal point.

          11.1  Calling Sequence                _______ ________

               Ierror = LGETR4 ( Prompt, Var, [ReturnCode], [Default],
                                 [Minimum], [Maximum]                )

          11.2  Parameter Description                _________ ___________

          Prompt:             Required parameter.  User supplied  string
                              which   will  be  output  to  the  console
                              listing device to prompt for input.
          Var:                Required parameter.  Real*4 variable which
                              will  contain  the internal representation
                              of value input from the keyboard.
          ReturnCode:         Optional parameter.   Value  will  be  the
                              number   of   characters  input  from  the
                              keyboard  if  there  was   no   error   in
                              processing,  otherwise  it will contain an
                              error code value.
          Default:            Optional parameter.  Value  that  will  be
                              returned  if  a carriage return is entered
                              in response to the prompt for input.
          Minimum:            Optional parameter.  Minimum  valid  input
                              value.   Entering  a valued less than this
                              will cause an error message and the  valid
                              range of input values to be displayed, and
                              the user will be prompted to enter another
                              value.
          Maximum:            Optional parameter.  Maximum  valid  input
                              value.  Entering a value greater than this
                              will cause an error message and the  valid
                              range of input values to be displayed, and
                              the user will be prompted to enter another
                              value.


                         ALEDA User Documentation                PAGE 16
          Detailed Description of Aleda User Interfacing Routines


          LGETYN

          12.0  Description                ___________

          Fortran callable subroutine to access the console input device
          for  a  yes  or  no response to a question.  This routine will
          return a 1 if a break was requested, a 2 if a yes response was
          entered,  and  a 3 if a no response was entered.  These return
          values imply that the routine  completed  normally.   Negative
          return  values are ALEDA errors.  The user supplies the prompt
          for input.

          12.1  Calling Sequence                _______ ________

               Ierror = LGETYN ( Prompt, [ReturnCode] )

          12.2  Parameter Description                _________ ___________

          Prompt:             Required parameter.  User supplied  string
                              which  will  represent a question having a
                              yes   or   no   answer.     LGETYN    will
                              automatically append a question mark and a
                              blank to the string.
          ReturnCode:         Optional  parameter.    Integer   variable
                              which  will,  after returning, contain the
                              same value as the functional return  value
                              of  the routine, ie.  1 = break requested,
                              2 = a yes response was entered, 3 =  a  no
                              response was entered, and negative value =
                              an ALEDA error occured.



                         ALEDA User Documentation                PAGE 17
          Detailed Description of Aleda User Interfacing Routines


          LBREAK

          12.0  Description                ___________

          Fortran callable subroutine to  check  if  the  console  input
          device  has a pending break request.  This routine will return
          a true functional value if a  break  has  been  requested.   A
          repercussion  of this routine is that the input buffer will be
          drained, thus eliminating any characters which may  have  been
          typed  ahead.  This routine is useful to escape from processes
          on demand.

          13.1  Calling Sequence                _______ ________

               If (LBREAK) Goto Exit




                         ALEDA User Documentation                PAGE 18
          Appendix A - Aleda Return Codes/Error Codes


          The following is a brief description of the  meaning  of  each
          numeric  return  code.  The meaning associated with each value
          returned  should  be  consistent  across  all  calls  to   all
          functions.

          Return Code         Description          ______ ____         ___________

               1              Break requested.
               0              Normal completion.
           -1 .. -19          Required parameter  n not provided.
             -20              No device descriptor.
             -21              Device not enabled.
             -22              Device already enabled.
             -23              CSR not in I/O page.
             -24              Vector out of range.
             -25              Device is not an input device.
             -26              Device is not an output device.
             -27              ALVIN enable failure.
             -28              ALVIN disable failure.
             -29              Device already active (Seized) and using a
                              different buffer.
             -30              Buffer not at least 20 bytes.
             -31              Buffer not word aligned.
             -32              Buffer overrun.
             -33              Terminator   processing   specified    but
                              terminator array not provided.
             -34              Terminator not found.
             -35              Input  error   detected   (parity   error,
                              character overrun, or framing error).
             -36              Console is seized.
             -37              No   buffer   descriptor   for   attempted
                              operation.
             -38              Failed to connect to CL.
             -39              Could not configure  for  CL  under  RT-11
                              (RT-11 direct interrupt support not genned
                              in).
             -40              Unit number is out of range.
             -41              Can not enable this device under TSX-plus.
             -42              Could not open channel to CL.
             -43              Direct interrupt table is full.
             -44              Vector is seized.