TSXLIB

                                       A
                             Library Implementation
                                       of
                              Programmed Requests
                                      for
                                 TSX-Plus V6.0




                                 DECUS #11-490




                          N. A. Bourgeois, Jr.       
                          NAB Software Services, Inc.
                          PO Box 20009               
                          Albuquerque, NM 87154      








                                    Abstract

                A library  of  FORTRAN  callable  routines  that
                implement  the EMTs provided by TSX-Plus is des-
                cribed.     Complete    descriptions,    calling
                sequences, examples of use, and library building
                procedures are given.






                                    [86b27a]


        TSXLIB V6.0                                               PAGE 2







                The information in this document is  subject  to
                change  without  notice  and  should not be con-
                strued as a commitment by NAB Software Services,
                Inc.   NAB  Software  Services , Inc. assumes no
                responsibility for any errors that may appear in
                this document.




                This document was originally  issued  by  Sandia
                National  Laboratories,  operated for the United
                States Department of Energy by  Sandia  Corpora-
                tion.


                                     Notice


                This document was originally  sponsored  by  the
                United  States  Government.   Neither the United
                States Government nor the United States  Depart-
                ment  of Energy, nor any of their employees, nor
                any of  their  contractors,  subcontractors,  or
                their  employees  makes any warranty, express or
                implied,  or  assumes  any  legal  liability  or
                responsibility for the accuracy, completeness or
                usefulness of any information,  apparatus,  pro-
                duct  or  process  disclosed, or represents that
                its  use  would  not  infringe  privately  owned
                rights.


                This work was originally funded by:

                       Headquarters, ESD / OCB / Stop 36
                       Hanscom Air Force Base, MA 01731 


        TSXLIB V6.0                                               PAGE 3







                The Reader's Comment form on the  last  page  of
                this   document  requests  the  user's  critical
                evaluation  to  assist  NAB  Software  Services,
                Inc. in preparing future documentation.




                                Acknowledgments


                The author wishes to thank S & H  Computer  Sys-
                tems,  Inc. for  its permission to reprint parts
                of their "TSX-Plus  Reference  Manual"  in  this
                document.

                The author wishes also to thank W. L. Jacklin of
                Sandia  National Laboratories for his assistance
                in reviewing this document and particularly  for
                his  help  with the many FORTRAN examples in the
                third chapter.




                                  ***********
                                  * CAUTION *
                                  ***********


                Much of both the MACRO-11 source codes  and  the
                FORTRAN  examples described in this document are
                as yet untried.


        TSXLIB V6.0                                               PAGE 4
        Table of Contents






                               Table of Contents


                 1.  Introduction . . . . . . . . . . . . .  7

                 2.  General Description  . . . . . . . . .  8
                     Communication Line Support . . . . . .  9
                     Detached Job Support . . . . . . . . .  9
                     Device Allocating and Deallocating . .  9
                     Device Mounting and Dismounting  . . .  9
                     Interprogram Message Communication . . 10
                     Job Priveleges Control . . . . . . . . 10
                     Job Status Monitoring  . . . . . . . . 11
                     Miscellaneous EMT Support  . . . . . . 11
                     ODT Activation Mode Support  . . . . . 11
                     Performance Analysis Support . . . . . 12
                     Real Time Program Support  . . . . . . 12
                     Shared Run Time System Support . . . . 15
                     Shared File Support  . . . . . . . . . 15
                     Special File Information . . . . . . . 16
                     Spooler Support  . . . . . . . . . . . 16
                     System Status Information  . . . . . . 17
                     Terminal Communication Support . . . . 17
                     Terminal Control Support . . . . . . . 17
                     User Name Support  . . . . . . . . . . 18
                     Windowing Support  . . . . . . . . . . 18

                 3.  Routine Descriptions . . . . . . . . . 19
                     BRKCTL . . . . . . . . . . . . . . . . 19
                     CNVAPA . . . . . . . . . . . . . . . . 20
                     DISMNT . . . . . . . . . . . . . . . . 20
                     GETREG . . . . . . . . . . . . . . . . 21
                     GTUNAM . . . . . . . . . . . . . . . . 21
                     HIEFOF . . . . . . . . . . . . . . . . 22
                     HIEFON . . . . . . . . . . . . . . . . 22
                     IACTCH . . . . . . . . . . . . . . . . 23
                     IALOC  . . . . . . . . . . . . . . . . 23
                     IAQFLC . . . . . . . . . . . . . . . . 24
                     IASRNT . . . . . . . . . . . . . . . . 25
                     IBICIO . . . . . . . . . . . . . . . . 26
                     IBISIO . . . . . . . . . . . . . . . . 26
                     IBSTCH . . . . . . . . . . . . . . . . 27
                     ICALOC . . . . . . . . . . . . . . . . 27
                     ICKWTS . . . . . . . . . . . . . . . . 28
                     ICNINT . . . . . . . . . . . . . . . . 29
                     ICNMCN . . . . . . . . . . . . . . . . 30
                     ICNRTN . . . . . . . . . . . . . . . . 30
                     ICNTSP . . . . . . . . . . . . . . . . 31
                     ICONTM . . . . . . . . . . . . . . . . 32
                     ICPUTM . . . . . . . . . . . . . . . . 33
                     ICRWND . . . . . . . . . . . . . . . . 34


        TSXLIB V6.0                                               PAGE 5
        Table of Contents


                     IDALOC . . . . . . . . . . . . . . . . 35
                     IDCLSF . . . . . . . . . . . . . . . . 36
                     IDLWND . . . . . . . . . . . . . . . . 37
                     IESMCN . . . . . . . . . . . . . . . . 38
                     IEXSTS . . . . . . . . . . . . . . . . 39
                     IFLINF . . . . . . . . . . . . . . . . 40
                     IHERR  . . . . . . . . . . . . . . . . 41
                     ILNSTS . . . . . . . . . . . . . . . . 41
                     INITPA . . . . . . . . . . . . . . . . 42
                     IPEKIO . . . . . . . . . . . . . . . . 42
                     IPGNAM . . . . . . . . . . . . . . . . 43
                     IPOKIO . . . . . . . . . . . . . . . . 43
                     IPPNUM . . . . . . . . . . . . . . . . 44
                     IPRIV  . . . . . . . . . . . . . . . . 45
                     IPRWND . . . . . . . . . . . . . . . . 47
                     IRDRCL . . . . . . . . . . . . . . . . 47
                     IRLINT . . . . . . . . . . . . . . . . 48
                     IRSWND . . . . . . . . . . . . . . . . 49
                     ISERR  . . . . . . . . . . . . . . . . 49
                     ISLWND . . . . . . . . . . . . . . . . 50
                     ISPBLK . . . . . . . . . . . . . . . . 50
                     ISPCTL . . . . . . . . . . . . . . . . 51
                     ISPPA  . . . . . . . . . . . . . . . . 51
                     ISPWND . . . . . . . . . . . . . . . . 52
                     ISPY . . . . . . . . . . . . . . . . . 52
                     ISTDJ  . . . . . . . . . . . . . . . . 53
                     ISTFTM . . . . . . . . . . . . . . . . 54
                     ISTPA  . . . . . . . . . . . . . . . . 55
                     ISTPRV . . . . . . . . . . . . . . . . 55
                     ISVST  . . . . . . . . . . . . . . . . 55
                     ITCRTN . . . . . . . . . . . . . . . . 56
                     ITRCTL . . . . . . . . . . . . . . . . 57
                     ITRERR . . . . . . . . . . . . . . . . 57
                     ITRTYP . . . . . . . . . . . . . . . . 58
                     ITSLIC . . . . . . . . . . . . . . . . 58
                     ITSLIN . . . . . . . . . . . . . . . . 58
                     IUALBK . . . . . . . . . . . . . . . . 59
                     IUNLKM . . . . . . . . . . . . . . . . 60
                     IUSPBK . . . . . . . . . . . . . . . . 60
                     KLDTJB . . . . . . . . . . . . . . . . 61
                     LKANMY . . . . . . . . . . . . . . . . 61
                     LKBLK  . . . . . . . . . . . . . . . . 62
                     LKBLKW . . . . . . . . . . . . . . . . 63
                     LKLOMY . . . . . . . . . . . . . . . . 63
                     MAPRNT . . . . . . . . . . . . . . . . 64
                     MEMPOS . . . . . . . . . . . . . . . . 66
                     MEMSET . . . . . . . . . . . . . . . . 66
                     MEMUSE . . . . . . . . . . . . . . . . 67
                     MOUNT  . . . . . . . . . . . . . . . . 67
                     MPIOPS . . . . . . . . . . . . . . . . 68
                     MPRGN  . . . . . . . . . . . . . . . . 68
                     MPRMPS . . . . . . . . . . . . . . . . 69
                     MSGREQ . . . . . . . . . . . . . . . . 69
                     MSGSND . . . . . . . . . . . . . . . . 70
                     NONINT . . . . . . . . . . . . . . . . 71


        TSXLIB V6.0                                               PAGE 6
        Table of Contents


                     RCVMSG . . . . . . . . . . . . . . . . 72
                     RCVMSW . . . . . . . . . . . . . . . . 73
                     RLCTL  . . . . . . . . . . . . . . . . 74
                     RSTODT . . . . . . . . . . . . . . . . 74
                     SETODT . . . . . . . . . . . . . . . . 74
                     STDTJB . . . . . . . . . . . . . . . . 74
                     STPRLV . . . . . . . . . . . . . . . . 75
                     STUNAM . . . . . . . . . . . . . . . . 75
                     TERMPA . . . . . . . . . . . . . . . . 76
                     TIMOUT . . . . . . . . . . . . . . . . 77
                     TKCTL  . . . . . . . . . . . . . . . . 78
                     TRMIN  . . . . . . . . . . . . . . . . 78
                     TRMMSG . . . . . . . . . . . . . . . . 79
                     TRMOUT . . . . . . . . . . . . . . . . 79
                     TTCRTN . . . . . . . . . . . . . . . . 80

                 4.  Building the Library . . . . . . . . . 81

                 References . . . . . . . . . . . . . . . . 83

                 Appendix A:  KWIK Index  . . . . . . . . . 84

                 Appendix B:  Distribution Kit  . . . . . . 92


        TSXLIB V6.0                                               PAGE 7
        Introduction






                                1.  Introduction


             When application programs are executed under a time sharing
        executive  such  as  TSX-Plus  [1,2] certain capabilities become
        desirable  if  not  absolutely  essential.   These  capabilities
        relate  to  requirements  for  such things as hardware dependent
        I/O,  shared  files,  interprogram  communication,  and  others.
        TSX-Plus  provides  a  number of programmed requests or EMTs for
        these purposes.

             This document describes a number of FORTRAN [6,7]  callable
        routines  and their calling sequences that implement these EMTs.
        All of the routines are callable as FORTRAN subroutines and some
        are  also callable as FORTRAN functions.  The routines are writ-
        ten in MACRO-11 [3].

             The next  section  offers  a  general  description  of  the
        several  groups of routines.  It describes the process for link-
        ing the  routines  to  the  FORTRAN  application  program.   The
        general calling sequences are also described.

             The third section gives a detailed description of  each  of
        the individual routines.  The descriptions include both the cal-
        ling sequences and, in most cases, examples.

             Procedures for constructing the library  from  the  several
        source modules are given in the fourth section.

             Appendix A contains a key-word-in-context (KWIK)  index  of
        the routines.

             A description of  the  distribution  kit  is  contained  in
        Appendix B.


                                      NOTE

             TSX-Plus is a registered trademark of  S & H  Computer
             Systems Inc., Nashville, TN.




        TSXLIB V6.0                                               PAGE 8
        General Description






                            2.  General Description


             These TSX-Plus library routines provide facilities to  sup-
        port  communication  lines, detached jobs, device allocating and
        deallocating, file structured device mounting  and  dismounting,
        communication  between running programs, job privileges control,
        job status monitoring, program performance analysis,  real  time
        program  execution,  shared run time systems, shared files, spe-
        cial files information, spooler control,  communication  between
        running  programs  and a terminal, program control of the termi-
        nal, ODT activation mode,  user  name  control,  windowing,  and
        several miscellaneous EMTs.

             The standard  FORTRAN  [6,7]  subroutine  calling  sequence
        shown  below  may  be  used to access all of the routines in the
        TSX-Plus library.

                          CALL RTNAM ( ARG1,...,ARGn )

             Those routines that return only one value are also callable
        as FORTRAN functions.  This is as follows:

                         IRET = RTNAM ( ARG1,...,ARGn )

             The application program is first compiled as follows:

                                .RUN SY:FORTRAN
                                *MYPROG=MYPROG 
                                *^C            

             Then the routines are linked with the  application  program
        as shown below:

                            .RUN SY:LINK           
                            *MYPROG=MYPROG,TSXLIB/F
                            *^C                    
                                       or
                      .RUN SY:LINK                       
                      *MYPROG=MYPROG,TSXLIB,SYSLIB,FPULIB
                      *^C                                

             The application program is now ready for execution.

                                 .RUN DK:MYPROG

             The "TSX-Plus Reference Manual" [1] describes how the  EMTs
        implemented  in  this  TSX-Plus  library  are  accessed  from  a
        MACRO-11 program.  However,  the  FORTRAN/MACRO  interface  des-
        cribed in the "RT-11 Programmer's Reference Manual" [5] may also
        be used to access the routines in the library.


        TSXLIB V6.0                                               PAGE 9
        General Description


             In the sections that  follow,  the  name  of  the  MACRO-11
        source file containing the listed routines is given in the title
        of each of the tables.


    Communication Line Support

             Table 2-1 lists the TSXLIB routines that offer certain com-
        munication line support from within a running program.

                IRDRCL  Redirect a communication or timesharing line.
                ICNTSP  Control  the  speed  of   a   communication   or
                        timesharing line.

                          Communication line support.
                                   CLLINE.MAC
                                   Table 2-1.


    Detached Job Support

             Table 2-2 lists the routines that provide detached job sup-
        port from within an executing program.

                ISTDJ   Get the status of a detached job.
                KLDTJB  Kill a detached job.
                STDTJB  Start a detached job.

                             Detached job support.
                                   DETJBS.MAC
                                   Table 2-2.


    Device Allocating and Deallocating

             System services are available to allow a running program to
        control the allocation of a device for exclusive use.  Table 2-3
        lists these routines.  Once a device has  been  allocated  to  a
        job,  no  other  job  is allowed to access the device.  A device
        allocated to a primary line or associated virtual  line  may  be
        accessed by any of the associated lines.

                IALOC   Allocate a device.
                IDALOC  Deallocate a device.
                ICALOC  Check the allocation status of a device.

                      Device allocating and deallocating.
                                   DVALOC.MAC
                                   Table 2-3.


    Device Mounting and Dismounting

             It is possible to mount and dismount a file structured dev-
        ice  for  directory  caching from within a running program.  The


        TSXLIB V6.0                                              PAGE 10
        General Description


        routines listed in Table 2-4 provide these capabilities.

                DISMNT  Dismount a file structured device.
                MOUNT   Mount a file structured device.

                        Device mounting and dismounting.
                                   MNTDEV.MAC
                                   Table 2-4.


    Interprogram Message Communication

             TSX-Plus provides an optional facility that allows  running
        programs  to  communicate  with each other.  Table 2-5 lists the
        routines that support this interprogram message communication.

                MSGREQ  Post a read request for a message.
                MSGSND  Send a message to another job.
                RCVMSG  Try to receive a message from another job.
                RCVMSW  Wait for a message from another job.

                      Interprogram message ãommunication.
                                   MSGCOM.MAC
                                   Table 2-5.

             Messages are transferred between programs  by  using  named
        message  channels.   A  message channel accepts a message from a
        sending program, stores the message in a queue  associated  with
        the  channel, and delivers the message to a receiving program on
        its request for a message on the channel.  Message channels  are
        separate from I/O channels.

             Each active message channel has associated with it an ASCII
        character  name  that  is used by both the sending and receiving
        programs to identify the channel.  The names associated with the
        channels  are  defined  dynamically  by the running programs.  A
        message channel is active when messages are being  held  in  the
        queue associated with the channel or if a program is waiting for
        a message from the channel.  When message channels become  inac-
        tive they are returned to a free pool and may then be reused.

             Once a message is queued on a channel,  that  message  will
        remain in the queue until some program receives it.  A program's
        exiting to the keyboard monitor does not remove any pending mes-
        sages.   This  allows one program to leave a message for another
        program that will be run at a later time.


    Job Privileges Control

             Table 2-6 lists the routines that permit an executing  pro-
        gram  to determine and make certain changes in its own executing
        environment.


        TSXLIB V6.0                                              PAGE 11
        General Description


                IPRIV   Determine or change the job privilege sets.
                ISTPRV  Set the current job's priority value.
                NONINT  Set the [non]interactive job status.

                             Job Privileges Control
                                   JBPRIV.MAC
                                   Table 2-6.


    Job Status Monitoring

             A facility is available for one job to monitor  the  status
        of  one  or more other jobs.  Once a job has declared to monitor
        another job, a completion routine is executed in the  monitoring
        job  whenever  a  change of status occurs in the job being moni-
        tored.  The services provided for job monitoring are  listed  in
        Table 2-7.

                IESMCN  Establish a job status monitoring connection.
                ICNMCN  Cancell a job status monitoring connection.
                IBSTCH  Broadcast a job status change.

                             Job status monitoring.
                                   JBSTMN.MAC
                                   Table 2-7.


    Miscellaneous EMT Support

             Table 2-8 lists the routines that support the several  mis-
        cellaneous EMTs provided by TSX-Plus.

                GETREG  Get  the  word  and  byte  values  stored  in  a
                        processor register.
                IHERR   Enable abort on certain errors.
                ISERR   Inhibit abort on certain errors.
                ISPY    Return values from  within  the  simulated  RMON
                        (SYSLIB routine).
                ITSLIC  Determine the TSX-Plus license number.
                ITSLIN  Determine the TSX-Plus line number.
                MEMSET  Set the memory allocation.

                           Miscellaneous EMT support.
                                   TSXMSC.MAC
                                   Table 2-8.


    ODT Activation Mode Support

             ODT activation mode may be turned on and off from within  a
        running program.  Table 2-9 lists the routines that support this
        feature.  In this mode TSX-Plus considers all characters  to  be
        activation  characters  except the digits, the comma, the dollar
        sign and the semicolon.


        TSXLIB V6.0                                              PAGE 12
        General Description


                RSTODT  Reset normal activation mode.
                SETODT  Set ODT activation mode.

                          ODT activation mode support.
                                   TSXODT.MAC
                                   Table 2-9.


    Performance Analysis Support

             For many applications the keyboard  monitor  level  perfor-
        mance   analysis  control  provided  by  TSX-Plus  is  adequate.
        Specifically, in cases such as analyzing the performance  of  an
        overlayed  program it is necessary to have control over the per-
        formance  analysis  feature  from  the  running  program.    The
        routines listed in Table 2-10 provide just this capability.

                INITPA  Initialize for a performance analysis.
                ISPPA   Stop a performance analysis.
                ISTPA   Start a performance analysis.
                TERMPA  Terminate from a performance analysis.

                         Performance analysis support.
                                  PRFANL.MAC 
                                  Table 2-10.


    Real Time Program Support

             The real time program support provided by  TSX-Plus  allows
        multiple  real  time programs to be run concurrently with normal
        time sharing operations.  The basic functions provided  by  this
        facility are listed in Table 2-11.

             A program must have operator privilege to use  any  of  the
        real  time  routines.  The real time facilities are available to
        both normal  jobs  controlled  by  time  sharing  lines  and  to
        detached jobs.  Detached jobs started by time sharing users have
        operator privilege only if the user starting them does.

             A basic facility required by many real time programs is the
        ability  to  access  the  I/O page which contains the peripheral
        device registers.  A normal time sharing job does not have  this
        access.   It is instead mapped to a simulated RMON.  This allows
        programs that directly access offsets into RMON to run  correct-
        ly.

             A real time program can access the I/O page in one  of  two
        ways.   It  can map the I/O page into the program's space, or it
        can leave the simulated RMON mapped into the program's space and
        perform  peek,  poke, bit set, and bit clear operations into the
        I/O page.  It is much more efficient to directly access the dev-
        ice  registers  by mapping the I/O page into the program's space
        than to use the routines  to  perform  each  individual  access.
        However,  this  technique will not work if the program must also


        TSXLIB V6.0                                              PAGE 13
        General Description


        directly access offsets into RMON.  The correct  way  to  access
        offsets  into  RMON is with the SYSLIB routine, ISPY, which will
        work even if the I/O page is mapped into the program's space.

                CNVAPA  Convert a virtual address to a physical address.
                IBICIO  Bit clear a value into the I/O page.
                IBISIO  Bit set a value into the I/O page.
                ICNINT  Connect an  interrupt  vector  to  a  completion
                        routine.
                ICNRTN  Connect a service routine to an  interrupt  vec-
                        tor.
                IPEKIO  Peek at a value in the I/O page.
                IPOKIO  Poke a value into the I/O page.
                IRLINT  Release an interrupt vector connection.
                ITCRTN  Trigger a completion routine from  an  interrupt
                        service routine.
                IUNLKM  Unlock a job from memory.
                LKANMY  Lock a job into any memory.
                LKLOMY  Lock a job into low memory.
                MPIOPS  Map the I/O page into the program space.
                MPRGN   Map a region of virtual memory  to  a  specified
                        region of physical memory.
                MPRMPS  Map the simulated RMON into the program space.
                RLCTL   Relinquish exclusive control of the system.
                STPRLV  Set the user mode processor priority level.
                TKCTL   Take exclusive control of the system.

                           Real time program support.
                                   RELTIM.MAC
                                  Table 2-11.

             The  TSX-Plus  real  time  support  facility  provides  two
        methods  to  connect real time interrupts to TSX-Plus jobs.  The
        first of these methods uses the mechanism of completion routines
        to  perform  the  connection.  The second method provides a more
        direct connection between interrupts  and  service  routines  in
        TSX-Plus  jobs.   Once  a connection is established the routine,
        completion or service,  is  executed  each  time  the  specified
        interrupt  occurs.  It is possible for several interrupt vectors
        to be connected to the same completion routine in a job  but  it
        is  illegal  for more than one job to connect to the same inter-
        rupt vector.

             With the first method  an  interrupt  causes  a  completion
        routine  to  be  queued  for  the  job that was connected to the
        interrupt vector.  This method is very general  and  allows  the
        completion  routine  to call for system services (execute EMTs).
        Also the job does not have to be locked in memory.  On entry  to
        the  completion  routine,  R0 contains the address of the vector
        that caused the completion routine to be entered.

             The second method sets up  conditions  for  the  job  being
        called  and enters the interrupt service routine.  This approach
        minimizes the overhead in entering the service routine.   Hence,
        the  service  routine method can process interrupts at a greater


        TSXLIB V6.0                                              PAGE 14
        General Description


        rate than can be processed using the completion routine method.

             There are restrictions imposed on a program using the  ser-
        vice  routine  method.   Specifically,  the following conditions
        must be met to directly connect to an interrupt:

            1.  The job must be locked in memory before connecting it to
                the interrupt vector and must remain locked in memory as
                long as the interrupt connection is in effect.

            2.  The processing done by the service routine should not be
                very  lengthy  since  other  interrupts may be queued up
                during execution of the service routine.

            3.  Only two system services  may  be  legally  called  from
                within   the  service  routine.   They  are  the  SYSLIB
                routine, RESUME, and the TSXLIB routine, ITCRTN.

             The interrupt service routine runs in user  mode  and  uses
        memory  mapping that has been established for the job before the
        interrupt occurs.  Access to the I/O page via the MPIOPS routine
        is  possible  provided this mapping has been set up in the main-
        line code before the interrupt occurs.

             If an interrupt service routine needs to perform  a  system
        service  other  than  the  RESUME  call  listed above, it should
        trigger a completion routine via a call to ITCRTN and  have  the
        completion routine call for the required system service(s).

             An execution priority may be specified for each  completion
        routine.  This is not the same as the hardware selected priority
        of the interrupt.  All completion routines are synchronized with
        the job and run at hardware priority level zero.  The completion
        routine priority is used to  schedule  completion  routines  for
        execution.   The  available  priority  levels are 0 through 127.
        The execution of a real time completion routine for one job will
        be  interrupted and suspended if an interrupt occurs that causes
        a higher priority completion  routine  for  another  job  to  be
        queued for execution.  However, a completion routine for a given
        job will never be interrupted to run another completion  routine
        for the same job even if a higher priority completion routine is
        pending.

             Completion routine priorities one and larger are real  time
        priorities.   They  are higher than the priorities given to time
        sharing jobs and will always  preempt  the  time  sharing  jobs.
        Completion routine priority zero is not a real time priority but
        rather a very high normal priority.  Such zero priority  comple-
        tion  routines  are  time  sliced  in  the normal fashion.  If a
        completion routine enters a wait state it relinquishes its  real
        time  priority.  Jobs that have real time, interrupt driven com-
        pletion routines need not be locked in memory.

             In time critical, real time applications  where  a  program
        must  respond  to  an  interrupt  with  minimum delay, it may be


        TSXLIB V6.0                                              PAGE 15
        General Description


        necessary for the job to lock itself in memory to avoid the time
        consumed in program swapping.  This facility should be used with
        caution since if a number of large programs are locked in memory
        there may not be enough space left to run other programs.

             A running program may gain exclusive access to  the  system
        to perform some time-critical task.  The program may then relin-
        quish this exclusive access when it is not  needed.   A  running
        program  may  also  set  the  user mode priority level and map a
        region of virtual memory to a specified region of physical memo-
        ry.


    Shared Run Time System Support

             TSX-Plus provides a facility that allows  shared  run  time
        systems  or  data  areas to be mapped into the address spaces of
        multiple time sharing jobs.  Table 2-12 lists the routines  that
        support this feature.

                IASRNT  Associate/disassociate a shared run time  system
                        with a job.
                MAPRNT  Map a  shared  run  time  system  into  a  job's
                        region.

                        Shared run time system support.
                                  RUNTIM.MAC 
                                  Table 2-12.

             Memory space can be conserved by having several jobs access
        a  common  copy of a run time system rather than having to allo-
        cate space within each job.  Shared run time systems  are  never
        swapped out of memory.  When a job is associated with a run time
        system, a portion of the job's virtual memory is mapped so as to
        allow access to the run time system.


    Shared File Support

             Table 2-13 lists the routines  that  offer  access  to  the
        shared  file record locking facility provided by TSX-Plus.  This
        is useful in situations where programs being  run  from  several
        terminals  wish  to  update  a  common file.  Through the record
        locking facility a program may gain exclusive access to  one  or
        more  blocks  in  a  shared file by locking those blocks.  Other
        users attempting to lock the same blocks will be  denied  access
        until the first user releases the locked blocks.


        TSXLIB V6.0                                              PAGE 16
        General Description


                ICKWTS  Check for writes to a shared file.
                IDCLSF  Declare a file to be shared.
                ISVST   Save the status of a shared file.
                IUALBK  Unlock all locked blocks.
                IUSPBK  Unlock a specific block.
                LKBLK   Try to lock a block.
                LKBLKW  Wait for a block to lock.

                              Shared file support.
                                  SHRFIL.MAC 
                                  Table 2-13.

             The recommended procedure for updating a shared file  being
        accessed by several users is as follows:

            1.  Open the file.
            2.  Declare the file to be shared.
            3.  Lock all blocks which contain the desired record.
            4.  Read the locked blocks into memory.
            5.  Update the record.
            6.  Write the updated blocks to the file.
            7.  Unlock the blocks.
            8.  Repeat steps three through seven as required.
            9.  Close the file.


    Special File Information

             TSX-Plus allows a running program to obtain certain  status
        information about a file and to set the creation time of a file.
        Table 2-14 lists the routines that support this facility.

                IFLINF  Obtain some information about a file.
                ISTFTM  Set the creation time of a file.

                           Special file information.
                                  TSFILS.MAC 
                                  Table 2-14.


    Spooler Support

             Table 2-15 lists the routines that provide spooler  support
        available to an executing program.

                ISPBLK  Determine the number of free blocks in the spool
                        file.
                ISPCTL  Control the release time of a spooled file.

                                Spooler Support.
                                  SPOLER.MAC 
                                  Table 2-15.


        TSXLIB V6.0                                              PAGE 17
        General Description


    System Status Information

             Information typical of that returned by the SYSTAT keyboard
        command  is  made available to a running program by the routines
        listed in Table 2-16.

                ICONTM  Determine the connect time for a job.
                ICPUTM  Get the CPU time used by a job.
                IEXSTS  Get a job's execution status.
                ILNSTS  Check the status of a line.
                IPGNAM  Get the name of the program being run by a job.
                IPPNUM  Get the project-programmer number for a job.
                MEMPOS  Determine the position of a job in memory.
                MEMUSE  Determine the amount of memory used by a job.

                           System status information.
                                  SYSTAT.MAC 
                                  Table 2-16.


    Terminal Communications Support

             The routines that allow a running  program  to  communicate
        with a terminal are listed in Table 2-17.

                TRMIN   Accept a string of characters from the terminal.
                TRMMSG  Send a message to another terminal.
                TRMOUT  Send a string of characters to the terminal.

                        Terminal ãommunications support.
                                  TRMCOM.MAC 
                                  Table 2-17.


    Terminal Control Support

             The terminal control support routines are listed  in  Table
        2-18.

                BRKCTL  Establish break sentinel control.
                HIEFOF  Turn off the high efficiency terminal mode.
                HIEFON  Turn on the high efficiency terminal mode.
                IACTCH  Check for pending activation characters.
                ITRCTL  Perform lead-in character type terminal  control
                        functions.
                ITRERR  Check for terminal input errors.
                ITRTYP  Determine the terminal type.
                TIMOUT  Set the terminal read time out value.
                TTCRTN  Establish a terminal completion routine.

                           Terminal control support.
                                  TRMCTL.MAC 
                                  Table 2-18.


        TSXLIB V6.0                                              PAGE 18
        General Description


    User Name Support

             An executing program may set and change the user  name  for
        the connected job.  The routines for this facility are listed in
        Table 2-19.

                GTUNAM  Get the user name associated  with  the  current
                        job.
                STUNAM  Set the user name associated  with  the  current
                        job.

                               User name support.
                                  USRNAM.MAC 
                                  Table 2-19.


    Windowing Support

             TSX-Plus offers a full screen process windowing system that
        allows  the  system  to  remember the contents and status of the
        terminal display.  A running program may  redisplay  windows  on
        demand.   The  routines  for  this  facility are listed in Table
        2-20.

             When windowing is used, the system monitors all  characters
        sent  to the terminal and maintains an updated screen image dis-
        play  in  memory.   Terminal  attributes  such  as  line  width,
        reverse/norman  video,  application  keypad  mode,  and etc. are
        saved along with line attribures (double wide, double high)  and
        character   attributes.    The   attributes  retained  for  each
        character consist of blinking, bold, underlined, reverse  video,
        and  character  set information (ASCII, UK, DEC supplemental, or
        graphics).

             The most common use of windows is to completely refresh the
        display when switching among subprocesses to avoid the confusion
        of mixed displays.  For some program  applications,  it  may  be
        useful to utilize multiple windows from the same job.

                ICRWND  Create a window.
                IDLWND  Delete a window.
                IPRWND  Print the contents of a window.
                IRSWND  Resume window processing.
                ISLWND  Select a window.
                ISPWND  Suspend window processing.

                               Windowing Support
                                  WINDOW.MAC 
                                  Table 2-20.


        TSXLIB V6.0                                              PAGE 19
        Routine Descriptions






                            3.  Routine Descriptions


             This section presents  all  of  the  TSX-Plus  routines  in
        alphabetical  order  and provides a detailed description of each
        one.  The FORTRAN calling  sequence  and  where  appropriate  an
        example of each call in a FORTRAN program is given.

             The user should be thoroughly  familiar  with  the  general
        description  of this TSX-Plus library given in the previous sec-
        tion of this document.  Additional information is  available  in
        the  "TSX-Plus Reference Manual" [1] and the "RT-11 Programmer's
        Reference Manual" [5].  Some of these  TSXLIB  routines  require
        calls to various SYSLIB routines.

             In the following descriptions, arguments enclosed in square
        brackets, [], are optional.


    BRKCTL

             This routine is used to declare a completion  routine  that
        will  be  triggered  when the BREAK key or a declared key on the
        terminal is pressed.  The calling sequence is:

                         CALL BRKCTL ( IBRKCH,CPLRTN )

        where:  IBRKCH  is the value of the character that is to be used
                        for the break control.

                CPLRTN  is the name of the completion routine to be exe-
                        cuted when the break character is pressed.

             The specified  completion  routine  will  be  entered  when
        either  the  BREAK  key  or  the declared key is pressed.  If no
        declared key is wanted specify a value of zero for  IBRKCH.   On
        some  systems  the  console terminal BREAK key causes entry into
        console ODT and for this reason requires a declared key value.

             Only one break routine may be specified at a time for  each
        user.   If  a break routine was previously specified, it is can-
        celled when a new break routine is declared.  If a value of zero
        is specified for the name of the completion routine, CPLRTN, any
        previously specified break routine is cancelled.

             The following example first declares the completion routine
        as  an  external,  then establishes break sentinel control using
        the letter H, and later cancels the control.

                        EXTERNAL CPLRTN                 
                        IBRKCH = 72                     


        TSXLIB V6.0                                              PAGE 20
        Routine Descriptions


                            .                           
                            .                           
                        CALL BRKCTL ( IBRKCH,CPLRTN )   
                            .                           
                            .                           
                        CALL BRKCTL ( 0,0 )             
                            .                           
                            .                           


    CNVAPA

             This routine is used to convert a virtual  address  into  a
        physical  address.   This  is necessary when controlling devices
        that do direct memory access transfers.  The program should lock
        itself  into  memory before executing this routine.  The calling
        sequence is as follows:

                          CALL CNVAPA ( IVADR,IPADR )

        where:  IVADR   is the virtual address that is to be converted.

                IPADR   is the name of the two element buffer into which
                        the physical address is to be returned.

             The low order sixteen bits  of  the  physical  address  are
        returned in the first element of the buffer, IPADR, and the high
        order bits of the physical address are returned in bit positions
        four through nine of the second element of the buffer.

             The following example first locks itself into  memory  then
        converts a virtual address to a physical address.

                       DIMENSION IPADR ( 2 )            
                       CALL LKANMY                      
                       CALL CNVAPA ( "54720,IPADR,IERR )
                           .                            
                           .                            


    DISMNT

             This routine is used to dismount a file structured  device.
        This causes TSX-Plus to stop doing directory caching of the dev-
        ice.  The effect of this routine is the  same  as  the  TSX-Plus
        DISMOUNT keyboard command.  The calling sequence is as follows:

                             CALL DISMNT ( IDVNAM )

        where:  IDVNAM  is the RAD50 value of the file structured device
                        name.

             The following example uses the SYSLIB routine,  IRAD50,  to
        convert  the  ASCII  value of the device name, DL:, to its RAD50
        value.  It then mounts the device and later dismounts it.


        TSXLIB V6.0                                              PAGE 21
        Routine Descriptions


                         CALL IRAD50 ( 3,'DL ',IDVNAM )
                         CALL MOUNT ( IDVNAM )         
                             .                         
                             .                         
                         CALL DISMNT ( IDVNAM )        
                             .                         
                             .                         


    GETREG

             This routine is used to get the word and byte values stored
        in the specified processor register.  The calling sequence is as
        follows:

                         CALL GETREG ( IREG,IRET,IERR )

        where:  IREG    is the number of the processor register  in  the
                        range  of  zero  to three whose values are to be
                        returned.

                IRET    is a three-element  integer  array  that  is  to
                        receive  the values returned.  The first element
                        receives the word value stored in the  specified
                        processor register.  The second element receives
                        the  low  byte  value  and  the  third   element
                        receives the high byte value.

                IERR    is one of the following:

                        0   no error.

                        1   an invalid  processor  register  number  was
                            specified.

             The following example returns the values stored in  proces-
        sor register one.

                           DIMENSION IRET(3)        
                               .                    
                               .                    
                           CALL GETREG (1,IRET,IERR)
                               .                    
                               .                    


    GTUNAM

             This routine is used to get the user name  associated  with
        the current job.  The calling sequence is as follows:

                             CALL GTUNAM ( USRNAM )

        where:  USRNAM  is the name of the twelve-character  array  that
                        is to receive the user name ASCII string.


        TSXLIB V6.0                                              PAGE 22
        Routine Descriptions


             The following example declares the byte array and then gets
        the user name.

                             LOGICAL*1 USRNAM(18)  
                             CALL GTUNAM ( USRNAM )
                                 .                 
                                 .                 


    HIEFOF

             This routine is used to turn the high  efficiency  terminal
        mode off.  The calling sequence in as follows:

                                  CALL HIEFOF

             The following example first turns high efficiency  terminal
        mode on and later turns it off.

                                  CALL HIEFON
                                      .      
                                      .      
                                  CALL HIEFOF
                                      .      
                                      .      


    HIEFON

             This routine is used to turn the high  efficiency  terminal
        mode on.  The calling sequence is as follows:

                                  CALL HIEFON

             TSX-Plus offers a high efficiency mode of  terminal  opera-
        tion that eliminates a substantial amount of system overhead for
        terminal character processing by reducing the amount of process-
        ing  that  is  done  on each character.  When in high efficiency
        mode, characters are sent directly to the terminal with  minimum
        handling  by  TSX-Plus.   Operations  such  as expanding tabs to
        spaces and form feeds to line feeds are omitted as well as input
        processing  such  as  echoing characters and recognizing control
        characters such as rubout, control-U and  control-C.   The  only
        characters  treated  specially on input are user defined activa-
        tion characters and the  user  specified  break  character.   At
        least  one  user specified activation character must be declared
        if high efficiency mode is to be used.  This  form  of  terminal
        I/O is designed to facilitate high speed machine to machine com-
        munication.  It can  be  used  effectively  with  buffered  mode
        terminals.


        TSXLIB V6.0                                              PAGE 23
        Routine Descriptions


    IACTCH

             This  routine  is  used  to  determine  if  any  activation
        characters  have  been received by the line but not yet accepted
        by the program.  The calling sequences are as follows:

                              CALL IACTCH ( IRET )
                                       or
                                IRET = IACTCH ()

        where:  IRET    is one of the following:

                        0   at least one activation character  is  pend-
                            ing.

                        1   no activation character is pending.


    IALOC

             This routine is used to allocate a device for the exclusive
        use of a job.  The calling sequence is as follows:

                        CALL IALOC ( DEVPTR,IRET,IERR )

        where:  DEVPTR  is the name of the four  element  integer  array
                        which  contains the device name in RAD50 form in
                        the first element and zeros in the  other  three
                        elements.

                IRET    is undefined, or the number of the job to  which
                        the  device  is currently allocated if IERR = 1,
                        or the job which is currently using  the  device
                        if IERR = 4.

                IERR    is negative or one of the following:

                        1   the device is already allocated  to  another
                            user.

                        2   an invalid device has been specified.

                        3   the device allocation table is full.

                        4   the device is currently being used by anoth-
                            er user.

                        5   the job does  not  have  ALLOCATE  privilege
                            (IPRIV 1/14).

             The following example sets up for and allocates  a  device.
        If  the  device  is already allocated or busy, the program loops
        back for another try.  If any other  error  condition  prevails,
        the program aborts.



        TSXLIB V6.0                                              PAGE 24
        Routine Descriptions


                          INTEGER DEVPTR(4)              
                          DATA DEVPTR /3RDY1,0,0,0/      
                              .                          
                              .                          
                      100 CONTINUE                       
                          CALL IALOC ( DEVPTR,IRET,IERR )
                          IF ( IERR .LT. 0 ) GO TO 110   
                          IF ( IERR .EQ. 1 ) GO TO 100   
                          IF ( IERR .EQ. 2 ) STOP        
                          IF ( IERR .EQ. 3 ) STOP        
                          IF ( IERR .EQ. 4 ) GO TO 100   
                      110 CONTINUE                       
                              .                          
                              .                          


    IAQFLC

             This routine is  used  to  allow  the  running  program  to
        acquire  the file context of another job.  The calling sequences
        are as follows:

                          CALL IAQFLC ( JOBNUM,IERR )
                                       or
                            IERR = IAQFLC ( JOBNUM )

        where:  JOBNUM  is the number of the job whose file  context  is
                        to be acquired.

                IERR    is negative or one of the following:

                        0   the  job  is  not  peivileged  to  use  this
                            routine.

                        1   the specified job number is  invalid  or  is
                            not logged on.

             GETCXT privilege (IPRIV 2/7) is required for a job  to  use
        this  routine except in the case where the job being accessed is
        the parent job of the job executing this routine.

             This routine allows a job to perform  file  service  opera-
        tions  for  other  jobs  that  it  may  be servicing.  When this
        routine is executed, the following actions occur:

        1.  All channels for the job that are opened to files on logical
            disks are purged.

        2.  All devices mounted by the job are dismounted.

        3.  The following items are copied from the job being  accessed,
            replacing  the  previous  information  for the job executing
            this routine:

            a)  ASSIGN commands.


        TSXLIB V6.0                                              PAGE 25
        Routine Descriptions


            b)  ACCESS command restrictions.

            c)  Logical disk information.

            d)  Mounted device information.

             The following example first determines the  job  number  of
        the  parent  process  and then acquires the file context of that
        process.  If the job is the primary one the program aborts.

                           JOBNUM = ISPY ( -30 )    
                           IERR = IAQFLC ( JOBNUM ) 
                           IF ( JOBNUM .EQ. 0 ) STOP
                               .                    
                               .                    


    IASRNT

             This routine is used to associate a shared run time  system
        with a job.  It is also used to disassociate all shared run time
        systems from a job.  The calling sequences are as follows:

                        CALL IASRNT ( IRNTIM [ ,IERR ] )
                                       or
                            IERR = IASRNT ( IRNTIM )

        where:  IRNTIM  is the six character RAD50 value of the name  of
                        the shareable run time system.

                IERR    is one of the following:

                        0   no error.

                        1   run time system name not recognized.

             The effect of this routine is  to  associate  a  particular
        shareable  run  time system with the job.  However, this routine
        does not affect the memory mapping for the job or make  the  run
        time  system  visible  to  the  job.  That is done by the MAPRNT
        routine described later.  If some other run time system has been
        previously  mapped  into the job's region, that mapping is unaf-
        fected by this routine.  Thus it is possible  to  have  multiple
        run time systems mapped into the job's region by associating and
        mapping them one at a time into different regions of  the  job's
        virtual memory space.

             If the name pointer, IRNTIM, is set to zero,  this  routine
        causes all run time systems to become disassociated from the job
        and reestablishes normal memory mapping for the job.

             The following example uses the SYSLIB routine,  IRAD50,  to
        declare  the  name of the run time system and then associates it
        with the job.  If the error condition is returned the program is
        halted.


        TSXLIB V6.0                                              PAGE 26
        Routine Descriptions


                       DIMENSION IRNTIM ( 2 )           
                       CALL IRAD50 ( 6,'TSXLIB',IRNTIM )
                       IERR = IASRNT ( IRNTIM )         
                       IF ( IERR .EQ. 1 ) STOP          
                           .                            
                           .                            


    IBICIO

             This routine is used to perform a bit clear operation  into
        a  word  in  the  I/O  page  without requiring the job's virtual
        address region to be  mapped  to  the  I/O  page.   The  calling
        sequences are as follows:

                      CALL IBICIO ( IADR,IVAL [ ,IERR ] )
                                       or
                          IERR = IBICIO ( IADR,IVAL )

        where:  IADR    is the address of the word in the I/O page to be
                        accessed.

                IVAL    is the value to be  bit  cleared  into  the  I/O
                        page.

                IERR    is negative or the following:

                        0   real time support is not available  or  this
                            job  does  not  have MEMMAP privilege (IPRIV
                            1/10).

             The following example bit clears a value in the register at
        the  octal  address  176500  in  the  I/O  page.  The program is
        stopped if the error condition is returned.

                         IERR = IBICIO ( "176500,"100 )
                         IF ( IERR .EQ. 0 ) STOP       
                             .                         
                             .                         


    IBISIO

             This routine is used to perform a bit set operation into  a
        word in the I/O page without requiring the job's virtual address
        region to be mapped to the I/O page.  The calling sequences  are
        as follows:

                      CALL IBISIO ( IADR,IVAL [ ,IERR ] )
                                       or
                          IERR = IBISIO ( IADR, IVAL )

        where:  IADR    is the address of the word in the I/O page to be
                        accessed.



        TSXLIB V6.0                                              PAGE 27
        Routine Descriptions


                IVAL    is the value to be bit set into the I/O page.

                IERR    is negative or the following:

                        0   real time support is not available  or  this
                            job  does  not  have MEMMAP privilege (IPRIV
                            1/10.

             The following example bit sets a value into the register at
        the  octal  address  176500  in  the  I/O  page.  The program is
        stopped if the error condition returns.

                         IERR = IBISIO ( "176500,"100 )
                         IF ( IERR .EQ. 0 ) STOP       
                             .                         
                             .                         


    IBSTCH

             This routine is used to broadcast a status  change  to  all
        jobs  that  are  monitoring  the status of the broadcasting job.
        The calling sequences are as follows:

                         CALL IBSTCH ( IVAL [ ,IERR ] )
                                       or
                             IERR = IBSTCH ( IVAL )

        where:  IVAL    is the 16-bit status code value that  is  to  be
                        broadcast.

                IERR    is negative or the following:

                        0   no jobs are monitoring the job  making  this
                            call.

             On entry  to  the  completion  routine  in  the  monitoring
        job(s), the status value is in processor register R1, the number
        of the job issuing this call is in the low-order byte of R0, and
        the  high-order bit of R0 is set to one.  The GETREG routine may
        be used to recover the values stored in R0 and R1.

             In the following example the job aborts if no other job  is
        monitoring its status.

                            IERR = IBSTCH ( IVAL ) 
                            IF ( IERR .EQ. 0 ) STOP
                                .                  
                                .                  


    ICALOC

             This routine is used to check the allocation  status  of  a
        device.  The calling sequence is as follows:


        TSXLIB V6.0                                              PAGE 28
        Routine Descriptions


                       CALL ICALOC ( DEVPTR,JBNUM,IRET )

        where:  DEVPTR  is the name of the four  element  integer  array
                        which  contains the device name in RAD50 form in
                        the first element and zeros in the  other  three
                        elements.

                JBNUM   is undefined, or the number of the job to  which
                        the  device  is currently allocated if IRET = 1,
                        of the number of  the  job  which  is  currently
                        using the device if IERR = 4.

                IRET    is negative or one of the following:

                        1   the device is allocated to another user.

                        2   an invalid device has been specified.

                        4   the device is currently being used by anoth-
                            er user.

             In the following example, the program aborts if an  invalid
        device has been specified.

                       INTEGER DEVPTR(4)                
                       DATA DEVPTR /3RMT3,0,0,0/        
                           .                            
                           .                            
                       CALL ICALOC ( DEVPTR,JBNUM,IRET )
                       IF ( IRET .EQ. 2 ) STOP          
                           .                            
                           .                            


    ICKWTSC

             This routine is used to determine if  any  other  user  has
        written to a shared file.  The calling sequence is as follows:

                           CALL ICKWTS ( ICHAN,IERR )
                                       or
                            IERR = ICKWTS ( ICHAN )

        where:  ICHAN   is the I/O channel open to the shared file.

                IERR    is negative or one of the following:

                        0   the job does not have RLOCK privilege (IPRIV
                            2/9),  or  shared file support is not avail-
                            able on the system, or the  channel  is  not
                            opened to a shared file.

                        2   writes have been performed.

             This routine can be used to advantage in a situation  where


        TSXLIB V6.0                                              PAGE 29
        Routine Descriptions


        data  from  some block in the file is being held in a buffer and
        it is desired to determine if the data is valid or if it may  be
        invalid because some other user might have altered it by writing
        to the file.

             The following example opens a file, declares the file to be
        shared and then checks for writes to the shared file.  If writes
        have been performed to the file the program is halted.

                       CALL ASSIGN ( 33,'RK3:THIS.DAT' )
                       ICHAN = ( 33 )                   
                       CALL IDCLSF ( ICHAN,5 )          
                           .                            
                           .                            
                       IERR = ICKWTS ( ICHAN )          
                       IF ( IERR .EQ. 2 ) STOP          
                           .                            
                           .                            


    ICNINT

             This routine is used to connect a completion routine to  an
        interrupt vector.  The calling sequences are as follows:

                   CALL ICNINT ( IVEC,CPLRTN,IPRI [ ,IERR ] )
                                       or
                       IERR = ICNINT ( IVEC,CPLRTN,IPRI )

        where:  IVEC    is the interrupt vector address.

                CPLRTN  is the six ASCII character name of  the  comple-
                        tion routine.

                IPRI    is the priority for the  completion  routine  in
                        the range of 0 to 127.

                IERR    is negative or one of the following:

                        0   real time support is not available  or  this
                            job  does not have REALTIME privilege (IPRIV
                            1/6).

                        1   the maximum number of interrupts are already
                            in use.

                        2   some other job is already connected to  this
                            interrupt vector.

                        3   the job is not locked into memory.

             The vector remains  connected  to  the  completion  routine
        until  the  program  terminates or until the routine, IRLINT, is
        executed.  On entry to the completion routine, R0  contains  the
        address  of  the vector that caused the completion routine to be


        TSXLIB V6.0                                              PAGE 30
        Routine Descriptions


        executed.  The GETREG routine may be used to  obtain  the  value
        stored in R0.

             The following example declares the completion routine as an
        external  and  connects  an  interrupt  vector to the completion
        routine.  The  program  is  halted  if  an  error  condition  is
        returned.

                        EXTERNAL CPLRTN                 
                        IERR = ICNINT ( "320,CPLRTN,3 ) 
                        IF ( IERR .GE. 0 ) STOP         
                            .                           
                            .                           


    ICNMCN

             This routine is used to cancel the job  monitoring  connec-
        tion(s)  for  the  calling  job.   The  calling sequences are as
        follows:

                        CALL ICNMCN ( JBNUM [ ,IERR ] )
                                       or
                            IERR = ICNMCN ( JBNUM )

        where:  JBNUM   is the number of the job for which status  moni-
                        toring is to be cancelled.  If JBNUM = zero, all
                        job status monitoring requests for the job  mak-
                        ing this call are cancelled.

                IERR    is negative or the following:

                        1   an invalid job number was specified.

             All job monitoring requests issued by a job  are  cancelled
        by  the system when the job terminates, chains, or issues either
        a hard or soft reset request.

             The following example program  aborts  if  an  invalid  job
        number is specified.

                           CALL ICNMCN ( JBNUM,IERR )
                           IF ( IERR .EQ. 1 ) STOP   
                               .                     
                               .                     


    ICNRTN

             This routine is used to connect a  service  routine  to  an
        interrupt vector.  The calling sequences are as follows:

                  CALL ICNRTN ( IVEC , SVCRTN , 0 [ , IERR ] )
                                       or
                       IERR = ICNRTN ( IVEC , SVCRTN, 0 )


        TSXLIB V6.0                                              PAGE 31
        Routine Descriptions


        where:  IVEC    is the interrupt vector address.

                SVCRTN  is the six ASCII character name of  the  service
                        routine.

                IERR    is negative or one of the following:

                        0   real time support is not available  or  this
                            job  does not have REALTIME privilege (IPRIV
                            1/6).

                        1   no interrupt control blocks are available

                        2   some other job is connected to the vector.

                        3   the job is not locked in memory.

             The vector remains connected to the service  routine  until
        the  program terminates or until the routine, IRLINT, is execut-
        ed.  The only system services (EMTs) permissible from within the
        service  routine  are the SYSLIB routine, RESUME, and the TSXLIB
        routine, ITCRTN.  If other system services  are  required,  they
        must  be  called  from a completion routine which has been trig-
        gered by ITCRTN.  The "0" argument is required.

             The following example declares the service  routine  as  an
        external,  locks  the job in memory, and then connects an inter-
        rupt vector to the service routine.  The program is halted if an
        error condition is returned.

                      EXTERNAL SVCRTN                    
                      IERR = ICNRTN ( IVEC,SVCRTN,IZERO )
                      CALL LKANMY                        
                      IF ( IERR .GE. 1 ) STOP            
                          .                              
                          .                              


    ICNTSP

             This routine is used to set the transmit/receive  speed  or
        baud rate of a of a communication or timesharing line.  The cal-
        ling sequencs are as follows:

                      CALL ICNTSP ( LINUM,ISPCD [,IERR ] )
                                       or
                         IERR = ICNTSP ( LINUM,ISPCD )

        where:  LINUM   is the number of the line for which the speed is
                        to  be  controlled.  If the line number is zero,
                        the speed is set for the line on which the  cal-
                        ling program is executing.

                ISPCD   is one of the following:



        TSXLIB V6.0                                              PAGE 32
        Routine Descriptions


                        0   50 baud.

                        1   75 baud.

                        2   110 baud.

                        3   134.5 baud.

                        4   150 baud.

                        5   300 baud.

                        6   600 baud.

                        7   1200 baud.

                        8   1800 baud.

                        9   2000 baud.

                        10  2400 baud.

                        11  3600 baud.

                        12  4800 baud.

                        13  7200 baud.

                        14  9600 baud.

                        15  19200 baud.

                IERR    is negative or one of the following:

                        1   the job does  not  have  TERMINAL  privilege
                            (IPRIV 2/15).

                        2   the specified line number was invalid.

             This routine is only  functional  for  lines  connected  to
        hardware controllers that support programmable baud rates.

             The following example sets the speed of the line  on  which
        the program is running to 9600 baud.

                              CALL ICNTSP ( 0,14 )
                                  .               
                                  .               


    ICONTM

             This routine is used to return the connect time of a job to
        the calling program.  The calling sequence is as follows:



        TSXLIB V6.0                                              PAGE 33
        Routine Descriptions


                      CALL ICONTM ( LINUM,IRET [ ,IERR ] )

        where:  LINUM   is the TSX-Plus line for which connect  time  is
                        to be returned.

                IRET    is the returned connect time in minutes.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.

             In the following example the connect times of the logged on
        lines are returned in the variable, IRET.

                        LINUM = 0                          
                     10 CONTINUE                           
                            LINUM = LINUM + 1              
                            CALL ICONTM ( LINUM,IRET,IERR )
                            IF ( IERR .EQ. 0 ) GO TO 10    
                            IF ( IERR .EQ. 2 ) GO TO 20    
                                .                          
                                .                          
                        GO TO 10                           
                     20 CONTINUE                           


    ICPUTM

             This routine is used to return a job's CPU time to the cal-
        ling program.  The calling sequence is as follows:

                     CALL ICPUTM ( LINUM,ITIME [ ,IERR ] )

        where:  LINUM   is the TSX-Plus line for which CPU time is to be
                        returned.

                ITIME   is the CPU time returned in clock ticks.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.

             The variable, ITIME, is a two element array where the first
        element  will receive the high order 16 bits and the second ele-
        ment will receive  the  low  order  16  bits  of  the  CPU  time
        returned.

             The CPU time of line five  is  returned  in  the  following
        example.  The program aborts if an error condition prevails.



        TSXLIB V6.0                                              PAGE 34
        Routine Descriptions


                          DIMENSION ITIME(2)          
                              .                       
                              .                       
                          CALL ICPUTM ( 5,ITIME,IERR )
                          IF ( IERR .GE. 0 ) STOP     
                              .                       
                              .                       


    ICRWND

             This routine is used  to  create  a  window.   The  calling
        sequences are as follows:

              CALL ICRWND ( ID,IFLG,IWDTH,ISCRL,IDCPY,JBCPY,IERR )
                                       or
               IERR = ICRWND ( ID,IFLG,IWDTH,ISCRL,IDCPY,JBCPY )

        where:  ID      is is a  window  identification  number  in  the
                        range of 1 to 26 which identifies the window for
                        this job.

                IFLG    is one of the following:

                        0   the window is a temporary window and will be
                            deleted  when  the program exits to the key-
                            board monitor.

                        1   the window is a permanent window and is only
                            deleted  when  explicitly  requested (by the
                            IDLWND routine, or the SET WINDOW  OFF  key-
                            board command) or when the job logs off.

                IWDTH   is the width of the window in columns and should
                        not exceed 132.

                ISCRL   is the maximum number of lines which are allowed
                        to  scroll off the window during a time when the
                        window  is  disconnected  from   the   terminal.
                        Specify  0 to disallow any scrolling.  Specify 1
                        to allow unlimited scrolling.

                IDCPY   is the window identification number of the  win-
                        dow   from   which   to   copy   certain  window
                        characteristics.   If  0,  no   information   is
                        copied.  If in the range of 1 to 26, the follow-
                        ing characteristics are copied:

                        1)  The number of columns per line.

                        2)  The maximum allowed number of  lines  to  be
                            scrolled  while switched to a different pro-
                            cess.

                        3)  80 or 132 column mode.


        TSXLIB V6.0                                              PAGE 35
        Routine Descriptions


                        4)  Light or dark video mode.

                JBCPY   is the job number of the job from which to  copy
                        certain  window characteristics.  If 0, the cur-
                        rent job is assumed.

                IERR    is negative or one of the following:

                        0   Window management is  not  included  in  the
                            system.

                        1   Maximum  allowed  number  of   windows   are
                            already in use.

                        2   Unable to create the window.   Job  may  not
                            have  SYSGBL privilege (IPRIV 2/8) or suffi-
                            cient memory may not be available.

             The following example creates a permanent  72  column  wide
        window  with  an identification number of 13 and allows up to 20
        lines to scroll off the window.  The program aborts if an  error
        condition is returned.

                        IERR = ICRWND ( 13,1,72,20,0,0 )
                        IF ( IERR .GE. 0 ) STOP         
                            .                           
                            .                           


    IDALOC

             This routine is used to deallocate a device.   The  calling
        sequence is as follows:

                        CALL IDALOC ( DEVPTR,IRET,IERR )

        where:  DEVPTR  is the name of the four  element  integer  array
                        which  contains the device name in RAD50 form in
                        the first element and zeros in the  other  three
                        elements.

                IRET    is undefined, or the number of the job to  which
                        the  device  is currently allocated if IERR = 1,
                        or the number of  the  job  which  is  currently
                        using the device if IERR = 4.

                IERR    is negative or one of the following:

                        1   the device is allocated to another user.

                        2   an invalid device has been specified.

                        4   the device is currently in  use  by  another
                            job.



        TSXLIB V6.0                                              PAGE 36
        Routine Descriptions


                        5   the job does  not  have  ALLOCATE  privilege
                            (IPRIV 1/14).

             The following example program aborts if the device is allo-
        cated to another user.

                        INTEGER (4)                     
                        DATA /3RDX0,0,0,0/              
                            .                           
                            .                           
                        CALL IDALOC ( DEVPTR,IRET,IERR )
                        IF ( IERR .EQ. 1 ) STOP         
                            .                           
                            .                           


    IDCLSF

             This routine is used to declare an open file to be  shared.
        The calling sequences are as follows:

                     CALL IDCLSF ( ICHAN,IACES [ ,IERR ] )
                                       or
                         IERR = IDCLSF ( ICHAN,IACES )

        where:  ICHAN   is the I/O channel number  open  to  the  shared
                        file.

                IACES   is one of the following protection/access codes:

                        0   exclusive/input.

                        1   exclusive/update.

                        2   protected/input.

                        3   protected/update.

                        4   shared/input.

                        5   shared/update.

                IERR    is negative or one of the following:

                        0   shared file support is not available on  the
                            system  or  the  job  does  not  have  RLOCK
                            privilege (IPRIV 2/9).

                        1   the I/O channel has not  been  opened  to  a
                            file.

                        2   attempted  to  open  too  many  channels  to
                            shared files.

                        3   attempted to open too many shared files.


        TSXLIB V6.0                                              PAGE 37
        Routine Descriptions


                        4   a file protection/access conflict exists.

             The protection/access code specifies two things,  the  type
        of protection (exclusive, protected, shared) that you are claim-
        ing on your use of the file and the type  of  access  (input  or
        update)  that you intend to make to the file.  Exclusive protec-
        tion means that you require exclusive access  to  the  file  and
        will  allow  no  other  users to access the file in any fashion.
        Protected protection means that you will allow  other  users  to
        open  the  file  for input but wish to prohibit any from opening
        the file for update.  Shared protection means that you are  wil-
        ling  to  allow  other users to open the file for both input and
        update.

             The following example opens a file and then declares exclu-
        sive/update   protection/access.    If  an  error  condition  is
        returned the program aborts.

                        CALL ASSIGN ( 40,'DK:FILE.DAT' )
                        REWIND 40                       
                        ICHAN = ILUN ( 40 )             
                        IERR = IDCLSF ( ICHAN,2 )       
                        IF ( IERR .NE. 0 ) STOP         
                            .                           
                            .                           


    IDLWND

             This routine is used to delete one  or  more  windows  that
        were created with the ICRWND routine.  The calling sequences are
        as follows:

                          CALL IDLWND ( ID [, IERR ])
                                       or
                              IERR = IDLWND ( ID )

        where:  ID      is the window identification number of the  win-
                        dow that is to be deleted.

                IERR    is negative or one of the following:

                        0   window management support is not included in
                            the system.

                        3   unable to locate the window with the  speci-
                            fied window identification number.

             If the window identification number is zero,  then  all  of
        the  temporary  windows  for the job are deleted.  If the window
        identification number is 255, then all the  temporary  and  per-
        manent  windows  for the job are deleted.  This routine requires
        the SYSGBL privilege (IPRIV 2/8).


        TSXLIB V6.0                                              PAGE 38
        Routine Descriptions


    IESMCN

             This routine is used to establish a job monitoring  connec-
        tion  between  the  calling  job  and  another job.  The calling
        sequences are as follows:

                     CALL IESMCN ( JBNUM,CPLRTN [ ,IERR ] )
                                       or
                         IERR = IESMCN ( JBNUM,CPLRTN )

        where:  JBNUM   is the number of the job to be monitored.

                CPLRTN  is the name of  the  completion  routine  to  be
                        entered  when  the  status  of the monitored job
                        changes.

                IERR    is negative or one of the following:

                        1   an invalid job number was specified.

                        2   there are no  free  job  monitoring  control
                            blocks available.

             The specified completion routine will be entered each  time
        the  status  of  the  monitored job changes or the monitored job
        broadcasts a status change.  On entry to the completion routine,
        the  low-order byte of processor register R0 contains the number
        of  the  job  whose  status  change  is  being  reported.    The
        high-order  bit of R0 is zero if the status report was generated
        by the system and is one if the status report was generated by a
        program  broadcasting a status change.  The status value is con-
        tained in processor register R1.  The values stored in R0 and R1
        may  be recovered with the GETREG routine.  The system generated
        status values are listed below:

                 1   The job has been initialized.             

                 2   The job logged on using the LOGON program.

                 3   The job began running a program.          

                 4   The job returned control to KMON.         

                 5   The job has logged off.                   

             The following example program establishes a job status mon-
        itoring  connection.   If there are no control blocks available,
        it loops back for another try.  The program aborts if an invalid
        job number has been specified.

                           EXTERNAL CPLRTN               
                               .                         
                               .                         
                       100 CONTINUE                      
                           IERR = IESMCN ( JBNUM,CPLRTN )


        TSXLIB V6.0                                              PAGE 39
        Routine Descriptions


                           IF ( IERR .EQ. 2 ) GO TO 100  
                           IF ( IERR .EQ. 1 ) STOP       
                               .                         
                               .                         


    IEXSTS

             This routine is used to return the  execution  state  of  a
        TSX-Plus line.  The calling sequence is as follows:

                     CALL IEXSTS ( LINUM,ISTAT [ ,IERR ] )

        where:  LINUM   is the number of the line  for  which  execution
                        state is returned.

                ISTAT   is the one  of  the  following  execution  state
                        values:

                        1   high priority run state.

                        2   normal priority run state.

                        3   low priority run state.

                        4   waiting for terminal input.

                        5   waiting to write terminal output.

                        6   doing a timed wait.

                        7   suspended by SUSPND or .SPND.

                        8   waiting to access a shared file.

                        9   waiting for a message.

                        10  waiting for access to the USR.

                        11  waiting for I/O to finish.

                        12  waiting to access spool file.

                        13  Interactive high priority run state.

                        14  Fixed high priority run state.

                        15  Waiting for memory expansion.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.



        TSXLIB V6.0                                              PAGE 40
        Routine Descriptions


             The program in the following example halts  if  line  2  is
        doing a timed wait.

                          CALL IEXSTS ( LINUM,ISTAT )
                          IF ( ISTAT .EQ. 6 ) STOP   
                              .                      
                              .                      


    IFLINF

             This routine obtains some information about  a  file.   The
        calling sequence is as follows:

                 CALL IFLINF ( ICHAN , IDEV , INFO [ , IERR ] )

        where:  ICHAN   is a channel number in the range of zero through
                        sixteen that is currently not in use.

                IDEV    is the name of a four-word array  that  contains
                        the file specification in RAD50.

                INFO    is the name of the seven-word array that  is  to
                        receive  the  following  information  about  the
                        file:

                        Word 1  is the number of  512-byte  blocks  con-
                                tained in the file.

                        Word 2  is zero if the file is not protected, or
                                one if the file is protedted.

                        Word 3  is the creation  date  of  the  file  in
                                RT-11 internal format.

                        Word 4  is the creation  time  of  the  file  in
                                three-second units.

                        Word 5  is the  starting  block  number  of  the
                                file.

                        Word 6  is reserved.

                        Word 7  is reserved.

                IERR    is negative or one of the following

                        0   The channel is currently in use.

                        1   Unable to locate the specified file.

                        2   The specified device is not file structured.

             The following example obtains  the  information  about  the
        file, DY1:STUFF.DAT.


        TSXLIB V6.0                                              PAGE 41
        Routine Descriptions


                      DIMENSION IDEV(4),INFO(7)              
                      ICHAN = IGETC ()                       
                      CALL IRAD50 ( 12,'DY1STUFF DAT',IDEV)  
                      CALL IFLINF ( ICHAN,IDEV,INFO,IERR )   
                      IF ( IERR .GT. 0 ) STOP 'IFLINF error' 
                          .                                  
                          .                                  


    IHERR

             This routine is used to  restore  monitor  interception  of
        certain  soft error conditions.  It must be called at some point
        following a call to ISERR.  The calling sequence is as follows:

                                   CALL IHERR


    ILNSTS

             This routine is used to return information about the status
        of a line.  The calling sequence is as follows:

                      CALL ILNSTS ( LINUM,IRET [ ,IERR ] )

        where:  LINUM   is the TSX-Plus line for which  status  informa-
                        tion is returned.

                IRET    is the value  returned  and  contains  bit-flags
                        that indicate the status for the line.  The fol-
                        lowing bit-flags are defined:

                        000000  physical line.

                        000001  virtual line.

                        000002  detached job line.

                        000100  job is locked in memory.

                        000200  job has operator privilege.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.

             The program in the example below stops if the  line  number
        is invalid.

                        CALL ILNSTS ( LINUM,IRET,IERR )
                        IF ( IERR .EQ. 2 ) STOP        
                            .                          
                            .                          


        TSXLIB V6.0                                              PAGE 42
        Routine Descriptions


    INITPA

             This routine is used to set up parameters that will control
        a   performance  analysis.   It  does  not  actually  begin  the
        analysis.  The calling sequences are as follows:

              CALL INITPA ( IBSADR,ITPADR,ICLSZ,IFLAG [ ,IERR ] )
                                       or
                  IERR = INITPA ( IBSADR,ITPADR,ICLSZ,IFLAG )

        where:  IBSADR  is the base address of the region  to  be  moni-
                        tored.

                ITPADR  is  the  top  address  of  the  region   to   be
                        monitored.

                ICLSZ   is the number of bytes to group into each histo-
                        gram cell.

                IFLAG   is one of the following:

                        0   do not include I/O wait time.

                        1   include I/O wait time.

                IERR    is negative or one of the following:

                        0   performance analysis is already in use.

                        1   performance analysis feature is not included
                            in this version of TSX-Plus.

             The  following  example  initializes  for   a   performance
        analysis.  The program aborts if an error condition is returned.

                      IERR = INITPA ( "2000,"5400,"100,0 )
                      IF ( IERR .GE. 0 ) STOP             
                          .                               
                          .                               


    IPEKIO

             This routine is used to access or peek at a word in the I/O
        page  without  requiring  the job's virtual address region to be
        mapped to the I/O page.  The calling sequence is as follows:

                      CALL IPEKIO ( IADR,IRET [ ,IERR ] )

        where:  IADR    is the address of the word in the I/O page  that
                        is to be accessed.

                IRET    is the value returned from the I/O page.

                IERR    is negative or the following:


        TSXLIB V6.0                                              PAGE 43
        Routine Descriptions


                        0   real time support is not available  or  this
                            job  does  not  have MEMMAP privilege (IPRIV
                            1/10).

             The following example obtains the value from  the  register
        at octal address 176502 in the I/O page.  The program is aborted
        if the error condition is returned.

                       CALL IPEKIO ( "176502,IRET,IERR )
                       IF ( IERR .EQ. 0 ) STOP          
                           .                            
                           .                            


    IPGNAM

             This routine is used to return  the  name  of  the  program
        being  executed  by a TSX-Plus line.  The calling sequence is as
        follows:

                     CALL IPGNAM ( LINUM,PGNAME [ ,IERR ] )

        where:  LINUM   is the number of the line executing the returned
                        program name.

                PGNAME  is the two-word variable into  which  the  RAD50
                        value of the program name is returned.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.

             The SYSLIB routine R50ASC is used to convert  the  returned
        program name to an ASCII string in the following example.

                        LOGICAL*1 STRING(8)             
                            .                           
                            .                           
                        CALL IPGNAM ( LINUM,PGNAM,IERR )
                        IF ( IERR .GE. 0 ) STOP         
                        CALL R50ASC ( 6,PGNAM,STRING )  


    IPOKIO

             This routine is used to deliver a value into a word in  the
        I/O  page  without requiring the job's virtual address region to
        be mapped to  the  I/O  page.   The  calling  sequences  are  as
        follows:

                      CALL IPOKIO ( IADR,IVAL [ ,IERR ] )
                                       or
                          IERR = IPOKIO ( IADR,IVAL )


        TSXLIB V6.0                                              PAGE 44
        Routine Descriptions


        where:  IADR    is the address of the word in the I/O page to be
                        accessed.

                IVAL    is the value to be deposited in the I/O page.

                IERR    is negative or the following:

                        0   real time support is not available  or  this
                            job  does  not  have MEMMAP privilege (IPRIV
                            1/10).

             The following example pokes a value into  the  register  at
        octal  address 176506 in the I/O page.  The program stops if the
        error condition is returned.

                         IERR = IPOKIO ( "176506,"101 )
                         IF ( IERR .EQ. 0 ) STOP       
                             .                         
                             .                         


    IPPNUM

             This routine is used to return the project  and  programmer
        numbers  for  a  TSX-Plus  line.   The  calling  sequence  is as
        follows:

                      CALL IPPNUM ( LINUM,IBUF [ ,IERR ] )

        where:  LINUM   is the number of the line for which the  project
                        and programmer numbers are returned.

                IBUF    is the two word array into which the project and
                        programmer numbers are returned.  The first word
                        contains the project number and the second  word
                        contains the programmer number.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.

             The program in the following example stops if an error con-
        dition is encountered.

                        DIMENSION IBUF(2)              
                            .                          
                            .                          
                        CALL IPPNUM ( LINUM,IBUF,IERR )
                        IF ( IERR .GE. 0 ) STOP        
                            .                          
                            .                          


        TSXLIB V6.0                                              PAGE 45
        Routine Descriptions


    IPRIV

             This routine permits the running program to determine or to
        change  the job privilege sets.  The calling sequence is as fol-
        lows:

                   CALL IPRIV ( IFUN,IPRVT,BUFFER [ ,IERR ] )

        where:  IFUN    is one of the following function control values:

                        0   causes the privilege flags to be stored into
                            the specified buffer.

                        1   causes the privilege flags that are  set  in
                            the  buffer to be cleared in the correspond-
                            ing system table.

                        2   causes the privilege flags that are  set  in
                            the  buffer  to  be set in the corresponding
                            system table.

                IPRVT   indicates which of the three sets  of  privilege
                        flags  are to be accessed and must be one of the
                        following values:

                        0   the current job privileges are selected.

                        1   the set privileges for the job are selected.
                            If  any  privileges are changed, the current
                            privileges are also changed.

                        2   the authorized privileges are selected.

                BUFFER  is the name of the four-word buffer that  is  to
                        receive or contains the privilege flags.  A flag
                        value of 1 enables the privilege and a value  of
                        0  denies  the  privilege.   The  following list
                        shows  the  privilege  related  to   each   flag
                        (word/bit).

                        1/0   system  privilege  (system  manager   type
                              operations).

                        1/1   non-file structured read/write access.

                        1/2   non-file-structured read access.

                        1/3   affect own privileges.

                        1/4   change user name or password.

                        1/5   sending messages between jobs (not using a
                              named message channel).

                        1/6   real time support.


        TSXLIB V6.0                                              PAGE 46
        Routine Descriptions


                        1/7   change process swap mode.

                        1/8   operator.

                        1/9   bypass device/file access restrictions.

                        1/10  access memory that may be  significant  to
                              the system.

                        1/11  use the .SPFUN EMT.

                        1/12  affect detached jobs.

                        1/13  use of the debugging facilities.

                        1/14  device allocation.

                        1/15  reserved.

                        2/0   user-defined privilege #1.

                        2/1   user defined privilege #2.

                        2/2   user-defined privilege #3.

                        2/3   user-defined privilege #4.

                        2/4 through 2/6 reserved.

                        2/7   get file context from another job.

                        2/8   global regions.

                        2/9   shared file record locking.

                        2/10  named message channels.

                        2/11  use subprocesses (virtual lines).

                        2/12  affect jobs with the same project and pro-
                              grammer numbers.

                        2/13  affect jobs with the same project number.

                        2/14  affect any job.

                        2/15  terminal and CL commands.

                        3/0 through 4/15 reserved.

                IERR    is negative or the following:

                        1   attempt to enable privileges for  which  the
                            job is not authorized.



        TSXLIB V6.0                                              PAGE 47
        Routine Descriptions


             Only those privileges for which the job is  authorized  are
        set.   SETPRV privilege is required to set any new privileges in
        the authorized privilege set.

             The following example returns the  set  of  authorized  job
        privileges to the buffer.

                        INTEGER BUFFER(4)               
                        DATA IFUN,IPRVT /0,2/           
                        CALL IPRIV ( IFUN,IPRVT,BUFFER )


    IPRWND

             This routine causes the contents of a window to be printed.
        The calling sequences are as follows:

                            CALL IPRWND ( ID,IERR )
                                       or
                              IERR = IPRWND ( ID )

        where:  ID      is the window identification number of the  win-
                        dow whose contents are to be printed.

                IERR    is negative or one of the following:

                        0   Windowing support is not  available  on  the
                            system.

                        3   the specified window  identification  number
                            is invalid.

                        4   the WINPRT program is not running.

             The following example  aborts  if  an  error  condition  is
        detected.

                            IERR = IPRWND ( ID )   
                            IF ( IERR .GE. 0 ) STOP
                                .                  
                                .                  


    IRDRCL

             This routine is used to redirect a dedicated  communication
        line, CL unit, or a timesharing line.  The calling sequences are
        as follows:

                     CALL IRDRCL ( ICLNO,LINUM [ ,IERR ] )
                                       or
                         IERR = IRDRCL ( LCLNO,LINUM )

        where:  ICLNO   is the dedicated communication line number, CLn.



        TSXLIB V6.0                                              PAGE 48
        Routine Descriptions


                LINUM   is the number of the  timesharing  line  or  the
                        dedicated communication line.

                IERR    is negative or one of the following:

                        1   the user making this call does not have TER-
                            MINAL privilege (IPRIV 2/15).

                        2   an  invalid  CL  unit  number,  ICLNO,   was
                            specified.

                        3   an   invalid   line   number,   LINUM,   was
                            specified.

                        4   the specified line number, LINUM, is already
                            assigned to a CL unit.

                        5   a  timesharing  user  is  logged  onto   the
                            specified line number, LINUM.

                        6   the specified CL unit, ICLNO,  is  currently
                            in use.

             The following sample program aborts if an error is returned
        when it attempts to redirect CL3 to line number 9.

                            CALL IRDRCL ( 3,9,IERR )
                            IF ( IERR .GT. 0 ) STOP 
                                .                   
                                .                   


    IRLINT

             This routine releases the connection of an interrupt vector
        and  a  completion routine or a service routine.  The connection
        must have been made by previously executing the routine,  ICNINT
        or ICNRTN.  The calling sequence is as follows:

                              CALL IRLINT ( IVEC )

        where:  IVEC    is the interrupt vector address.

             REALTIME privilege (IPRIV 1/6) is required to execute  this
        routine.

             The following example first declares the completion routine
        as an external, then connects it to a vector, and finally breaks
        the connection.

                        EXTERNAL CPLRTN                 
                        CALL ICNINT ( "320,CPLRTN,0 )   
                            .                           
                            .                           
                        CALL IRLINT ( "320 )            


        TSXLIB V6.0                                              PAGE 49
        Routine Descriptions


                            .                           
                            .                           


    IRSWND

             This routine is used to resume processing of the  currently
        selected window.  The calling sequence is as follows:

                                  CALL IRSWND

             No operation is performed if the job has no active  window.
        The  SYSGBL  privilege  (IPRIV  2/8) is required to execute this
        routine.


    ISERR

             This routine is used to permit a running program to  inter-
        cept  certain soft error conditions.  These conditions may occur
        only on the execution  of  other  TSXLIB  and  SYSLIB  routines.
        Execution  of  ISERR must at some point be followed by execution
        of IHERR.  The calling sequence is as follows:

                                   CALL ISERR

             The following soft error codes may be returned on execution
        of other TSXLIB and SYSLIB routines:

                -1  Called "USR" from a completion routine.

                -2  No device handler;  this operation needs one.

                -3  Error doing directory I/O.

                -4  ".FETCH" error.  Either an I/O error occurred  while
                    the  handler  was being used, or an attempt was made
                    to load the handler over "USR"  or  "RMON".   (RT-11
                    only)

                -5  Error reading an overlay.

                -6  No more room for files in the directory.

                -7  Illegal address ("FB" only);   tried  to  perform  a
                    monitor operation outside the job partition.  (RT-11
                    only)

                -8  Illegal channel  number.   Number  is  greater  than
                    actual number of channels that exist.

                -9  Illegal "EMT";  an illegal function  code  has  been
                    decoded.

             The example below tests for the existence of a handler  for


        TSXLIB V6.0                                              PAGE 50
        Routine Descriptions


        the logical device named DEV.

                     DIMENSION IDVBLK(4)                   
                     DATA IDVBLK /0,0,0,0/                 
                         .                                 
                         .                                 
                     CALL ISERR                            
                     I = LOOKUP( ICHAN,IDVBLK)             
                     IF ( IDVBLK .EQ -2 ) STOP 'NO HANDLER'
                         .                                 
                         .                                 
                     CALL IHERR                            


    ISLWND

             This routine is used to select a window  that  has  already
        been created with the ICRWND routine.  The calling sequences are
        as follows:

                            CALL ISLWND ( ID,IERR )
                                       or
                              IERR = ISLWND ( ID )

        where:  ID      is the window identification number of the  win-
                        dow to be selected and displayed.

                IERR    is negative or one of the following:

                        0   window management support is not included in
                            the system.

                        3   unable to locate the window with the  speci-
                            fied window identification number.

             A window identification number of zero causes windowing  to
        be  disabled for the job.  However, the contents of all existing
        windows are retained and may be reselected  later.   The  SYSGBL
        privilege (IPRIV 2/8) is required to execute this routine.

             In the following example, the program aborts  if  an  error
        condition prevails typing out an appropriate error message.

                  CALL ISLWND ( ID,IERR )                     
                  IF ( IERR .EQ. 0 ) STOP 'No window support' 
                  IF ( IERR .EQ. 3 ) STOP 'Cannot find window'
                      .                                       
                      .                                       


    ISPBLK

             This routine is used to determine the number of free blocks
        in the spool file.  The calling sequences are as follows:


        TSXLIB V6.0                                              PAGE 51
        Routine Descriptions


                              CALL ISPBLK ( IRET )
                                       or
                                IRET = ISPBLK ()

        where:  IRET    is the number of free blocks in the spool file.


    ISPCTL

             This routine is used to  control  the  release  time  of  a
        spooled file.  The calling sequence is as follows:

                         CALL ISPCTL ( ICHAN , IFLAG )

        where:  ICHAN   is the number of the channel that is open to the
                        file.

                IFLAG   is an integer value as follows:

                        0   release the file immediately.

                        1   hold the release until the file is closed.

             This routine must be called after the file has been  opened
        and  before  any data is written to the file.  If the channel is
        open  to  a  non-spooled  device,  the  call  is  treated  as  a
        no-operation.  OPER privilege (IPRIV 1/8) is required to execute
        this routine.

             The following example causes the file to be written to  the
        spooled line printer to be released immediately.

                           OPEN ( UNIT=30,NAME=LP: )
                           ICHAN = ILUN ( 30 )      
                           CALL ISPCTL ( ICHAN,1 )  
                               .                    
                               .                    


    ISPPA

             This routine is used to suspend the collection of data  for
        a performance analysis.  The data collection can be restarted by
        using the ISTPA routine described later.  The calling  sequences
        are as follows:

                              CALL ISPPA [ IERR ]
                                       or
                                IERR = ISPPA ()

        where:  IERR    is negative or the following:

                        0   performance analysis has not been previously
                            initialized.



        TSXLIB V6.0                                              PAGE 52
        Routine Descriptions


             The  following  example  initializes  for   a   performance
        analysis,  then  starts and stops the collection of data for the
        analysis within a loop.

                        CALL INITPA ( "2000,"5400,"100,0 )
                        DO 10 I = 1,53                    
                            CALL ISTPA                    
                                .                         
                                .                         
                            CALL ISPPA                    
                                .                         
                                .                         
                     10 CONTINUE                          
                                .                         
                                .                         


    ISPWND

             This routine is used to suspend window  processing  of  the
        currently selected window.  The calling sequence is as follows:

                                  CALL ISPWND

             When window processing is suspended, characters are sent to
        the  terminal  without  being processed by the window management
        system.  No operation is performed if the job has no active win-
        dows.   The  SYSGBL privilege (IPRIV 2/8) is required to execute
        this routine.


    ISPY

             This is a SYSLIB routine that is used to return  the  value
        located  at a specific offset into the simulated RMON.  TSX-Plus
        has extended it to return several TSX-Plus values.  Refer to the
        "RT-11  Programmer's  Reference  Manual"  [5] for information on
        getting values from within  the  simulated  RMON.   The  calling
        sequence is as follows:

                             IRET = ISPY ( IOFFST )

        where:  IRET    is the integer value returned.

                IOFFST  is the integer offset into the simulated RMON or
                        to return a TSX-Plus value is one of the follow-
                        ing:

                        -2  job number.

                        -4  lead-in   character   used   for    terminal
                            controlled options.

                        -6  zero if  job  is  nonprivileged  or  one  if
                            privileged.


        TSXLIB V6.0                                              PAGE 53
        Routine Descriptions


                        -8  zero if PAR 7 is  mapped  to  the  simulated
                            RMON  or  one  if PAR 7 is mapped to the I/O
                            page.

                        -10 project number job is logged on under.

                        -12 programmer number job is logged on under.

                        -14 TSX-Plus license number.

                        -16 get the job's priority level.

                        -18 get the  job's  maximum  allowable  priority
                            level.

                        -20 the number of blocks per  job  in  the  file
                            UCL.TSX.

                        -22 get the job number of the primary line (0 if
                            this is the primary line).

                        -24 get the name of the physical SY: device.

                        -26 Value of the PRILOW sysgen parameter.

                        -28 Value of the PRIHI sysgen parameter.

                        -30 Job number of the parent process (0 for  the
                            primary process).

             The following example aborts if the job is not privileged.

                            IRET = ISPY ( -6 )     
                            IF ( IRET .EQ. 0 ) STOP
                                .                  
                                .                  


    ISTDJ

             This routine is used to check the status of a detached job.
        The calling sequences are as follows:

                          CALL ISTDJ ( JOBNUM,ISTAT )
                                       or
                            ISTAT = ISTDJ ( JOBNUM )

        where:  JOBNUM  is the job number of the detached job.

                ISTAT   is one of the following:

                        0   the job is not active.

                        1   the job is active.



        TSXLIB V6.0                                              PAGE 54
        Routine Descriptions


             The following example starts a detached job then checks the
        detached job's status until the job becomes inactive.

                          CALL STDTJB ( JOBNAM, JOBNUM )
                       10 CONTINUE                      
                          ISTAT = ISTDJ ( JOBNUM )      
                          IF ( ISTAT .NE. 1 ) GO TO 10  
                              .                         
                              .                         


    ISTFTM

             This routine is used to set the creation time for  a  file.
        The calling sequences are as follows:

                CALL ISTFTM ( ICHAN , IDEV , ITIME [ , IERR ] )
                                       or
                     IERR = ISTFTM ( ICHAN , IDEV , ITIME )

        where:  ICHAN   is a channel number in the range of zero through
                        sixteen that is currently not in use.

                IDEV    is the name of the  four-word  array  containing
                        the file specification in RAD50.

                ITIME   is an integer time value in  three-second  units
                        since midnight.

                IERR    is negative or one of the following.

                        0   the channel is currently in use.

                        1   unable to locate the specified file.

                        2   the specified device is not file structured.

             The following example sets the creation time for the  file,
        NICKS.DAT, at 300 three-second units past midnight.

                       DIMENSION IDEV(4)                     
                       DATA ICHAN,ITIME /0,300/              
                       CALL IRAD50 ( 12,DM4NICKS DAT,IDEV)   
                   100 CONTINUE                              
                       IERR = ISTFTM ( ICHAN,IDEV,ITIME )    
                       IF ( ICHAN .GT 16 ) STOP 'No channels'
                       IF ( IERR .EQ. 0 ) GO TO 100          
                       IF ( IERR .GT. 0 ) STOP 'ISTFTM error'
                           .                                 
                           .                                 


        TSXLIB V6.0                                              PAGE 55
        Routine Descriptions


    ISTPA

             This routine is used to begin the actual collection of per-
        formance  analysis  data.   The  INITPA  routine  must have been
        executed to set up parameters  about  the  performance  analysis
        before  this  routine  is  called.  The calling sequences are as
        follows:

                              CALL ISTPA [ IERR ]
                                       or
                                IERR = ISTPA ()

        where:  IERR    is negative or the following:

                        0   performance   analysis    has    not    been
                            initialized.

             The following example initializes for and starts a  perfor-
        mance analysis.  The program is halted if the error condition is
        returned from the call to ISTPA.

                       CALL INITPA ( "2000,"5400,"100,0 )
                       IERR = ISTPA ()                   
                       IF ( IERR .EQ. 0 ) STOP           
                           .                             
                           .                             


    ISTPRV

             This routine is used to set the priority value for the cur-
        rent job.  The calling sequence is as follows:

                             CALL ISTPRV ( IPRVAL )

        where:  IPRVAL  is an integer priority value in the range  of  0
                        through 127.

             If the job attempts to set its  priority  level  above  its
        maximum  allowed  priority level, its priority level will be set
        to the maximum value allowed.


    ISVST

             This routine is used to save the status of a  shared  file.
        The  effect of this routine is to suspend the connection between
        the shared file table and the I/O channel.  Any blocks that  are
        locked  in  the file remain locked until the channel is reopened
        to the file by using the SYSLIB routine, IREOPN.   After  return
        from  this  routine the channel may be freed by using the SYSLIB
        routine, PURGE.  The calling sequence is as follows:

                              CALL ISVST ( ICHAN )



        TSXLIB V6.0                                              PAGE 56
        Routine Descriptions


        where:  ICHAN   is the I/O channel number  open  to  the  shared
                        file.

             The RLOCK privilege (IPRIV 2/9) is required to execute this
        routine.

             When using a single channel number to access several shared
        files it is for each file convenient to initially open the file,
        declare the file to be shared and to save the status of the file
        with  the  SYSLIB  routine,  ISAVES.   The channel being used to
        access the set of files can then be switched from  one  file  to
        another  with  the  SYSLIB routines, PURGE and IREOPN.  However,
        before doing the PURGE, TSX-Plus must be told that you  wish  to
        save  the  shared  file status of the file (otherwise all locked
        blocks will be unlocked and the file will be  removed  from  the
        shared file list).

             The following example opens  a  file,  declares  it  to  be
        shared and then saves the status of the file for TSX-Plus.

                        CALL ASSIGN ( 30,'DK:SOME.FIL' )
                        ICHAN = ILUN ( 30 )             
                        CALL IDCLSF ( ICHAN,4 )         
                            .                           
                            .                           
                        CALL ISVST ( ICHAN )            
                            .                           
                            .                           


    ITCRTN

             This routine is used to trigger a completion  routine  from
        within an interrupt service routine.  The calling sequence is as
        follows:

                     CALL ITCRTN ( CPLRTN , IPRI , ID , 0 )

        where:  CPLRTN  is the six ASCII character name of  the  comple-
                        tion routine.

                IPRI    is the execution  priority  for  the  completion
                        routine in the range of zero to seven.

                ID      is an integer value  passed  to  the  completion
                        routine.

             The service routine that calls this ITCRTN must  have  been
        connected  to  an  interrupt  vector  by  executing  the  ICNRTN
        routine.  The "0" argument is required.

             The following example declares the completion routine as an
        external and then triggers its execution.



        TSXLIB V6.0                                              PAGE 57
        Routine Descriptions


                      EXTERNAL CPLRTN                     
                      CALL ITCRTN ( CPLRTN,IPRI,ID,IZERO )
                          .                               
                          .                               


    ITRCTL

             This routine is used to perform all of the terminal control
        functions  that  can  be performed using the "lead-in" character
        method.  The calling sequence is as follows:

                          CALL ITRCTL ( IFUN , IARG )

        where:  IFUN    is an integer  value  that  corresponds  to  the
                        ASCII  code  for  the  desired  function  in the
                        ranges of 65 through 70 (A-F) and 72 through  90
                        (H-Z).

                IARG    is zero or an integer value as required by  some
                        functions.

             The following example declares the slash character  (/)  to
        be an activation character.

                        DATA IFUN,IARG /"000104,"000057/
                            .                           
                            .                           
                        CALL ITRCTL ( IFUN,IARG )       
                            .                           
                            .                           


    ITRERR

             This routine is used to determine  if  any  terminal  input
        errors have occurred.  The calling sequences are as follows:

                              CALL ITRERR ( IERR )
                                       or
                                IERR = ITRERR ()

        where:  IERR    is one of the following:

                        0   no errors have occurred.

                        1   an input error has occurred.

             The following example checks for terminal input errors  and
        aborts the program if one has occurred.

                                .                  
                                .                  
                            IERR = ITRERR ()       
                            IF ( IERR .NE. 0 ) STOP


        TSXLIB V6.0                                              PAGE 58
        Routine Descriptions


                                .                  
                                .                  


    ITRTYP

             This routine is used to determine the terminal  type  being
        used  on  the  time  sharing line.  The calling sequences are as
        follows:

                              CALL ITRTYP ( IRET )
                                       or
                                IRET = ITRTYP ()

        where:  IRET    is one of the following:

                        0   terminal type unknown.

                        1   VT52.

                        2   VT100.

                        3   Hazeltine.

                        4   ADM3A.

                        5   LA36.

                        6   LA120.

                        7   Diablo and Qume.

                        8   VT200.


    ITSLIC

             This routine is used  to  determine  the  TSX-Plus  license
        number.  The calling sequences are as follows:

                              CALL ITSLIC ( IRET )
                                       or
                                IRET = ITSLIC ()

        where:  IRET    is the requested TSX-Plus license number.


    ITSLIN

             This routine is used to determine the TSX-Plus time sharing
        line number to which the job is attached.  The calling sequences
        are as follows:


        TSXLIB V6.0                                              PAGE 59
        Routine Descriptions


                              CALL ITSLIN ( IRET )
                                       or
                                IRET = ITSLIN ()

        where:  IRET    is zero if RT-11 is  running  or  the  requested
                        line number if TSX-Plus is running.

             The following example aborts if RT-11 is running or contin-
        ues if TSX-Plus is running.

                            IRET = ITSLIN ()       
                            IF ( IRET .EQ. 0 ) STOP
                                .                  
                                .                  


    IUALBK

             This routine is used to  unlock  all  locked  blocks  in  a
        shared file.  The calling sequences are as follows:

                        CALL IUALBK ( ICHAN [ ,IERR ] )
                                       or
                            IERR = IUALBK ( ICHAN )

        where:  ICHAN   is the I/O channel number  that  is  open  to  a
                        shared file.

                IERR    is negative or one of the following:

                        0   the job does not have RLOCK privilege (IPRIV
                            2/9).

                        1   this channel is not open to a shared file.

             When this routine is executed all blocks previously  locked
        by  the  user on the shared file are unlocked.  Blocks locked by
        the user on other files are not released nor are blocks  of  the
        same file that are locked by other users.

             The following example first opens a file, declares it to be
        shared,  locks  some  blocks,  and then unlocks the blocks.  The
        program is stopped if the error condition is returned.

                         CALL ASSIGN ( 40,'DK:FILE.DAT' )
                         ICHAN = ILUN ( 40 )             
                         CALL IDCLSF ( ICHAN,1 )         
                         DO 10 IBLK = 4,6                
                             CALL LKBLKW ( ICHAN,IBLK )  
                      10 CONTINUE                        
                             .                           
                             .                           
                         IERR = IUALBK ( ICHAN )         
                         IF ( IERR .NE. 0 ) STOP         
                             .                           


        TSXLIB V6.0                                              PAGE 60
        Routine Descriptions


                             .                           


    IUNLKM

             This routine is used to unlock a job from memory.  The cal-
        ling sequences are as follows:

                                  CALL IUNLKM

             The PSWAPM privilege (IPRIV 1/7)  is  required  to  execute
        this routine.

             The following example first locks itself  into  memory  and
        then unlocks itself.

                                  CALL LKANMY
                                      .      
                                      .      
                                  CALL IUNLKM
                                      .      
                                      .      


    IUSPBK

             This routine is used to unlock a specific locked block in a
        shared file.  The calling sequences are as follows:

                     CALL IUSPBK ( ICHAN,IBLOCK [ ,IERR ] )
                                       or
                         IERR = IUSPBK ( ICHAN,IBLOCK )

        where:  ICHAN   is the I/O channel number that is  open  to  the
                        shared file.

                IBLOCK  is the number of the block to be unlocked.

                IERR    is negative or one of the following:

                        0   the job does not have RLOCK privilege (IPRIV
                            2/9) or shared file support is not available
                            on the system.

                        1   the channel is not open to a shared file.

             The following example opens a file, declares the file to be
        shared, locks all blocks in the file and then unlocks a specific
        block in the file.  The program is stopped if an error condition
        is returned.

                       CALL ASSIGN ( 30,'DL0:THAT.DAT' )
                       ICHAN = ILUN ( 30 )              
                       CALL IDCLSF ( ICHAN,2 )          
                       CALL LKBLKW ( ICHAN,-1 )         


        TSXLIB V6.0                                              PAGE 61
        Routine Descriptions


                       IERR = IUSPBK ( ICHAN,7 )        
                       IF ( IERR .NE. 0 ) STOP          
                           .                            
                           .                            


    KLDTJB

             This routine is used to abort a detached job.  The  calling
        sequences are as follows:

                        CALL KLDTJB ( JOBNUM [ ,IERR ] )
                                       or
                            IERR = KLDTJB ( JOBNUM )

        where:  JOBNUM  is the job number of the detached job.

                IERR    is negative or the following:

                        1   invalid job number.

             The DETACH privilege (IPRIV 1/12) is  required  to  execute
        this routine.

             The following example first starts a detached job and  then
        later kills the detached job.  If an error condition is returned
        the program is halted.

                         CALL STDTJB ( JOBNAM,JOBNUM )
                             .                        
                             .                        
                         CALL KLDTJB ( JOBNUM,IERR )  
                         IF ( IERR .EQ. 1 ) STOP      
                             .                        
                             .                        


    LKANMY

             This routine is used to lock a job  into  any  memory.   It
        causes  the  job  to  become  locked into the memory space it is
        occupying when this routine is executed.  This routine  executes
        extremely  fast  as  compared  to the routine, LKLOMY, described
        later.  The calling sequences are as follows:

                              CALL LKANMY [ IERR ]
                                       or
                                IERR = LKANMY ()

        where:  IERR    is negative or the following:

                        0   job does not have  PSWAPM  privilege  (IPRIV
                            1/7).

             The job remains locked  until  the  program  exits  or  the


        TSXLIB V6.0                                              PAGE 62
        Routine Descriptions


        routine, IUNLKM, is executed.

             The following example locks the job into the  memory  space
        that it currently occupies.  The program terminates if the error
        condition is returned.

                            IERR = LKANMY ()       
                            IF ( IERR .EQ. 0 ) STOP
                                .                  
                                .                  


    LKBLK

             This routine is used to try to lock a specific block  in  a
        shared  file.   If  the  requested  block  is  not available the
        routine returns immediately with an error code.  If the block is
        available  it  is locked for the requesting user and no error is
        reported.  The calling sequences are as follows:

                     CALL LKBLK ( ICHAN,IBLOCK [ ,IERR ] )
                                       or
                            IERR = ( ICHAN,IBLOCK )

        where:  ICHAN   is the I/O channel number  open  to  the  shared
                        file.

                IBLOCK  is the number of the block to be locked.

                IERR    is negative or one of the following:

                        0   job does not  have  RLOCK  privilege  (IPRIV
                            2/9)  or system does not include shared file
                            support.

                        1   this channel is not open to a shared file.

                        2   request is to lock too many  blocks  in  the
                            file.

                        3   the requested block  is  locked  by  another
                            user.

             The following example opens a file, declares the file to be
        shared  and  tries to lock a block in the file.  If the block is
        already locked the program loops back for another try and if  an
        error condition is returned the program halts.

                         CALL ASSIGN ( 40,'DY1:JUNK.DAT' )
                         ICHAN = ILUN ( 40 )              
                         CALL IDCLSF ( ICHAN,2 )          
                      10 CONTINUE                         
                         IERR = LKBLK ( ICHAN,3 )         
                         IF ( IERR .EQ. 3 ) GO TO 10      
                         IF ( IERR .NE. 0 ) STOP          


        TSXLIB V6.0                                              PAGE 63
        Routine Descriptions


                             .                            
                             .                            


    LKBLKW

             This routine is used to wait for a specific block  to  lock
        in  a  shared file.  If the requested block is locked by another
        job, the requesting job will  be  suspended  until  the  desired
        block becomes available.  The calling sequences are as follows:

                     CALL LKBLKW ( ICHAN,IBLOCK [ ,IERR ] )
                                       or
                         IERR = LKBLKW ( ICHAN,IBLOCK )

        where:  ICHAN   is the I/O channel number  open  to  the  shared
                        file.

                IBLOCK  is the number of the block to be locked.

                IERR    is negative or one of the following:

                        0   job does not  have  RLOCK  privilege  (IPRIV
                            2/9)  or system does not include shared file
                            support.

                        1   this channel is not open to a shared file.

                        2   request is to lock too many  blocks  in  the
                            file.

             Other blocks in  the  file  which  were  previously  locked
        remain  locked.   A  block  number  of  minus one can be used to
        request that all blocks in the file be locked.  If several users
        request  the  same block, access will be granted sequentially in
        the order that the requests are received.

             The following example opens a file, declares the file to be
        shared,  and  locks  all of the blocks in the file.  If an error
        condition is returned the program stops.

                        CALL ASSIGN ( 40,'DK:FILE.DAT' )
                        ICHAN = ILUN ( 40 )             
                        CALL IDCLSF = ( ICHAN,0 )       
                        IERR = LKBLKW ( ICHAN,-1 )      
                        IF ( IERR .NE. 0 ) STOP         
                            .                           
                            .                           


    LKLOMY

             This routine is used to lock a job  into  low  memory.   It
        causes  the  job  to  be  relocated  into low memory and then to
        become locked there.  This type of lock is relatively  slow  and


        TSXLIB V6.0                                              PAGE 64
        Routine Descriptions


        should  be  done  only if the job is to remain locked for a long
        period of time.  The calling sequences are as follows:

                              CALL LKLOMY [ IERR ]
                                       or
                                IERR = LKLOMY ()

        where:  IERR    is negative or the following:

                        0   job does not have  PSWAPM  privilege  (IPRIV
                            1/7).

             The job remains locked in memory until the  program  termi-
        nates or until the routine, IUNLKM, is executed.

             The  following  example  locks  the  job  into  low  memory
        aborting if the error condition is returned.

                            IERR = LKLOMY ()        
                            IF ( IERR .EQ. 0 ) STOP 
                                .                   
                                .                   


    MAPRNT

             This routine is used to map a  shareable  run  time  system
        into  a job's region.  The run time system must first be associ-
        ated with the job by  executing  the  IASRNT  routine  described
        earlier.  The calling sequences are as follows:

                  CALL MAPRNT ( IPAR,IOFFST,MAPSIZ [ ,IERR ] )
                                       or
                      IERR = MAPRNT ( IPAR,IOFFST,MAPSIZ )

        where:  IPAR    is a number in the range of zero to  seven  that
                        indicates  the job's page address register (PAR)
                        that is to be used to access the run  time  sys-
                        tem.   The  PAR  number  selects  the  region of
                        virtual memory in the job that will be mapped to
                        the  run  time system.  The following correspon-
                        dence exists between  PAR  numbers  and  virtual
                        octal address regions within the job:

                                0  000000 - 017777
                                1  020000 - 037777
                                2  040000 - 057777
                                3  060000 - 077777
                                4  100000 - 117777
                                5  120000 - 137777
                                6  140000 - 157777
                                7  160000 - 177777

                IOFFST  specifies which portion of the run  time  system
                        is  to be mapped into the PAR region.  It speci-


        TSXLIB V6.0                                              PAGE 65
        Routine Descriptions


                        fies the number of the 64-byte block within  the
                        run time system where mapping is to begin.  This
                        makes it possible to access  different  sections
                        of  a  run  time  system  at  different times or
                        through different regions.

                MAPSIZ  is the number of 64-byte blocks  to  be  mapped.
                        If  this  value  is larger than can be contained
                        within a single PAR region, multiple PAR regions
                        are automatically mapped as necessary to contain
                        the entire specified section  of  the  run  time
                        system.

                IERR    is one of the following:

                        0   no error.

                        1   there is no run time system associated  with
                            this job.

             This routine affects the mapping of  only  the  PAR  region
        specified  in  IPAR  and following PARs if the size so requires.
        It does not affect the mapping of any other PAR regions that may
        previously  have  been mapped to a run time system.  Thus, a job
        may have different PAR regions mapped to different  sections  of
        the same run time system or to different run time systems.  Real
        time programs may map PAR region number seven to  the  I/O  page
        and map other PAR regions to shared run time systems.

             The memory size of a job is not affected by the use of  the
        this  routine.   Mapping  a  portion  of a job's virtual address
        space  to  a  shared  run  time  system  neither  increases  nor
        decreases  the  size  of memory occupied by the job.  If a job's
        size is such that a portion of its normal memory is under a  PAR
        region  that is mapped to a run time system, that section of its
        normal memory becomes inaccessible to the job as long as the run
        time system mapping is in effect but the memory contents are not
        lost and may be reaccessed by disassociating all run  time  sys-
        tems from the job.

             Any of the PAR regions may be mapped to a run  time  system
        including PAR region number seven which is normally not accessi-
        ble to a job.

             The  following  example  first  uses  the  SYSLIB  routine,
        IRAD50,  to  name  the  run time system, associates the run time
        system with the job, then maps a PAR region to a section of  the
        run  time  system, and finally disassociates the run time system
        from the job.

                       DIMENSION IRNTIM ( 2 )           
                       CALL IRAD50 ( 6,'TSXLIB',IRNTIM )
                       CALL IASRNT ( IRNTIM )           
                       CALL MAPRNT ( 3,1,4 )            
                           .                            


        TSXLIB V6.0                                              PAGE 66
        Routine Descriptions


                           .                            
                       CALL IASRNT ( 0 )                
                           .                            
                           .                            


    MEMPOS

             This routine is used to determine the position of a job  in
        memory for a TSX-Plus line.  The calling sequence is as follows:

                      CALL MEMPOS ( LINUM,IPOS [ ,IERR ] )

        where:  LINUM   is the number of the line for which memory posi-
                        tion information is returned.

                IPOS    is the 512-word block number of the start of the
                        memory  area  allocated  to the job.  This value
                        will be zero if the job is swapped out of  memo-
                        ry.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.


    MEMSET

             This routine is used to set the amount of memory that  will
        be allocated for the job.  The calling sequences are as follows:

                         CALL MEMSET ( IARG [ ,IRET ] )
                                       or
                             IRET = MEMSET ( IARG )

        where:  IARG    is the top memory address requested.

                IRET    is the top memory address allocated.

             The size allocated to a job reverts to the  size  specified
        by the most recent MEMORY keyboard command when the job exits or
        chains.

             The following example requests  a  top  memory  address  of
        120000 (octal).  The program is halted if the allocation is less
        than the request.

                           DATA IARG/"120000/        
                           IRET = MEMSET ( IARG )    
                          IF ( IRET .LMT. IARG ) STOP
                               .                     
                               .                     


        TSXLIB V6.0                                              PAGE 67
        Routine Descriptions


    MEMUSE

             This routine is used to return the amount of  memory  allo-
        cated to a TSX-Plus line.  The calling sequence is as follows:

                     CALL MEMUSE ( LINUM,MEMSIZ [ ,IERR ] )

        where:  LINUM   is the number of the  line  about  which  memory
                        allocation information is returned.

                MEMSIZ  is the amount of memory allocated to the line in
                        512-word blocks.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.


    MOUNT

             This routine is used to mount a file structured device  for
        directory  caching.   The  effect of this routine is the same as
        the TSX-Plus MOUNT keyboard command.  The calling sequences  are
        as follows:

                        CALL MOUNT ( IDVNAM [ ,IERR ] )
                                       or
                            IERR = MOUNT ( IDVNAM )

        where:  IDVNAM  is the RAD50 value of the device name.

                IERR    is one of the following:

                        0   no error.

                        1   no room left in the table  of  mounted  dev-
                            ices.

             The following example uses the SYSLIB routine,  IRAD50,  to
        convert  the  ASCII  device name, DY3, to its RAD50 value.  Then
        the file structured device is mounted.  The program is halted if
        an error condition is returned.

                         CALL IRAD50 ( 3,'DY3',IDVNAM )
                         IERR = MOUNT ( IDVNAM )       
                         IF ( IERR .EQ. 1 ) STOP       
                             .                         
                             .                         


        TSXLIB V6.0                                              PAGE 68
        Routine Descriptions


    MPIOPS

             This routine is used to map the I/O page into  the  program
        space  between  the  octal  addresses of 160000 and 177777.  The
        calling sequences are as follows:

                            CALL MPIOPS ( [ IERR ] )
                                       or
                                 IERR = MPIOPS

        where:  IERR    is negative or the following:

                        0   the  job  does  not  have  MEMMAP  privilege
                            (IPRIV  1/10) or the system does not include
                            real time support.

             The mapping set up by this routine remains in effect  until
        the routine, MPRMPS, is executed or the program terminates.


    MPRGN

             This routine is used to map a region of virtual memory to a
        specified  region of physical memory.  The calling sequences are
        as follows:

                  CALL MPRGN ( IPAR,IPAD,ISIZ,IACS [ ,IERR ] )
                                       or
                      IERR = MPRGN ( IPAR,IPAD,ISIZ,IACS )

        where:  IPAR    is one of the following  Page  Address  Register
                        (PAR)  numbers  indicating  the beginning of the
                        virtual region to be mapped:

                        PAR     Virtual Region
                        0       000000-017777
                        1       020000-037777
                        2       040000-057777
                        3       060000-077777
                        4       100000-177777
                        5       120000-137777
                        6       140000-157777
                        7       160000-177777

                IPAD    is the physical address divided by  100  (octal)
                        to which the virtual address is to be mapped.

                ISIZ    is the number of 100-byte (octal)  pages  to  be
                        mapped.   If zero all PAR mapping is restored to
                        normal.

                IACS    indicates the read/write access  of  the  mapped
                        region as follows:

                        0   Read only.


        TSXLIB V6.0                                              PAGE 69
        Routine Descriptions


                        1   Read and write.

                IERR    is negative or the following:

                        0   real time support is not available  or  this
                            job  does  not  have MEMMAP privilege (IPRIV
                            1/10).


    MPRMPS

             This routine is used to map a simulated RMON into the  pro-
        gram  space  between  the  octal addresses of 160000 and 177777.
        The calling sequences are as follows:

                            CALL MPRMPS ( [ IERR ] )
                                       or
                                 IERR = MPRMPS

        where:  IERR    is negative or the following:

                        0   the  job  does  not  have  MEMMAP  privilege
                            (IPRIV  1/10) or the system does not include
                            real time support.


    MSGREQ

             This routine is used to post a read request for a  TSX-Plus
        interjob message.  The calling sequences are as follows:

                CALL MSGREQ ( CHNL,BUFR,ISIZ,CPLRTN [ ,IERR ] )
                                       or
                    IERR = MSGREQ ( CNLI,BUFR,ISIZ,CPLRTN )

        where:  CHNL    is the name of the string array  containing  the
                        six character name of the message channel.

                BUFR    is the name of  the  string  array  that  is  to
                        receive the message.

                ISIZ    is the length of the message buffer.

                CPLRTN  is the name of  the  completion  routine  to  be
                        entered when the message is received.

                IERR    is negative or as follows:

                        0   job does not have MESSAGE  privilege  (IPRIV
                            2/10)  or system does not have message chan-
                            nel support.

                        1   all message channels are busy.

                        4   message  was  longer  than   the   receiving


        TSXLIB V6.0                                              PAGE 70
        Routine Descriptions


                            buffer.

                        5   the maximum allowed number of  requests  are
                            active.

             On entry to the completion routine, processor  register  R0
        contains  the  number of bytes in the message that was received,
        and R1 contains the number of the job  that  sent  the  message.
        The  GETREG  routine may be used to recover the values stored in
        R0 and R1.  Another call to this routine may be made from within
        the  completion  routine  if it is desired to receive additional
        messages.

             The SUSPND and RESUME SYSLIB calls may be  used  with  this
        facility  if  the  program reaches a point where it must suspend
        its execution until a message arrives.

             The following sample program aborts if an  error  condition
        is  returned  after attempting to post a read request for a mes-
        sage.  It later issues a SUSPND call.  The associated completion
        routine must issue a RESUME call after processing the message.

                    LOGICAL*1 CHNL(6),BUFR(75)             
                    DATA ISIZ /75/                         
                    EXTERNAL CPLRTN                        
                    CALL SCOPY ( 'CHNL04',CHNL,6 )         
                        .                                  
                        .                                  
                    IERR = MSGREQ ( CHNL,BUFR,ISIZ,CPLRTN )
                    IF ( IERR .GT. 0 ) STOP                
                        .                                  
                        .                                  
                    CALL SUSPND                            
                        .                                  
                        .                                  


    MSGSND

             This routine is used to queue up a message to  another  job
        on  a  named  channel.  If other messages are already pending on
        the channel, the new message is added to the end of the list  of
        waiting  messages.   The sending program continues execution and
        does not wait for the message to be accepted by a receiving pro-
        gram.   During  processing  the message is copied to an internal
        buffer, and the sending program is free to destroy  its  message
        on  return from this routine.  The calling sequences are as fol-
        lows:

                 CALL MSGSND ( ICHNAM,MSGBUF,MSGSIZ [ ,IERR ] )
                                       or
                     IERR = MSGSND ( ICHNAM,MSGBUF,MSGSIZ )

        where:  ICHNAM  is the six ASCII character name of  the  message
                        channel.


        TSXLIB V6.0                                              PAGE 71
        Routine Descriptions


                MSGBUF  is the name of the string array  containing  the
                        message.

                MSGSIZ  is the length of the message in characters.

                IERR    is negative or one of the following:

                        0   job does not have MESSAGE  privilege  (IPRIV
                            2/10) or the system does not include message
                            channel support.

                        1   all message channels are busy.

                        2   the maximum allowed number of  messages  are
                            being held in the message queues.

                        4   the transmitted message was too long and was
                            truncated to the maximum allowed length.

                        5   maximum  number  of  message  requests   are
                            already pending.

             The following example uses the SYSLIB  routine,  SCOPY,  to
        load  the string variables, MSGBUF and ICHNAM, then sends a mes-
        sage to the named channel, JUNK.  The program aborts if an error
        condition is returned.

                    LOGICAL*1 MSGBUF ( 14 )                
                    LOGICAL*1 ICHNAM ( 8 )                 
                    CALL SCOPY ( ' HELLO THERE',MSGBUF,12 )
                    CALL SCOPY ( 'JUNK  ',ICHNAM,6 )       
                    IERR = MSGSND ( ICHNAM,MSGBUF,12 )     
                    IF ( IERR .NE. 0 ) STOP                
                        .                                  
                        .                                  


    NONINT

             This routine is used to schedule the running job as  either
        an  interactive  job  or  as a non-interactive job.  The calling
        sequence is as follows:

                              CALL NONINT ( MODE )

        where:  MODE    is either one of the following two values:

                        0   causes  the   job   to   be   scheduled   as
                            non-interactive.

                        1   causes the job to be scheduled  as  interac-
                            tive.

             Programs that do a large amount of terminal input, but that
        are  not truly interactive jobs in the usual sense, such as file


        TSXLIB V6.0                                              PAGE 72
        Routine Descriptions


        transfer programs, should use this routine  to  avoid  excessive
        interference with normal interactive time sharing jobs.

             The  following  example  first  schedules  the  job  to  be
        non-interactive and then interactive.

                              MODE = 0            
                              CALL NONINT ( MODE )
                                  .               
                                  .               
                              MODE = 1            
                              CALL NONINT ( MODE )
                                  .               
                                  .               


    RCVMSG

             This routine is used to receive  a  message  from  a  named
        channel  if  a message is pending on the channel.  If no message
        is pending, an error code is returned, and the  calling  program
        is  allowed  to  continue execution.  The calling sequence is as
        follows:

             CALL RCVMSG ( ICHNAM,MSGBUF,IBUFSZ,MSGSIZ [ ,IERR ] )

        where:  ICHNAM  is the six ASCII character name of  the  message
                        channel.

                MSGBUF  is the name of the receiving string array.

                IBUFSZ  is  the  length  of  the  receiving  buffer   in
                        characters.

                MSGSIZ  is  the  length  of  the  received  message   in
                        characters.

                IERR    is negative or one of the following:

                        0   job does not have MESSAGE  privilege  (IPRIV
                            2/10) or the system does not include message
                            channel support.

                        1   all message channels are busy.

                        3   no message was queued on the named channel.

                        4   the message was longer  than  the  receiving
                            buffer.

                        5   maximum number of message requests are pend-
                            ing.

             The following example sets up  using  the  SYSLIB  routine,
        SCOPY, to receive a message, and then attempts to receive a mes-


        TSXLIB V6.0                                              PAGE 73
        Routine Descriptions


        sage on the named channel, JUNK.  The program is stopped  if  an
        error condition is returned.

                  LOGICAL*1 ICHNAM ( 8 )                     
                  LOGICAL*1 MSGBUF ( 72 )                    
                  CALL SCOPY ( 'JUNK  ',ICHNAM,6)            
                  CALL RCVMSG ( ICHNAM,MSGBUF,72,MSGSIZ,IERR)
                  IF ( IERR .NE. 0 ) STOP                    
                      .                                      
                      .                                      


    RCVMSW

             This routine is used to suspend the execution of a  program
        until  a message becomes available on a named channel.  The cal-
        ling sequence is as follows:

             CALL RCVMSW ( ICHNAM,MSGBUF,IBUFSZ,MSGSIZ [ ,IERR ] )

        where:  ICHNAM  is the six ASCII character name of  the  message
                        channel.

                MSGBUF  is the name of the receiving string array.

                IBUFSZ  is  the  length  of  the  receiving   array   in
                        characters.

                MSGSIZ  is  the  length  of  the  received  message   in
                        characters.

                IERR    is negative or one of the following:

                        0   job does not have MESSAGE  privilege  (IPRIV
                            2/10) or the system does not include message
                            channel support.

                        1   all message channels are busy.

                        4   the message was longer  than  the  receiving
                            buffer.

                        5   maximum number of message requests pending.

             The following example uses the SYSLIB  routine,  SCOPY,  to
        load the variable, ICHNAM, then waits for a message to arrive on
        the named channel.  The program is stopped if an error condition
        is returned.

                LOGICAL*1 MSGBUF ( 72 )                        
                LOGICAL*1 ICHNAM ( 8 )                         
                CALL SCOPY ( 'JUNK  ',ICHNAM,6 )               
                CALL RCVMSW ( ICHNAM,MSGBUF,IBUFSZ,MSGSIZ,IERR)
                IF ( IERR .NE. 0 ) STOP                        
                    .                                          


        TSXLIB V6.0                                              PAGE 74
        Routine Descriptions


                    .                                          


    RLCTL

             This routine is used to allow a running program to relinqu-
        ish  exclusive  control of the system after the program finishes
        performing some time-critical task.  The calling sequence is  as
        follows:

                                   CALL RLCTL

             REALTIME privilege (IPRIV 1/6) is required to execute  this
        routine.


    RSTODT

             This routine is used to reset or clear the  ODT  activation
        mode.  The calling sequence is as follows:

                                  CALL RSTODT


    SETODT

             This routine is used to set the ODT activation  mode.   The
        calling sequence is as follows:

                                  CALL SETODT

             In this  mode  TSX-Plus  considers  all  characters  to  be
        activation  characters  except the digits, the comma, the dollar
        sign, and the semicolon.


    STDTJB

             This routine is used to start the execution of  a  detached
        job.  The calling sequence is as follows:

                    CALL STDTJB ( JOBNAM,JOBNUM [ ,IERR ] )

        where:  JOBNAM  is the ASCII string, dev:filnam.ext,  terminated
                        by a null byte.

                JOBNUM  is the returned job number.

                IERR    is negative or the following:

                        1   no detached job line is available.

             The DETACH privilege (IPRIV 1/12) is  required  to  execute
        this routine.



        TSXLIB V6.0                                              PAGE 75
        Routine Descriptions


             If a free detached job line  is  available,  the  specified
        command  file,  JOBNAM,  is  initiated as a detached job and the
        number of the detached job is returned in the variable, JOBNUM.

             The following example uses the SYSLIB  routine,  SCOPY,  to
        load  the  variable,  JOBNAM,  then  initiates the detached job,
        DETJOB.COM, from device, DY2:, storing the  job  number  in  the
        variable,  JOBNUM.  The program is terminated if an error condi-
        tion is returned.

                    LOGICAL*1 JOBNAM ( 16 )                 
                    CALL SCOPY ( 'DY2:DETJOB.COM',JOBNAM,14)
                    CALL STDTJB ( JOBNAM,JOBNUM,IERR )      
                    IF ( IERR .EQ. 1 ) STOP                 
                        .                                   
                        .                                   


    STPRLV

             This routine  is  used  to  set  the  user  mode  processor
        priority level from a running program.  This may be used when it
        is necessary for a real time program to block interrupts  for  a
        short  period  of time while it is performing some time critical
        operation.  The calling sequence is as follows:

                             CALL STPRLV ( IPRLVL )

        where:  IPRLVL  is the  desired  user  mode  processor  priority
                        level in the range of zero through seven.

             REALTIME privilege (IPRIV 1/6) is required to execute  this
        routine.   Interrupts should not be disabled for long periods of
        time or system clock interrupts and character  input  interrupts
        will  be  lost.  The following example raises the priority level
        to seven and later reduces it back to zero.

                               CALL STPRLV ( 7 )
                                   .            
                                   .            
                               CALL STPRLV ( 0 )
                                   .            
                                   .            


    STUNAM

             This routine is used to set the user name  associated  with
        the current job.  The calling sequences are as follows:

                       CALL STUNAM ( USRNAM [ , IERR ] )
                                       or
                            IERR = STUNAM ( USRNAM )



        TSXLIB V6.0                                              PAGE 76
        Routine Descriptions


        where:  USRNAM  is the name of the twelve-character  array  that
                        contains the new user name ASCII string.

                IERR    is negative or as follows:

                        0   the job  does  not  have  SETNAME  privilege
                            (IPRIV 1/4).

             The following example sets the user name to JOEBLOWHARD.

                      LOGICAL*1 USRNAM(14)               
                      CALL SCOPY ( 'JOEBLOWHARD',USRNAM )
                      IERR = STUNAM ( USRNAM )           
                      IF ( IERR .GE. 0 ) STOP            
                          .                              
                          .                              


    TERMPA

             This routine is used to conclude  a  performance  analysis.
        It  has  the effect of returning into a user supplied buffer the
        results of the analysis and  freeing  the  performance  analysis
        feature for use by other users.  The calling sequence is as fol-
        lows:

                 CALL TERMPS ( IPARBF,IHSTBF,IHBSIZ [ ,IERR ] )

        where:  IPARBF  is the name of a four element  parameter  buffer
                        with the elements assigned as follows:

                        1   is the base address of the monitored region.

                        2   is the top address of the monitored region.

                        3   is the number of bytes per histogram cell.

                        4   is  a  control  and  status  flag  with  bit
                            assignments as follows:

                            1       I/O wait time was included.

                            100000  at least one of the histogram  cells
                                    overflowed.

                IHSTBF  is the name of the histogram buffer.

                IHBSIZ  is the number of elements or cells in the histo-
                        gram buffer.

                IERR    is negative or one of the following:

                        0   this  job  is  not   doing   a   performance
                            analysis.



        TSXLIB V6.0                                              PAGE 77
        Routine Descriptions


                        1   area provided for the histogram count vector
                            is too small.

             The histogram data returned consists of a vector of  16-bit
        binary  values,  one  value for each cell in the histogram.  The
        first value corresponds to the histogram cell that starts at the
        base address of the region that was monitored.

             The  following  example  shows  the  complete   performance
        analysis  from  initialization  to  termination.  The program is
        stopped if an error condition is returned on termination of  the
        analysis.

                   DIMENSION IPARBF ( 4 )                   
                   DIMENSION IHSTBF ( 16 )                  
                   CALL INITPA ( "2000,"4000,"100,0 )       
                   CALL ISTPA                               
                       .                                    
                       .                                    
                   CALL ISPPA                               
                   CALL TERMPA ( IPARBF,IHSTBF,IHBSIZ,IERR )
                   IF ( IERR .GE. 0 ) STOP                  
                       .                                    
                       .                                    


    TIMOUT

             This routine is used to set the time out value that  is  to
        be  applied  to  the next terminal input operation.  The calling
        sequence is as follows:

                          CALL TIMOUT ( ITIME,IACTCH )

        where:  ITIME   is the time out value in 0.5 second units.

                IACTCH  is the value of the single character that is  to
                        be  returned as the last or activation character
                        of the field if a time out occurs.

             The value specified with this routine applies only  to  the
        next  terminal  input  field.   The time value is reset when the
        next field is received from the terminal or the time out occurs.
        A new time out value must be specified for each input field that
        is to be time controlled.

             The following example uses  a  time  out  value  of  twenty
        seconds  and specifies that a control-X is to be returned if the
        timeout occurs.

                                 .                
                                 .                
                             CALL TIMOUT ( 40,24 )
                                 .                
                                 .                


        TSXLIB V6.0                                              PAGE 78
        Routine Descriptions


    TKCTL

             This routine is used to allow a  running  program  to  gain
        exclusive  access  to  the  system to perform some time-critical
        task.  The calling sequence is as follows:

                                   CALL TKCTL

             The effect of this routine is to  cause  the  TSX-Plus  job
        scheduler  to ignore all other jobs during the interval that the
        calling program has exclusive control of the  system.   REALTIME
        privilege (IPRIV 1/6) is required to execute this routine.

             Exclusive access is relinquished when the  calling  program
        calls   RLCTL,  terminates,  or  aborts.   Exclusive  access  is
        retained if the calling program chains to another program.


    TRMIN

             This routine is used to accept a string of characters  from
        the terminal.  The calling sequence is as follows:

                 CALL TRMIN ( ICHBUF,IBFSIZ,ICOUNT [ ,IERR ] )

        where:  ICHBUF  is the name of the buffer that is to receive the
                        string.

                IBFSIZ  is  the  length  of  the  receiving  buffer   in
                        characters.

                ICOUNT  is the number of characters actually received.

                IERR    is one of the following:

                        0   no error.

                        1   the specified buffer overflowed.

             This routine causes a program to wait until  an  activation
        character  is  entered  on  the  terminal  and  then returns all
        characters received up to  and  including  the  last  activation
        character.   This  routine  is substancially more efficient than
        doing a series of the SYSLIB routin ITTINR.  It is  particularly
        well suited for accepting input from page buffered terminals.

             The following example accepts a string of  characters  from
        the  terminal.   The program is halted if the error condition is
        returned.

                      LOGICAL*1 ICHBUF ( 24 )             
                      CALL TRMIN ( ICHBUF,24,ICOUNT,IERR )
                      IF ( IERR .EQ. 1 ) STOP             
                          .                               
                          .                               


        TSXLIB V6.0                                              PAGE 79
        Routine Descriptions


    TRMMSG

             This routine is used to send a message  to  another  line's
        terminal.  The calling sequences are as follows:

                     CALL TRMMSG ( ILINE,IMSGBF [ ,IERR ] )
                                       or
                         IERR = TRMMSG ( ILINE,IMSGBF )

        where:  ILINE   is the line number of the terminal that the mes-
                        sage is to be sent.

                IMSGBF  is the name of  the  buffer  that  contains  the
                        message.

                IERR    is negative or one of the following:

                        0   job does  not  have  SEND  privilege  (IPRIV
                            1/5).

                        1   receiving line is SET TT GAG.

             The message must be terminated with a null character.

             The following example sends a message to the terminal  con-
        nected to line 14.  If the job does not have SEND privilege, the
        program aborts.  If the receiving line is SET TT GAG,  the  pro-
        gram loops until the condition changes to NOGAG.

                  LOGICAL*1 IMSGBF ( 30 )                        
                  CALL SCOPY ( ' THIS IS THE MESSAGE',IMSGBF,20 )
              100 CONTINUE                                       
                  CALL TRMMSG ( 14,IMSGBF,IERR )                 
                  IF ( IERR .EQ. 0 ) STOP                        
                  IF ( IERR .EQ. 1 ) GO TO 100                   
                      .                                          
                      .                                          


    TRMOUT

             This routine is used to send a string of characters to  the
        terminal.  The calling sequence is as follows:

                         CALL TRMOUT ( ICHSTR,ICOUNT )

        where:  ICHSTR  is the name of the buffer containing the  string
                        of characters.

                ICOUNT  is the number of characters in the string.

             This routine is much more efficient to use than a series of
        the  SYSLIB  routine, ITTOUR.  It has the same efficiency as the
        SYSLIB routine, PRINT, but it uses a  count  of  the  number  of
        characters  to send instead of having the string terminated with


        TSXLIB V6.0                                              PAGE 80
        Routine Descriptions


        a null character.

             The following example sends a string of characters  to  the
        terminal.

                 LOGICAL*1 ICHSTR ( 22 )                       
                 CALL SCOPY ( ' THIS IS THE STRING.'ICHSTR,20 )
                 CALL TRMOUT ( ICHSTR,20 )                     
                     .                                         
                     .                                         


    TTCRTN

             This routine is used  to  establish  a  completion  routine
        which  will be executed as each input character is received from
        the terminal.  The calling sequence is as follows:

                             CALL TTCRTN ( CPLRTN )

        where:  CPLRTN  is the name of the completion routine that is to
                        be entered for each input character.

             On entry to the completion routine, the received  character
        is  in  R0.   The  EMT to connect the completion routine must be
        reexecuted each time a character is received.   This  should  be
        done  at  the end of the completion routine after processing the
        last received character.  The program  should  be  running  with
        single  character  activation  and  with  bit  12 set in the job
        status word.

             The following example sets up  for  and  calls  a  terminal
        input  completion routine.  A skeleton of the completion routine
        is also given.

                           EXTERNAL CPLRTN          
                           CALL IPOKE ( "10000,"44 )
                           CALL TTCRTN ( CPLRTN )   
                               .                    
                               .                    

                           SUBROUTINE CPLRTN        
                               .                    
                               .                    
                           CALL TTCRTN ( CPLRTN )   
                           RETURN                   


        TSXLIB V6.0                                              PAGE 81
        Building the Library






                            4.  Building the Library


             The  sources  for  the  TSX-Plus  Library  consist  of  the
        MACRO-11 modules listed in Table 4-1.  The process of construct-
        ing the library file, TSXLIB.OBJ, is the same when  accomplished
        under either RT-11 or under TSX-Plus.


                Module  Content

                CLLINE  Communication line support.
                DETJBS  Detached job support.
                DVALOC  Device allocating and deallocating.
                JBPRIV  Job priveleges control.
                JBSTMN  Job status monitoring.
                MNTDEV  Device mounting and dismounting.
                MSGCOM  Interjob message communication.
                PRFANL  Performance analysis support.
                RELTIM  Real time program support.
                RUNTIM  Shared run time system support.
                SHRFIL  Shared file system support.
                SPOLER  Spooler support.
                SYSTAT  System status information.
                TRMCOM  Terminal communication.
                TRMCTL  Terminal control.
                TSFILS  Special file information.
                TSLBID  TSXLIB identification.
                TSXMSC  Miscellaneous EMTs.
                TSXODT  ODT activation mode support.
                USRNAM  User name support.
                WINDOW  Windowing support.

                        TSXLIB MACRO-11 source modules.
                                   Table 4-1.


             First the MACRO-11 modules are assembled as follows:

                                 .RUN SY:MACRO 
                                 *CLLINE=CLLINE
                                 *DETJBS=DETJBS
                                 *JBPRIV=JBPRIV
                                 *JBSTMN=JBSTMN
                                 *MNTDEV=MNTDEV
                                 *MSGCOM=MSGCOM
                                 *PRFANL=PRFANL
                                 *RELTIM=RELTIM
                                 *RUNTIM=RUNTIM
                                 *SHRFIL=SHRFIL
                                 *SPOLER=SPOLER


        TSXLIB V6.0                                              PAGE 82
        Building the Library


                                 *SYSTAT=SYSTAT
                                 *TRMCOM=TRMCOM
                                 *TRMCTL=TRMCTL
                                 *TSFILS=TSFILS
                                 *TSLBID=TSLBID
                                 *TSXMSC=TSXMSC
                                 *TSXODT=TSXODT
                                 *USRNAM=USRNAM
                                 *WINDOW=WINDOW
                                 *^C           

             Next the library file is constructed as follows:

                                .RUN SY:LIBR    
                                *TSXLIB=CLLINE//
                                *DETJBS         
                                *DVALOC         
                                *JBPRIV         
                                *JBSTMN         
                                *MNTDEV         
                                *MSGCOM         
                                *PRFANL         
                                *RELTIM         
                                *RUNTIM         
                                *SHRFIL         
                                *SPOLER         
                                *SYSTAT         
                                *TRMCOM         
                                *TRMCTL         
                                *TSFILS         
                                *TSLBID         
                                *TSXMSC         
                                *TSXODT         
                                *USRNAM         
                                *WINDOW         
                                *//             
                                *^C             

             The command file, TSXLIB.COM, in the distribution kit  will
        accomplish the construction of the library file, TSXLIB.OBJ.


        TSXLIB V6.0                                              PAGE 83
        References






                                   References


        1.  S & H Computer Systems, Inc., "TSX-Plus  Reference  Manual",
            Fifth Edition, First Printing, Nashville, TN, November 1985

        2.  S & H Computer Systems, Inc., "TSX-Plus Version 6.0  Release
            Notes", Nashville, TN, November 1985.

        3.  Digital Equipment  Corporation,  "PDP-11  MACRO-11  Language
            Reference Manual", AA-V027A-TC, Maynard, MA, March 1983.

        4.  Digital Equipment Corporation, "RT-11 System User's  Guide",
            AA-5279C-TC, Maynard, MA, March 1983.

        5.  Digital Equipment Corporation, "RT-11 Programmer's Reference
            Manual", AA-H378B-TC, Maynard, MA, March 1983.

        6.  Digital Equipment Corporation, "PDP-11 FORTRAN  IV  Language
            Reference Manual", AA-R953A-TK, Maynard, MA, March 1983.

        7.  Digital Equipment Corporation, "PDP-11  FORTRAN-77  Language
            Reference Manual", AA-V193A-TK, Maynard, MA, July 1983.


        TSXLIB V6.0                                              PAGE 84
        Appendix A:  KWIK Index






                            Appendix A:  KWIK Index

             This appendix lists the TSXLIB routines in  a  key-word-in-
        context  (KWIK)  index.   It is meant to help the user to locate
        the particular routine that is needed.


         IHERR                       Enable abort on error.             
         ISERR                      Inhibit abort on error.             
         IFLINF     Obtain some information about file.                 
         TRMIN    from terminal.            Accept string of characters 
         IAQFLC   another job.              Acquire file context of     
         IACTCH           Check for pending activation characters.      
         RSTODT                Reset normal activation mode.            
         SETODT                     Set ODT activation mode.            
         CNVAPA   address.  Convert virtual address to physical         
         CNVAPA         address to physical address.     Convert virtual
         IUALBK                      Unlock all locked blocks.          
         IALOC                              Allocate device.            
         ICALOC   device.             Check allocation status of        
         MEMSET                  Set memory allocation.                 
         MEMUSE   job.            Determine amount of memory used by    
         INITPA             for performance analysis.         Initialize
         ISTPA            Start performance analysis.                   
         ISPPA             Stop performance analysis.                   
         TERMPA            from performance analysis.          Terminate
         GTUNAM   job.        Get user name associated with current     
         STUNAM   job.        Set user name associated with current     
         IDCLSF             Declare file to be shared.                  
         IPGNAM         Get name of program being run by job.           
         IBICIO   page.                     Bit clear value into I/O    
         IBISIO   page.                     Bit set value into I/O      
         LKBLKW                    Wait for block to lock.              
         LKBLK                  Try to lock block.                      
         IUSPBK             Unlock specific block.                      
         ISPBLK    Determine number of free blocks in spool file.       
         IUALBK           Unlock all locked blocks.                     
         BRKCTL                   Establish break sentinel control.     
         IBSTCH   change.                   Broadcast job status        
         ICNMCN   monitoring connection.    Cancell job status          
         IPRIV                   Determine, change privileges for job.  
         IBSTCH        Broadcast job status change.                     
         ITRCTL   functions.        Lead-in character terminal control  
         TRMIN             Accept string of characters from terminal.   
         TRMOUT              Send string of characters to terminal.     
         IACTCH      for pending activation characters.            Check
         ICALOC   device.                   Check allocation status of  
         IACTCH   activation characters.    Check for pending           
         ITRERR   errors.                   Check for terminal input    
         ICKWTS   file.                     Check for writes to shared  
         ILNSTS                             Check status of line.       


        TSXLIB V6.0                                              PAGE 85
        Appendix A:  KWIK Index


         ICNTSP            Control speed of CL line.                    
         IBICIO                         Bit clear value into I/O page.  
         IRDRCL   timesharing line.Redirect communication or            
         ITCRTN   routine.          Trigger completion from interrupt   
         ICNINT    Connect interrupt vector completion routine.         
         TTCRTN          Establish terminal completion routine.         
         ICNINT   completion routine.       Connect interrupt vector    
         ICNRTN   interrupt vector.         Connect service routine to  
         ICONTM                   Determine connect time for job.       
         ICNMCN       job status monitoring connection.          Cancell
         IESMCN       job status monitoring connection.        Establish
         IRLINT         an interrupt vector connection.          Release
         IPRWND                   Print the contents of a window.       
         IAQFLC                Acquire file context of another job.     
         ISPCTL   spooled file.             Control release time of     
         ICNTSP                             Control speed of CL line.   
         ITRCTL          character terminal control functions.   Lead-in
         RLCTL         Relinquish exclusive control of system.          
         TKCTL               Take exclusive control of system.          
         BRKCTL    Establish break sentinel control.                    
         CNVAPA   physical address.         Convert virtual address to  
         ICPUTM                         Get CPU time used by job.       
         ICRWND                             Create a window.            
         ISTFTM                         Set creation time of file.      
         ISTPRV                         Set current job priority value. 
         GTUNAM        name associated with current job.        Get user
         STUNAM        name associated with current job.        Set user
         IDALOC                             Deallocate device.          
         IDCLSF                             Declare file to be shared.  
         IDLWND                             Delete a window.            
         ISTDJ                Get status of detached job.               
         KLDTJB                        Kill detached job.               
         STDTJB                       Start detached job.               
         ITSLIC   number.                   Determine TSX-Plus license  
         ITSLIN   number.                   Determine TSX-Plus line     
         MEMUSE   used by job.              Determine amount of memory  
         ICONTM   job.                      Determine connect time for  
         ISPBLK   blocks in spool file.     Determine number of free    
         MEMPOS   in memory.                Determine position of job   
         ITRTYP                             Determine terminal type.    
         IPRIV    privileges for job.       Determine, change           
         IALOC                     Allocate device.                     
         ICALOC        allocation status of device.                Check
         IDALOC                  Deallocate device.                     
         DISMNT    Dismount file structured device.                     
         MOUNT        Mount file structured device.                     
         IASRNT   time system and job.     [Dis]associate shared run    
         DISMNT   device.                   Dismount file structured    
         HIEFOF               Turn off high efficiency terminal mode.   
         HIEFON                Turn on high efficiency terminal mode.   
         IHERR                              Enable abort on error.      
         IHERR              Enable abort on error.                      
         ISERR             Inhibit abort on error.                      
         ITRERR    Check for terminal input errors.                     
         BRKCTL   control.                  Establish break sentinel    


        TSXLIB V6.0                                              PAGE 86
        Appendix A:  KWIK Index


         IESMCN   monitoring connection.    Establish job status        
         TTCRTN   completion routine.       Establish terminal          
         RLCTL    system.        Relinquish exclusive control of        
         TKCTL    system.              Take exclusive control of        
         IEXSTS                     Get job execution status.           
         IAQFLC   job.              Acquire file context of another     
         DISMNT                    Dismount file structured device.     
         MOUNT                        Mount file structured device.     
         IDCLSF                     Declare file to be shared.          
         ICKWTS        for writes to shared file.                  Check
         ISPCTL     release time of spooled file.                Control
         ISPBLK     of free blocks in spool file.       Determine number
         IFLINF      some information about file.                 Obtain
         ISVST        Save status of shared file.                       
         ISTFTM        Set creation time of file.                       
         ISPBLK         Determine number of free blocks in spool file.  
         ITRCTL            terminal control functions. Lead-in character
         ICPUTM                             Get CPU time used by job.   
         IEXSTS                             Get job execution status.   
         IPGNAM   run by job.               Get name of program being   
         IPPNUM   number for job.           Get project, programmer     
         ISTDJ                              Get status of detached job. 
         GTUNAM   with current job.         Get user name associated    
         GETREG   register.                 Get value stored processor  
         HIEFOF   mode.            Turn off high efficiency terminal    
         HIEFON   mode.             Turn on high efficiency terminal    
         MPIOPS   space.                Map I/O page into program       
         IBICIO        Bit clear value into I/O page.                   
         IBISIO          Bit set value into I/O page.                   
         IPEKIO            Peek at value in I/O page.                   
         IPOKIO             Poke value into I/O page.                   
         IFLINF                 Obtain some information about file.     
         ISERR                              Inhibit abort on error.     
         INITPA   analysis.                 Initialize for performance  
         ITRERR          Check for terminal input errors.               
         ITCRTN     Trigger completion from interrupt routine.          
         ICNINT   routine.          Connect interrupt vector completion 
         IRLINT   connection.    Release an interrupt vector            
         ICNRTN          service routine to interrupt vector.    Connect
         IEXSTS                         Get job execution status.       
         IUNLKM                      Unlock job from memory.            
         MEMPOS       Determine position of job in memory.              
         LKANMY                        Lock job into any memory.        
         LKLOMY                        Lock job into low memory.        
         ISTPRV                 Set current job priority value.         
         MAPRNT        run time system into job region.       Map shared
         IBSTCH                   Broadcast job status change.          
         ICNMCN   connection.       Cancell job status monitoring       
         IESMCN   connection.     Establish job status monitoring       
         NONINT        Set [non]interactive job status.                 
         IAQFLC     file context of another job.                 Acquire
         MEMUSE    amount of memory used by job.               Determine
         ICONTM            connect time for job.               Determine
         IPRIV        change privileges for job.              Determine,
         ICPUTM        Get CPU time used by job.                        


        TSXLIB V6.0                                              PAGE 87
        Appendix A:  KWIK Index


         IPGNAM     of program being run by job.                Get name
         IPPNUM       programmer number for job.            Get project,
         ISTDJ       Get status of detached job.                        
         GTUNAM     associated with current job.           Get user name
         KLDTJB               Kill detached job.                        
         MSGSND     Send message to another job.                        
         STUNAM     associated with current job.           Set user name
         STDTJB              Start detached job.                        
         RCVMSG        message from another job.          Try to receive
         RCVMSW    for message from another job.                    Wait
         IASRNT         run time system and job.   [Dis]associate shared
         KLDTJB                             Kill detached job.          
         ITRCTL   control functions.        Lead-in character terminal  
         STPRLV     mode processor priority level.              Set user
         ITSLIC          Determine TSX-Plus license number.             
         ITSLIN          Determine TSX-Plus line number.                
         ILNSTS             Check status of line.                       
         ICNTSP         Control speed of CL line.                       
         IRDRCL              or timesharing line. Redirect communication
         LKANMY                             Lock job into any memory.   
         LKLOMY                             Lock job into low memory.   
         LKBLK                       Try to lock block.                 
         LKBLKW           Wait for block to lock.                       
         IUALBK                  Unlock all locked blocks.              
         LKLOMY               Lock job into low memory.                 
         MPIOPS   space.                    Map I/O page into program   
         MAPRNT   into job region.          Map shared run time system  
         MPRMPS   program space.            Map simulated RMON into     
         MPRGN    to physical memory.       Map virtual memory region   
         MEMSET                         Set memory allocation.          
         MPRGN    memory.       Map virtual memory region to physical   
         MEMUSE         Determine amount of memory used by job.         
         MEMPOS          position of job in memory.            Determine
         LKANMY           Lock job into any memory.                     
         LKLOMY           Lock job into low memory.                     
         MPRGN           region to physical memory.   Map virtual memory
         IUNLKM             Unlock job from memory.                     
         RCVMSG              Try to receive message from another job.   
         RCVMSW                    Wait for message from another job.   
         MSGSND                        Send message to another job.     
         TRMMSG   terminal.            Send message to another          
         MSGREQ       Post read request for message.                    
         STPRLV   level.           Set user mode processor priority     
         RSTODT     Reset normal activation mode.                       
         SETODT          Set ODT activation mode.                       
         HIEFOF    high efficiency terminal mode.               Turn off
         HIEFON    high efficiency terminal mode.                Turn on
         ICNMCN          Cancell job status monitoring connection.      
         IESMCN        Establish job status monitoring connection.      
         MOUNT    device.                   Mount file structured       
         GTUNAM   current job.     Get user name associated with        
         STUNAM   current job.     Set user name associated with        
         IPGNAM   by job.               Get name of program being run   
         NONINT                        Set [non]interactive job status. 
         RSTODT                       Reset normal activation mode.     


        TSXLIB V6.0                                              PAGE 88
        Appendix A:  KWIK Index


         IPPNUM     Get project, programmer number for job.             
         ISPBLK   spool file.     Determine number of free blocks in    
         ITSLIC            TSX-Plus license number.            Determine
         ITSLIN     Determine TSX-Plus line number.                     
         IFLINF   about file.               Obtain some information     
         SETODT                         Set ODT activation mode.        
         HIEFOF   terminal mode.       Turn off high efficiency         
         TIMOUT      Set terminal read time out value.                  
         MPIOPS                     Map I/O page into program space.    
         IBICIO    Bit clear value into I/O page.                       
         IBISIO      Bit set value into I/O page.                       
         IPEKIO        Peek at value in I/O page.                       
         IPOKIO         Poke value into I/O page.                       
         IPEKIO                             Peek at value in I/O page.  
         IACTCH   characters.     Check for pending activation          
         INITPA              Initialize for performance analysis.       
         ISTPA                        Start performance analysis.       
         ISPPA                         Stop performance analysis.       
         TERMPA              Terminate from performance analysis.       
         CNVAPA          virtual address to physical address.    Convert
         MPRGN     virtual memory region to physical memory.         Map
         IPOKIO                             Poke value into I/O page.   
         MEMPOS                   Determine position of job in memory.  
         MSGREQ   message.                  Post read request for       
         IPRWND   window.                   Print the contents of a     
         STPRLV     Set user mode processor priority level.             
         ISTPRV             Set current job priority value.             
         IPRIV            Determine, change privileges for job.         
         IRSWND               Resume window processing.                 
         ISPWND              Suspend window processing.                 
         STPRLV               Set user mode processor priority level.   
         GETREG            Get value stored processor register.         
         IPGNAM                 Get name of program being run by job.   
         MPIOPS           Map I/O page into program space.              
         MPRMPS     Map simulated RMON into program space.              
         IPPNUM                Get project, programmer number for job.  
         IPPNUM   for job.              Get project, programmer number  
         MSGREQ                        Post read request for message.   
         TIMOUT                Set terminal read time out value.        
         RCVMSG   another job.       Try to receive message from        
         IRDRCL   timesharing line.         Redirect communication or   
         MPRGN           Map virtual memory region to physical memory.  
         MAPRNT    run time system into job region.           Map shared
         GETREG      value stored processor register.                Get
         IRLINT   connection.               Release an interrupt vector 
         ISPCTL   file.             Control release time of spooled     
         RLCTL    control of system.        Relinquish exclusive        
         MSGREQ                   Post read request for message.        
         RSTODT   mode.                     Reset normal activation     
         IRSWND                             Resume window processing.   
         ISPY     simulated RMON.           Return values from within   
         MPRMPS               Map simulated RMON into program space.    
         ISPY         from within simulated RMON.          Return values
         ICNRTN   vector.   Connect service routine to interrupt        
         ICNINT           vector completion routine.   Connect interrupt


        TSXLIB V6.0                                              PAGE 89
        Appendix A:  KWIK Index


         TTCRTN         terminal completion routine.           Establish
         ITCRTN              from interrupt routine.  Trigger completion
         IPGNAM       name of program being run by job.              Get
         IASRNT       [Dis]associate shared run time system and job.    
         MAPRNT   region.        Map shared run time system into job    
         ISVST                              Save status of shared file. 
         ISLWND                             Select a window.            
         MSGSND   job.                      Send message to another     
         TRMMSG   terminal.                 Send message to another     
         TRMOUT   to terminal.              Send string of characters   
         BRKCTL             Establish break sentinel control.           
         ICNRTN   interrupt vector. Connect service routine to          
         SETODT                             Set ODT activation mode.    
         NONINT   status.                   Set [non]interactive job    
         ISTFTM                             Set creation time of file.  
         ISTPRV   value.                    Set current job priority    
         MEMSET                             Set memory allocation.      
         TIMOUT   value.                    Set terminal read time out  
         STPRLV   priority level.           Set user mode processor     
         STUNAM   with current job.         Set user name associated    
         IBISIO                         Bit set value into I/O page.    
         ICKWTS         Check for writes to shared file.                
         ISVST               Save status of shared file.                
         IASRNT   job.       [Dis]associate shared run time system and  
         MAPRNT   job region.           Map shared run time system into 
         IDCLSF          Declare file to be shared.                     
         MPRMPS   space.                Map simulated RMON into program 
         ISPY            values from within simulated RMON.       Return
         MPIOPS       I/O page into program space.                   Map
         MPRMPS           RMON into program space.         Map simulated
         IUSPBK                      Unlock specific block.             
         ICNTSP                     Control speed of CL line.           
         ISPBLK    number of free blocks in spool file.        Determine
         ISPCTL     Control release time of spooled file.               
         STDTJB                             Start detached job.         
         ISTPA                              Start performance analysis. 
         IBSTCH               Broadcast job status change.              
         ICNMCN   connection.   Cancell job status monitoring           
         IESMCN   connection. Establish job status monitoring           
         ISTDJ                          Get status of detached job.     
         ICALOC            Check allocation status of device.           
         ILNSTS                       Check status of line.             
         ISVST                         Save status of shared file.      
         IEXSTS           Get job execution status.                     
         NONINT    Set [non]interactive job status.                     
         ISPPA                              Stop performance analysis.  
         GETREG                   Get value stored processor register.  
         TRMIN    terminal.          Accept string of characters from   
         TRMOUT   terminal.            Send string of characters to     
         DISMNT               Dismount file structured device.          
         MOUNT                   Mount file structured device.          
         ISPWND                             Suspend window processing.  
         IASRNT             shared run time system and job[Dis]associate
         MAPRNT         Map shared run time system into job region.     
         RLCTL         exclusive control of system.           Relinquish


        TSXLIB V6.0                                              PAGE 90
        Appendix A:  KWIK Index


         TKCTL         exclusive control of system.                 Take
         TKCTL    system.                   Take exclusive control of   
         TTCRTN   routine.        Establish terminal completion         
         ITRCTL           Lead-in character terminal control functions. 
         ITRERR                   Check for terminal input errors.      
         HIEFOF    Turn off high efficiency terminal mode.              
         HIEFON     Turn on high efficiency terminal mode.              
         TIMOUT   value.                Set terminal read time out      
         ITRTYP                   Determine terminal type.              
         TRMIN           of characters from terminal.      Accept string
         TRMMSG     Send message to another terminal.                   
         TRMOUT     string of characters to terminal.               Send
         TERMPA   analysis.                 Terminate from performance  
         ICONTM           Determine connect time for job.               
         ISTFTM                Set creation time of file.               
         ISPCTL             Control release time of spooled file.       
         TIMOUT           Set terminal read time out value.             
         IASRNT                  shared run time system an[Dis]associate
         MAPRNT   region.    Map shared run time system into job        
         ICPUTM                     Get CPU time used by job.           
         IRDRCL            communication or timesharing line.   Redirect
         ITCRTN   interrupt routine.        Trigger completion from     
         LKBLK                              Try to lock block.          
         RCVMSG   another job.              Try to receive message from 
         ITSLIC                   Determine TSX-Plus license number.    
         ITSLIN                   Determine TSX-Plus line number.       
         HIEFOF   terminal mode.            Turn off high efficiency    
         HIEFON   terminal mode.            Turn on high efficiency     
         ITRTYP          Determine terminal type.                       
         IUALBK                             Unlock all locked blocks.   
         IUNLKM                             Unlock job from memory.     
         IUSPBK                             Unlock specific block.      
         MEMUSE            amount of memory used by job.       Determine
         ICPUTM                Get CPU time used by job.                
         STPRLV   priority level.       Set user mode processor         
         GTUNAM   current job.          Get user name associated with   
         STUNAM   current job.          Set user name associated with   
         IPEKIO                     Peek at value in I/O page.          
         IBICIO                   Bit clear value into I/O page.        
         IBISIO                     Bit set value into I/O page.        
         IPOKIO                        Poke value into I/O page.        
         GETREG   register.             Get value stored processor      
         ISTPRV    Set current job priority value.                      
         TIMOUT      terminal read time out value.                   Set
         ISPY     simulated RMON.    Return values from within          
         ICNINT           Connect interrupt vector completion routine.  
         IRLINT        Release an interrupt vector connection.          
         ICNRTN        routine to interrupt vector.      Connect service
         CNVAPA   address.          Convert virtual address to physical 
         MPRGN    physical memory.      Map virtual memory region to    
         LKBLKW                             Wait for block to lock.     
         RCVMSW   another job.              Wait for message from       
         IRSWND                      Resume window processing.          
         ISPWND                     Suspend window processing.          
         ICRWND                    Create a window.                     


        TSXLIB V6.0                                              PAGE 91
        Appendix A:  KWIK Index


         IDLWND                    Delete a window.                     
         IPRWND     Print the contents of a window.                     
         ISLWND                    Select a window.                     
         ICKWTS                   Check for writes to shared file.      


        TSXLIB V6.0                                              PAGE 92
        Appendix B:  Distribution Kit






                         Appendix B:  Distribution Kit

             The TSXLIB distribution kit (DECUS #11-490) consists of the
        following files:

                TSXLIB.COM  TSXLIB builder.                    

                ABSTRA.DOC  Abstract.                          
                TSXLIB.DOC  This document.                     

                CLLINE.MAC  Communication line support.        
                DETJBS.MAC  Detached job support.              
                DVALOC.MAC  Device allocatind and deallocating.
                JBPRIV.MAC  Job privileges control.            
                JBSTMN.MAC  Job status monitoring.             
                MNTDEV.MAC  Device mounting and dismounting.   
                MSGCOM.MAC  Interjob message communication.    
                PRFANL.MAC  Performance analysis support.      
                RELTIM.MAC  Real time program support.         
                RUNTIM.MAC  Shared run time system support.    
                SHRFIL.MAC  Shared file system support.        
                SPOLER.MAC  Spooler support.                   
                SYSTAT.MAC  System status information.         
                TRMCOM.MAC  Terminal communication.            
                TRMCTL.MAC  Terminal control.                  
                TSFILS.MAC  Special file information.          
                TSLBID.MAC  TSXLIB identification.             
                TSXMSC.MAC  Miscellaneous EMTs.                
                TSXODT.MAC  ODT activation mode support.       
                USRNAM.MAC  User name support.                 
                WINDOW.MAC  Windowing support.                 

                TSXLIB.OBJ  The implemented library.           


        TSXLIB V6.0                                              PAGE 93
        Reader's Comments


        Did you find any errors in this document?  If so, please specify
        page and describe.












        Did you find this  document  understandable,  usable,  and  well
        organized?  Please make suggestions for improvement.












        Did you find this document sufficiently complete?  If not,  what
        material is missing and where should it be placed?












        Name/Date:

        Company:

        Address:

        City/State/Zip:


                          NAB Software Services, Inc.
                          PO Box 20009               
                          Albuquerque, NM 87154-0009