TSXLIB

                                       A
                             Library Implementation
                                       of
                              Programmed Requests
                                      for
                                 TSX-Plus V6.2




                                 DECUS #11-490




                          N. A. Bourgeois, Jr.       
                          NAB Software Services, Inc.
                          PO Box 20009               
                          Albuquerque, NM 87154      








                                    Abstract

                A library of FORTRAN callable routines that
                implement the EMTs provided by TSX-Plus is
                described.  Complete descriptions, calling
                sequences, examples of use, and library building
                procedures are given.






                                    [87d07a]


        TSXLIB V6.2                                               PAGE 2







                The information in this document is subject to
                change without notice and should not be
                construed as a commitment by NAB Software
                Services, Inc.  NAB Software Services, Inc.
                assumes no responsibility for any errors that
                may appear in this document.




                This document was originally issued by Sandia
                National Laboratories, operated for the United
                States Department of Energy by Sandia
                Corporation.


                                     Notice


                This document was originally sponsored by the
                United States Government.  Neither the United
                States Government nor the United States
                Department of Energy, nor any of their
                employees, nor any of their contractors,
                subcontractors, or their employees makes any
                warranty, express or implied, or assumes any
                legal liability or responsibility for the
                accuracy, completeness or usefulness of any
                information, apparatus, product or process
                disclosed, or represents that its use would not
                infringe privately owned rights.


                This work was originally funded by:

                       Headquarters, ESD / OCB / Stop 36
                       Hanscom Air Force Base, MA 01731 


        TSXLIB V6.2                                               PAGE 3







                The Reader's Comment form on the last page of
                this document requests the user's critical
                evaluation to assist NAB Software Services,
                Inc. in preparing future documentation.




                                Acknowledgments


                The author wishes to thank S & H Computer
                Systems, Inc. for its permission to reprint
                parts of their "TSX-Plus Reference Manual" in
                this document.

                The author wishes also to thank W. L. Jacklin of
                Sandia National Laboratories for his assistance
                in reviewing this document and particularly for
                his help with the many FORTRAN examples in the
                third chapter.




                                  ***********
                                  * CAUTION *
                                  ***********


                Much of both the MACRO-11 source codes and the
                FORTRAN examples described in this document are
                as yet untried.


        TSXLIB V6.2                                               PAGE 4
        Table of Contents






                               Table of Contents


                 1.  Introduction . . . . . . . . . . . . .  7

                 2.  General Description  . . . . . . . . .  8
                     Communication Line Support . . . . . .  9
                     Detached Job Support . . . . . . . . .  9
                     Device Allocating and Deallocating . .  9
                     Device Mounting and Dismounting  . . . 10
                     Interprogram Message Communication . . 10
                     Job Priveleges Control . . . . . . . . 11
                     Job Status Monitoring  . . . . . . . . 11
                     Miscellaneous EMT Support  . . . . . . 11
                     ODT Activation Mode Support  . . . . . 12
                     Performance Analysis Support . . . . . 12
                     Real Time Program Support  . . . . . . 12
                     Shared Run Time System Support . . . . 15
                     Shared File Support  . . . . . . . . . 16
                     Special File Information . . . . . . . 16
                     Spooler Support  . . . . . . . . . . . 17
                     Subprocess Control . . . . . . . . . . 17
                     System Status Information  . . . . . . 17
                     Terminal Communication Support . . . . 18
                     Terminal Control Support . . . . . . . 18
                     User Name Support  . . . . . . . . . . 18
                     Windowing Support  . . . . . . . . . . 19

                 3.  Routine Descriptions . . . . . . . . . 20
                     BRKCTL . . . . . . . . . . . . . . . . 20
                     CNVAPA . . . . . . . . . . . . . . . . 21
                     DISMNT . . . . . . . . . . . . . . . . 21
                     DSMNTA . . . . . . . . . . . . . . . . 22
                     GETREG . . . . . . . . . . . . . . . . 22
                     GTJBNM . . . . . . . . . . . . . . . . 23
                     GTUNAM . . . . . . . . . . . . . . . . 23
                     HIEFOF . . . . . . . . . . . . . . . . 24
                     HIEFON . . . . . . . . . . . . . . . . 24
                     IACTCH . . . . . . . . . . . . . . . . 24
                     IALOC  . . . . . . . . . . . . . . . . 25
                     IAQFLC . . . . . . . . . . . . . . . . 26
                     IASRNT . . . . . . . . . . . . . . . . 27
                     IBICIO . . . . . . . . . . . . . . . . 28
                     IBISIO . . . . . . . . . . . . . . . . 28
                     IBSTCH . . . . . . . . . . . . . . . . 29
                     ICALOC . . . . . . . . . . . . . . . . 29
                     ICKWTS . . . . . . . . . . . . . . . . 30
                     ICNINT . . . . . . . . . . . . . . . . 31
                     ICNMCN . . . . . . . . . . . . . . . . 32
                     ICNRTN . . . . . . . . . . . . . . . . 32
                     ICNTSP . . . . . . . . . . . . . . . . 33


        TSXLIB V6.2                                               PAGE 5
        Table of Contents


                     ICONTM . . . . . . . . . . . . . . . . 34
                     ICPUTM . . . . . . . . . . . . . . . . 35
                     ICRWND . . . . . . . . . . . . . . . . 36
                     IDALOC . . . . . . . . . . . . . . . . 37
                     IDCLSF . . . . . . . . . . . . . . . . 38
                     IDLWND . . . . . . . . . . . . . . . . 39
                     IDMLD  . . . . . . . . . . . . . . . . 39
                     IESMCN . . . . . . . . . . . . . . . . 40
                     IEXSTS . . . . . . . . . . . . . . . . 41
                     IFLINF . . . . . . . . . . . . . . . . 42
                     IHERR  . . . . . . . . . . . . . . . . 43
                     ILDTR  . . . . . . . . . . . . . . . . 43
                     ILNSTS . . . . . . . . . . . . . . . . 44
                     INITPA . . . . . . . . . . . . . . . . 45
                     INITSP . . . . . . . . . . . . . . . . 46
                     IPEKIO . . . . . . . . . . . . . . . . 47
                     IPGNAM . . . . . . . . . . . . . . . . 47
                     IPOKIO . . . . . . . . . . . . . . . . 48
                     IPPNUM . . . . . . . . . . . . . . . . 48
                     IPRIV  . . . . . . . . . . . . . . . . 49
                     IPRWND . . . . . . . . . . . . . . . . 51
                     IRDRCL . . . . . . . . . . . . . . . . 52
                     IRDTR  . . . . . . . . . . . . . . . . 53
                     IRLINT . . . . . . . . . . . . . . . . 53
                     IRSWND . . . . . . . . . . . . . . . . 54
                     IRXOFF . . . . . . . . . . . . . . . . 54
                     ISERR  . . . . . . . . . . . . . . . . 55
                     ISLWND . . . . . . . . . . . . . . . . 56
                     ISPBLK . . . . . . . . . . . . . . . . 56
                     ISPCTL . . . . . . . . . . . . . . . . 56
                     ISPPA  . . . . . . . . . . . . . . . . 57
                     ISPWND . . . . . . . . . . . . . . . . 58
                     ISPY . . . . . . . . . . . . . . . . . 58
                     ISTDJ  . . . . . . . . . . . . . . . . 59
                     ISTFTM . . . . . . . . . . . . . . . . 60
                     ISTLD  . . . . . . . . . . . . . . . . 60
                     ISTPA  . . . . . . . . . . . . . . . . 61
                     ISTPRV . . . . . . . . . . . . . . . . 61
                     ISVST  . . . . . . . . . . . . . . . . 62
                     ISWESP . . . . . . . . . . . . . . . . 62
                     ITCRTN . . . . . . . . . . . . . . . . 63
                     ITRCTL . . . . . . . . . . . . . . . . 63
                     ITRERR . . . . . . . . . . . . . . . . 64
                     ITRTYP . . . . . . . . . . . . . . . . 64
                     ITRYSP . . . . . . . . . . . . . . . . 65
                     ITSLIC . . . . . . . . . . . . . . . . 66
                     ITSLIN . . . . . . . . . . . . . . . . 66
                     IUALBK . . . . . . . . . . . . . . . . 67
                     IUNLKM . . . . . . . . . . . . . . . . 67
                     IUSPBK . . . . . . . . . . . . . . . . 68
                     IYELL  . . . . . . . . . . . . . . . . 69
                     JOBPRI . . . . . . . . . . . . . . . . 69
                     KLDTJB . . . . . . . . . . . . . . . . 70
                     LKANMY . . . . . . . . . . . . . . . . 70
                     LKBLK  . . . . . . . . . . . . . . . . 71


        TSXLIB V6.2                                               PAGE 6
        Table of Contents


                     LKBLKW . . . . . . . . . . . . . . . . 72
                     LKLOMY . . . . . . . . . . . . . . . . 73
                     MAPRNT . . . . . . . . . . . . . . . . 73
                     MEMPOS . . . . . . . . . . . . . . . . 75
                     MEMSET . . . . . . . . . . . . . . . . 75
                     MEMUSE . . . . . . . . . . . . . . . . 76
                     MNTLD  . . . . . . . . . . . . . . . . 76
                     MOUNT  . . . . . . . . . . . . . . . . 77
                     MPIOPS . . . . . . . . . . . . . . . . 78
                     MPRGN  . . . . . . . . . . . . . . . . 78
                     MPRMPS . . . . . . . . . . . . . . . . 79
                     MSGREQ . . . . . . . . . . . . . . . . 80
                     MSGSND . . . . . . . . . . . . . . . . 81
                     NONINT . . . . . . . . . . . . . . . . 82
                     RCVMSG . . . . . . . . . . . . . . . . 82
                     RCVMSW . . . . . . . . . . . . . . . . 82
                     RLCTL  . . . . . . . . . . . . . . . . 84
                     RSTODT . . . . . . . . . . . . . . . . 84
                     SETODT . . . . . . . . . . . . . . . . 85
                     STDTJB . . . . . . . . . . . . . . . . 85
                     STPRLV . . . . . . . . . . . . . . . . 85
                     STUNAM . . . . . . . . . . . . . . . . 86
                     TERMPA . . . . . . . . . . . . . . . . 86
                     TIMOUT . . . . . . . . . . . . . . . . 88
                     TKCTL  . . . . . . . . . . . . . . . . 88
                     TRMIN  . . . . . . . . . . . . . . . . 88
                     TRMMSG . . . . . . . . . . . . . . . . 89
                     TRMOUT . . . . . . . . . . . . . . . . 90
                     TTCRTN . . . . . . . . . . . . . . . . 90

                 4.  Building the Library . . . . . . . . . 92

                 References . . . . . . . . . . . . . . . . 94

                 Appendix A:  KWIK Index  . . . . . . . . . 95

                 Appendix B:  Distribution Kit  . . . . .  103


        TSXLIB V6.2                                               PAGE 7
        Introduction






                                1.  Introduction


             When application programs are executed under a time sharing
        executive such as TSX-Plus [1,2,8] certain capabilities become
        desirable if not absolutely essential.  These capabilities
        relate to requirements for such things as hardware dependent
        I/O, shared files, interprogram communication, and others.
        TSX-Plus provides a number of programmed requests or EMTs for
        these purposes.

             This document describes a number of FORTRAN [6,7] callable
        routines and their calling sequences that implement these EMTs.
        All of the routines are callable as FORTRAN subroutines and some
        are also callable as FORTRAN functions.  The routines are
        written in MACRO-11 [3].

             The next section offers a general description of the
        several groups of routines.  It describes the process for
        linking the routines to the FORTRAN application program.  The
        general calling sequences are also described.

             The third section gives a detailed description of each of
        the individual routines.  The descriptions include both the
        calling sequences and, in most cases, examples.

             Procedures for constructing the library from the several
        source modules are given in the fourth section.

             Appendix A contains a key-word-in-context (KWIK) index of
        the routines.

             A description of the distribution kit is contained in
        Appendix B.


                                      NOTE

             TSX-Plus is a registered trademark of  S & H  Computer
             Systems Inc., Nashville, TN.




        TSXLIB V6.2                                               PAGE 8
        General Description






                            2.  General Description


             These TSX-Plus library routines provide facilities to
        support communication lines, detached jobs, device allocating
        and deallocating, file structured device mounting and
        dismounting, communication between running programs, job
        privileges control, job status monitoring, ODT activation mode,
        program performance analysis, real time program execution,
        shared run time systems, shared files, special files
        information, spooler control, subprocess control, system status
        information, communication between running programs and a
        terminal, program control of the terminal, user name control,
        windowing, and several miscellaneous EMTs.

             The standard FORTRAN [6,7] subroutine calling sequence
        shown below may be used to access all of the routines in the
        TSX-Plus library.

                          CALL RTNAM ( ARG1,...,ARGn )

             Those routines that return only one value are also callable
        as FORTRAN functions.  This is as follows:

                         IRET  RTNAM ( ARG1,...,ARGn )

             The application program is first compiled as follows:

                                .RUN SY:FORTRAN
                                 *MYPROGMYPROG 
                                *^C            

             Then the routines are linked with the application program
        as shown below:

                           .RUN SY:LINK              
                           *MYPROGMYPROG,SY:TSXLIB/F
                           *^C                       
                                       or
                        .RUN SY:LINK                   
                         *MYPROGMYPROG,SY:TSXLIB,FPULIB
                        *^C                            

             The application program is now ready for execution.

                                 .RUN DK:MYPROG

             The "TSX-Plus Reference Manual" [1] describes how the EMTs
        implemented in this TSX-Plus library are accessed from a
        MACRO-11 program.  However, the FORTRAN/MACRO interface
        described in the "RT-11 Programmer's Reference Manual" [5] may


        TSXLIB V6.2                                               PAGE 9
        General Description


        also be used to access the routines in the library from a
        MACRO-11 program.

             In the sections that follow, the name of the MACRO-11
        source file containing the listed routines is given in the title
        of each of the tables.


    Communication Line Support

             Table 2-1 lists the TSXLIB routines that offer certain
        communication line support from within a running program.

                ICNTSP  Control the speed of a communication or
                        timesharing line.
                ILDTR   Lower a communication or timesharing line's DTR
                        status.
                IRDRCL  Redirect a communication or timesharing line.
                IRDTR   Raise a communication or timesharing line's DTR
                        status.
                IRXOFF  Reset a communication or timesharing line's XOFF
                        status.

                          Communication line support.
                                   CLLINE.MAC
                                   Table 2-1.


    Detached Job Support

             Table 2-2 lists the routines that provide detached job
        support from within an executing program.

                ISTDJ   Get the status of a detached job.
                KLDTJB  Kill a detached job.
                STDTJB  Start a detached job.

                             Detached job support.
                                   DETJBS.MAC
                                   Table 2-2.


    Device Allocating and Deallocating

             System services are available to allow a running program to
        control the allocation of a device for exclusive use.  Table 2-3
        lists these routines.  Once a device has been allocated to a
        job, no other job is allowed to access the device.  A device
        allocated to a primary line or associated virtual line may be
        accessed by any of the associated lines.


        TSXLIB V6.2                                              PAGE 10
        General Description


                IALOC   Allocate a device.
                ICALOC  Check the allocation status of a device.
                IDALOC  Deallocate a device.

                      Device allocating and deallocating.
                                   DVALOC.MAC
                                   Table 2-3.


    Device Mounting and Dismounting

             It is possible to mount and dismount a file structured
        device for directory caching from within a running program.  The
        routines listed in Table 2-4 provide these capabilities.

                DISMNT  Dismount a file structured device.
                DSMNTA  Dismount all file structured devices.
                IDMLD   Dismount a specific logical device.
                ISTLD   Check the status of a logical device.
                MNTLD   Mount a logical device.
                MOUNT   Mount a file structured device.

                        Device mounting and dismounting.
                                   MNTDEV.MAC
                                   Table 2-4.


    Interprogram Message Communication

             TSX-Plus provides an optional facility that allows running
        programs to communicate with each other.  Table 2-5 lists the
        routines that support this interprogram message communication.

                MSGREQ  Post a read request for a message.
                MSGSND  Send a message to another job.
                RCVMSG  Try to receive a message from another job.
                RCVMSW  Wait for a message from another job.

                      Interprogram message communication.
                                   MSGCOM.MAC
                                   Table 2-5.

             Messages are transferred between programs by using named
        message channels.  A message channel accepts a message from a
        sending program, stores the message in a queue associated with
        the channel, and delivers the message to a receiving program on
        its request for a message on the channel.  Message channels are
        separate from I/O channels.

             Each active message channel has associated with it an ASCII
        character name that is used by both the sending and receiving
        programs to identify the channel.  The names associated with the
        channels are defined dynamically by the running programs.  A
        message channel is active when messages are being held in the
        queue associated with the channel or if a program is waiting for


        TSXLIB V6.2                                              PAGE 11
        General Description


        a message from the channel.  When message channels become
        inactive they are returned to a free pool and may then be
        reused.

             Once a message is queued on a channel, that message will
        remain in the queue until some program receives it.  A program's
        exiting to the keyboard monitor does not remove any pending
        messages.  This allows one program to leave a message for
        another program that will be run at a later time.


    Job Privileges Control

             Table 2-6 lists the routines that permit an executing
        program to determine and make certain changes in its own
        executing environment.

                IPRIV   Determine or change the job privilege sets.
                ISTPRV  Set the current job's priority value.
                NONINT  Set the [non]interactive job status.

                             Job Privileges Control
                                   JBPRIV.MAC
                                   Table 2-6.


    Job Status Monitoring

             A facility is available for one job to monitor the status
        of one or more other jobs.  Once a job has declared to monitor
        another job, a completion routine is executed in the monitoring
        job whenever a change of status occurs in the job being
        monitored.  The services provided for job monitoring are listed
        in Table 2-7.

                IBSTCH  Broadcast a job status change.
                ICNMCN  Cancell a job status monitoring connection.
                IESMCN  Establish a job status monitoring connection.

                             Job status monitoring.
                                   JBSTMN.MAC
                                   Table 2-7.


    Miscellaneous EMT Support

             Table 2-8 lists the routines that support the several
        miscellaneous EMTs provided by TSX-Plus.


        TSXLIB V6.2                                              PAGE 12
        General Description


                GETREG  Get the word and byte values stored in a
                        processor register.
                IHERR   Enable abort on certain errors.
                ISERR   Inhibit abort on certain errors.
                ISPY    Return values from within the simulated RMON
                        (SYSLIB routine).
                ITSLIC  Determine the TSX-Plus license number.
                ITSLIN  Determine the TSX-Plus line number.
                MEMSET  Set the memory allocation.

                           Miscellaneous EMT support.
                                   TSXMSC.MAC
                                   Table 2-8.


    ODT Activation Mode Support

             ODT activation mode may be turned on and off from within a
        running program.  Table 2-9 lists the routines that support this
        feature.  In this mode TSX-Plus considers all characters to be
        activation characters except the digits, the comma, the dollar
        sign and the semicolon.

                RSTODT  Reset normal activation mode.
                SETODT  Set ODT activation mode.

                          ODT activation mode support.
                                   TSXODT.MAC
                                   Table 2-9.


    Performance Analysis Support

             For many applications the keyboard monitor level
        performance analysis control provided by TSX-Plus is adequate.
        Specifically, in cases such as analyzing the performance of an
        overlayed program it is necessary to have control over the
        performance analysis feature from the running program.  The
        routines listed in Table 2-10 provide just this capability.

                INITPA  Initialize for a performance analysis.
                ISPPA   Stop a performance analysis.
                ISTPA   Start a performance analysis.
                TERMPA  Terminate from a performance analysis.

                         Performance analysis support.
                                  PRFANL.MAC 
                                  Table 2-10.


    Real Time Program Support

             The real time program support provided by TSX-Plus allows
        multiple real time programs to be run concurrently with normal
        time sharing operations.  The basic functions provided by this


        TSXLIB V6.2                                              PAGE 13
        General Description


        facility are listed in Table 2-11.

                CNVAPA  Convert a virtual address to a physical address.
                IBICIO  Bit clear a value into the I/O page.
                IBISIO  Bit set a value into the I/O page.
                ICNINT  Connect an interrupt vector to a completion
                        routine.
                ICNRTN  Connect a service routine to an interrupt
                        vector.
                IPEKIO  Peek at a value in the I/O page.
                IPOKIO  Poke a value into the I/O page.
                IRLINT  Release an interrupt vector connection.
                ITCRTN  Trigger a completion routine from an interrupt
                        service routine.
                IUNLKM  Unlock a job from memory.
                LKANMY  Lock a job into any memory.
                LKLOMY  Lock a job into low memory.
                MPIOPS  Map the I/O page into the program space.
                MPRGN   Map a region of virtual memory to a specified
                        region of physical memory.
                MPRMPS  Map the simulated RMON into the program space.
                RLCTL   Relinquish exclusive control of the system.
                STPRLV  Set the user mode processor priority level.
                TKCTL   Take exclusive control of the system.

                           Real time program support.
                                  RELTIM.MAC 
                                  Table 2-11.

             A program must have one or more of the several real time
        related privileges to use the real time routines.  The real time
        facilities are available to both normal jobs controlled by time
        sharing lines and to detached jobs.  Detached jobs started by a
        time sharing user have the same privileges as does the user
        starting them.

             A basic facility required by many real time programs is the
        ability to access the I/O page which contains the peripheral
        device registers.  A normal time sharing job does not have this
        access.  It is instead mapped to a simulated RMON.  This allows
        programs that directly access offsets into RMON to run
        correctly.

             A real time program can access the I/O page in one of two
        ways.  It can map the I/O page into the program's space, or it
        can leave the simulated RMON mapped into the program's space and
        perform peek, poke, bit set, and bit clear operations into the
        I/O page.  It is much more efficient to directly access the
        device registers by mapping the I/O page into the program's
        space than to use the routines to perform each individual
        access.  However, this technique will not work if the program
        must also directly access offsets into RMON.  The correct way to
        access offsets into RMON is with the SYSLIB routine, ISPY, which
        will work even if the I/O page is mapped into the program's
        space.


        TSXLIB V6.2                                              PAGE 14
        General Description


             The TSX-Plus real time support facility provides two
        methods to connect real time interrupts to TSX-Plus jobs.  The
        first of these methods uses the mechanism of completion routines
        to perform the connection.  The second method provides a more
        direct connection between interrupts and service routines in
        TSX-Plus jobs.  Once a connection is established the routine,
        completion or service, is executed each time the specified
        interrupt occurs.  It is possible for several interrupt vectors
        to be connected to the same completion routine in a job but it
        is illegal for more than one job to connect to the same
        interrupt vector.

             With the first method an interrupt causes a completion
        routine to be queued for the job that was connected to the
        interrupt vector.  This method is very general and allows the
        completion routine to call for system services (execute EMTs).
        Also the job does not have to be locked in memory.  On entry to
        the completion routine, R0 contains the address of the vector
        that caused the completion routine to be entered.

             The second method sets up conditions for the job being
        called and enters the interrupt service routine.  This approach
        minimizes the overhead in entering the service routine.  Hence,
        the service routine method can process interrupts at a greater
        rate than can be processed using the completion routine method.

             There are restrictions imposed on a program using the
        service routine method.  Specifically, the following conditions
        must be met to directly connect to an interrupt:

            1.  The job must be locked in memory before connecting it to
                the interrupt vector and must remain locked in memory as
                long as the interrupt connection is in effect.

            2.  The processing done by the service routine should not be
                very lengthy since other interrupts may be queued up
                during execution of the service routine.

            3.  Only two system services may be legally called from
                within the service routine.  They are the SYSLIB
                routine, RESUME, and the TSXLIB routine, ITCRTN.

             The interrupt service routine runs in user mode and uses
        memory mapping that has been established for the job before the
        interrupt occurs.  Access to the I/O page via the MPIOPS routine
        is possible provided this mapping has been set up in the
        mainline code before the interrupt occurs.

             If an interrupt service routine needs to perform a system
        service other than the RESUME call listed above, it should
        trigger a completion routine via a call to ITCRTN and have the
        completion routine call for the required system service(s).

             An execution priority may be specified for each completion
        routine.  This is not the same as the hardware selected priority


        TSXLIB V6.2                                              PAGE 15
        General Description


        of the interrupt.  All completion routines are synchronized with
        the job and run at hardware priority level zero.  The completion
        routine priority is used to schedule completion routines for
        execution.  The available priority levels are 0 through 127.
        The execution of a real time completion routine for one job will
        be interrupted and suspended if an interrupt occurs that causes
        a higher priority completion routine for another job to be
        queued for execution.  However, a completion routine for a given
        job will never be interrupted to run another completion routine
        for the same job even if a higher priority completion routine is
        pending.

             Completion routine priorities one and larger are real time
        priorities.  They are higher than the priorities given to time
        sharing jobs and will always preempt the time sharing jobs.
        Completion routine priority zero is not a real time priority but
        rather a very high normal priority.  Such zero priority
        completion routines are time sliced in the normal fashion.  If a
        completion routine enters a wait state it relinquishes its real
        time priority.  Jobs that have real time, interrupt driven
        completion routines need not be locked in memory.

             In time critical, real time applications where a program
        must respond to an interrupt with minimum delay, it may be
        necessary for the job to lock itself in memory to avoid the time
        consumed in program swapping.  This facility should be used with
        caution since if a number of large programs are locked in memory
        there may not be enough space left to run other programs.

             A running program may gain exclusive access to the system
        to perform some time-critical task.  The program may then
        relinquish this exclusive access when it is not needed.  A
        running program may also set the user mode priority level and
        map a region of virtual memory to a specified region of physical
        memory.


    Shared Run Time System Support

             TSX-Plus provides a facility that allows shared run time
        systems or data areas to be mapped into the address spaces of
        multiple time sharing jobs.  Table 2-12 lists the routines that
        support this feature.

                IASRNT  Associate/disassociate a shared run time system
                        with a job.
                MAPRNT  Map a shared run time system into a job's
                        region.

                        Shared run time system support.
                                  RUNTIM.MAC 
                                  Table 2-12.

             Memory space can be conserved by having several jobs access
        a common copy of a run time system rather than having to


        TSXLIB V6.2                                              PAGE 16
        General Description


        allocate space within each job.  Shared run time systems are
        never swapped out of memory.  When a job is associated with a
        run time system, a portion of the job's virtual memory is mapped
        so as to allow access to the run time system.


    Shared File Support

             Table 2-13 lists the routines that offer access to the
        shared file record locking facility provided by TSX-Plus.  This
        is useful in situations where programs being run from several
        terminals wish to update a common file.  Through the record
        locking facility a program may gain exclusive access to one or
        more blocks in a shared file by locking those blocks.  Other
        users attempting to lock the same blocks will be denied access
        until the first user releases the locked blocks.

                ICKWTS  Check for writes to a shared file.
                IDCLSF  Declare a file to be shared.
                ISVST   Save the status of a shared file.
                IUALBK  Unlock all locked blocks.
                IUSPBK  Unlock a specific block.
                LKBLK   Try to lock a block.
                LKBLKW  Wait for a block to lock.

                              Shared file support.
                                  SHRFIL.MAC 
                                  Table 2-13.

             The recommended procedure for updating a shared file being
        accessed by several users is as follows:

            1.  Open the file.
            2.  Declare the file to be shared.
            3.  Lock all blocks which contain the desired record.
            4.  Read the locked blocks into memory.
            5.  Update the record.
            6.  Write the updated blocks to the file.
            7.  Unlock the blocks.
            8.  Repeat steps three through seven as required.
            9.  Close the file.


    Special File Information

             TSX-Plus allows a running program to obtain certain status
        information about a file and to set the creation time of a file.
        Table 2-14 lists the routines that support this facility.

                IFLINF  Obtain some information about a file.
                ISTFTM  Set the creation time of a file.

                           Special file information.
                                  TSFILS.MAC 
                                  Table 2-14.


        TSXLIB V6.2                                              PAGE 17
        General Description


    Spooler Support

             Table 2-15 lists the routines that provide spooler support
        available to an executing program.

                ISPBLK  Determine the number of free blocks in the spool
                        file.
                ISPCTL  Control the release time of a spooled file.

                                Spooler Support.
                                  SPOLER.MAC 
                                  Table 2-15.


    Subprocess Control

             The routines listed in Table 2-16 allow a running program
        to switch terminal control between subprocesses as if a
        CTRL-W-digit sequence had been typed.  The routines initiate new
        subprocesses and/or switch terminal control between
        subprocesses.

                INITSP  Initialize a new or switch to an existing
                        subprocess.
                ISWESP  Switch to an existing subprocess.
                ITRYSP  Try to initialize a new subprocess.

                               Subprocess Control
                                  SUBPRO.MAC 
                                  Table 2-16.


    System Status Information

             Information typical of that returned by the SYSTAT keyboard
        command is made available to a running program by the routines
        listed in Table 2-17.

                GTJBNM  Get the name for a job.
                ICONTM  Determine the connect time for a job.
                ICPUTM  Get the CPU time used by a job.
                IEXSTS  Get a job's execution status.
                ILNSTS  Check the status of a line.
                IPGNAM  Get the name of the program being run by a job.
                IPPNUM  Get the project-programmer number for a job.
                JOBPRI  Get the priority for a job.
                MEMPOS  Determine the position of a job in memory.
                MEMUSE  Determine the amount of memory used by a job.

                           System status information.
                                  SYSTAT.MAC 
                                  Table 2-17.


        TSXLIB V6.2                                              PAGE 18
        General Description


    Terminal Communications Support

             The routines that allow a running program to communicate
        with a terminal are listed in Table 2-18.

                IYELL   Override the TT-GAG option.
                TRMIN   Accept a string of characters from the terminal.
                TRMMSG  Send a message to another terminal.
                TRMOUT  Send a string of characters to the terminal.

                        Terminal communications support.
                                  TRMCOM.MAC 
                                  Table 2-18.


    Terminal Control Support

             The terminal control support routines are listed in Table
        2-19.

                BRKCTL  Establish break sentinel control.
                HIEFOF  Turn off the high efficiency terminal mode.
                HIEFON  Turn on the high efficiency terminal mode.
                IACTCH  Check for pending activation characters.
                ITRCTL  Perform lead-in character type terminal control
                        functions.
                ITRERR  Check for terminal input errors.
                ITRTYP  Determine the terminal type.
                TIMOUT  Set the terminal read time out value.
                TTCRTN  Establish a terminal completion routine.

                           Terminal control support.
                                  TRMCTL.MAC 
                                  Table 2-19.


    User Name Support

             An executing program may set and change the user name for
        the connected job.  The routines for this facility are listed in
        Table 2-20.

                GTUNAM  Get the user name associated with the current
                        job.
                STUNAM  Set the user name associated with the current
                        job.

                               User name support.
                                  USRNAM.MAC 
                                  Table 2-20.


        TSXLIB V6.2                                              PAGE 19
        General Description


    Windowing Support

             TSX-Plus offers a full screen process windowing system that
        allows the system to remember the contents and status of the
        terminal display.  A running program may redisplay windows on
        demand.  The routines for this facility are listed in Table
        2-21.

             When windowing is used, the system monitors all characters
        sent to the terminal and maintains an updated screen image
        display in memory.  Terminal attributes such as line width,
        reverse/norman video, application keypad mode, and etc. are
        saved along with line attribures (double wide, double high) and
        character attributes.  The attributes retained for each
        character consist of blinking, bold, underlined, reverse video,
        and character set information (ASCII, UK, DEC supplemental, or
        graphics).

             The most common use of windows is to completely refresh the
        display when switching among subprocesses to avoid the confusion
        of mixed displays.  For some program applications, it may be
        useful to utilize multiple windows from the same job.

                ICRWND  Create a window.
                IDLWND  Delete a window.
                IPRWND  Print the contents of a window.
                IRSWND  Resume window processing.
                ISLWND  Select a window.
                ISPWND  Suspend window processing.

                               Windowing Support
                                  WINDOW.MAC 
                                  Table 2-21.


        TSXLIB V6.2                                              PAGE 20
        Routine Descriptions






                            3.  Routine Descriptions


             This section presents all of the TSX-Plus routines in
        alphabetical order and provides a detailed description of each
        one.  The FORTRAN calling sequence and where appropriate an
        example of each call in a FORTRAN program is given.

             The user should be thoroughly familiar with the general
        description of this TSX-Plus library given in the previous
        section of this document.  Additional information is available
        in the "TSX-Plus Reference Manual" [1] and the "RT-11
        Programmer's Reference Manual" [5].  Some of these TSXLIB
        routines require calls to various SYSLIB routines.


                                    CAUTION

             An  "Invalid  EMT"  error  message  may  result   when
             attempting  to  execute  any of the following routines
             with a prior version of TSX-Plus.   This  occurs  when
             the  underlying  EMT is not implemented in the version
             of TSX-Plus being used.



             In the following descriptions, arguments enclosed in square
        brackets, [], are optional.


    BRKCTL

             This routine is used to declare a completion routine that
        will be triggered when the BREAK key or a declared key on the
        terminal is pressed.  The calling sequence is:

                         CALL BRKCTL ( IBRKCH,CPLRTN )

        where:  IBRKCH  is the value of the character that is to be used
                        for the break control.

                CPLRTN  is the name of the completion routine to be
                        executed when the break character is pressed.

             The specified completion routine will be entered when
        either the BREAK key or the declared key is pressed.  If no
        declared key is wanted specify a value of zero for IBRKCH.  On
        some systems the console terminal BREAK key causes entry into
        console ODT and for this reason requires a declared key value.

             Only one break routine may be specified at a time for each


        TSXLIB V6.2                                              PAGE 21
        Routine Descriptions


        user.  If a break routine was previously specified, it is
        cancelled when a new break routine is declared.  If a value of
        zero is specified for the name of the completion routine,
        CPLRTN, any previously specified break routine is cancelled.

             The following example first declares the completion routine
        as an external, then establishes break sentinel control using
        the letter H, and later cancels the control.

                        EXTERNAL CPLRTN                 
                        IBRKCH = 72                     
                            .                           
                            .                           
                        CALL BRKCTL ( IBRKCH,CPLRTN )   
                            .                           
                            .                           
                        CALL BRKCTL ( 0,0 )             
                            .                           
                            .                           


    CNVAPA

             This routine is used to convert a virtual address into a
        physical address.  This is necessary when controlling devices
        that do direct memory access transfers.  The program should lock
        itself into memory before executing this routine.  The calling
        sequence is as follows:

                          CALL CNVAPA ( IVADR,IPADR )

        where:  IVADR   is the virtual address that is to be converted.

                IPADR   is the name of the two element buffer into which
                        the physical address is to be returned.

             The low order sixteen bits of the physical address are
        returned in the first element of the buffer, IPADR, and the high
        order bits of the physical address are returned in bit positions
        four through nine of the second element of the buffer.

             The following example first locks itself into memory then
        converts a virtual address to a physical address.

                       DIMENSION IPADR ( 2 )            
                       CALL LKANMY                      
                       CALL CNVAPA ( "54720,IPADR,IERR )
                           .                            
                           .                            


    DISMNT

             This routine is used to dismount a file structured device.
        This causes TSX-Plus to stop doing directory caching of the


        TSXLIB V6.2                                              PAGE 22
        Routine Descriptions


        device.  The effect of this routine is the same as the TSX-Plus
        DISMOUNT keyboard command.  The calling sequence is as follows:

                             CALL DISMNT ( IDVNAM )

        where:  IDVNAM  is the RAD50 value of the file structured device
                        name.

             The following example uses the SYSLIB routine, IRAD50, to
        convert the ASCII value of the device name, DL:, to its RAD50
        value.  It then mounts the device and later dismounts it.

                         CALL IRAD50 ( 3,'DL ',IDVNAM )
                         CALL MOUNT ( IDVNAM )         
                             .                         
                             .                         
                         CALL DISMNT ( IDVNAM )        
                             .                         
                             .                         


    DSMNTA

             This routine is used to dismount all mounted file
        structured devices.  The calling sequence is as follows:

                                  CALL DSMNTA


    GETREG

             This routine is used to get the word and byte values stored
        in the specified processor register.  The calling sequence is as
        follows:

                         CALL GETREG ( IREG,IRET,IERR )

        where:  IREG    is the number of the processor register in the
                        range of zero to three whose values are to be
                        returned.

                IRET    is a three-element integer array that is to
                        receive the values returned.  The first element
                        receives the word value stored in the specified
                        processor register.  The second element receives
                        the low byte value and the third element
                        receives the high byte value.

                IERR    is one of the following:

                        0   no error.

                        1   an invalid processor register number was
                            specified.



        TSXLIB V6.2                                              PAGE 23
        Routine Descriptions


             The following example returns the values stored in
        processor register one.

                           DIMENSION IRET(3)        
                               .                    
                               .                    
                           CALL GETREG (1,IRET,IERR)
                               .                    
                               .                    


    GTJBNM

             This routine is used to get the ASCII name of a job.  The
        calling sequence is as follows:

                     CALL GTJBNM ( LINUM,JOBNAM [ ,IERR ] )

        where:  LINUM   is the number of the line whose job name is to
                        be obtained.

                JOBNAM  is the name of the twelve-byte array that is to
                        receive the ASCII name of the job.

                IERR    is negative or one of the following:

                        O   the line is not currently logged on.

                        1   an invalid line number was specified.

             The following example aborts if the line is not logged on.

                           .                            
                           .                            
                       LOGICAL*1 JOBNAM(12)             
                       CALL GTJBNM ( LINUM,JOBNAM,IERR )
                       IF ( IERR .EQ. 0 ) STOP          
                           .                            
                           .                            


    GTUNAM

             This routine is used to get the user name associated with
        the current job.  The calling sequence is as follows:

                             CALL GTUNAM ( USRNAM )

        where:  USRNAM  is the name of the twelve-character array that
                        is to receive the user name ASCII string.

             The following example declares the byte array and then gets
        the user name.

                             LOGICAL*1 USRNAM(18)  


        TSXLIB V6.2                                              PAGE 24
        Routine Descriptions


                             CALL GTUNAM ( USRNAM )
                                 .                 
                                 .                 


    HIEFOF

             This routine is used to turn the high efficiency terminal
        mode off.  The calling sequence in as follows:

                                  CALL HIEFOF

             The following example first turns high efficiency terminal
        mode on and later turns it off.

                                  CALL HIEFON
                                      .      
                                      .      
                                  CALL HIEFOF
                                      .      
                                      .      


    HIEFON

             This routine is used to turn the high efficiency terminal
        mode on.  The calling sequence is as follows:

                                  CALL HIEFON

             TSX-Plus offers a high efficiency mode of terminal
        operation that eliminates a substantial amount of system
        overhead for terminal character processing by reducing the
        amount of processing that is done on each character.  When in
        high efficiency mode, characters are sent directly to the
        terminal with minimum handling by TSX-Plus.  Operations such as
        expanding tabs to spaces and form feeds to line feeds are
        omitted as well as input processing such as echoing characters
        and recognizing control characters such as rubout, control-U and
        control-C.  The only characters treated specially on input are
        user defined activation characters and the user specified break
        character.  At least one user specified activation character
        must be declared if high efficiency mode is to be used.  This
        form of terminal I/O is designed to facilitate high speed
        machine to machine communication.  It can be used effectively
        with buffered mode terminals.


    IACTCH

             This routine is used to determine if any activation
        characters have been received by the line but not yet accepted
        by the program.  The calling sequences are as follows:

                              CALL IACTCH ( IRET )


        TSXLIB V6.2                                              PAGE 25
        Routine Descriptions


                                       or
                                IRET = IACTCH ()

        where:  IRET    is one of the following:

                        0   at least one activation character is
                            pending.

                        1   no activation character is pending.


    IALOC

             This routine is used to allocate a device for the exclusive
        use of a job.  The calling sequence is as follows:

                        CALL IALOC ( DEVPTR,IRET,IERR )

        where:  DEVPTR  is the name of the four element integer array
                        which contains the device name in RAD50 form in
                        the first element and zeros in the other three
                        elements.

                IRET    is undefined, or the number of the job to which
                        the device is currently allocated if IERR = 1,
                        or the job which is currently using the device
                        if IERR = 4.

                IERR    is negative or one of the following:

                        1   the device is already allocated to another
                            user.

                        2   an invalid device has been specified.

                        3   the device allocation table is full.

                        4   the device is currently being used by
                            another user.

                        5   the job does not have ALLOCATE privilege
                            (IPRIV 1/14).

             The following example sets up for and allocates a device.
        If the device is already allocated or busy, the program loops
        back for another try.  If any other error condition prevails,
        the program aborts.

                          INTEGER DEVPTR(4)              
                          DATA DEVPTR /3RDY1,0,0,0/      
                              .                          
                              .                          
                      100 CONTINUE                       
                          CALL IALOC ( DEVPTR,IRET,IERR )
                          IF ( IERR .LT. 0 ) GO TO 110   


        TSXLIB V6.2                                              PAGE 26
        Routine Descriptions


                          IF ( IERR .EQ. 1 ) GO TO 100   
                          IF ( IERR .EQ. 2 ) STOP        
                          IF ( IERR .EQ. 3 ) STOP        
                          IF ( IERR .EQ. 4 ) GO TO 100   
                      110 CONTINUE                       
                              .                          
                              .                          


    IAQFLC

             This routine is used to allow the running program to
        acquire the file context of another job.  The calling sequences
        are as follows:

                          CALL IAQFLC ( JOBNUM,IERR )
                                       or
                            IERR = IAQFLC ( JOBNUM )

        where:  JOBNUM  is the number of the job whose file context is
                        to be acquired.

                IERR    is negative or one of the following:

                        0   the job is not peivileged to use this
                            routine.

                        1   the specified job number is invalid or is
                            not logged on.

             GETCXT privilege (IPRIV 2/7) is required for a job to use
        this routine except in the case where the job being accessed is
        the parent job of the job executing this routine.

             This routine allows a job to perform file service
        operations for other jobs that it may be servicing.  When this
        routine is executed, the following actions occur:

        1.  All channels for the job that are opened to files on logical
            disks are purged.

        2.  All devices mounted by the job are dismounted.

        3.  The following items are copied from the job being accessed,
            replacing the previous information for the job executing
            this routine:

            a)  ASSIGN commands.

            b)  ACCESS command restrictions.

            c)  Logical disk information.

            d)  Mounted device information.



        TSXLIB V6.2                                              PAGE 27
        Routine Descriptions


             The following example first determines the job number of
        the parent process and then acquires the file context of that
        process.  If the job is the primary one the program aborts.

                           JOBNUM = ISPY ( -30 )    
                           IERR = IAQFLC ( JOBNUM ) 
                           IF ( JOBNUM .EQ. 0 ) STOP
                               .                    
                               .                    


    IASRNT

             This routine is used to associate a shared run time system
        with a job.  It is also used to disassociate all shared run time
        systems from a job.  The calling sequences are as follows:

                        CALL IASRNT ( IRNTIM [ ,IERR ] )
                                       or
                            IERR = IASRNT ( IRNTIM )

        where:  IRNTIM  is the six character RAD50 value of the name of
                        the shareable run time system.

                IERR    is one of the following:

                        0   no error.

                        1   run time system name not recognized.

             The effect of this routine is to associate a particular
        shareable run time system with the job.  However, this routine
        does not affect the memory mapping for the job or make the run
        time system visible to the job.  That is done by the MAPRNT
        routine described later.  If some other run time system has been
        previously mapped into the job's region, that mapping is
        unaffected by this routine.  Thus it is possible to have
        multiple run time systems mapped into the job's region by
        associating and mapping them one at a time into different
        regions of the job's virtual memory space.

             If the name pointer, IRNTIM, is set to zero, this routine
        causes all run time systems to become disassociated from the job
        and reestablishes normal memory mapping for the job.

             The following example uses the SYSLIB routine, IRAD50, to
        declare the name of the run time system and then associates it
        with the job.  If the error condition is returned the program is
        halted.

                       DIMENSION IRNTIM ( 2 )           
                       CALL IRAD50 ( 6,'TSXLIB',IRNTIM )
                       IERR = IASRNT ( IRNTIM )         
                       IF ( IERR .EQ. 1 ) STOP          
                           .                            


        TSXLIB V6.2                                              PAGE 28
        Routine Descriptions


                           .                            


    IBICIO

             This routine is used to perform a bit clear operation into
        a word in the I/O page without requiring the job's virtual
        address region to be mapped to the I/O page.  The calling
        sequences are as follows:

                      CALL IBICIO ( IADR,IVAL [ ,IERR ] )
                                       or
                          IERR = IBICIO ( IADR,IVAL )

        where:  IADR    is the address of the word in the I/O page to be
                        accessed.

                IVAL    is the value to be bit cleared into the I/O
                        page.

                IERR    is negative or the following:

                        0   real time support is not available or this
                            job does not have MEMMAP privilege (IPRIV
                            1/10).

             The following example bit clears a value in the register at
        the octal address 176500 in the I/O page.  The program is
        stopped if the error condition is returned.

                         IERR = IBICIO ( "176500,"100 )
                         IF ( IERR .EQ. 0 ) STOP       
                             .                         
                             .                         


    IBISIO

             This routine is used to perform a bit set operation into a
        word in the I/O page without requiring the job's virtual address
        region to be mapped to the I/O page.  The calling sequences are
        as follows:

                      CALL IBISIO ( IADR,IVAL [ ,IERR ] )
                                       or
                          IERR = IBISIO ( IADR, IVAL )

        where:  IADR    is the address of the word in the I/O page to be
                        accessed.

                IVAL    is the value to be bit set into the I/O page.

                IERR    is negative or the following:

                        0   real time support is not available or this


        TSXLIB V6.2                                              PAGE 29
        Routine Descriptions


                            job does not have MEMMAP privilege (IPRIV
                            1/10.

             The following example bit sets a value into the register at
        the octal address 176500 in the I/O page.  The program is
        stopped if the error condition returns.

                         IERR = IBISIO ( "176500,"100 )
                         IF ( IERR .EQ. 0 ) STOP       
                             .                         
                             .                         


    IBSTCH

             This routine is used to broadcast a status change to all
        jobs that are monitoring the status of the broadcasting job.
        The calling sequences are as follows:

                         CALL IBSTCH ( IVAL [ ,IERR ] )
                                       or
                             IERR = IBSTCH ( IVAL )

        where:  IVAL    is the 16-bit status code value that is to be
                        broadcast.

                IERR    is negative or the following:

                        0   no jobs are monitoring the job making this
                            call.

             On entry to the completion routine in the monitoring
        job(s), the status value is in processor register R1, the number
        of the job issuing this call is in the low-order byte of R0, and
        the high-order bit of R0 is set to one.  The GETREG routine may
        be used to recover the values stored in R0 and R1.

             In the following example the job aborts if no other job is
        monitoring its status.

                            IERR = IBSTCH ( IVAL ) 
                            IF ( IERR .EQ. 0 ) STOP
                                .                  
                                .                  


    ICALOC

             This routine is used to check the allocation status of a
        device.  The calling sequence is as follows:

                       CALL ICALOC ( DEVPTR,JBNUM,IRET )

        where:  DEVPTR  is the name of the four element integer array
                        which contains the device name in RAD50 form in


        TSXLIB V6.2                                              PAGE 30
        Routine Descriptions


                        the first element and zeros in the other three
                        elements.

                JBNUM   is undefined, or the number of the job to which
                        the device is currently allocated if IRET = 1,
                        of the number of the job which is currently
                        using the device if IERR = 4.

                IRET    is negative or one of the following:

                        1   the device is allocated to another user.

                        2   an invalid device has been specified.

                        4   the device is currently being used by
                            another user.

             In the following example, the program aborts if an invalid
        device has been specified.

                       INTEGER DEVPTR(4)                
                       DATA DEVPTR /3RMT3,0,0,0/        
                           .                            
                           .                            
                       CALL ICALOC ( DEVPTR,JBNUM,IRET )
                       IF ( IRET .EQ. 2 ) STOP          
                           .                            
                           .                            


    ICKWTS

             This routine is used to determine if any other user has
        written to a shared file.  The calling sequence is as follows:

                           CALL ICKWTS ( ICHAN,IERR )
                                       or
                            IERR = ICKWTS ( ICHAN )

        where:  ICHAN   is the I/O channel open to the shared file.

                IERR    is negative or one of the following:

                        0   the job does not have RLOCK privilege (IPRIV
                            2/9), or shared file support is not
                            available on the system, or the channel is
                            not opened to a shared file.

                        2   writes have been performed.

             This routine can be used to advantage in a situation where
        data from some block in the file is being held in a buffer and
        it is desired to determine if the data is valid or if it may be
        invalid because some other user might have altered it by writing
        to the file.


        TSXLIB V6.2                                              PAGE 31
        Routine Descriptions


             The following example opens a file, declares the file to be
        shared and then checks for writes to the shared file.  If writes
        have been performed to the file the program is halted.

                       CALL ASSIGN ( 33,'RK3:THIS.DAT' )
                       ICHAN = ( 33 )                   
                       CALL IDCLSF ( ICHAN,5 )          
                           .                            
                           .                            
                       IERR = ICKWTS ( ICHAN )          
                       IF ( IERR .EQ. 2 ) STOP          
                           .                            
                           .                            


    ICNINT

             This routine is used to connect a completion routine to an
        interrupt vector.  The calling sequences are as follows:

                   CALL ICNINT ( IVEC,CPLRTN,IPRI [ ,IERR ] )
                                       or
                       IERR = ICNINT ( IVEC,CPLRTN,IPRI )

        where:  IVEC    is the interrupt vector address.

                CPLRTN  is the six ASCII character name of the
                        completion routine.

                IPRI    is the priority for the completion routine in
                        the range of 0 to 127.

                IERR    is negative or one of the following:

                        0   real time support is not available or this
                            job does not have REALTIME privilege (IPRIV
                            1/6).

                        1   the maximum number of interrupts are already
                            in use.

                        2   some other job is already connected to this
                            interrupt vector.

                        3   the job is not locked into memory.

             The vector remains connected to the completion routine
        until the program terminates or until the routine, IRLINT, is
        executed.  On entry to the completion routine, R0 contains the
        address of the vector that caused the completion routine to be
        executed.  The GETREG routine may be used to obtain the value
        stored in R0.

             The following example declares the completion routine as an
        external and connects an interrupt vector to the completion


        TSXLIB V6.2                                              PAGE 32
        Routine Descriptions


        routine.  The program is halted if an error condition is
        returned.

                        EXTERNAL CPLRTN                 
                        IERR = ICNINT ( "320,CPLRTN,3 ) 
                        IF ( IERR .GE. 0 ) STOP         
                            .                           
                            .                           


    ICNMCN

             This routine is used to cancel the job monitoring
        connection(s) for the calling job.  The calling sequences are as
        follows:

                        CALL ICNMCN ( JBNUM [ ,IERR ] )
                                       or
                            IERR = ICNMCN ( JBNUM )

        where:  JBNUM   is the number of the job for which status
                        monitoring is to be cancelled.  If JBNUM = zero,
                        all job status monitoring requests for the job
                        making this call are cancelled.

                IERR    is negative or the following:

                        1   an invalid job number was specified.

             All job monitoring requests issued by a job are cancelled
        by the system when the job terminates, chains, or issues either
        a hard or soft reset request.

             The following example program aborts if an invalid job
        number is specified.

                           CALL ICNMCN ( JBNUM,IERR )
                           IF ( IERR .EQ. 1 ) STOP   
                               .                     
                               .                     


    ICNRTN

             This routine is used to connect a service routine to an
        interrupt vector.  The calling sequences are as follows:

                  CALL ICNRTN ( IVEC , SVCRTN , 0 [ , IERR ] )
                                       or
                       IERR = ICNRTN ( IVEC , SVCRTN, 0 )

        where:  IVEC    is the interrupt vector address.

                SVCRTN  is the six ASCII character name of the service
                        routine.


        TSXLIB V6.2                                              PAGE 33
        Routine Descriptions


                IERR    is negative or one of the following:

                        0   real time support is not available or this
                            job does not have REALTIME privilege (IPRIV
                            1/6).

                        1   no interrupt control blocks are available

                        2   some other job is connected to the vector.

                        3   the job is not locked in memory.

             The vector remains connected to the service routine until
        the program terminates or until the routine, IRLINT, is
        executed.  The only system services (EMTs) permissible from
        within the service routine are the SYSLIB routine, RESUME, and
        the TSXLIB routine, ITCRTN.  If other system services are
        required, they must be called from a completion routine which
        has been triggered by ITCRTN.  The "0" argument is required.

             The following example declares the service routine as an
        external, locks the job in memory, and then connects an
        interrupt vector to the service routine.  The program is halted
        if an error condition is returned.

                      EXTERNAL SVCRTN                    
                      IERR = ICNRTN ( IVEC,SVCRTN,IZERO )
                      CALL LKANMY                        
                      IF ( IERR .GE. 1 ) STOP            
                          .                              
                          .                              


    ICNTSP

             This routine is used to set the transmit/receive speed or
        baud rate of a of a communication or timesharing line.  The
        calling sequencs are as follows:

                      CALL ICNTSP ( LINUM,ISPCD [,IERR ] )
                                       or
                         IERR = ICNTSP ( LINUM,ISPCD )

        where:  LINUM   is the number of the line for which the speed is
                        to be controlled.  If the line number is zero,
                        the speed is set for the line on which the
                        calling program is executing.

                ISPCD   is one of the following:

                        0   50 baud.

                        1   75 baud.

                        2   110 baud.


        TSXLIB V6.2                                              PAGE 34
        Routine Descriptions


                        3   134.5 baud.

                        4   150 baud.

                        5   300 baud.

                        6   600 baud.

                        7   1200 baud.

                        8   1800 baud.

                        9   2000 baud.

                        10  2400 baud.

                        11  3600 baud.

                        12  4800 baud.

                        13  7200 baud.

                        14  9600 baud.

                        15  19200 baud.

                IERR    is negative or one of the following:

                        1   the job does not have TERMINAL privilege
                            (IPRIV 2/15).

                        2   the specified line number was invalid.

             This routine is only functional for lines connected to
        hardware controllers that support programmable baud rates.

             The following example sets the speed of the line on which
        the program is running to 9600 baud.

                              CALL ICNTSP ( 0,14 )
                                  .               
                                  .               


    ICONTM

             This routine is used to return the connect time of a job to
        the calling program.  The calling sequence is as follows:

                      CALL ICONTM ( LINUM,IRET [ ,IERR ] )

        where:  LINUM   is the TSX-Plus line for which connect time is
                        to be returned.

                IRET    is the returned connect time in minutes.


        TSXLIB V6.2                                              PAGE 35
        Routine Descriptions


                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.

             In the following example the connect times of the logged on
        lines are returned in the variable, IRET.

                        LINUM = 0                          
                     10 CONTINUE                           
                            LINUM = LINUM + 1              
                            CALL ICONTM ( LINUM,IRET,IERR )
                            IF ( IERR .EQ. 0 ) GO TO 10    
                            IF ( IERR .EQ. 2 ) GO TO 20    
                                .                          
                                .                          
                        GO TO 10                           
                     20 CONTINUE                           


    ICPUTM

             This routine is used to return a job's CPU time to the
        calling program.  The calling sequence is as follows:

                     CALL ICPUTM ( LINUM,ITIME [ ,IERR ] )

        where:  LINUM   is the TSX-Plus line for which CPU time is to be
                        returned.

                ITIME   is the CPU time returned in clock ticks.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.

             The variable, ITIME, is a two element array where the first
        element will receive the high order 16 bits and the second
        element will receive the low order 16 bits of the CPU time
        returned.

             The CPU time of line five is returned in the following
        example.  The program aborts if an error condition prevails.

                          DIMENSION ITIME(2)          
                              .                       
                              .                       
                          CALL ICPUTM ( 5,ITIME,IERR )
                          IF ( IERR .GE. 0 ) STOP     
                              .                       
                              .                       


        TSXLIB V6.2                                              PAGE 36
        Routine Descriptions


    ICRWND

             This routine is used to create a window.  The calling
        sequences are as follows:

              CALL ICRWND ( ID,IFLG,IWDTH,ISCRL,IDCPY,JBCPY,IERR )
                                       or
               IERR = ICRWND ( ID,IFLG,IWDTH,ISCRL,IDCPY,JBCPY )

        where:  ID      is is a window identification number in the
                        range of 1 to 26 which identifies the window for
                        this job.

                IFLG    is one of the following:

                        0   the window is a temporary window and will be
                            deleted when the program exits to the
                            keyboard monitor.

                        1   the window is a permanent window and is only
                            deleted when explicitly requested (by the
                            IDLWND routine, or the SET WINDOW OFF
                            keyboard command) or when the job logs off.

                IWDTH   is the width of the window in columns and should
                        not exceed 132.

                ISCRL   is the maximum number of lines which are allowed
                        to scroll off the window during a time when the
                        window is disconnected from the terminal.
                        Specify 0 to disallow any scrolling.  Specify 1
                        to allow unlimited scrolling.

                IDCPY   is the window identification number of the
                        window from which to copy certain window
                        characteristics.  If 0, no information is
                        copied.  If in the range of 1 to 26, the
                        following characteristics are copied:

                        1)  The number of columns per line.

                        2)  The maximum allowed number of lines to be
                            scrolled while switched to a different
                            process.

                        3)  80 or 132 column mode.

                        4)  Light or dark video mode.

                JBCPY   is the job number of the job from which to copy
                        certain window characteristics.  If 0, the
                        current job is assumed.

                IERR    is negative or one of the following:



        TSXLIB V6.2                                              PAGE 37
        Routine Descriptions


                        0   Window management is not included in the
                            system.

                        1   Maximum allowed number of windows are
                            already in use.

                        2   Unable to create the window.  Job may not
                            have SYSGBL privilege (IPRIV 2/8) or
                            sufficient memory may not be available.

             The following example creates a permanent 72 column wide
        window with an identification number of 13 and allows up to 20
        lines to scroll off the window.  The program aborts if an error
        condition is returned.

                        IERR = ICRWND ( 13,1,72,20,0,0 )
                        IF ( IERR .GE. 0 ) STOP         
                            .                           
                            .                           


    IDALOC

             This routine is used to deallocate a device.  The calling
        sequence is as follows:

                        CALL IDALOC ( DEVPTR,IRET,IERR )

        where:  DEVPTR  is the name of the four element integer array
                        which contains the device name in RAD50 form in
                        the first element and zeros in the other three
                        elements.

                IRET    is undefined, or the number of the job to which
                        the device is currently allocated if IERR = 1,
                        or the number of the job which is currently
                        using the device if IERR = 4.

                IERR    is negative or one of the following:

                        1   the device is allocated to another user.

                        2   an invalid device has been specified.

                        4   the device is currently in use by another
                            job.

                        5   the job does not have ALLOCATE privilege
                            (IPRIV 1/14).

             The following example program aborts if the device is
        allocated to another user.

                        INTEGER (4)                     
                        DATA /3RDX0,0,0,0/              


        TSXLIB V6.2                                              PAGE 38
        Routine Descriptions


                            .                           
                            .                           
                        CALL IDALOC ( DEVPTR,IRET,IERR )
                        IF ( IERR .EQ. 1 ) STOP         
                            .                           
                            .                           


    IDCLSF

             This routine is used to declare an open file to be shared.
        The calling sequences are as follows:

                     CALL IDCLSF ( ICHAN,IACES [ ,IERR ] )
                                       or
                         IERR = IDCLSF ( ICHAN,IACES )

        where:  ICHAN   is the I/O channel number open to the shared
                        file.

                IACES   is one of the following protection/access codes:

                        0   exclusive/input.

                        1   exclusive/update.

                        2   protected/input.

                        3   protected/update.

                        4   shared/input.

                        5   shared/update.

                IERR    is negative or one of the following:

                        0   shared file support is not available on the
                            system or the job does not have RLOCK
                            privilege (IPRIV 2/9).

                        1   the I/O channel has not been opened to a
                            file.

                        2   attempted to open too many channels to
                            shared files.

                        3   attempted to open too many shared files.

                        4   a file protection/access conflict exists.

             The protection/access code specifies two things, the type
        of protection (exclusive, protected, shared) that you are
        claiming on your use of the file and the type of access (input
        or update) that you intend to make to the file.  Exclusive
        protection means that you require exclusive access to the file


        TSXLIB V6.2                                              PAGE 39
        Routine Descriptions


        and will allow no other users to access the file in any fashion.
        Protected protection means that you will allow other users to
        open the file for input but wish to prohibit any from opening
        the file for update.  Shared protection means that you are
        willing to allow other users to open the file for both input and
        update.

             The following example opens a file and then declares
        exclusive/update protection/access.  If an error condition is
        returned the program aborts.

                        CALL ASSIGN ( 40,'DK:FILE.DAT' )
                        REWIND 40                       
                        ICHAN = ILUN ( 40 )             
                        IERR = IDCLSF ( ICHAN,2 )       
                        IF ( IERR .NE. 0 ) STOP         
                            .                           
                            .                           


    IDLWND

             This routine is used to delete one or more windows that
        were created with the ICRWND routine.  The calling sequences are
        as follows:

                          CALL IDLWND ( ID [, IERR ])
                                       or
                              IERR = IDLWND ( ID )

        where:  ID      is the window identification number of the
                        window that is to be deleted.

                IERR    is negative or one of the following:

                        0   window management support is not included in
                            the system.

                        3   unable to locate the window with the
                            specified window identification number.

             If the window identification number is zero, then all of
        the temporary windows for the job are deleted.  If the window
        identification number is 255, then all the temporary and
        permanent windows for the job are deleted.  This routine
        requires the SYSGBL privilege (IPRIV 2/8).


    IDMLD

             This routine is used to dismount a logical device (LD).
        The calling sequences are as follows:

                         CALL IDMLD ( LDNUM [ ,IERR ] )
                                       or


        TSXLIB V6.2                                              PAGE 40
        Routine Descriptions


                             IERR = IDMLD ( LDNUM )

        where:  LDNUM   is the LD unit number in the range of zero
                        through seven.

                IERR    is negative or one of the following:

                        0   the specified LD unit is not associated with
                            a file.

                        1   an invalid LD unit number was specified.

                        3   some channel is open to a file on the
                            specified LD.

             The following example aborts if the LD is in use by another
        job.

                                .                  
                                .                  
                            IERR = IDMLD ( LDNUM ) 
                            IF ( IERR .EQ. 3 ) STOP
                                .                  
                                .                  


    IESMCN

             This routine is used to establish a job monitoring
        connection between the calling job and another job.  The calling
        sequences are as follows:

                     CALL IESMCN ( JBNUM,CPLRTN [ ,IERR ] )
                                       or
                         IERR = IESMCN ( JBNUM,CPLRTN )

        where:  JBNUM   is the number of the job to be monitored.  If
                        zero is specified as the number of the job to be
                        monitored, all jobs are monitored (including
                        those that are not currently logged on).

                CPLRTN  is the name of the completion routine to be
                        entered when the status of the monitored job
                        changes.

                IERR    is negative or one of the following:

                        1   an invalid job number was specified.

                        2   there are no free job monitoring control
                            blocks available.

             The specified completion routine will be entered each time
        the status of the monitored job changes or the monitored job
        broadcasts a status change.  On entry to the completion routine,


        TSXLIB V6.2                                              PAGE 41
        Routine Descriptions


        the low-order byte of processor register R0 contains the number
        of the job whose status change is being reported.  The
        high-order bit of R0 is zero if the status report was generated
        by the system and is one if the status report was generated by a
        program broadcasting a status change.  The status value is
        contained in processor register R1.  The values stored in R0 and
        R1 may be recovered with the GETREG routine.  The system
        generated status values are listed below:

                 1   The job has been initialized.             

                 2   The job logged on using the LOGON program.

                 3   The job began running a program.          

                 4   The job returned control to KMON.         

                 5   The job has logged off.                   

             The following example program establishes a job status
        monitoring connection.  If there are no control blocks
        available, it loops back for another try.  The program aborts if
        an invalid job number has been specified.

                           EXTERNAL CPLRTN               
                               .                         
                               .                         
                       100 CONTINUE                      
                           IERR = IESMCN ( JBNUM,CPLRTN )
                           IF ( IERR .EQ. 2 ) GO TO 100  
                           IF ( IERR .EQ. 1 ) STOP       
                               .                         
                               .                         


    IEXSTS

             This routine is used to return the execution state of a
        TSX-Plus line.  The calling sequence is as follows:

                     CALL IEXSTS ( LINUM,ISTAT [ ,IERR ] )

        where:  LINUM   is the number of the line for which execution
                        state is returned.

                ISTAT   is the one of the following execution state
                        values:

                        1   high priority run state.

                        2   normal priority run state.

                        3   low priority run state.

                        4   waiting for terminal input.


        TSXLIB V6.2                                              PAGE 42
        Routine Descriptions


                        5   waiting to write terminal output.

                        6   doing a timed wait.

                        7   suspended by SUSPND or .SPND.

                        8   waiting to access a shared file.

                        9   waiting for a message.

                        10  waiting for access to the USR.

                        11  waiting for I/O to finish.

                        12  waiting to access spool file.

                        13  Interactive high priority run state.

                        14  Fixed high priority run state.

                        15  Waiting for memory expansion.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.

             The program in the following example halts if line 2 is
        doing a timed wait.

                          CALL IEXSTS ( LINUM,ISTAT )
                          IF ( ISTAT .EQ. 6 ) STOP   
                              .                      
                              .                      


    IFLINF

             This routine obtains some information about a file.  The
        calling sequence is as follows:

                 CALL IFLINF ( ICHAN , IDEV , INFO [ , IERR ] )

        where:  ICHAN   is a channel number in the range of zero through
                        sixteen that is currently not in use.

                IDEV    is the name of a four-word array that contains
                        the file specification in RAD50.

                INFO    is the name of the seven-word array that is to
                        receive the following information about the
                        file:

                        Word 1  is the number of 512-byte blocks


        TSXLIB V6.2                                              PAGE 43
        Routine Descriptions


                                contained in the file.

                        Word 2  is zero if the file is not protected, or
                                one if the file is protected.

                        Word 3  is the creation date of the file in
                                RT-11 internal format.

                        Word 4  is the creation time of the file in
                                three-second units.

                        Word 5  is the starting block number of the
                                file.

                        Word 6  is reserved.

                        Word 7  is reserved.

                IERR    is negative or one of the following

                        0   The channel is currently in use.

                        1   Unable to locate the specified file.

                        2   The specified device is not file structured.

             The following example obtains the information about the
        file, DY1:STUFF.DAT.

                      DIMENSION IDEV(4),INFO(7)              
                      ICHAN = IGETC ()                       
                      CALL IRAD50 ( 12,'DY1STUFF DAT',IDEV)  
                      CALL IFLINF ( ICHAN,IDEV,INFO,IERR )   
                      IF ( IERR .GT. 0 ) STOP 'IFLINF error' 
                          .                                  
                          .                                  


    IHERR

             This routine is used to restore monitor interception of
        certain soft error conditions.  It must be called at some point
        following a call to ISERR.  The calling sequence is as follows:

                                   CALL IHERR


    ILDTR

             This routine is used to lower the DTR signal on a
        communication or a timesharing line.  The calling sequences are
        as follows:

                         CALL ILDTR ( LINUM [ ,IERR ] )
                                       or


        TSXLIB V6.2                                              PAGE 44
        Routine Descriptions


                             IERR = ILDTR ( LINUM )

        where:  LINUM   is the number of the line whose DTR signal is to
                        be lowered.  TERMINAL (IPRIV 2/15) is required
                        if the line number is not the same as the one on
                        which the job is running.

                IERR    is negative or one of the following:

                        1   the job does not have TERMINAL (IPRIV 2/15)
                            privilege.

                        2   an invalid line number was specified.

             This is only effective if the interface supports modem
        control signals.  This can be useful in situations where a modem
        or data PBX requires the DTR signal.

             The following example first determines its line number and
        then lowers its DTR signal.

                                 .                 
                                 .                 
                             LINUM = ITSLIN ()     
                             CALL = ILDTR ( LINUM )
                                 .                 
                                 .                 


    ILNSTS

             This routine is used to return information about the status
        of a line.  The calling sequence is as follows:

                      CALL ILNSTS ( LINUM,IRET [ ,IERR ] )

        where:  LINUM   is the TSX-Plus line for which status
                        information is returned.

                IRET    is the value returned and contains bit-flags
                        that indicate the status for the line.  The
                        following bit-flags are defined:

                        000000  physical line.

                        000001  virtual line.

                        000002  detached job line.

                        000100  job is locked in memory.

                        000200  job has operator privilege.

                IERR    is negative or one of the following:



        TSXLIB V6.2                                              PAGE 45
        Routine Descriptions


                        0   line is not currently logged on.

                        2   invalid line number.

             The program in the example below stops if the line number
        is invalid.

                        CALL ILNSTS ( LINUM,IRET,IERR )
                        IF ( IERR .EQ. 2 ) STOP        
                            .                          
                            .                          


    INITPA

             This routine is used to set up parameters that will control
        a performance analysis.  It does not actually begin the
        analysis.  The calling sequences are as follows:

              CALL INITPA ( IBSADR,ITPADR,ICLSZ,IFLAG [ ,IERR ] )
                                       or
                  IERR = INITPA ( IBSADR,ITPADR,ICLSZ,IFLAG )

        where:  IBSADR  is the base address of the region to be
                        monitored.

                ITPADR  is the top address of the region to be
                        monitored.

                ICLSZ   is the number of bytes to group into each
                        histogram cell.

                IFLAG   is one of the following:

                        0   do not include I/O wait time.

                        1   include I/O wait time.

                IERR    is negative or one of the following:

                        0   performance analysis is already in use.

                        1   performance analysis feature is not included
                            in this version of TSX-Plus.

             The following example initializes for a performance
        analysis.  The program aborts if an error condition is returned.

                      IERR = INITPA ( "2000,"5400,"100,0 )
                      IF ( IERR .GE. 0 ) STOP             
                          .                               
                          .                               


        TSXLIB V6.2                                              PAGE 46
        Routine Descriptions


    INITSP

             This routine is used to initialize a new or switch to an
        existing subprocess.  It performs the same function as if a
        CTRL-W-digit sequence had been typed at the terminal.  The
        calling sequence is as follows:

               CALL INITSP ( ISPN,IRPN,0,CMDFIL,IRET [ ,IERR ] )

        where:  ISPN    indicates the subprocess number and is analogous
                        to the digit typed after CTRL-W when manually
                        switching between subprocesses.  The value must
                        be in the range of zero to MAXSEC, a TSGEN
                        parameter.  If a minus one is specified, the
                        system locates the first unused subprocess
                        number and uses it.

                IRPN    indicates which process to return to when the
                        process initiated by this routine terminates as
                        follows:

                        0   specifies return to the primary process.

                        1   specifies return to the process which is
                            executing this routine to initiate the
                            subprocess.

                CMDFIL  is the name of the string variable containing
                        the file specification of a command file to be
                        executed when the subprocess is initiated.  This
                        command file executes without start-up privilege
                        following any other start-up command file
                        specified with the SET SUBPROCESS/FILE command.
                        If the variable is empty, no command file is
                        executed.

                IRET    if ISPN is too large, the TSGEN parameter,
                        MAXSEC, is returned.  If ISPN is minus one, the
                        number of the subprocess initiated is returned.

                IERR    is negative or one of the following:

                        1   the job does not have SUBPROCESS (IPRIV
                            2/11) privilege.

                        2   the specified subprocess number is too
                            large.

                        3   all of the job's subprocesses are already
                            active.

                        4   there is insufficient memory available for
                            the subprocess.


        TSXLIB V6.2                                              PAGE 47
        Routine Descriptions


    IPEKIO

             This routine is used to access or peek at a word in the I/O
        page without requiring the job's virtual address region to be
        mapped to the I/O page.  The calling sequence is as follows:

                      CALL IPEKIO ( IADR,IRET [ ,IERR ] )

        where:  IADR    is the address of the word in the I/O page that
                        is to be accessed.

                IRET    is the value returned from the I/O page.

                IERR    is negative or the following:

                        0   real time support is not available or this
                            job does not have MEMMAP privilege (IPRIV
                            1/10).

             The following example obtains the value from the register
        at octal address 176502 in the I/O page.  The program is aborted
        if the error condition is returned.

                       CALL IPEKIO ( "176502,IRET,IERR )
                       IF ( IERR .EQ. 0 ) STOP          
                           .                            
                           .                            


    IPGNAM

             This routine is used to return the name of the program
        being executed by a TSX-Plus line.  The calling sequence is as
        follows:

                     CALL IPGNAM ( LINUM,PGNAME [ ,IERR ] )

        where:  LINUM   is the number of the line executing the returned
                        program name.

                PGNAME  is the two-word variable into which the RAD50
                        value of the program name is returned.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.

             The SYSLIB routine R50ASC is used to convert the returned
        program name to an ASCII string in the following example.

                        LOGICAL*1 STRING(8)             
                            .                           
                            .                           


        TSXLIB V6.2                                              PAGE 48
        Routine Descriptions


                        CALL IPGNAM ( LINUM,PGNAM,IERR )
                        IF ( IERR .GE. 0 ) STOP         
                        CALL R50ASC ( 6,PGNAM,STRING )  


    IPOKIO

             This routine is used to deliver a value into a word in the
        I/O page without requiring the job's virtual address region to
        be mapped to the I/O page.  The calling sequences are as
        follows:

                      CALL IPOKIO ( IADR,IVAL [ ,IERR ] )
                                       or
                          IERR = IPOKIO ( IADR,IVAL )

        where:  IADR    is the address of the word in the I/O page to be
                        accessed.

                IVAL    is the value to be deposited in the I/O page.

                IERR    is negative or the following:

                        0   real time support is not available or this
                            job does not have MEMMAP privilege (IPRIV
                            1/10).

             The following example pokes a value into the register at
        octal address 176506 in the I/O page.  The program stops if the
        error condition is returned.

                         IERR = IPOKIO ( "176506,"101 )
                         IF ( IERR .EQ. 0 ) STOP       
                             .                         
                             .                         


    IPPNUM

             This routine is used to return the project and programmer
        numbers for a TSX-Plus line.  The calling sequence is as
        follows:

                      CALL IPPNUM ( LINUM,IBUF [ ,IERR ] )

        where:  LINUM   is the number of the line for which the project
                        and programmer numbers are returned.

                IBUF    is the two word array into which the project and
                        programmer numbers are returned.  The first word
                        contains the project number and the second word
                        contains the programmer number.

                IERR    is negative or one of the following:



        TSXLIB V6.2                                              PAGE 49
        Routine Descriptions


                        0   line is not currently logged on.

                        2   invalid line number.

             The program in the following example stops if an error
        condition is encountered.

                        DIMENSION IBUF(2)              
                            .                          
                            .                          
                        CALL IPPNUM ( LINUM,IBUF,IERR )
                        IF ( IERR .GE. 0 ) STOP        
                            .                          
                            .                          


    IPRIV

             This routine permits the running program to determine or to
        change the job privilege sets.  The calling sequence is as
        follows:

                   CALL IPRIV ( IFUN,IPRVT,BUFFER [ ,IERR ] )

        where:  IFUN    is one of the following function control values:

                        0   causes the privilege flags to be stored into
                            the specified buffer.

                        1   causes the privilege flags that are set in
                            the buffer to be cleared in the
                            corresponding system table.

                        2   causes the privilege flags that are set in
                            the buffer to be set in the corresponding
                            system table.

                IPRVT   indicates which of the three sets of privilege
                        flags are to be accessed and must be one of the
                        following values:

                        0   the current job privileges are selected.

                        1   the set privileges for the job are selected.
                            If any privileges are changed, the current
                            privileges are also changed.

                        2   the authorized privileges are selected.

                BUFFER  is the name of the four-word buffer that is to
                        receive or contains the privilege flags.  A flag
                        value of 1 enables the privilege and a value of
                        0 denies the privilege.  The following list
                        shows the privilege related to each flag
                        (word/bit).


        TSXLIB V6.2                                              PAGE 50
        Routine Descriptions


                        1/0   SYSPRV, system privilege (system manager
                              type operations).

                        1/1   NFSWRITE, non-file structured read/write
                              access.

                        1/2   NFSREAD, non-file-structured read access.

                        1/3   SETPRV, affect own privileges.

                        1/4   SETNAME, change user name or password.

                        1/5   SEND, sending messages between jobs (not
                              using a named message channel).

                        1/6   REALTIME, real time support.

                        1/7   PSWAPM, change process swap mode.

                        1/8   OPER, operator.

                        1/9   BYPASS, bypass device/file access
                              restrictions.

                        1/10  MEMMAP, access memory that may be
                              significant to the system.

                        1/11  SPFUN, use the .SPFUN EMT.

                        1/12  DETACH, affect detached jobs.

                        1/13  DEBUG, use of the debugging facilities.

                        1/14  ALLOCATE, device allocation.

                        1/15  reserved.

                        2/0   UP1, user-defined privilege #1.

                        2/1   UP2, user defined privilege #2.

                        2/2   UP3, user-defined privilege #3.

                        2/3   UP4, user-defined privilege #4.

                        2/4 through 2/6 reserved.

                        2/7   GETCXT, get file context from another job.

                        2/8   SYSGBL, global regions.

                        2/9   RLOCK, shared file record locking.

                        2/10  MESSAGE, named message channels.



        TSXLIB V6.2                                              PAGE 51
        Routine Descriptions


                        2/11  SUBPROCESS, use subprocesses (virtual
                              lines).

                        2/12  SAME, affect jobs with the same project
                              and programmer numbers.

                        2/13  GROUP, affect jobs with the same project
                              number.

                        2/14  WORLD, affect any job.

                        2/15  TERMINAL, terminal and CL commands.

                        3/0 through 4/15 reserved.

                IERR    is negative or the following:

                        1   attempt to enable privileges for which the
                            job is not authorized.

             Only those privileges for which the job is authorized are
        set.  SETPRV privilege is required to set any new privileges in
        the authorized privilege set.

             The following example returns the set of authorized job
        privileges to the buffer.

                        INTEGER BUFFER(4)               
                        DATA IFUN,IPRVT /0,2/           
                        CALL IPRIV ( IFUN,IPRVT,BUFFER )


    IPRWND

             This routine causes the contents of a window to be printed.
        The calling sequences are as follows:

                            CALL IPRWND ( ID,IERR )
                                       or
                              IERR = IPRWND ( ID )

        where:  ID      is the window identification number of the
                        window whose contents are to be printed.

                IERR    is negative or one of the following:

                        0   Windowing support is not available on the
                            system.

                        3   the specified window identification number
                            is invalid.

                        4   the WINPRT program is not running.

             The following example aborts if an error condition is


        TSXLIB V6.2                                              PAGE 52
        Routine Descriptions


        detected.

                            IERR = IPRWND ( ID )   
                            IF ( IERR .GE. 0 ) STOP
                                .                  
                                .                  


    IRDRCL

             This routine is used to redirect a dedicated communication
        line, CL unit, or a timesharing line.  The calling sequences are
        as follows:

                     CALL IRDRCL ( ICLNO,LINUM [ ,IERR ] )
                                       or
                         IERR = IRDRCL ( LCLNO,LINUM )

        where:  ICLNO   is the dedicated communication line number, CLn.

                LINUM   is the number of the timesharing line or the
                        dedicated communication line.

                IERR    is negative or one of the following:

                        1   the user making this call does not have
                            TERMINAL privilege (IPRIV 2/15).

                        2   an invalid CL unit number, ICLNO, was
                            specified.

                        3   an invalid line number, LINUM, was
                            specified.

                        4   the specified line number, LINUM, is already
                            assigned to a CL unit.

                        5   a timesharing user is logged onto the
                            specified line number, LINUM.

                        6   the specified CL unit, ICLNO, is currently
                            in use.

             The following sample program aborts if an error is returned
        when it attempts to redirect CL3 to line number 9.

                            CALL IRDRCL ( 3,9,IERR )
                            IF ( IERR .GT. 0 ) STOP 
                                .                   
                                .                   


        TSXLIB V6.2                                              PAGE 53
        Routine Descriptions


    IRDTR

             This routine is used to raise the DTR signal on a
        communication or a timesharing line.  The calling sequences are
        as follows:

                         CALL IRDTR ( LINUM [ ,IERR ] )
                                       or
                             IERR = IRDTR ( LINUM )

        where:  LINUM   is the number of the line whose DTR signal is to
                        be raised.  TERMINAL (IPRIV 2/15) privilege is
                        required if the line number is not the sams as
                        the one on which the job is running.

                IERR    is negative or one of the following:

                        1   the job does not have TERMINAL (IPRIV 2/15)
                            privilege.

                        2   an invalid line number was specified.

             This is only effective if the interface supports modem
        control signals.  This can be useful in situations where a modem
        or data PBX requires the DTR signal.

             The following example aborts if it does not have TERMINAL
        (IPRIV 2/15) privilege.

                                .                  
                                .                  
                            IERR = IRDTR ( LINUM ) 
                            IF ( IERR .EQ. 1 ) STOP
                                .                  
                                .                  


    IRLINT

             This routine releases the connection of an interrupt vector
        and a completion routine or a service routine.  The connection
        must have been made by previously executing the routine, ICNINT
        or ICNRTN.  The calling sequence is as follows:

                              CALL IRLINT ( IVEC )

        where:  IVEC    is the interrupt vector address.

             REALTIME privilege (IPRIV 1/6) is required to execute this
        routine.

             The following example first declares the completion routine
        as an external, then connects it to a vector, and finally breaks
        the connection.



        TSXLIB V6.2                                              PAGE 54
        Routine Descriptions


                        EXTERNAL CPLRTN                 
                        CALL ICNINT ( "320,CPLRTN,0 )   
                            .                           
                            .                           
                        CALL IRLINT ( "320 )            
                            .                           
                            .                           


    IRSWND

             This routine is used to resume processing of the currently
        selected window.  The calling sequence is as follows:

                                  CALL IRSWND

             No operation is performed if the job has no active window.
        The SYSGBL privilege (IPRIV 2/8) is required to execute this
        routine.


    IRXOFF

             This routine is used to reset the XOFF (CTRL-S) state of a
        communication or a timesharing line.  This only affects XOFFs
        received by the system from a terminal and not the XOFFs sent to
        the terminal by the system.  The calling sequences are:

                        CALL IRXOFF ( LINUM [ ,IERR ] )
                                       or
                            IERR = IRXOFF ( LINUM )

        where:  LINUM   is the number of the line on which the XOFF
                        state is to be reset.  TERMINAL (IPRIV 2/15)
                        privilege is required if the line to be affected
                        is not the line on which the job is running.

                IERR    is negative or one of the following:

                        1   the job does not have TERMINAL (IPRIV 2/15)
                            privilege.

                        2   an invalid line number was specified.

             The following example aborts if an invalid line number is
        specified.

                                .                  
                                .                  
                            IERR = IRXOFF ( LINUM )
                            IF ( IERR .EQ. 2 ) STOP
                                .                  
                                .                  


        TSXLIB V6.2                                              PAGE 55
        Routine Descriptions


    ISERR

             This routine is used to permit a running program to
        intercept certain soft error conditions.  These conditions may
        occur only on the execution of other TSXLIB and SYSLIB routines.
        Execution of ISERR must at some point be followed by execution
        of IHERR.  The calling sequence is as follows:

                                   CALL ISERR

             The following soft error codes may be returned on execution
        of other TSXLIB and SYSLIB routines:

                -1  Called "USR" from a completion routine.

                -2  No device handler;  this operation needs one.

                -3  Error doing directory I/O.

                -4  ".FETCH" error.  Either an I/O error occurred while
                    the handler was being used, or an attempt was made
                    to load the handler over "USR" or "RMON".  (RT-11
                    only)

                -5  Error reading an overlay.

                -6  No more room for files in the directory.

                -7  Illegal address ("FB" only);  tried to perform a
                    monitor operation outside the job partition.  (RT-11
                    only)

                -8  Illegal channel number.  Number is greater than
                    actual number of channels that exist.

                -9  Illegal "EMT";  an illegal function code has been
                    decoded.

             The example below tests for the existence of a handler for
        the logical device named DEV.

                     DIMENSION IDVBLK(4)                   
                     DATA IDVBLK /0,0,0,0/                 
                         .                                 
                         .                                 
                     CALL ISERR                            
                     I = LOOKUP( ICHAN,IDVBLK)             
                     IF ( IDVBLK .EQ -2 ) STOP 'NO HANDLER'
                         .                                 
                         .                                 
                     CALL IHERR                            


        TSXLIB V6.2                                              PAGE 56
        Routine Descriptions


    ISLWND

             This routine is used to select a window that has already
        been created with the ICRWND routine.  The calling sequences are
        as follows:

                            CALL ISLWND ( ID,IERR )
                                       or
                              IERR = ISLWND ( ID )

        where:  ID      is the window identification number of the
                        window to be selected and displayed.

                IERR    is negative or one of the following:

                        0   window management support is not included in
                            the system.

                        3   unable to locate the window with the
                            specified window identification number.

             A window identification number of zero causes windowing to
        be disabled for the job.  However, the contents of all existing
        windows are retained and may be reselected later.  The SYSGBL
        privilege (IPRIV 2/8) is required to execute this routine.

             In the following example, the program aborts if an error
        condition prevails typing out an appropriate error message.

                  CALL ISLWND ( ID,IERR )                     
                  IF ( IERR .EQ. 0 ) STOP 'No window support' 
                  IF ( IERR .EQ. 3 ) STOP 'Cannot find window'
                      .                                       
                      .                                       


    ISPBLK

             This routine is used to determine the number of free blocks
        in the spool file.  The calling sequences are as follows:

                              CALL ISPBLK ( IRET )
                                       or
                                IRET = ISPBLK ()

        where:  IRET    is the number of free blocks in the spool file.


    ISPCTL

             This routine is used to control the release time of a
        spooled file.  The calling sequence is as follows:

                         CALL ISPCTL ( ICHAN , IFLAG )



        TSXLIB V6.2                                              PAGE 57
        Routine Descriptions


        where:  ICHAN   is the number of the channel that is open to the
                        file.

                IFLAG   is an integer value as follows:

                        0   release the file immediately.

                        1   hold the release until the file is closed.

             This routine must be called after the file has been opened
        and before any data is written to the file.  If the channel is
        open to a non-spooled device, the call is treated as a
        no-operation.  OPER privilege (IPRIV 1/8) is required to execute
        this routine.

             The following example causes the file to be written to the
        spooled line printer to be released immediately.

                           OPEN ( UNIT=30,NAME=LP: )
                           ICHAN = ILUN ( 30 )      
                           CALL ISPCTL ( ICHAN,1 )  
                               .                    
                               .                    


    ISPPA

             This routine is used to suspend the collection of data for
        a performance analysis.  The data collection can be restarted by
        using the ISTPA routine described later.  The calling sequences
        are as follows:

                              CALL ISPPA [ IERR ]
                                       or
                                IERR = ISPPA ()

        where:  IERR    is negative or the following:

                        0   performance analysis has not been previously
                            initialized.

             The following example initializes for a performance
        analysis, then starts and stops the collection of data for the
        analysis within a loop.

                        CALL INITPA ( "2000,"5400,"100,0 )
                        DO 10 I = 1,53                    
                            CALL ISTPA                    
                                .                         
                                .                         
                            CALL ISPPA                    
                                .                         
                                .                         
                     10 CONTINUE                          
                                .                         


        TSXLIB V6.2                                              PAGE 58
        Routine Descriptions


                                .                         


    ISPWND

             This routine is used to suspend window processing of the
        currently selected window.  The calling sequence is as follows:

                                  CALL ISPWND

             When window processing is suspended, characters are sent to
        the terminal without being processed by the window management
        system.  No operation is performed if the job has no active
        windows.  The SYSGBL privilege (IPRIV 2/8) is required to
        execute this routine.


    ISPY

             This is a SYSLIB routine that is used to return the value
        located at a specific offset into the simulated RMON.  TSX-Plus
        has extended it to return several TSX-Plus values.  Refer to the
        "RT-11 Programmer's Reference Manual" [5] for information on
        getting values from within the simulated RMON.  The calling
        sequence is as follows:

                             IRET = ISPY ( IOFFST )

        where:  IRET    is the integer value returned.

                IOFFST  is the integer offset into the simulated RMON or
                        to return a TSX-Plus value is one of the
                        following:

                        -2  job number.

                        -4  lead-in character used for terminal
                            controlled options.

                        -6  zero if job does not have system privilege,
                            SYSPRIV (IPRIV 1/0), or one if job does have
                            system privilege.

                        -8  zero if PAR 7 is mapped to the simulated
                            RMON or one if PAR 7 is mapped to the I/O
                            page.

                        -10 project number job is logged on under.

                        -12 programmer number job is logged on under.

                        -14 TSX-Plus license number.

                        -16 get the job's priority level.



        TSXLIB V6.2                                              PAGE 59
        Routine Descriptions


                        -18 get the job's maximum allowable priority
                            level.

                        -20 the number of blocks per job in the file
                            SY:TSXUCL.TSX.

                        -22 get the job number of the primary line (0 if
                            this is the primary line).

                        -24 get the RAD50 name of the physical
                            SY: device.

                        -26 value of the PRILOW sysgen parameter.

                        -28 value of the PRIHI sysgen parameter.

                        -30 job number of the parent process (0 for the
                            primary process).

                        -32 get the TSX-Plus version number times 100.

                        -34 get the job's relative subprocess number.
                            Primary and detached lines return zero.
                            Subprocesses return the relative subprocess
                            number equivalent to the digit typed after a
                            CTRL-W.

             The following example aborts if the job is not privileged.

                            IRET = ISPY ( -6 )     
                            IF ( IRET .EQ. 0 ) STOP
                                .                  
                                .                  


    ISTDJ

             This routine is used to check the status of a detached job.
        The calling sequences are as follows:

                          CALL ISTDJ ( JOBNUM,ISTAT )
                                       or
                            ISTAT = ISTDJ ( JOBNUM )

        where:  JOBNUM  is the job number of the detached job.

                ISTAT   is one of the following:

                        0   the job is not active.

                        1   the job is active.

             The following example starts a detached job then checks the
        detached job's status until the job becomes inactive.



        TSXLIB V6.2                                              PAGE 60
        Routine Descriptions


                          CALL STDTJB ( JOBNAM, JOBNUM )
                       10 CONTINUE                      
                          ISTAT = ISTDJ ( JOBNUM )      
                          IF ( ISTAT .NE. 1 ) GO TO 10  
                              .                         
                              .                         


    ISTFTM

             This routine is used to set the creation time for a file.
        The calling sequences are as follows:

                CALL ISTFTM ( ICHAN , IDEV , ITIME [ , IERR ] )
                                       or
                     IERR = ISTFTM ( ICHAN , IDEV , ITIME )

        where:  ICHAN   is a channel number in the range of zero through
                        sixteen that is currently not in use.

                IDEV    is the name of the four-word array containing
                        the file specification in RAD50.

                ITIME   is an integer time value in three-second units
                        since midnight.

                IERR    is negative or one of the following.

                        0   the channel is currently in use.

                        1   unable to locate the specified file.

                        2   the specified device is not file structured.

             The following example sets the creation time for the file,
        NICKS.DAT, at 300 three-second units past midnight.

                       DIMENSION IDEV(4)                     
                       DATA ICHAN,ITIME /0,300/              
                       CALL IRAD50 ( 12,DM4NICKS DAT,IDEV)   
                   100 CONTINUE                              
                       IERR = ISTFTM ( ICHAN,IDEV,ITIME )    
                       IF ( ICHAN .GT 16 ) STOP 'No channels'
                       IF ( IERR .EQ. 0 ) GO TO 100          
                       IF ( IERR .GT. 0 ) STOP 'ISTFTM error'
                           .                                 
                           .                                 


    ISTLD

             This routine is user to obtain certain status information
        about a logical device (LD).  The calling sequence is as
        follows:



        TSXLIB V6.2                                              PAGE 61
        Routine Descriptions


                           CALL ISTLD ( LDNUM,ISTBF )

        where:  LDNUM   is the LD unit number in the range of zero
                        through seven.

                ISTBF   is a five element buffer that is to receive the
                        status information about the specified LD.  If
                        the LD is associated with a file, the first four
                        elements will receive the RAD50 value for the
                        dev:filnam.ext of the file.  The fifth element
                        is a flag word.  If the LD is mounted for
                        read-only access, bit zero of the flag word will
                        be set.  If the LD is not currently accessable,
                        bit one of the flag word will be set.


    ISTPA

             This routine is used to begin the actual collection of
        performance analysis data.  The INITPA routine must have been
        executed to set up parameters about the performance analysis
        before this routine is called.  The calling sequences are as
        follows:

                              CALL ISTPA [ IERR ]
                                       or
                                IERR = ISTPA ()

        where:  IERR    is negative or the following:

                        0   performance analysis has not been
                            initialized.

             The following example initializes for and starts a
        performance analysis.  The program is halted if the error
        condition is returned from the call to ISTPA.

                       CALL INITPA ( "2000,"5400,"100,0 )
                       IERR = ISTPA ()                   
                       IF ( IERR .EQ. 0 ) STOP           
                           .                             
                           .                             


    ISTPRV

             This routine is used to set the priority value for the
        current job.  The calling sequence is as follows:

                             CALL ISTPRV ( IPRVAL )

        where:  IPRVAL  is an integer priority value in the range of 0
                        through 127.

             If the job attempts to set its priority level above its


        TSXLIB V6.2                                              PAGE 62
        Routine Descriptions


        maximum allowed priority level, its priority level will be set
        to the maximum value allowed.


    ISVST

             This routine is used to save the status of a shared file.
        The effect of this routine is to suspend the connection between
        the shared file table and the I/O channel.  Any blocks that are
        locked in the file remain locked until the channel is reopened
        to the file by using the SYSLIB routine, IREOPN.  After return
        from this routine the channel may be freed by using the SYSLIB
        routine, PURGE.  The calling sequence is as follows:

                              CALL ISVST ( ICHAN )

        where:  ICHAN   is the I/O channel number open to the shared
                        file.

             The RLOCK privilege (IPRIV 2/9) is required to execute this
        routine.

             When using a single channel number to access several shared
        files it is for each file convenient to initially open the file,
        declare the file to be shared and to save the status of the file
        with the SYSLIB routine, ISAVES.  The channel being used to
        access the set of files can then be switched from one file to
        another with the SYSLIB routines, PURGE and IREOPN.  However,
        before doing the PURGE, TSX-Plus must be told that you wish to
        save the shared file status of the file (otherwise all locked
        blocks will be unlocked and the file will be removed from the
        shared file list).

             The following example opens a file, declares it to be
        shared and then saves the status of the file for TSX-Plus.

                        CALL ASSIGN ( 30,'DK:SOME.FIL' )
                        ICHAN = ILUN ( 30 )             
                        CALL IDCLSF ( ICHAN,4 )         
                            .                           
                            .                           
                        CALL ISVST ( ICHAN )            
                            .                           
                            .                           


    ISWESP

             This routine is used to switch terminal control to an
        existing subprocess.  The calling sequence is as follows:

                   CALL ISWESP ( ISPN,0,0,0,IRET [ ,IERR ] )

        where:  ISPN    indicates the subprocess number and is analogous
                        to the digit typed after CTRL-W when manually


        TSXLIB V6.2                                              PAGE 63
        Routine Descriptions


                        switching between subprocesses.  The value must
                        be in the range of zero to MAXSEC, a TSGEN
                        parameter.

                IRET    if ISPN is too large, the TSGEN parameter,
                        MAXSEC, is returned.

                IERR    is negative or one of the following:

                        1   the job does not have SUBPROCESS (IPRIV
                            2/11) privilege.

                        2   the specified subprocess number is too
                            large.

                        6   the specified subprocess has not been
                            initiated.


    ITCRTN

             This routine is used to trigger a completion routine from
        within an interrupt service routine.  The calling sequence is as
        follows:

                     CALL ITCRTN ( CPLRTN , IPRI , ID , 0 )

        where:  CPLRTN  is the six ASCII character name of the
                        completion routine.

                IPRI    is the execution priority for the completion
                        routine in the range of zero to seven.

                ID      is an integer value passed to the completion
                        routine.

             The service routine that calls this ITCRTN must have been
        connected to an interrupt vector by executing the ICNRTN
        routine.  The "0" argument is required.

             The following example declares the completion routine as an
        external and then triggers its execution.

                      EXTERNAL CPLRTN                     
                      CALL ITCRTN ( CPLRTN,IPRI,ID,IZERO )
                          .                               
                          .                               


    ITRCTL

             This routine is used to perform all of the terminal control
        functions that can be performed using the "lead-in" character
        method.  The calling sequence is as follows:



        TSXLIB V6.2                                              PAGE 64
        Routine Descriptions


                          CALL ITRCTL ( IFUN , IARG )

        where:  IFUN    is an integer value that corresponds to the
                        ASCII code for the desired function in the
                        ranges of 65 through 70 (A-F) and 72 through 90
                        (H-Z).

                IARG    is zero or an integer value as required by some
                        functions.

             The following example declares the slash character (/) to
        be an activation character.

                        DATA IFUN,IARG /"000104,"000057/
                            .                           
                            .                           
                        CALL ITRCTL ( IFUN,IARG )       
                            .                           
                            .                           


    ITRERR

             This routine is used to determine if any terminal input
        errors have occurred.  The calling sequences are as follows:

                              CALL ITRERR ( IERR )
                                       or
                                IERR = ITRERR ()

        where:  IERR    is one of the following:

                        0   no errors have occurred.

                        1   an input error has occurred.

             The following example checks for terminal input errors and
        aborts the program if one has occurred.

                                .                  
                                .                  
                            IERR = ITRERR ()       
                            IF ( IERR .NE. 0 ) STOP
                                .                  
                                .                  


    ITRTYP

             This routine is used to determine the terminal type being
        used on the time sharing line.  The calling sequences are as
        follows:

                              CALL ITRTYP ( IRET )
                                       or


        TSXLIB V6.2                                              PAGE 65
        Routine Descriptions


                                IRET = ITRTYP ()

        where:  IRET    is one of the following:

                        0   terminal type unknown.

                        1   VT52.

                        2   VT100.

                        3   Hazeltine.

                        4   ADM3A.

                        5   LA36.

                        6   LA120.

                        7   Diablo and Qume.

                        9   VT200.


    ITRYSP

             This routine is used to try to initialize a subprocess.
        The calling sequence is as follows:

             CALL ISWESP ( ISPN,IRPN,INITO,CMDFIL,IRET [ ,IERR ] )

        where:  ISPN    indicates the subprocess number and is analogous
                        to the digit typed after CTRL-W when manually
                        switching between subprocesses.  The value must
                        be in the range of zero to MAXSEC, a TSGEN
                        parameter.

                IRPN    indicates which process to return to when the
                        process initiated by this routine terminates as
                        follows:

                        0   specifies return to the primary process.

                        1   specifies return to the process which is
                            executing this routine to initiate the
                            subprocess.

                INITO   controls whether the terminal connection is
                        switched to the subprocess as shown below:

                        0   the subprocess is initiated (if it has not
                            already been initiated) and terminal control
                            is switched to the subprocess.

                        1   the subprocess is initiated but terminal
                            control remains with the current process.


        TSXLIB V6.2                                              PAGE 66
        Routine Descriptions


                CMDFIL  is the name of the string variable containing
                        the file specification of a command file to be
                        executed when the subprocess is initiated.  This
                        command file executes without start-up privilege
                        following any other start-up command file
                        specified with the SET SUBPROCESS/FILE command.
                        If the variable is empty, no command file is
                        executed.

                IRET    if ISPN is too large, the TSGEN parameter,
                        MAXSEC, is returned.

                IERR    is negative or one of the following:

                        1   the job does not have SUBPROCESS (IPRIV
                            2/11) privilege.

                        2   the specified subprocess number is too
                            large.

                        3   all of the job's subprocesses are already
                            active.

                        4   there is insufficient memory available for
                            the subprocess.

                        5   the specified subprocess has already been
                            initiated.


    ITSLIC

             This routine is used to determine the TSX-Plus license
        number.  The calling sequences are as follows:

                              CALL ITSLIC ( IRET )
                                       or
                                IRET = ITSLIC ()

        where:  IRET    is the requested TSX-Plus license number.


    ITSLIN

             This routine is used to determine the TSX-Plus time sharing
        line number to which the job is attached.  The calling sequences
        are as follows:

                              CALL ITSLIN ( IRET )
                                       or
                                IRET = ITSLIN ()

        where:  IRET    is zero if RT-11 is running or the requested
                        line number if TSX-Plus is running.



        TSXLIB V6.2                                              PAGE 67
        Routine Descriptions


             The following example aborts if RT-11 is running or
        continues if TSX-Plus is running.

                            IRET = ITSLIN ()       
                            IF ( IRET .EQ. 0 ) STOP
                                .                  
                                .                  


    IUALBK

             This routine is used to unlock all locked blocks in a
        shared file.  The calling sequences are as follows:

                        CALL IUALBK ( ICHAN [ ,IERR ] )
                                       or
                            IERR = IUALBK ( ICHAN )

        where:  ICHAN   is the I/O channel number that is open to a
                        shared file.

                IERR    is negative or one of the following:

                        0   the job does not have RLOCK privilege (IPRIV
                            2/9).

                        1   this channel is not open to a shared file.

             When this routine is executed all blocks previously locked
        by the user on the shared file are unlocked.  Blocks locked by
        the user on other files are not released nor are blocks of the
        same file that are locked by other users.

             The following example first opens a file, declares it to be
        shared, locks some blocks, and then unlocks the blocks.  The
        program is stopped if the error condition is returned.

                         CALL ASSIGN ( 40,'DK:FILE.DAT' )
                         ICHAN = ILUN ( 40 )             
                         CALL IDCLSF ( ICHAN,1 )         
                         DO 10 IBLK = 4,6                
                             CALL LKBLKW ( ICHAN,IBLK )  
                      10 CONTINUE                        
                             .                           
                             .                           
                         IERR = IUALBK ( ICHAN )         
                         IF ( IERR .NE. 0 ) STOP         
                             .                           
                             .                           


    IUNLKM

             This routine is used to unlock a job from memory.  The
        calling sequences are as follows:


        TSXLIB V6.2                                              PAGE 68
        Routine Descriptions


                                  CALL IUNLKM

             The PSWAPM privilege (IPRIV 1/7) is required to execute
        this routine.

             The following example first locks itself into memory and
        then unlocks itself.

                                  CALL LKANMY
                                      .      
                                      .      
                                  CALL IUNLKM
                                      .      
                                      .      


    IUSPBK

             This routine is used to unlock a specific locked block in a
        shared file.  The calling sequences are as follows:

                     CALL IUSPBK ( ICHAN,IBLOCK [ ,IERR ] )
                                       or
                         IERR = IUSPBK ( ICHAN,IBLOCK )

        where:  ICHAN   is the I/O channel number that is open to the
                        shared file.

                IBLOCK  is the number of the block to be unlocked.

                IERR    is negative or one of the following:

                        0   the job does not have RLOCK privilege (IPRIV
                            2/9) or shared file support is not available
                            on the system.

                        1   the channel is not open to a shared file.

             The following example opens a file, declares the file to be
        shared, locks all blocks in the file and then unlocks a specific
        block in the file.  The program is stopped if an error condition
        is returned.

                       CALL ASSIGN ( 30,'DL0:THAT.DAT' )
                       ICHAN = ILUN ( 30 )              
                       CALL IDCLSF ( ICHAN,2 )          
                       CALL LKBLKW ( ICHAN,-1 )         
                       IERR = IUSPBK ( ICHAN,7 )        
                       IF ( IERR .NE. 0 ) STOP          
                           .                            
                           .                            


        TSXLIB V6.2                                              PAGE 69
        Routine Descriptions


    IYELL

             This routine is used to override the SET TT GAG command.
        The calling sequences are as follows:

                     CALL IYELL ( LINUM,MSGBUF [ ,IERR ] )
                                       or
                         IERR = IYELL ( LINUM,MSGBUF )

        where:  LINUM   is the line number of the terminal to which the
                        message is to be sent.

                MSGBUF  is the name of the buffer that contains the
                        message.

                IERR    is negative or the following:

                        0   the job does not have SEND (IPRIV 1/5)
                            privilege.

             The job calling this routine must have SEND (IPRIV 1/5)
        privilege.  If the job calling this routine does not also have
        OPER (IPRIV 1/8) privilege, the GAG-override is ignored and the
        routine operates the same as the TRMMSG routine.

             The following example aborts if the job does not have SEND
        privilege.

                             .                        
                             .                        
                         IERR = IYELL ( LINUM,MSGBUF )
                         IF ( IERR .EQ. O ) STOP      
                             .                        
                             .                        


    JOBPRI

             This routine is used to get the priority for a job.  The
        calling sequence is as follows:

                      CALL JOBPRI ( LINUM,IPRI [ ,IERR ] )

        where:  LINUM   is the number if the line whose job priority is
                        to be returned.

                IPRI    is the name of a two-element array, the first
                        element of which will receive the job's priority
                        value in the range of 0 to 127.

                IERR    is negative or one of the following:

                        0   the line is not currently logged on.

                        1   an invalid line number was specified.


        TSXLIB V6.2                                              PAGE 70
        Routine Descriptions


             The following example aborts if either error condition
        prevails.

                            .                          
                            .                          
                        DIMENSION IPRI(2)              
                        CALL JOBPRI ( LINUM,IPRI,IERR )
                        IF ( IERR .GE. 0 ) STOP        
                            .                          
                            .                          


    KLDTJB

             This routine is used to abort a detached job.  The calling
        sequences are as follows:

                        CALL KLDTJB ( JOBNUM [ ,IERR ] )
                                       or
                            IERR = KLDTJB ( JOBNUM )

        where:  JOBNUM  is the job number of the detached job.

                IERR    is negative or the following:

                        1   invalid job number.

             The DETACH privilege (IPRIV 1/12) is required to execute
        this routine.

             The following example first starts a detached job and then
        later kills the detached job.  If an error condition is returned
        the program is halted.

                         CALL STDTJB ( JOBNAM,JOBNUM )
                             .                        
                             .                        
                         CALL KLDTJB ( JOBNUM,IERR )  
                         IF ( IERR .EQ. 1 ) STOP      
                             .                        
                             .                        


    LKANMY

             This routine is used to lock a job into any memory.  It
        causes the job to become locked into the memory space it is
        occupying when this routine is executed.  This routine executes
        extremely fast as compared to the routine, LKLOMY, described
        later.

                              CALL LKANMY [ IERR ]
                                       or
                                IERR = LKANMY ()



        TSXLIB V6.2                                              PAGE 71
        Routine Descriptions


        where:  IERR    is negative or the following:

                        0   job does not have PSWAPM privilege (IPRIV
                            1/7).

             The job remains locked until the program exits or the
        routine, IUNLKM, is executed.

             The following example locks the job into the memory space
        that it currently occupies.  The program terminates if the error
        condition is returned.

                            IERR = LKANMY ()       
                            IF ( IERR .EQ. 0 ) STOP
                                .                  
                                .                  


    LKBLK

             This routine is used to try to lock a specific block in a
        shared file.  If the requested block is not available the
        routine returns immediately with an error code.  If the block is
        available it is locked for the requesting user and no error is
        reported.  The calling sequences are as follows:

                     CALL LKBLK ( ICHAN,IBLOCK [ ,IERR ] )
                                       or
                            IERR = ( ICHAN,IBLOCK )

        where:  ICHAN   is the I/O channel number open to the shared
                        file.

                IBLOCK  is the number of the block to be locked.

                IERR    is negative or one of the following:

                        0   job does not have RLOCK privilege (IPRIV
                            2/9) or system does not include shared file
                            support.

                        1   this channel is not open to a shared file.

                        2   request is to lock too many blocks in the
                            file.

                        3   the requested block is locked by another
                            user.

             The following example opens a file, declares the file to be
        shared and tries to lock a block in the file.  If the block is
        already locked the program loops back for another try and if an
        error condition is returned the program halts.

                         CALL ASSIGN ( 40,'DY1:JUNK.DAT' )


        TSXLIB V6.2                                              PAGE 72
        Routine Descriptions


                         ICHAN = ILUN ( 40 )              
                         CALL IDCLSF ( ICHAN,2 )          
                      10 CONTINUE                         
                         IERR = LKBLK ( ICHAN,3 )         
                         IF ( IERR .EQ. 3 ) GO TO 10      
                         IF ( IERR .NE. 0 ) STOP          
                             .                            
                             .                            


    LKBLKW

             This routine is used to wait for a specific block to lock
        in a shared file.  If the requested block is locked by another
        job, the requesting job will be suspended until the desired
        block becomes available.  The calling sequences are as follows:

                     CALL LKBLKW ( ICHAN,IBLOCK [ ,IERR ] )
                                       or
                         IERR = LKBLKW ( ICHAN,IBLOCK )

        where:  ICHAN   is the I/O channel number open to the shared
                        file.

                IBLOCK  is the number of the block to be locked.

                IERR    is negative or one of the following:

                        0   job does not have RLOCK privilege (IPRIV
                            2/9) or system does not include shared file
                            support.

                        1   this channel is not open to a shared file.

                        2   request is to lock too many blocks in the
                            file.

             Other blocks in the file which were previously locked
        remain locked.  A block number of minus one can be used to
        request that all blocks in the file be locked.  If several users
        request the same block, access will be granted sequentially in
        the order that the requests are received.

             The following example opens a file, declares the file to be
        shared, and locks all of the blocks in the file.  If an error
        condition is returned the program stops.

                        CALL ASSIGN ( 40,'DK:FILE.DAT' )
                        ICHAN = ILUN ( 40 )             
                        CALL IDCLSF = ( ICHAN,0 )       
                        IERR = LKBLKW ( ICHAN,-1 )      
                        IF ( IERR .NE. 0 ) STOP         
                            .                           
                            .                           


        TSXLIB V6.2                                              PAGE 73
        Routine Descriptions


    LKLOMY

             This routine is used to lock a job into low memory.  It
        causes the job to be relocated into low memory and then to
        become locked there.  This type of lock is relatively slow and
        should be done only if the job is to remain locked for a long
        period of time.  The calling sequences are as follows:

                              CALL LKLOMY [ IERR ]
                                       or
                                IERR = LKLOMY ()

        where:  IERR    is negative or the following:

                        0   job does not have PSWAPM privilege (IPRIV
                            1/7).

             The job remains locked in memory until the program
        terminates or until the routine, IUNLKM, is executed.

             The following example locks the job into low memory
        aborting if the error condition is returned.

                            IERR = LKLOMY ()        
                            IF ( IERR .EQ. 0 ) STOP 
                                .                   
                                .                   


    MAPRNT

             This routine is used to map a shareable run time system
        into a job's region.  The run time system must first be
        associated with the job by executing the IASRNT routine
        described earlier.  The calling sequences are as follows:

                  CALL MAPRNT ( IPAR,IOFFST,MAPSIZ [ ,IERR ] )
                                       or
                      IERR = MAPRNT ( IPAR,IOFFST,MAPSIZ )

        where:  IPAR    is a number in the range of zero to seven that
                        indicates the job's page address register (PAR)
                        that is to be used to access the run time
                        system.  The PAR number selects the region of
                        virtual memory in the job that will be mapped to
                        the run time system.  The following
                        correspondence exists between PAR numbers and
                        virtual octal address regions within the job:

                                0  000000 - 017777

                                1  020000 - 037777

                                2  040000 - 057777



        TSXLIB V6.2                                              PAGE 74
        Routine Descriptions


                                3  060000 - 077777

                                4  100000 - 117777

                                5  120000 - 137777

                                6  140000 - 157777

                                7  160000 - 177777

                IOFFST  specifies which portion of the run time system
                        is to be mapped into the PAR region.  It
                        specifies the number of the 64-byte block within
                        the run time system where mapping is to begin.
                        This makes it possible to access different
                        sections of a run time system at different times
                        or through different regions.

                MAPSIZ  is the number of 64-byte blocks to be mapped.
                        If this value is larger than can be contained
                        within a single PAR region, multiple PAR regions
                        are automatically mapped as necessary to contain
                        the entire specified section of the run time
                        system.

                IERR    is one of the following:

                        0   no error.

                        1   there is no run time system associated with
                            this job.

             This routine affects the mapping of only the PAR region
        specified in IPAR and following PARs if the size so requires.
        It does not affect the mapping of any other PAR regions that may
        previously have been mapped to a run time system.  Thus, a job
        may have different PAR regions mapped to different sections of
        the same run time system or to different run time systems.  Real
        time programs may map PAR region number seven to the I/O page
        and map other PAR regions to shared run time systems.

             The memory size of a job is not affected by the use of the
        this routine.  Mapping a portion of a job's virtual address
        space to a shared run time system neither increases nor
        decreases the size of memory occupied by the job.  If a job's
        size is such that a portion of its normal memory is under a PAR
        region that is mapped to a run time system, that section of its
        normal memory becomes inaccessible to the job as long as the run
        time system mapping is in effect but the memory contents are not
        lost and may be reaccessed by disassociating all run time
        systems from the job.

             Any of the PAR regions may be mapped to a run time system
        including PAR region number seven which is normally not
        accessible to a job.


        TSXLIB V6.2                                              PAGE 75
        Routine Descriptions


             The following example first uses the SYSLIB routine,
        IRAD50, to name the run time system, associates the run time
        system with the job, then maps a PAR region to a section of the
        run time system, and finally disassociates the run time system
        from the job.

                       DIMENSION IRNTIM ( 2 )           
                       CALL IRAD50 ( 6,'TSXLIB',IRNTIM )
                       CALL IASRNT ( IRNTIM )           
                       CALL MAPRNT ( 3,1,4 )            
                           .                            
                           .                            
                       CALL IASRNT ( 0 )                
                           .                            
                           .                            


    MEMPOS

             This routine is used to determine the position of a job in
        memory for a TSX-Plus line.  The calling sequence is as follows:

                      CALL MEMPOS ( LINUM,IPOS [ ,IERR ] )

        where:  LINUM   is the number of the line for which memory
                        position information is returned.

                IPOS    is the 512-word block number of the start of the
                        memory area allocated to the job.  This value
                        will be zero if the job is swapped out of
                        memory.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.


    MEMSET

             This routine is used to set the amount of memory that will
        be allocated for the job.  The calling sequences are as follows:

                         CALL MEMSET ( IARG [ ,IRET ] )
                                       or
                             IRET = MEMSET ( IARG )

        where:  IARG    is the top memory address requested.

                IRET    is the top memory address allocated.

             The size allocated to a job reverts to the size specified
        by the most recent MEMORY keyboard command when the job exits or
        chains.


        TSXLIB V6.2                                              PAGE 76
        Routine Descriptions


             The following example requests a top memory address of
        120000 (octal).  The program is halted if the allocation is less
        than the request.

                           DATA IARG/"120000/        
                           IRET = MEMSET ( IARG )    
                          IF ( IRET .LMT. IARG ) STOP
                               .                     
                               .                     


    MEMUSE

             This routine is used to return the amount of memory
        allocated to a TSX-Plus line.  The calling sequence is as
        follows:

                     CALL MEMUSE ( LINUM,MEMSIZ [ ,IERR ] )

        where:  LINUM   is the number of the line about which memory
                        allocation information is returned.

                MEMSIZ  is the amount of memory allocated to the line in
                        512-word blocks.

                IERR    is negative or one of the following:

                        0   line is not currently logged on.

                        2   invalid line number.


    MNTLD

             This routine is used to mount a logical device (LD).  The
        calling sequences are as follows:

               CALL MNTLD ( ICHAN,LDNUM,IROFLG,FILPTR [ ,IERR ] )
                                       or
                   IERR = MNTLD ( ICHAN,LDNUM,IROFLG,FILPTR )

        where:  ICHAN   is the number of the I/O channel which must be
                        closed (available) at the time that this routine
                        is called.

                LDMUM   is the LD unit number in the range of zero
                        through seven.

                IROFLG  is the read-only flag and is zero to allow both
                        reads and writes or one to allow reads only to
                        the LD.

                FILPTR  is a four word buffer containing the RAD50 value
                        for the dev:filnam.ext that is to be associated
                        with the LD.


        TSXLIB V6.2                                              PAGE 77
        Routine Descriptions


                IERR    is negative or one of the following:

                        0   the channel provided is already open.

                        1   an invalid LD unit number was specified.

                        2   LD support is not generated into this
                            TSX-Plus system.

                        3   the LD unit is already associated with a
                            file.

                        4   an invalid file specification was given.

                        5   invalid LD unit number nesting.

                        6   unable to open the specified file.

             The following example selects a channel number and aborts
        if either the channel number is greater than 15 or if the LD
        unit is already associated with a file.

                         .                                     
                         .                                     
                     ICHAN = 0                                 
                 100 CONTINUE                                  
                     ICHAN = ICHAN + 1                         
                     IF ( ICHAN .GT. 15) STOP                  
                     IERR = MNTLD ( ICHAN,LDNUM,IROFLG,FILPTR )
                     IF ( IERR .EQ. 0 ) GO TO 100              
                     IF ( IERR .EQ. 3 ) STOP                   
                         .                                     
                         .                                     


    MOUNT

             This routine is used to mount a file structured device for
        directory caching.  The effect of this routine is the same as
        the TSX-Plus MOUNT keyboard command.  The calling sequences are
        as follows:

                        CALL MOUNT ( IDVNAM [ ,IERR ] )
                                       or
                            IERR = MOUNT ( IDVNAM )

        where:  IDVNAM  is the RAD50 value of the device name.

                IERR    is one of the following:

                        0   no error.

                        1   no room left in the table of mounted
                            devices.



        TSXLIB V6.2                                              PAGE 78
        Routine Descriptions


             The following example uses the SYSLIB routine, IRAD50, to
        convert the ASCII device name, DY3, to its RAD50 value.  Then
        the file structured device is mounted.  The program is halted if
        an error condition is returned.

                         CALL IRAD50 ( 3,'DY3',IDVNAM )
                         IERR = MOUNT ( IDVNAM )       
                         IF ( IERR .EQ. 1 ) STOP       
                             .                         
                             .                         


    MPIOPS

             This routine is used to map the I/O page into the program
        space between the octal addresses of 160000 and 177777.  The
        calling sequences are as follows:

                            CALL MPIOPS ( [ IERR ] )
                                       or
                                 IERR = MPIOPS

        where:  IERR    is negative or the following:

                        0   the job does not have MEMMAP privilege
                            (IPRIV 1/10) or the system does not include
                            real time support.

             The mapping set up by this routine remains in effect until
        the routine, MPRMPS, is executed or the program terminates.


    MPRGN

             This routine is used to map a region of virtual memory to a
        specified region of physical memory.  The calling sequences are
        as follows:

               CALL MPRGN ( IPAR,IPAD,ISIZ,IACS,ICBF [ ,IERR ] )
                                       or
                   IERR = MPRGN ( IPAR,IPAD,ISIZ,IACS,ICBF )

        where:  IPAR    is one of the following Page Address Register
                        (PAR) numbers indicating the beginning of the
                        virtual region to be mapped:

                        PAR     Virtual Region

                        0       000000-017777

                        1       020000-037777

                        2       040000-057777

                        3       060000-077777


        TSXLIB V6.2                                              PAGE 79
        Routine Descriptions


                        4       100000-177777

                        5       120000-137777

                        6       140000-157777

                        7       160000-177777

                IPAD    is the physical address divided by 100 (octal)
                        to which the virtual address is to be mapped.

                ISIZ    is the number of 100-byte (octal) pages to be
                        mapped.  If zero all PAR mapping is restored to
                        normal.

                IACS    indicates the read/write access of the mapped
                        region as follows:

                        0   read only.

                        1   read and write.

                ICBF    is a cache bypass flag and may have either of
                        the following values:

                        0   cache is enabled.

                        1   cache is disabled.

                IERR    is negative or the following:

                        0   real time support is not available or this
                            job does not have MEMMAP privilege (IPRIV
                            1/10).


    MPRMPS

             This routine is used to map a simulated RMON into the
        program space between the octal addresses of 160000 and 177777.
        The calling sequences are as follows:

                            CALL MPRMPS ( [ IERR ] )
                                       or
                                 IERR = MPRMPS

        where:  IERR    is negative or the following:

                        0   the job does not have MEMMAP privilege
                            (IPRIV 1/10) or the system does not include
                            real time support.


        TSXLIB V6.2                                              PAGE 80
        Routine Descriptions


    MSGREQ

             This routine is used to post a read request for a TSX-Plus
        interjob message.  The calling sequences are as follows:

                CALL MSGREQ ( CHNL,BUFR,ISIZ,CPLRTN [ ,IERR ] )
                                       or
                    IERR = MSGREQ ( CNLI,BUFR,ISIZ,CPLRTN )

        where:  CHNL    is the name of the string array containing the
                        six character name of the message channel.

                BUFR    is the name of the string array that is to
                        receive the message.

                ISIZ    is the length of the message buffer.

                CPLRTN  is the name of the completion routine to be
                        entered when the message is received.

                IERR    is negative or as follows:

                        0   job does not have MESSAGE privilege (IPRIV
                            2/10) or system does not have message
                            channel support.

                        1   all message channels are busy.

                        4   message was longer than the receiving
                            buffer.

                        5   the maximum allowed number of requests are
                            active.

             On entry to the completion routine, processor register R0
        contains the number of bytes in the message that was received,
        and R1 contains the number of the job that sent the message.
        The GETREG routine may be used to recover the values stored in
        R0 and R1.  Another call to this routine may be made from within
        the completion routine if it is desired to receive additional
        messages.

             The SUSPND and RESUME SYSLIB calls may be used with this
        facility if the program reaches a point where it must suspend
        its execution until a message arrives.

             The following sample program aborts if an error condition
        is returned after attempting to post a read request for a
        message.  It later issues a SUSPND call.  The associated
        completion routine must issue a RESUME call after processing the
        message.

                    LOGICAL*1 CHNL(6),BUFR(75)             
                    DATA ISIZ /75/                         
                    EXTERNAL CPLRTN                        


        TSXLIB V6.2                                              PAGE 81
        Routine Descriptions


                    CALL SCOPY ( 'CHNL04',CHNL,6 )         
                        .                                  
                        .                                  
                    IERR = MSGREQ ( CHNL,BUFR,ISIZ,CPLRTN )
                    IF ( IERR .GT. 0 ) STOP                
                        .                                  
                        .                                  
                    CALL SUSPND                            
                        .                                  
                        .                                  


    MSGSND

             This routine is used to queue up a message to another job
        on a named channel.  If other messages are already pending on
        the channel, the new message is added to the end of the list of
        waiting messages.  The sending program continues execution and
        does not wait for the message to be accepted by a receiving
        program.  During processing the message is copied to an internal
        buffer, and the sending program is free to destroy its message
        on return from this routine.  The calling sequences are as
        follows:

                 CALL MSGSND ( ICHNAM,MSGBUF,MSGSIZ [ ,IERR ] )
                                       or
                     IERR = MSGSND ( ICHNAM,MSGBUF,MSGSIZ )

        where:  ICHNAM  is the six ASCII character name of the message
                        channel.

                MSGBUF  is the name of the string array containing the
                        message.

                MSGSIZ  is the length of the message in characters.

                IERR    is negative or one of the following:

                        0   job does not have MESSAGE privilege (IPRIV
                            2/10) or the system does not include message
                            channel support.

                        1   all message channels are busy.

                        2   the maximum allowed number of messages are
                            being held in the message queues.

                        4   the transmitted message was too long and was
                            truncated to the maximum allowed length.

                        5   maximum number of message requests are
                            already pending.

             The following example uses the SYSLIB routine, SCOPY, to
        load the string variables, MSGBUF and ICHNAM, then sends a


        TSXLIB V6.2                                              PAGE 82
        Routine Descriptions


        message to the named channel, JUNK.  The program aborts if an
        error condition is returned.

                    LOGICAL*1 MSGBUF ( 14 )                
                    LOGICAL*1 ICHNAM ( 8 )                 
                    CALL SCOPY ( ' HELLO THERE',MSGBUF,12 )
                    CALL SCOPY ( 'JUNK  ',ICHNAM,6 )       
                    IERR = MSGSND ( ICHNAM,MSGBUF,12 )     
                    IF ( IERR .NE. 0 ) STOP                
                        .                                  
                        .                                  


    NONINT

             This routine is used to schedule the running job as either
        an interactive job or as a non-interactive job.  The calling
        sequence is as follows:

                              CALL NONINT ( MODE )

        where:  MODE    is either one of the following two values:

                        0   causes the job to be scheduled as
                            non-interactive.

                        1   causes the job to be scheduled as
                            interactive.

             Programs that do a large amount of terminal input, but that
        are not truly interactive jobs in the usual sense, such as file
        transfer programs, should use this routine to avoid excessive
        interference with normal interactive time sharing jobs.

             The following example first schedules the job to be
        non-interactive and then interactive.

                              MODE = 0            
                              CALL NONINT ( MODE )
                                  .               
                                  .               
                              MODE = 1            
                              CALL NONINT ( MODE )
                                  .               
                                  .               


    RCVMSG

             This routine is used to receive a message from a named
        channel if a message is pending on the channel.  If no message
        is pending, an error code is returned, and the calling program
        is allowed to continue execution.  The calling sequence is as
        follows:



        TSXLIB V6.2                                              PAGE 83
        Routine Descriptions


             CALL RCVMSG ( ICHNAM,MSGBUF,IBUFSZ,MSGSIZ [ ,IERR ] )

        where:  ICHNAM  is the six ASCII character name of the message
                        channel.

                MSGBUF  is the name of the receiving string array.

                IBUFSZ  is the length of the receiving buffer in
                        characters.

                MSGSIZ  is the length of the received message in
                        characters.

                IERR    is negative or one of the following:

                        0   job does not have MESSAGE privilege (IPRIV
                            2/10) or the system does not include message
                            channel support.

                        1   all message channels are busy.

                        3   no message was queued on the named channel.

                        4   the message was longer than the receiving
                            buffer.

                        5   maximum number of message requests are
                            pending.

             The following example sets up using the SYSLIB routine,
        SCOPY, to receive a message, and then attempts to receive a
        message on the named channel, JUNK.  The program is stopped if
        an error condition is returned.

                  LOGICAL*1 ICHNAM ( 8 )                     
                  LOGICAL*1 MSGBUF ( 72 )                    
                  CALL SCOPY ( 'JUNK  ',ICHNAM,6)            
                  CALL RCVMSG ( ICHNAM,MSGBUF,72,MSGSIZ,IERR)
                  IF ( IERR .NE. 0 ) STOP                    
                      .                                      
                      .                                      


    RCVMSW

             This routine is used to suspend the execution of a program
        until a message becomes available on a named channel.  The
        calling sequence is as follows:

             CALL RCVMSW ( ICHNAM,MSGBUF,IBUFSZ,MSGSIZ [ ,IERR ] )

        where:  ICHNAM  is the six ASCII character name of the message
                        channel.

                MSGBUF  is the name of the receiving string array.


        TSXLIB V6.2                                              PAGE 84
        Routine Descriptions


                IBUFSZ  is the length of the receiving array in
                        characters.

                MSGSIZ  is the length of the received message in
                        characters.

                IERR    is negative or one of the following:

                        0   job does not have MESSAGE privilege (IPRIV
                            2/10) or the system does not include message
                            channel support.

                        1   all message channels are busy.

                        4   the message was longer than the receiving
                            buffer.

                        5   maximum number of message requests pending.

             The following example uses the SYSLIB routine, SCOPY, to
        load the variable, ICHNAM, then waits for a message to arrive on
        the named channel.  The program is stopped if an error condition
        is returned.

                LOGICAL*1 MSGBUF ( 72 )                        
                LOGICAL*1 ICHNAM ( 8 )                         
                CALL SCOPY ( 'JUNK  ',ICHNAM,6 )               
                CALL RCVMSW ( ICHNAM,MSGBUF,IBUFSZ,MSGSIZ,IERR)
                IF ( IERR .NE. 0 ) STOP                        
                    .                                          
                    .                                          


    RLCTL

             This routine is used to allow a running program to
        relinquish exclusive control of the system after the program
        finishes performing some time-critical task.  The calling
        sequence is as follows:

                                   CALL RLCTL

             REALTIME privilege (IPRIV 1/6) is required to execute this
        routine.


    RSTODT

             This routine is used to reset or clear the ODT activation
        mode.  The calling sequence is as follows:

                                  CALL RSTODT


        TSXLIB V6.2                                              PAGE 85
        Routine Descriptions


    SETODT

             This routine is used to set the ODT activation mode.  The
        calling sequence is as follows:

                                  CALL SETODT

             In this mode TSX-Plus considers all characters to be
        activation characters except the digits, the comma, the dollar
        sign, and the semicolon.


    STDTJB

             This routine is used to start the execution of a detached
        job.  The calling sequence is as follows:

                    CALL STDTJB ( JOBNAM,JOBNUM [ ,IERR ] )

        where:  JOBNAM  is the ASCII string, dev:filnam.ext, terminated
                        by a null byte.

                JOBNUM  is the returned job number.

                IERR    is negative or the following:

                        1   no detached job line is available.

             The DETACH privilege (IPRIV 1/12) is required to execute
        this routine.

             If a free detached job line is available, the specified
        command file, JOBNAM, is initiated as a detached job and the
        number of the detached job is returned in the variable, JOBNUM.

             The following example uses the SYSLIB routine, SCOPY, to
        load the variable, JOBNAM, then initiates the detached job,
        DETJOB.COM, from device, DY2:, storing the job number in the
        variable, JOBNUM.  The program is terminated if an error
        condition is returned.

                    LOGICAL*1 JOBNAM ( 16 )                 
                    CALL SCOPY ( 'DY2:DETJOB.COM',JOBNAM,14)
                    CALL STDTJB ( JOBNAM,JOBNUM,IERR )      
                    IF ( IERR .EQ. 1 ) STOP                 
                        .                                   
                        .                                   


    STPRLV

             This routine is used to set the user mode processor
        priority level from a running program.  This may be used when it
        is necessary for a real time program to block interrupts for a
        short period of time while it is performing some time critical


        TSXLIB V6.2                                              PAGE 86
        Routine Descriptions


        operation.  The calling sequence is as follows:

                             CALL STPRLV ( IPRLVL )

        where:  IPRLVL  is the desired user mode processor priority
                        level in the range of zero through seven.

             REALTIME privilege (IPRIV 1/6) is required to execute this
        routine.  Interrupts should not be disabled for long periods of
        time or system clock interrupts and character input interrupts
        will be lost.  The following example raises the priority level
        to seven and later reduces it back to zero.

                               CALL STPRLV ( 7 )
                                   .            
                                   .            
                               CALL STPRLV ( 0 )
                                   .            
                                   .            


    STUNAM

             This routine is used to set the user name associated with
        the current job.  The calling sequences are as follows:

                       CALL STUNAM ( USRNAM [ , IERR ] )
                                       or
                            IERR = STUNAM ( USRNAM )

        where:  USRNAM  is the name of the twelve-character array that
                        contains the new user name ASCII string.

                IERR    is negative or as follows:

                        0   the job does not have SETNAME privilege
                            (IPRIV 1/4).

             The following example sets the user name to JOEBLOWHARD.

                      LOGICAL*1 USRNAM(14)               
                      CALL SCOPY ( 'JOEBLOWHARD',USRNAM )
                      IERR = STUNAM ( USRNAM )           
                      IF ( IERR .GE. 0 ) STOP            
                          .                              
                          .                              


    TERMPA

             This routine is used to conclude a performance analysis.
        It has the effect of returning into a user supplied buffer the
        results of the analysis and freeing the performance analysis
        feature for use by other users.  The calling sequence is as
        follows:


        TSXLIB V6.2                                              PAGE 87
        Routine Descriptions


                 CALL TERMPS ( IPARBF,IHSTBF,IHBSIZ [ ,IERR ] )

        where:  IPARBF  is the name of a four element parameter buffer
                        with the elements assigned as follows:

                        1   is the base address of the monitored region.

                        2   is the top address of the monitored region.

                        3   is the number of bytes per histogram cell.

                        4   is a control and status flag with bit
                            assignments as follows:

                            1       I/O wait time was included.

                            100000  at least one of the histogram cells
                                    overflowed.

                IHSTBF  is the name of the histogram buffer.

                IHBSIZ  is the number of elements or cells in the
                        histogram buffer.

                IERR    is negative or one of the following:

                        0   this job is not doing a performance
                            analysis.

                        1   area provided for the histogram count vector
                            is too small.

             The histogram data returned consists of a vector of 16-bit
        binary values, one value for each cell in the histogram.  The
        first value corresponds to the histogram cell that starts at the
        base address of the region that was monitored.

             The following example shows the complete performance
        analysis from initialization to termination.  The program is
        stopped if an error condition is returned on termination of the
        analysis.

                   DIMENSION IPARBF ( 4 )                   
                   DIMENSION IHSTBF ( 16 )                  
                   CALL INITPA ( "2000,"4000,"100,0 )       
                   CALL ISTPA                               
                       .                                    
                       .                                    
                   CALL ISPPA                               
                   CALL TERMPA ( IPARBF,IHSTBF,IHBSIZ,IERR )
                   IF ( IERR .GE. 0 ) STOP                  
                       .                                    
                       .                                    


        TSXLIB V6.2                                              PAGE 88
        Routine Descriptions


    TIMOUT

             This routine is used to set the time out value that is to
        be applied to the next terminal input operation.  The calling
        sequence is as follows:

                          CALL TIMOUT ( ITIME,IACTCH )

        where:  ITIME   is the time out value in 0.5 second units.

                IACTCH  is the value of the single character that is to
                        be returned as the last or activation character
                        of the field if a time out occurs.

             The value specified with this routine applies only to the
        next terminal input field.  The time value is reset when the
        next field is received from the terminal or the time out occurs.
        A new time out value must be specified for each input field that
        is to be time controlled.

             The following example uses a time out value of twenty
        seconds and specifies that a control-X is to be returned if the
        timeout occurs.

                                 .                
                                 .                
                             CALL TIMOUT ( 40,24 )
                                 .                
                                 .                


    TKCTL

             This routine is used to allow a running program to gain
        exclusive access to the system to perform some time-critical
        task.  The calling sequence is as follows:

                                   CALL TKCTL

             The effect of this routine is to cause the TSX-Plus job
        scheduler to ignore all other jobs during the interval that the
        calling program has exclusive control of the system.  REALTIME
        privilege (IPRIV 1/6) is required to execute this routine.

             Exclusive access is relinquished when the calling program
        calls RLCTL, terminates, or aborts.  Exclusive access is
        retained if the calling program chains to another program.


    TRMIN

             This routine is used to accept a string of characters from
        the terminal.  The calling sequence is as follows:

                 CALL TRMIN ( ICHBUF,IBFSIZ,ICOUNT [ ,IERR ] )


        TSXLIB V6.2                                              PAGE 89
        Routine Descriptions


        where:  ICHBUF  is the name of the buffer that is to receive the
                        string.

                IBFSIZ  is the length of the receiving buffer in
                        characters.

                ICOUNT  is the number of characters actually received.

                IERR    is one of the following:

                        0   no error.

                        1   the specified buffer overflowed.

             This routine causes a program to wait until an activation
        character is entered on the terminal and then returns all
        characters received up to and including the last activation
        character.  This routine is substancially more efficient than
        doing a series of the SYSLIB routin= ITTINR.  It is particularly
        well suited for accepting input from page buffered terminals.

             The following example accepts a string of characters from
        the terminal.  The program is halted if the error condition is
        returned.

                      LOGICAL*1 ICHBUF ( 24 )             
                      CALL TRMIN ( ICHBUF,24,ICOUNT,IERR )
                      IF ( IERR .EQ. 1 ) STOP             
                          .                               
                          .                               


    TRMMSG

             This routine is used to send a message to another line's
        terminal.  The calling sequences are as follows:

                     CALL TRMMSG ( ILINE,IMSGBF [ ,IERR ] )
                                       or
                         IERR = TRMMSG ( ILINE,IMSGBF )

        where:  ILINE   is the line number of the terminal that the
                        message is to be sent.

                IMSGBF  is the name of the buffer that contains the
                        message.

                IERR    is negative or one of the following:

                        0   job does not have SEND privilege (IPRIV
                            1/5).

                        1   receiving line is SET TT GAG.

             The message must be terminated with a null character.


        TSXLIB V6.2                                              PAGE 90
        Routine Descriptions


             The following example sends a message to the terminal
        connected to line 14.  If the job does not have SEND privilege,
        the program aborts.  If the receiving line is SET TT GAG, the
        program loops until the condition changes to NOGAG.

                  LOGICAL*1 IMSGBF ( 30 )                        
                  CALL SCOPY ( ' THIS IS THE MESSAGE',IMSGBF,20 )
              100 CONTINUE                                       
                  CALL TRMMSG ( 14,IMSGBF,IERR )                 
                  IF ( IERR .EQ. 0 ) STOP                        
                  IF ( IERR .EQ. 1 ) GO TO 100                   
                      .                                          
                      .                                          


    TRMOUT

             This routine is used to send a string of characters to the
        terminal.  The calling sequence is as follows:

                         CALL TRMOUT ( ICHSTR,ICOUNT )

        where:  ICHSTR  is the name of the buffer containing the string
                        of characters.

                ICOUNT  is the number of characters in the string.

             This routine is much more efficient to use than a series of
        the SYSLIB routine, ITTOUR.  It has the same efficiency as the
        SYSLIB routine, PRINT, but it uses a count of the number of
        characters to send instead of having the string terminated with
        a null character.

             The following example sends a string of characters to the
        terminal.

                 LOGICAL*1 ICHSTR ( 22 )                       
                 CALL SCOPY ( ' THIS IS THE STRING.'ICHSTR,20 )
                 CALL TRMOUT ( ICHSTR,20 )                     
                     .                                         
                     .                                         


    TTCRTN

             This routine is used to establish a completion routine
        which will be executed as each input character is received from
        the terminal.  The calling sequence is as follows:

                             CALL TTCRTN ( CPLRTN )

        where:  CPLRTN  is the name of the completion routine that is to
                        be entered for each input character.

             On entry to the completion routine, the received character


        TSXLIB V6.2                                              PAGE 91
        Routine Descriptions


        is in R0.  The EMT to connect the completion routine must be
        reexecuted each time a character is received.  This should be
        done at the end of the completion routine after processing the
        last received character.  The program should be running with
        single character activation and with bit 12 set in the job
        status word.

             The following example sets up for and calls a terminal
        input completion routine.  A skeleton of the completion routine
        is also given.

                           EXTERNAL CPLRTN          
                           CALL IPOKE ( "10000,"44 )
                           CALL TTCRTN ( CPLRTN )   
                               .                    
                               .                    

                           SUBROUTINE CPLRTN        
                               .                    
                               .                    
                           CALL TTCRTN ( CPLRTN )   
                           RETURN                   


        TSXLIB V6.2                                              PAGE 92
        Building the Library






                            4.  Building the Library


             The sources for the TSX-Plus Library consist of the
        MACRO-11 modules listed in Table 4-1.  The process of
        constructing the library file, TSXLIB.OBJ, is the same when
        accomplished under either RT-11 or under TSX-Plus.


                Module  Content

                CLLINE  Communication line support.
                DETJBS  Detached job support.
                DVALOC  Device allocating and deallocating.
                JBPRIV  Job priveleges control.
                JBSTMN  Job status monitoring.
                MNTDEV  Device mounting and dismounting.
                MSGCOM  Interjob message communication.
                PRFANL  Performance analysis support.
                RELTIM  Real time program support.
                RUNTIM  Shared run time system support.
                SHRFIL  Shared file system support.
                SPOLER  Spooler support.
                SUBPRO  Subprocess control.
                SYSTAT  System status information.
                TRMCOM  Terminal communication.
                TRMCTL  Terminal control.
                TSFILS  Special file information.
                TSLBID  TSXLIB identification.
                TSXMSC  Miscellaneous EMTs.
                TSXODT  ODT activation mode support.
                USRNAM  User name support.
                WINDOW  Windowing support.

                        TSXLIB MACRO-11 source modules.
                                   Table 4-1.


             First the MACRO-11 modules are assembled as follows:

                                 .RUN SY:MACRO 
                                 *CLLINE=CLLINE
                                 *DETJBS=DETJBS
                                 *JBPRIV=JBPRIV
                                 *JBSTMN=JBSTMN
                                 *MNTDEV=MNTDEV
                                 *MSGCOM=MSGCOM
                                 *PRFANL=PRFANL
                                 *RELTIM=RELTIM
                                 *RUNTIM=RUNTIM
                                 *SHRFIL=SHRFIL


        TSXLIB V6.2                                              PAGE 93
        Building the Library


                                 *SPOLER=SPOLER
                                 *SUBPRO=SUBPRO
                                 *SYSTAT=SYSTAT
                                 *TRMCOM=TRMCOM
                                 *TRMCTL=TRMCTL
                                 *TSFILS=TSFILS
                                 *TSLBID=TSLBID
                                 *TSXMSC=TSXMSC
                                 *TSXODT=TSXODT
                                 *USRNAM=USRNAM
                                 *WINDOW=WINDOW
                                 *^C           

             Next the library file is constructed as follows:

                                .RUN SY:LIBR    
                                *TSXLIB=CLLINE//
                                *DETJBS         
                                *DVALOC         
                                *JBPRIV         
                                *JBSTMN         
                                *MNTDEV         
                                *MSGCOM         
                                *PRFANL         
                                *RELTIM         
                                *RUNTIM         
                                *SHRFIL         
                                *SPOLER         
                                *SUBPRO         
                                *SYSTAT         
                                *TRMCOM         
                                *TRMCTL         
                                *TSFILS         
                                *TSLBID         
                                *TSXMSC         
                                *TSXODT         
                                *USRNAM         
                                *WINDOW         
                                *//             
                                *^C             

             The command file, TSXLIB.COM, in the distribution kit will
        accomplish the construction of the library file, TSXLIB.OBJ.


        TSXLIB V6.2                                              PAGE 94
        References






                                   References


        1.  S & H Computer Systems, Inc., "TSX-Plus Reference Manual",
            Fifth Edition, First Printing, Nashville, TN, November 1985.

        2.  S & H Computer Systems, Inc., "TSX-Plus Version 6.0 Release
            Notes", Nashville, TN, November 1985.

        3.  Digital Equipment Corporation, "PDP-11 MACRO-11 Language
            Reference Manual", AA-V027A-TC, Maynard, MA, March 1983.

        4.  Digital Equipment Corporation, "RT-11 System User's Guide",
            AA-5279C-TC, Maynard, MA, March 1983.

        5.  Digital Equipment Corporation, "RT-11 Programmer's Reference
            Manual", AA-H378B-TC, Maynard, MA, March 1983.

        6.  Digital Equipment Corporation, "PDP-11 FORTRAN IV Language
            Reference Manual", AA-R953A-TK, Maynard, MA, March 1983.

        7.  Digital Equipment Corporation, "PDP-11 FORTRAN-77 Language
            Reference Manual", AA-V193A-TK, Maynard, MA, July 1983.

        8.  S & H Computer Systems, Inc., "TSX-Plus Version 6.2 Release
            Notes", Nashville, TN, January 1987.


        TSXLIB V6.2                                              PAGE 95
        Appendix A:  KWIK Index






                            Appendix A:  KWIK Index

             This appendix lists the TSXLIB routines in a key-word-in-
        context (KWIK) index.  It is meant to help the user to locate
        the particular routine that is needed.


         IHERR                       Enable abort on error.             
         ISERR                      Inhibit abort on error.             
         IFLINF     Obtain some information about file.                 
         TRMIN    from terminal.            Accept string of characters 
         IAQFLC   another job.              Acquire file context of     
         IACTCH           Check for pending activation characters.      
         RSTODT                Reset normal activation mode.            
         SETODT                     Set ODT activation mode.            
         CNVAPA   address.  Convert virtual address to physical         
         CNVAPA         address to physical address.     Convert virtual
         DSMNTA   devices.         Dismount all file structured         
         IUALBK                      Unlock all locked blocks.          
         IALOC                              Allocate device.            
         ICALOC   device.             Check allocation status of        
         MEMSET                  Set memory allocation.                 
         MEMUSE   job.            Determine amount of memory used by    
         INITPA             for performance analysis.         Initialize
         ISTPA            Start performance analysis.                   
         ISPPA             Stop performance analysis.                   
         TERMPA            from performance analysis.          Terminate
         GTUNAM   job.        Get user name associated with current     
         STUNAM   job.        Set user name associated with current     
         IDCLSF             Declare file to be shared.                  
         IPGNAM         Get name of program being run by job.           
         IBICIO   page.                     Bit clear value into I/O    
         IBISIO   page.                     Bit set value into I/O      
         LKBLKW                    Wait for block to lock.              
         LKBLK                  Try to lock block.                      
         IUSPBK             Unlock specific block.                      
         ISPBLK    Determine number of free blocks in spool file.       
         IUALBK           Unlock all locked blocks.                     
         BRKCTL                   Establish break sentinel control.     
         IBSTCH   change.                   Broadcast job status        
         ICNMCN   monitoring connection.    Cancell job status          
         IPRIV                   Determine, change privileges for job.  
         IBSTCH        Broadcast job status change.                     
         ITRCTL   functions.        Lead-in character terminal control  
         TRMIN             Accept string of characters from terminal.   
         TRMOUT              Send string of characters to terminal.     
         IACTCH      for pending activation characters.            Check
         ICALOC   device.                   Check allocation status of  
         IACTCH   activation characters.    Check for pending           
         ITRERR   errors.                   Check for terminal input    
         ICKWTS   file.                     Check for writes to shared  


        TSXLIB V6.2                                              PAGE 96
        Appendix A:  KWIK Index


         ILNSTS                             Check status of line.       
         ISTLD    logical device.           Check the status of a       
         ICNTSP            Control speed of CL line.                    
         IBICIO                         Bit clear value into I/O page.  
         IRDRCL   timesharing line.Redirect communication or            
         ITCRTN   routine.          Trigger completion from interrupt   
         ICNINT    Connect interrupt vector completion routine.         
         TTCRTN          Establish terminal completion routine.         
         ICNINT   completion routine.       Connect interrupt vector    
         ICNRTN   interrupt vector.         Connect service routine to  
         ICONTM                   Determine connect time for job.       
         ICNMCN       job status monitoring connection.          Cancell
         IESMCN       job status monitoring connection.        Establish
         IRLINT         an interrupt vector connection.          Release
         IPRWND                   Print the contents of a window.       
         IAQFLC                Acquire file context of another job.     
         ISPCTL   spooled file.             Control release time of     
         ICNTSP                             Control speed of CL line.   
         ITRCTL          character terminal control functions.   Lead-in
         RLCTL         Relinquish exclusive control of system.          
         TKCTL               Take exclusive control of system.          
         BRKCTL    Establish break sentinel control.                    
         CNVAPA   physical address.         Convert virtual address to  
         ICPUTM                         Get CPU time used by job.       
         ICRWND                             Create a window.            
         ISTFTM                         Set creation time of file.      
         ISTPRV                         Set current job priority value. 
         GTUNAM        name associated with current job.        Get user
         STUNAM        name associated with current job.        Set user
         IDALOC                             Deallocate device.          
         IDCLSF                             Declare file to be shared.  
         IDLWND                             Delete a window.            
         ISTDJ                Get status of detached job.               
         KLDTJB                        Kill detached job.               
         STDTJB                       Start detached job.               
         ITSLIC   number.                   Determine TSX-Plus license  
         ITSLIN   number.                   Determine TSX-Plus line     
         MEMUSE   used by job.              Determine amount of memory  
         ICONTM   job.                      Determine connect time for  
         ISPBLK   blocks in spool file.     Determine number of free    
         MEMPOS   in memory.                Determine position of job   
         ITRTYP                             Determine terminal type.    
         IPRIV    privileges for job.       Determine, change           
         IALOC                     Allocate device.                     
         ICALOC        allocation status of device.                Check
         ISTLD      the status of a logical device.                Check
         IDALOC                  Deallocate device.                     
         DISMNT           a file structured device.             Dismount
         IDMLD           Dismount a logical device.                     
         MNTLD              Mount a logical device.                     
         MOUNT        Mount file structured device.                     
         DSMNTA         all file structured devices.            Dismount
         IASRNT   time system and job.     [Dis]associate shared run    
         DISMNT   device.                   Dismount a file structured  
         IDMLD                              Dismount a logical device.  


        TSXLIB V6.2                                              PAGE 97
        Appendix A:  KWIK Index


         DSMNTA   structured devices.       Dismount all file           
         ILDTR               Lower a line's DTR status.                 
         IRDTR               Raise a line's DTR status.                 
         HIEFOF               Turn off high efficiency terminal mode.   
         HIEFON                Turn on high efficiency terminal mode.   
         IHERR                              Enable abort on error.      
         IHERR              Enable abort on error.                      
         ISERR             Inhibit abort on error.                      
         ITRERR    Check for terminal input errors.                     
         BRKCTL   control.                  Establish break sentinel    
         IESMCN   monitoring connection.    Establish job status        
         TTCRTN   completion routine.       Establish terminal          
         RLCTL    system.        Relinquish exclusive control of        
         TKCTL    system.              Take exclusive control of        
         IEXSTS                     Get job execution status.           
         INITSP              new, switch to existing subprocesInitialize
         ISWESP                Switch to an existing subprocess.        
         IAQFLC   job.              Acquire file context of another     
         DISMNT                  Dismount a file structured device.     
         MOUNT                        Mount file structured device.     
         DSMNTA                Dismount all file structured devices.    
         IDCLSF                     Declare file to be shared.          
         ICKWTS        for writes to shared file.                  Check
         ISPCTL     release time of spooled file.                Control
         ISPBLK     of free blocks in spool file.       Determine number
         IFLINF      some information about file.                 Obtain
         ISVST        Save status of shared file.                       
         ISTFTM        Set creation time of file.                       
         ISPBLK         Determine number of free blocks in spool file.  
         ITRCTL            terminal control functions. Lead-in character
         ICPUTM                             Get CPU time used by job.   
         IEXSTS                             Get job execution status.   
         IPGNAM   run by job.               Get name of program being   
         IPPNUM   number for job.           Get project, programmer     
         ISTDJ                              Get status of detached job. 
         GTJBNM                             Get the name for a job.     
         JOBPRI                             Get the priority for a job. 
         GTUNAM   with current job.         Get user name associated    
         GETREG   register.                 Get value stored processor  
         HIEFOF   mode.            Turn off high efficiency terminal    
         HIEFON   mode.             Turn on high efficiency terminal    
         MPIOPS   space.                Map I/O page into program       
         IBICIO        Bit clear value into I/O page.                   
         IBISIO          Bit set value into I/O page.                   
         IPEKIO            Peek at value in I/O page.                   
         IPOKIO             Poke value into I/O page.                   
         IFLINF                 Obtain some information about file.     
         ISERR                              Inhibit abort on error.     
         INITPA   analysis.                 Initialize for performance  
         INITSP   existing subprocess.      Initialize new, switch to   
         ITRYSP   subprocess.        Try to initialize a new            
         ITRERR          Check for terminal input errors.               
         ITCRTN     Trigger completion from interrupt routine.          
         ICNINT   routine.          Connect interrupt vector completion 
         IRLINT   connection.    Release an interrupt vector            


        TSXLIB V6.2                                              PAGE 98
        Appendix A:  KWIK Index


         ICNRTN          service routine to interrupt vector.    Connect
         IEXSTS                         Get job execution status.       
         IUNLKM                      Unlock job from memory.            
         MEMPOS       Determine position of job in memory.              
         LKANMY                        Lock job into any memory.        
         LKLOMY                        Lock job into low memory.        
         ISTPRV                 Set current job priority value.         
         MAPRNT        run time system into job region.       Map shared
         IBSTCH                   Broadcast job status change.          
         ICNMCN   connection.       Cancell job status monitoring       
         IESMCN   connection.     Establish job status monitoring       
         NONINT        Set [non]interactive job status.                 
         IAQFLC     file context of another job.                 Acquire
         MEMUSE    amount of memory used by job.               Determine
         ICONTM            connect time for job.               Determine
         IPRIV        change privileges for job.              Determine,
         ICPUTM        Get CPU time used by job.                        
         IPGNAM     of program being run by job.                Get name
         IPPNUM       programmer number for job.            Get project,
         ISTDJ       Get status of detached job.                        
         GTJBNM          Get the name for a job.                        
         JOBPRI      Get the priority for a job.                        
         GTUNAM     associated with current job.           Get user name
         KLDTJB               Kill detached job.                        
         MSGSND     Send message to another job.                        
         STUNAM     associated with current job.           Set user name
         STDTJB              Start detached job.                        
         RCVMSG        message from another job.          Try to receive
         RCVMSW    for message from another job.                    Wait
         IASRNT         run time system and job.   [Dis]associate shared
         KLDTJB                             Kill detached job.          
         ITRCTL   control functions.        Lead-in character terminal  
         STPRLV     mode processor priority level.              Set user
         ITSLIC          Determine TSX-Plus license number.             
         ITSLIN          Determine TSX-Plus line number.                
         ILDTR                      Lower a line's DTR status.          
         IRDTR                      Raise a line's DTR status.          
         IRXOFF                     Reset a line's XOFF status.         
         ILNSTS             Check status of line.                       
         ICNTSP         Control speed of CL line.                       
         IRDRCL              or timesharing line. Redirect communication
         LKANMY                             Lock job into any memory.   
         LKLOMY                             Lock job into low memory.   
         LKBLK                       Try to lock block.                 
         LKBLKW           Wait for block to lock.                       
         IUALBK                  Unlock all locked blocks.              
         ISTLD        Check the status of a logical device.             
         IDMLD                   Dismount a logical device.             
         MNTLD                      Mount a logical device.             
         LKLOMY               Lock job into low memory.                 
         ILDTR                              Lower a line's DTR status.  
         MPIOPS   space.                    Map I/O page into program   
         MAPRNT   into job region.          Map shared run time system  
         MPRMPS   program space.            Map simulated RMON into     
         MPRGN    to physical memory.       Map virtual memory region   


        TSXLIB V6.2                                              PAGE 99
        Appendix A:  KWIK Index


         MEMSET                         Set memory allocation.          
         MPRGN    memory.       Map virtual memory region to physical   
         MEMUSE         Determine amount of memory used by job.         
         MEMPOS          position of job in memory.            Determine
         LKANMY           Lock job into any memory.                     
         LKLOMY           Lock job into low memory.                     
         MPRGN           region to physical memory.   Map virtual memory
         IUNLKM             Unlock job from memory.                     
         RCVMSG              Try to receive message from another job.   
         RCVMSW                    Wait for message from another job.   
         MSGSND                        Send message to another job.     
         TRMMSG   terminal.            Send message to another          
         MSGREQ       Post read request for message.                    
         STPRLV   level.           Set user mode processor priority     
         RSTODT     Reset normal activation mode.                       
         SETODT          Set ODT activation mode.                       
         HIEFOF    high efficiency terminal mode.               Turn off
         HIEFON    high efficiency terminal mode.                Turn on
         ICNMCN          Cancell job status monitoring connection.      
         IESMCN        Establish job status monitoring connection.      
         MNTLD                              Mount a logical device.     
         MOUNT    device.                   Mount file structured       
         GTUNAM   current job.     Get user name associated with        
         STUNAM   current job.     Set user name associated with        
         GTJBNM                     Get the name for a job.             
         IPGNAM   by job.               Get name of program being run   
         ITRYSP         Try to initialize a new subprocess.             
         INITSP   subprocess.    Initialize new, switch to existing     
         NONINT                        Set [non]interactive job status. 
         RSTODT                       Reset normal activation mode.     
         IPPNUM     Get project, programmer number for job.             
         ISPBLK   spool file.     Determine number of free blocks in    
         ITSLIC            TSX-Plus license number.            Determine
         ITSLIN     Determine TSX-Plus line number.                     
         IFLINF   about file.               Obtain some information     
         SETODT                         Set ODT activation mode.        
         HIEFOF   terminal mode.       Turn off high efficiency         
         IYELL          Override the TT-GAG option.                     
         TIMOUT      Set terminal read time out value.                  
         IYELL                              Override the TT-GAG option. 
         MPIOPS                     Map I/O page into program space.    
         IBICIO    Bit clear value into I/O page.                       
         IBISIO      Bit set value into I/O page.                       
         IPEKIO        Peek at value in I/O page.                       
         IPOKIO         Poke value into I/O page.                       
         IPEKIO                             Peek at value in I/O page.  
         IACTCH   characters.     Check for pending activation          
         INITPA              Initialize for performance analysis.       
         ISTPA                        Start performance analysis.       
         ISPPA                         Stop performance analysis.       
         TERMPA              Terminate from performance analysis.       
         CNVAPA          virtual address to physical address.    Convert
         MPRGN     virtual memory region to physical memory.         Map
         IPOKIO                             Poke value into I/O page.   
         MEMPOS                   Determine position of job in memory.  


        TSXLIB V6.2                                             PAGE 100
        Appendix A:  KWIK Index


         MSGREQ   message.                  Post read request for       
         IPRWND   window.                   Print the contents of a     
         JOBPRI                     Get the priority for a job.         
         STPRLV     Set user mode processor priority level.             
         ISTPRV             Set current job priority value.             
         IPRIV            Determine, change privileges for job.         
         IRSWND               Resume window processing.                 
         ISPWND              Suspend window processing.                 
         STPRLV               Set user mode processor priority level.   
         GETREG            Get value stored processor register.         
         IPGNAM                 Get name of program being run by job.   
         MPIOPS           Map I/O page into program space.              
         MPRMPS     Map simulated RMON into program space.              
         IPPNUM                Get project, programmer number for job.  
         IPPNUM   for job.              Get project, programmer number  
         IRDTR                              Raise a line's DTR status.  
         MSGREQ                        Post read request for message.   
         TIMOUT                Set terminal read time out value.        
         RCVMSG   another job.       Try to receive message from        
         IRDRCL   timesharing line.         Redirect communication or   
         MPRGN           Map virtual memory region to physical memory.  
         MAPRNT    run time system into job region.           Map shared
         GETREG      value stored processor register.                Get
         IRLINT   connection.               Release an interrupt vector 
         ISPCTL   file.             Control release time of spooled     
         RLCTL    control of system.        Relinquish exclusive        
         MSGREQ                   Post read request for message.        
         IRXOFF                             Reset a line's XOFF status. 
         RSTODT   mode.                     Reset normal activation     
         IRSWND                             Resume window processing.   
         ISPY     simulated RMON.           Return values from within   
         MPRMPS               Map simulated RMON into program space.    
         ISPY         from within simulated RMON.          Return values
         ICNRTN   vector.   Connect service routine to interrupt        
         ICNINT           vector completion routine.   Connect interrupt
         TTCRTN         terminal completion routine.           Establish
         ITCRTN              from interrupt routine.  Trigger completion
         IPGNAM       name of program being run by job.              Get
         IASRNT       [Dis]associate shared run time system and job.    
         MAPRNT   region.        Map shared run time system into job    
         ISVST                              Save status of shared file. 
         ISLWND                             Select a window.            
         MSGSND   job.                      Send message to another     
         TRMMSG   terminal.                 Send message to another     
         TRMOUT   to terminal.              Send string of characters   
         BRKCTL             Establish break sentinel control.           
         ICNRTN   interrupt vector. Connect service routine to          
         SETODT                             Set ODT activation mode.    
         NONINT   status.                   Set [non]interactive job    
         ISTFTM                             Set creation time of file.  
         ISTPRV   value.                    Set current job priority    
         MEMSET                             Set memory allocation.      
         TIMOUT   value.                    Set terminal read time out  
         STPRLV   priority level.           Set user mode processor     
         STUNAM   with current job.         Set user name associated    


        TSXLIB V6.2                                             PAGE 101
        Appendix A:  KWIK Index


         IBISIO                         Bit set value into I/O page.    
         ICKWTS         Check for writes to shared file.                
         ISVST               Save status of shared file.                
         IASRNT   job.       [Dis]associate shared run time system and  
         MAPRNT   job region.           Map shared run time system into 
         IDCLSF          Declare file to be shared.                     
         MPRMPS   space.                Map simulated RMON into program 
         ISPY            values from within simulated RMON.       Return
         MPIOPS       I/O page into program space.                   Map
         MPRMPS           RMON into program space.         Map simulated
         IUSPBK                      Unlock specific block.             
         ICNTSP                     Control speed of CL line.           
         ISPBLK    number of free blocks in spool file.        Determine
         ISPCTL     Control release time of spooled file.               
         STDTJB                             Start detached job.         
         ISTPA                              Start performance analysis. 
         IBSTCH               Broadcast job status change.              
         ICNMCN   connection.   Cancell job status monitoring           
         IESMCN   connection. Establish job status monitoring           
         ISTLD                    Check the status of a logical device. 
         ISTDJ                          Get status of detached job.     
         ICALOC            Check allocation status of device.           
         ILNSTS                       Check status of line.             
         ISVST                         Save status of shared file.      
         IEXSTS           Get job execution status.                     
         ILDTR           Lower a line's DTR status.                     
         IRDTR           Raise a line's DTR status.                     
         IRXOFF         Reset a line's XOFF status.                     
         NONINT    Set [non]interactive job status.                     
         ISPPA                              Stop performance analysis.  
         GETREG                   Get value stored processor register.  
         TRMIN    terminal.          Accept string of characters from   
         TRMOUT   terminal.            Send string of characters to     
         DISMNT             Dismount a file structured device.          
         MOUNT                   Mount file structured device.          
         DSMNTA           Dismount all file structured devices.         
         INITSP     new, switch to existing subprocess.       Initialize
         ISWESP       Switch to an existing subprocess.                 
         ITRYSP     Try to initialize a new subprocess.                 
         ISPWND                             Suspend window processing.  
         ISWESP   subprocess.               Switch to an existing       
         INITSP   subprocessInitialize new, switch to existing          
         IASRNT             shared run time system and job[Dis]associate
         MAPRNT         Map shared run time system into job region.     
         RLCTL         exclusive control of system.           Relinquish
         TKCTL         exclusive control of system.                 Take
         TKCTL    system.                   Take exclusive control of   
         TTCRTN   routine.        Establish terminal completion         
         ITRCTL           Lead-in character terminal control functions. 
         ITRERR                   Check for terminal input errors.      
         HIEFOF    Turn off high efficiency terminal mode.              
         HIEFON     Turn on high efficiency terminal mode.              
         TIMOUT   value.                Set terminal read time out      
         ITRTYP                   Determine terminal type.              
         TRMIN           of characters from terminal.      Accept string


        TSXLIB V6.2                                             PAGE 102
        Appendix A:  KWIK Index


         TRMMSG     Send message to another terminal.                   
         TRMOUT     string of characters to terminal.               Send
         TERMPA   analysis.                 Terminate from performance  
         ICONTM           Determine connect time for job.               
         ISTFTM                Set creation time of file.               
         ISPCTL             Control release time of spooled file.       
         TIMOUT           Set terminal read time out value.             
         IASRNT                  shared run time system an[Dis]associate
         MAPRNT   region.    Map shared run time system into job        
         ICPUTM                     Get CPU time used by job.           
         IRDRCL            communication or timesharing line.   Redirect
         ITCRTN   interrupt routine.        Trigger completion from     
         ITRYSP   subprocess.               Try to initialize a new     
         LKBLK                              Try to lock block.          
         RCVMSG   another job.              Try to receive message from 
         ITSLIC                   Determine TSX-Plus license number.    
         ITSLIN                   Determine TSX-Plus line number.       
         IYELL                 Override the TT-GAG option.              
         HIEFOF   terminal mode.            Turn off high efficiency    
         HIEFON   terminal mode.            Turn on high efficiency     
         ITRTYP          Determine terminal type.                       
         IUALBK                             Unlock all locked blocks.   
         IUNLKM                             Unlock job from memory.     
         IUSPBK                             Unlock specific block.      
         MEMUSE            amount of memory used by job.       Determine
         ICPUTM                Get CPU time used by job.                
         STPRLV   priority level.       Set user mode processor         
         GTUNAM   current job.          Get user name associated with   
         STUNAM   current job.          Set user name associated with   
         IPEKIO                     Peek at value in I/O page.          
         IBICIO                   Bit clear value into I/O page.        
         IBISIO                     Bit set value into I/O page.        
         IPOKIO                        Poke value into I/O page.        
         GETREG   register.             Get value stored processor      
         ISTPRV    Set current job priority value.                      
         TIMOUT      terminal read time out value.                   Set
         ISPY     simulated RMON.    Return values from within          
         ICNINT           Connect interrupt vector completion routine.  
         IRLINT        Release an interrupt vector connection.          
         ICNRTN        routine to interrupt vector.      Connect service
         CNVAPA   address.          Convert virtual address to physical 
         MPRGN    physical memory.      Map virtual memory region to    
         LKBLKW                             Wait for block to lock.     
         RCVMSW   another job.              Wait for message from       
         IRSWND                      Resume window processing.          
         ISPWND                     Suspend window processing.          
         ICRWND                    Create a window.                     
         IDLWND                    Delete a window.                     
         IPRWND     Print the contents of a window.                     
         ISLWND                    Select a window.                     
         ICKWTS                   Check for writes to shared file.      
         IRXOFF              Reset a line's XOFF status.                


        TSXLIB V6.2                                             PAGE 103
        Appendix B:  Distribution Kit






                         Appendix B:  Distribution Kit

             The TSXLIB distribution kit (DECUS #11-490) consists of the
        following files:

                TSXLIB.COM  TSXLIB builder.                    

                ABSTRA.DOC  Abstract.                          
                TSXLIB.DOC  This document.                     

                CLLINE.MAC  Communication line support.        
                DETJBS.MAC  Detached job support.              
                DVALOC.MAC  Device allocatind and deallocating.
                JBPRIV.MAC  Job privileges control.            
                JBSTMN.MAC  Job status monitoring.             
                MNTDEV.MAC  Device mounting and dismounting.   
                MSGCOM.MAC  Interjob message communication.    
                PRFANL.MAC  Performance analysis support.      
                RELTIM.MAC  Real time program support.         
                RUNTIM.MAC  Shared run time system support.    
                SHRFIL.MAC  Shared file system support.        
                SPOLER.MAC  Spooler support.                   
                SUBPRO.MAC  Subprocess control.                
                SYSTAT.MAC  System status information.         
                TRMCOM.MAC  Terminal communication.            
                TRMCTL.MAC  Terminal control.                  
                TSFILS.MAC  Special file information.          
                TSLBID.MAC  TSXLIB identification.             
                TSXMSC.MAC  Miscellaneous EMTs.                
                TSXODT.MAC  ODT activation mode support.       
                USRNAM.MAC  User name support.                 
                WINDOW.MAC  Windowing support.                 

                TSXLIB.OBJ  The implemented library.           


        TSXLIB V6.2                                             PAGE 104
        Reader's Comments


        Did you find any errors in this document?  If so, please specify
        page and describe.












        Did you find this document understandable, usable, and well
        organized?  Please make suggestions for improvement.












        Did you find this document sufficiently complete?  If not, what
        material is missing and where should it be placed?












        Name/Date:

        Company:

        Address:

        City/State/Zip:


                          NAB Software Services, Inc.
                          PO Box 20009               
                          Albuquerque, NM 87154-0009