SETLIN.DOC
SETLIN - An RT-11 macro program to set/alter values for the four
serial lines on the WEBSTER COMPUTER CORPRATION's PCLV11-J
(MFU) board. Users should be familiar with the PCLV11-J manual.

SETLIN overrides any initial serial lines values provided
by the MFU boot PROM.  These lines may be located at one
of two locations (176500 or 176540).  In addition the fourth line may
be defined as the console for a total of nine possible locations.  The
settable parameters for each line are the baud rate, number of characters,
parity and number of stop bits.

Invoking the SETLIN program :-

1)  Manually at the RT-11 command level by entering: SETLIN or
                                                     R SETLIN or
                                                     RUN SETLIN to
    alter the default values within the SETLIN program.

2)  Via a command file to establish SETLIN's default values on
    the PCLV11-J serial lines.  Enter: SETLIN DEF or
                                       R SETLIN DEF or
                                       RUN SETLIN DEF.
    It is anticipated that this will form part of the RT-11
    STARTS.COM file.


Modifying the default values in SETLIN.SAV :-

enter:	 SETLIN or R SETLIN or RUN SETLIN
receive: Enter option (HELP/MODIFY

enter:	 HELP
receive: help text

enter:	 MOD
receive: display of SETLIN.SAV's existing default values.  Operator
         selects CSR line to modify and responds to prompts.  Default
         answers are enclosed in [ ] and operator presses RETURN to
         accept default answer.  Modifications are implemented
         immediately and operator is again invited to either select
         another CSR line to modify or exit.  Upon exit operator may
         save the session's modifications as a new version of
         SETLIN.SAV or to another .SAV file.

Setting the PCLV11-J serial lines to SETLIN.SAV's default values :-

enter:	 SETLIN DEF or R SETLIN DEF or RUN SETLIN DEF
receive: next command in command file or RT-11 dot.  The SETLIN
         program does not produce any output when the default option
         is invoked.