HS: A HANDSHAKING SERIAL LINE HANDLER


                                   Written by

                                 GARY PRECKSHOT
                             UNIVERSITY OF ARIZONA
                                TUCSON, ARIZONA
                                October 27, 1980






          INTRODUCTION          ____________

               A major problem in  installations  where  a  number  of
          small  computers  exist is that of transfering data from one
          machine to another.  Usually this occurs when it is  desired
          to move program source files developed on one machine having
          peripherals convenient for program development to a  machine
          less well equipped.  For example, transferring programs from
          a hard disk machine to one having floppy disks or  no  disks
          at  all.   I present here a serial line handler which allows
          convenient file transfer between two machines running  under
          DEC  RT-11  Version  3B  or  later, and whose protocol is so
          simple that  a  complementary  serial  I/O  handler  may  be
          written easily for other operating systems.

          THE HS: HANDLER          ___ ___ _______

               The HS:  handler  is  a  modular  serial  line  handler
          configured  for  installation under RT-11 V3B which achieves
          block-by-block or line-by-line synchronized transmission  of
          data  across  a  serial  data link.  It does this by using a
          very simple handshake in  which  the  sending  end  requests
          permission  to  send  data  before actually transmitting the
          data object in question.  The  handler  operates  either  in
          data  transparent  block  (512 bytes) mode, or in ASCII-only
          line mode, parity suppressed.   Transmitting  mode  must  be
          selected  by  using the SET command, while receiving mode is
          selected automatically by handshake.

               In  either  mode,  synchronization   is   acheived   by
          transmitting  an  endless series of ENQ characters until the
          receiver responds with a single ACK.  Clearly this  requires
          that  the  link  be  operated  in  full  duplex  mode.   The
          transmitter  indicates  its  mode  in  the   first   non-ENQ
          character  it  transmits after receiving ACK.  STX indicates
          block mode, and any other  ASCII  character  indicates  line
          mode.

               In block mode, the next 512 bytes are considered to  be
          data,  and  are  terminated by the 513th byte, an ASCII ETB.
          There are no redundancy checks,  and  the  block  terminator
          represents  the  only  check on completed transmission.  The
          buffer size given to the handler must be an integral  number
          of  512 byte blocks, but resynchronization occurs after each
          block, so that the receiver needs a minimum buffer  size  of
          one block.

               In line mode, transmission continues until a  linefeed,
          control  Z, or end of transmission buffer is encountered, at
          which  point  resynchronization  occurs.   End   of   buffer
          resynchronization  is indicated to the receiver by appending
          an ETB character.  Control Z is used to indicate an  end  of
          file.

                                        1


                                                                     2



               In both modes, end of file is indicated by transmission
          of  control  Z.   Since  the block mode is data transparent,
          this is actually implemented by replacing the first  non-ENQ
          character  (STX  in  block  mode), with control Z, which the
          receiver interprets  as  a  line  containing  but  a  single
          control  Z,  indicating end of file.  However, control Z may
          be embedded in a line in line mode, which will give rise  to
          a receiver report of end of file.  The handler is configured
          so  that  it  automatically  transmits  a  single  character
          control  Z  line  upon  being  closed,  so  that closing the
          transmitter  will  cause  an  end  of  file  report  at  the
          receiver.

          USING THE HS: HANDLER          _____ ___ ___ _______

               Line mode of this handler  was  implemented  for  those
          uses  that generally involve line-by-line dialogue between a
          program and what it believes is a teletype or terminal.   It
          is  generally  unsatisfactory  for use with systems programs
          because it will usually result in files that have  only  one
          line  per  block.   It  is  very satisfactory for those uses
          which require  immediate  transmission  upon  a  terminating
          character,  in  this  case  linefeed,  which  block oriented
          handlers will not do.  The user should take care when  using
          the special characters ETB, control Z, and STX, as these may
          lead to unintended results in line mode.

               Block mode of HS: was implemented  so  that  HS:  would
          appear  to be a standard block oriented device that could be
          substituted by use of the RT-11 ASSIGN command for any legal
          device  in  the  system.   HS:DUMMYF.ILE  may be used in ANY                                                                   ___
          position  that  is  legal  for  an   RT-11   standard   file
          specification.  In particular, it may be used with the RT-11
          COPY command to copy a file to a link, on the other  end  of
          which  is  another RT-11 system using COPY and HS: to copy a
          file from the link.  In a close-coupled short-link situation
          the  lack  of  redundancy  checking in HS: may be easily got
          around by the following command strings in the  sending  and
          receiving systems:


                  SEND:   COPY
                          FILEN.AME
                          HS:
                          DIF
                          HS:FILEN.AME
                          FILEN.AME
                  RECV:   COPY
                          HS:FILEN.AME
                          SY:
                          COPY
                          FILEN.AME
                          HS:


                                                                     3



               The DIF command will compare the retransmitted file  to
          the original and provide an even more secure indication than
          partial redundancy checking, since, in  fact,  what  we  are
          doing is 100 % redundancy checking.

          CONCLUSION          __________

               A handshaking synchronizing handler  was  written  that
          satisfies  a  need for local transmission of data regardless
          of the speed of copying devices at either end  of  a  serial
          link.   The  fact  that  it  is modular enables its use with
          standard system utilities under RT-11 V3B in block mode, and
          a  line  mode  is  provided  for  those wishing line-by-line
          synchronized data transmission.  Because we envision its use
          only   in   a  closely  coupled  local  environment,  100  %
          redundancy  checking  for  accuracy   of   transmission   is
          practical.    Commented   copies   are   available  from  G.
          Preckshot.