**********************************
           *          Program TEK125        *
           *                                *
           * Submitted by Ronald Beetz      *
           *              AKZO PHARMA       *
           *              Oss, Holland      *
           *                                *
           **********************************

TEK125 is a program to display TEKTRONIX PLOT-10 information on a VT125
terminal. TEK125 is maybe the easiest solution for your conversion
problems.

The idea is :
1. The PLOT-10 library has minor changes: INITT,ADEOUT and FINITT
   Because of these changes all graphical information can be send
   to a file instead of the terminal.
2. TEK125 can read that file and converts its information to the
   VT125.
3. With few changes in TEK125 the program can be used for other
   devices than VT125 like a CALCOMP plotter.

Note: All alphanumirical information on the graphs must be written
      with the AOUTST routine of the PLOT-10 library to get it in
      the file. Writes to the terminal, what is rather usual for
      TEKTRONIX plots, will go to the terminal and not to the file.

The changes in PLOT-10:
1. INITT  The routine asks for an output file, default teminal what
          is the original situation, and opens that file on unit
          number 13 (Never use unit 13 yourself!)
2. ADEOUT This macro routine with the .TTYOUT program request has
          been replaced by a FORTRAN routine that writes characters
          one by one to unit 13. This way of output is somewhat
          slower than the original one.
3. FINITT Unit 13 is closed here. Additional I removed the stupid
          STOP-statement.

Device dependency of TEK125:
1. In the main program the terminal is initialized with a
   <ESC>[2J<ESC>PpS(E). For other devices you need another
   initialization.
2. Subroutine TRAS - draws a line to position IX,IY visible
   or unvisible.
3. Subroutine PCARS - writes L characters of TEXT starting on
   the current position. The character type, height and width
   are fixed, because TEKTRONIX does not know otherwise.