A Double-Sided Double-Density 8" Floppy Disk Handler

                                 Bob Schor
                           Eye and Ear Institute
                            203 Lothrop Street
                          Pittsburgh, PA   15213

                              (412) 647-2116


     Most users of DEC 8" floppy drives know about the RX01, the
single-density, single-sided 8" floppy drive, with 494 formatted blocks,
and the RX02, the double-density, single-sided 8" floppy, with 988 (twice
as many) blocks.  There is some evidence that an RX03 was contemplated,
namely the RX02, using double-sided media (and, of course, two read/write
heads), but DEC never implemented such a drive (to my knowledge).

     If one buys DEC-compatible hardware, however, it is possible to buy
double-sided drives, and controllers capable of selecting both heads.  Some
controllers even directly support 22-bit Q-Bus addressing, easing their use
on 11/73 systems.

     This article describes modifications to the DY handler, DY.MAC, which
will enable double-sided floppy use.  It has been used and tested with
floppy controllers from Data Systems Design (DSD, now Qualogy) and Sigma
Information Systems (Sigma).  These changes have been installed in RT-11
since Version 5.0; they have been field-tested in RT-11 5.5 (pre-release),
and should be continue to be portable through future versions.
Modifications to enable the handlers to be used under TSX-Plus (S&H
Computer Systems) will also be described.

     To aid in making changes, code segments will be divided into several
classes.  Code will be presented in the following sections:  header
comments, DSD-specific code, Sigma-specific code, double-sided code, and
TSX-specific code.  Code sections will be presented, along with a
description of the code location within the handler; this should provide
the most flexible means of dealing with various handler versions.

Header Code______ ____

     The following code should be placed on the "Conditional Assembly
Summary" page; you could also include specific definitions here to enable
desired versions:

;************************* Insert *************************************
;The following conditionals are available --

;       tsx$p   = 1             ;modify handler for TSX
;       dsd$    = 1             ;modify handler for DSD-880
;       sis$    = 1             ;modify handler for Sigma RXV31
;       dy$ds   = 1             ;modify handler for double-sided operation



                                - 1 -






;The original code modifications were courtesy of S&H Computer Systems (TSX),
;Data Systems Design (DSD), and Sigma Information Systems (SIS).  Code
;consolidated, maintained, and tracked through successive RT-11 versions
;by Bob Schor.  Current version (August, 1989) tested with RT-11 5.4 and
;RT-11 5.5 DY.MAC handlers.  Attempts made to keep changes simple, logical,
;and understandable.

;To generate a specific version, choose some combination of the above
;conditionals.

;Note minor error in DY handler -- extra word allocated in DYRBUF.  Total
;space required = 6 words, two registers + 4-word error block, only first word
;of which returned to ERRLOG.

;The following code sets undefined defaults, ensures conditional values are
;0 or 1:

.iif ndf tsx$p  tsx$p   = 0     ;if undefined, default to 0
.iif ndf dsd$   dsd$    = 0
.iif ndf sis$   sis$    = 0
.iif ndf dy$ds  dy$ds   = 0

.iif ne  tsx$p  tsx$p   = 1     ;ensure 0 or 1
.iif ne  dsd$   dsd$    = 1
.iif ne  sis$   sis$    = 1
.iif ne  dy$ds  dy$ds   = 1

;If compiling TSX version, use memory-management code

.iif ne  tsx$p  mmg$t   = 1
.iif ndf mmg$t  mmg$t   = 0
.iif ne  tsx$p  bf      = 1
.iif ne  tsx$p  tim$it  = 1

;Ensure both dsd$ and sis$ are not specified

.iif ne  dsd$&sis$      .error  ;Cannot choose both dsd$ and sis$

;If neither dsd$ nor sis$ specified, do not generate double-side code

.iif eq  dsd$!sis$      dy$ds   = 0
;************************* End Insert *********************************


DSD-specific Code____________ ____

     The only DSD-specific code concerns returning the extended error
registers to the error-logging routine; apparently the DSD protocol differs
slightly from the RX02 specification.  The change, below, consists of
conditionally removing part of the standard DY handler, located in the
error-handling section of the handler, in the conditional code guarded by
the conditional ".IF NE  ERL$G".  Locate the request for access to the


                                - 2 -






extended registers ("MOV  #CSMAIN!CSGO, @R4").  Following it are normally
two wait loops, one testing CSTR, the second CSDONE.  The second loop
should be conditionally removed by replacing it with the following:

;************************* Replace ************************************
.if eq  dsd$                            ;skip if DSD controller
61$:    BIT     #CSDONE,(R4)
        BEQ     61$
.endc   ; eq dsd$
;************************* End Replace ********************************


Sigma-specific Code______________ ____

     The Sigma controller has 22-bit capability, which is easily utilized,
allowing the floppy disk to be used in systems with more than 256 kB, and
without clumsy remapping games to keep the buffers in low memory.

     The first change is to add a definition to the command/status register
bits, located near the start of the handler, along with the other
definitions.  Add the following:

;************************* Insert *************************************
.if ne  sis$                            ;Sigma controller
        cs22    =   2000                ;22-bit addressing
.endc
;************************* End Insert *********************************

     The second change follows the Driver Request Entry Point.  Locate a
call to MPPTR, which retrieves an extended physical address from the
monitor.  Replace the two instructions "BIT  #1700, R4", "BNE.  DYERR" with
the following alternate:

;************************* Replace ************************************
.if eq  sis$                            ;alternate code for Sigma controller
        BIT     #1700,R4
        BNE.    DYERR
.iff                                    ;Sigma code
        mov     r4, -(sp)               ;put high address (shifted) on stack
        asr     (sp)                    ;shift right 4
        asr     (sp)                    ;to put high bits in bits 0-5
        asr     (sp)
        asr     (sp)
        mov     (sp)+, extadr           ;save extended address
        bic     #1700, r4               ;clear unneeded bits
.endc   ; eq/iff sis$
;************************* End Replace ********************************

     The above code fragment saves the high six address bits.  The next
fragment, located in Start Transfer or Retry, increments the high address
if a transfer "rolls over" the 16-bit boundary.  Near the end of the page,
after a call to DOSILO, a register TST, and a "BMI DYDONE", there should be


                                - 3 -






code to add to the buffer address (BUFRAD).  The conditional code guarded
by MMG$T will have a BCC instruction.  The code being skipped by the BCC
will cause #10000 to be added to a register (this will eventually set the
extended address bits in the CSR).  Include the following (just before the
.ENDC which ends the MMG$T-guarded code):

;************************* Insert *************************************
.if ne  tsx$p!sis$                      ;handle possible 22-bit address
        bic     #40000, r0              ;forbid carry out of bit 18
.endc   ; ne tsx$p!sis$
.if ne  sis$                            ;for Sigma controller
        inc     extadr                  ;adjust extended bus address
.endc   ; ne sis$
;************************* End Insert *********************************

The first instruction, which is also needed for TSX, guards against
incrementing addresses across an 18-bit boundary and inadvertantly setting
bit 14 in the CSR (bits 12 and 13 are the 18-bit extended address bits).
The second instruction increments the Sigma's 22-bit extended address.

     Twenty-two bit operation is enabled in the DOSILO routine.  At the
beginning of the routine, a register (probably r0) is being made ready to
be sent to the CSR.  Locate the instruction which clears some of the
command bits (probably "BIC  #6*2,R0"), and insert

;************************* Insert *************************************
.if ne  sis$&mmg$t                      ;Sigma controller, 22-bit mode
        bis     #cs22, r0               ;enable 22-bit addressing
.endc   ; ne sis$&mmg$t
;************************* End Insert *********************************

The end of the DOSILO routine should be a branch to DYDOFN (either a BR or
a .BR instruction, depending on version).  Replace it with the alternate
code (illustrating the .BR version, adjust as appropriate):

;************************* Replace ************************************
.if ne  sis$&mmg$t                      ;Sigma controller, 22-bit mode
        br      dydof2                  ;do 22-bit command protocol
.iff
        .BR     DYDOFN
.endc   ; ne sis$&mmg$t
;************************* End Replace ********************************

     The final code section for the Sigma controller provides the alternate
protocol just requested to handle 22-bit data transfers.  This code can
immediately follow the DYDOFN routine.








                                - 4 -






;************************* Insert *************************************
.if ne  sis$&mmg$t                      ;Sigma controller, 22-bit mode

;alternative protocol for 22-bit fill buff, empty buff, read error code

dydof2: bitb    #cstr!csdone, @r4       ;transfer or done?
        beq     dydof2
        bpl     dyerr2                  ;controller should want data
        mov     r3, @r5                 ;send command
1$:     bitb    #cstr!csdone, @r4       ;transfer or done?
        beq     1$
        bpl     dyerr2                  ;more data should be needed
        mov     r2, @r5                 ;continue protocol
2$:     bitb    #cstr!csdone, @r4       ;transfer or done?
        beq     2$
        bpl     dyerr2                  ;more data should be needed
        mov     extadr, @r5             ;load bus address extension register
        return                          ;successful completion
extadr: .word   0                       ;extended address goes here
.endc   ; ne sis$&mmg$t
;************************* End Insert *********************************

It is possible that the above code will generate "A" errors, due to the
"BPL DYERR2" address being out of bounds.  If this occurs, replace this
instruction with "BPL 4$", and include the line "4$:  JMP DYERR2" just
following the "RETURN" instruction at the end of this section of code.


Double-sided Floppy Code____________ ______ ____

     The following code handles the actual double-sided floppy addressing
and head selection logic.  Basically, a double-sided floppy is treated the
same as a single-sided one, except that blocks higher than 988. (assuming
double density) are placed on the second side.  Note that this scheme
provides for maximal interchangability between single-sided RX02 and
double-sided RX03 disks -- if you less-than-half-fill a double-sided disk,
your colleagues with single-sided drives will have no trouble reading the
information (be sure you SQUEEZE the disk to keep all blocks below 988!).
What will ultimately determine whether a disk is treated as single or
double-sided will be DUP, which initializes the directory (and thereby sets
the total number of blocks present).  Code below will test for double-sided
media (identifiable by a changed location of the index hole) and will
return the proper size when queried with .SPFUN #SIZ$FN.

     The initial changes are definitions, near the top of the handler.  The
first defines the "side-two present" bit in the error/status register.

;************************* Insert *************************************
.if ne  dy$ds                           ;double-side code
        essid2  =      2
.endc   ; ne dy$ds
;************************* End Insert *********************************


                                - 5 -







The second definition should follow the definition of DDNBLK, and defines
the number of blocks for double-sided (double-density) devices:

;************************* Insert *************************************
.if ne  dy$ds                           ;double-side code
        dsnblk  = ddnblk*2              ;twice as big
.endc   ; ne dy$ds
;************************* End Insert *********************************

     The next code, near the start of Start Transfer or Retry, dynamically
adjusts the size if a double-sided floppy is installed.  Locate code where
#DYDSIZ is pushed on the stack.  At that point, before testing the #ESDN
(density) bit, include the additional code

;************************* Insert *************************************
.if ne  dy$ds                           ;double-side code
        bit     #essid2, @r5            ;see if double-sided floppy
        beq     2$
        asl     @sp                     ;in which case, double the size
2$:
.endc   ; ne dy$ds
;************************* End Insert *********************************

     In Error Handling -- Change Density, Retry, alternative code is
included to handle double-sided capability.  Locate the bit-test with
ESDNER, and replace the BEQ following it with the alternative code

;************************* Replace ************************************
.if eq  dy$ds                           ;single-side code
        BEQ     5$
.iff                                    ;double-side code
        bne     1$                      ;skip ahead if density error
        bit     #escrc, @r5             ;CRC error?
        bne     5$                      ;yes, report error
        bit     #cshead, r0             ;see which side active
        beq     5$                      ;report error if first side
        bit     #csdn, r0               ;single or double density?
        bne     5$                      ;report error if double
1$:     bit     #cshead, r0             ;density error or SDDS
        beq     2$                      ;if double-sided,
        add     #dsnblk, dylsn          ;adjust logical sector number
2$:     bic     #cshead, r0             ;use first side
.endc   ; eq/iff dy$ds
;************************* End Replace ********************************

     At the start of DOXFER, Start a Sector Read or Write, the logical
sector number must be tested to see if the desired block is on the first or
second side.  This routine is entered with the desired status register in
R0, a pointer to the CSR in R4 -- you will replace the code loading the CSR
and loading registers with the word count and logical sector address as
shown below:


                                - 6 -







;************************* Replace ************************************
.if ne  dy$ds                           ;double-sided code
        mov     dylsn, r3               ;get logical sector number
        cmp     r3, #dsnblk             ;see if it fits on first side
        blt     1$                      ;skip if so
        sub     #dsnblk, r3             ;adjust location on side 2
        bis     #cshead, r0             ;and set second head
1$:     mov     r0, @r4                 ;set command
        mov     wrdcnt, r2              ;and word count
.iff
        MOV     R0,@R4
        MOV     WRDCNT,R2
        MOV     DYLSN,R3
.endc   ; ne/iff dy$ds
;************************* End Replace ********************************

     The final change in the handler is to modify the Bootstrap Read
Routine to use the appropriate head (depending on the logical sector
requested) for the read.  Locate the instruction which loads the bootstrap
CSR into R5 (it will look like "2$:  MOV  (PC)+,R5", "BOTCSR:  .WORD
DY$CSR").  Replace the first instruction as follows:

;************************* Replace ************************************
2$:
.if ne  dy$ds                           ;double-sided code
        cmp     r0, #dsnblk             ;skip if requested block number
        blt     12$                     ;on first side
        sub     #dsnblk, r0             ;second side, adjust block number
        bis     #cshead, redcmd         ;and enable second side
12$:
.endc   ; ne dy$ds
        MOV     (PC)+,R5
;************************* End Replace ********************************


Code for TSX-Plus____ ___ ________

     For TSX-Plus, a few changes need to be made.  First, some of the SET
code in the handler does not appear to be necessary (the .SLP files which
come with TSX conditionally omit part of it -- I have omitted a never-used
subroutine as well).  Second, a change is made to allow a smooth transition
across 16-bit address boundaries.  Finally, a change in the use of the PAR
registers (TSX uses PAR 6 instead of PAR 1) is required.

     The first changes are suggested by DYxxx.SLP, the files which come
with TSX-Plus.  They conditionally remove code in the handler which would
otherwise cause SET options to change the in-core loaded handler.  Two
pieces of code are involved.  The first is a routine labeled FINDRV, which
ends with a BR instruction (probably "BR O.GOOD"); the following location
following the removed code is labeled DAREA.  Insert the following just
before FINDRV:


                                - 7 -







;************************* Insert *************************************
.if eq  tsx$p                           ;RT only; TSX ignores loaded handler
;************************* End Insert *********************************

At the end of the routine, insert the following (probably right before
DAREA):

;************************* Insert *************************************
.endc   ; eq tsx$p
;************************* End Insert *********************************

This routine is called near the end of the Set Options.  Locate the "CALL
FINDRV" instruction; insert the following to remove it for TSX:

;************************* Insert *************************************
.if eq  tsx$p                           ;RT only; TSX ignores loaded handler
;************************* End Insert *********************************

After the FINDRV, there should be a BCS instruction, probably to O.GOOD;
the code which would be taken if the carry were clear should be eliminated.
This can best be accomplished by locating the unconditional branch to the
BCS target (or the target itself, if it should immediately follow), and
eliminating all of the code in between.  In Version 5.4, this would mean
inserting the following just before a "BR  O.GOOD" instruction, about seven
lines after the "CALL FINDRV":

;************************* Insert *************************************
.endc   ; eq tsx$p
;************************* End Insert *********************************

     The next modification is in the Driver Request Entry Point.  Locate
the second call to $PTWRD.  Following it is an increment of R0, which is
being used as a buffer pointer.  For TSX, this instruction is modified to
handle carries into the higher address bits in the CSR:

;************************* Replace ************************************
.if eq  tsx$p                           ;RT/TSX difference
        TST     (R0)+
.iff                                    ;for TSX,
        add     #2, r0                  ;increment bus address
        bcc     41$                     ;check for 16-bit overflow
        add     #10000, (sp)            ;adjust high bits on stack
        bic     #40000, (sp)            ;prevent 18-bit carry
41$:
.endc   ; eq/iff tsx$p
;************************* End Replace ********************************

Note that this above change appears to be an out-right "bug" in the
handler, which perhaps should be also included in the RT-11 versions.  DEC
has been notified of the potential problem.



                                - 8 -






     The final change in in Start Transfer or Retry, and concerns the use
of PAR 6 by TSX.  Locate the instructions which compare the buffer address
with the end of PAR 1 ("CMP Q.BUFF-Q.BLKN(R4),#20000", "BHIS $55"), and
replace the comparison as shown:

;************************* Replace ************************************
.if eq  tsx$p                           ;RT/TSX use of PAR registers
        CMP     Q.BUFF-Q.BLKN(R4),#20000
.iff                                    ;for TSX,
        cmp     q.buff-q.blkn(r4), #140000      ;use PAR 6 instead of PAR 1
.endc   ; eq/iff tsx$p
;************************* End Replace ********************************

     The above code changes for TSX-Plus assumes that you are working with
compatible versions of RT-11 and TSX, for example, RT-11 Version 5.2 to
5.4, and TSX Version 6.3 to 6.4.  At this particular time, the two systems
are slightly out-of-synch; the soon-to-be-released RT-11 Version 5.5
contains a few handler features which have not yet been incorporated into
the current TSX Version 6.4.  Once this version of RT-11 is released, an
update can be obtained from the author regarding these (minor) changes; this
may not be necessary, however, as S&H may also announce a compatible release
of TSX.


Assembly and linkage________ ___ _______

     Install the above changes into the handler; in this example, I will
assume that the revised double-sided handler is called DYDS.MAC.  Decide
which version (or versions) you wish.  For the sake of discussion, suppose
you wish a double-sided handler, tailored for the Sigma controller, and
wish Single Job, Extended Memory, and TSX versions.  Create three .MAC
header files, here called SJDYDS, XMDYDS, and TSDYDS, with contents as
follows:

        SJDYDS                  XMDYDS                  TSDYDS

        sis$    = 1             sis$    = 1             sis$    = 1
        dy$ds   = 1             dy$ds   = 1             dy$ds   = 1
                                mmg$t   = 1             mmg$t   = 1
                                tim$it  = 1             tsx$p   = 1

Note that in assembling the TSX-specific handler, code will automatically
be generated for device time-out support.  Many XM handlers also are genned
with this option; you would need to include the line "tim$it  = 1" in
XMDYDS to be compatible with these handlers.








                                - 9 -







Assemble the relevant object modules, using the following commands:

        MACRO/OBJ:SJDYDS SJDYDS+DYDS
        MACRO/OBJ:XMDYDS XMDYDS+DYDS
        MACRO/OBJ:TSDYDS TSDYDS+DYDS

Link the actual handlers with

        LINK/NOBITMAP/EXE:DY.SYS  SJDYDS
        LINK/NOBITMAP/EXE:DYX.SYS XMDYDS
        LINK/NOBITMAP/EXE:DY.TSX  TSDYDS

     These should all now work with the appropriate operating systems.
Note, however, that in order to get twice the storage on your floppies, you
must have (a) a drive with two read/write heads (several third-party
half-height drives fulfill this requirement), (b) a controller which
supports two heads (such as the one from Sigma), (c) a floppy
"recognizable" as double-sided (sold by most major vendors, recognizable
from the two head cut-outs, the altered position of the index hole, and
frequently by a designation like DS/DD, or similar indication), and (d) a
double-sided floppy handler, such as described herein.  Good luck.
































                                - 10 -