TELETYPE MODEL 4O LINEPRINTER HANDLER
                                       by
                              GEORGE G. PRECKSHOT



               The LPTT40 line printer handler was design to operate a
          TELETYPE  MODEL 4O lineprinter at the fastest printing speed
          possible  by  using  the  TELETYPE  provided  OEM  interface
          handshake  lines  to  control  the  exchange of output data.
          Essentially there are four lines besides the EIA RS-232 data
          line by which the lineprinter is turned on and indicates its
          status.  It is necessary to modify  an  asynchronous  serial
          line  interface to enable the computer to access these lines
          as bits in the  interface  control  status  register  (CSR).
          These lines and the bit in CSR are described below.

             DEVICE SELECTABLE             ______ __________

                     Read only, bit 5.  If set,  indicates  no  alarms
                present at lineprinter.

             DEVICE READY             ______ _____

                     Read only, bit  4.   If  set,  indicates  printer
                motor  is up to speed.  This bit must be wired so that
                a positive going transition  on  this  line  causes  a
                remote interupt[1].

             DEVICE NEXT CHARACTER             ______ ____ _________

                     Read only, bit 3.  If  set,  indicates  that  the
                lineprinter  is ready for another character.  This bit
                must be wired so that a positive going  transition  on
                this line causes a remote interupt[2].









                                       i
                                ---------------
          [1] Remote interupt means an interupt generated by a  change              ______ ________
          in  lineprinter  condition rather than a change in interface
          condition.  It should be noted that interupt conditions must
          be  buffered  through  a D-type flip-flop or some equivalent
          method to prevent them being forgotten if a second  interupt
          occurs during interupt service.
          [2] Separate D-type flip-flops are required when two or more
          conditions cause the same type of interupt to occur.


                                                                    ii



             REQUEST DEVICE ON             _______ ______ __

                     Read/write, bit O.  When set, turns  the  printer
                motor on.  When read, resets all remote interupts[3].

             ENABLE REMOTE INTERUPT             ______ ______ ________

                     Read/write, bit  1.   When  set,  enables  remote
                interupts.



          SET OPTIONS AND FEATURES          ___ _______ ___ ________

               Since the source code is fully commented on the subject
          of set options, we will merely list them here.

               PAGE      Sets page length
               FORM0     Sets page eject on first block
               AUTO      Sets automatic page ejection
               HANG      Sets printer will wait for error correction
               EOF       Printer will stop on Control Z
               CNTRL     Control characters passed to printer
               TAB       Allows setting of software tab stops
               CRLF      Converts CR to LF

























                                  ------------
          [3] Because of this, the entire byte should be read once and
          kept  in  a register or other memory location, since further
          reads may destroy additional interupts  that  have  occurred
          during the interim.


                                                                   iii