TAPER.DOC   TECHNICAL INFORMATION AND INSTALLATION GUIDE FOR
	            TAPE READER.  FOR USER INSTRUCTIONS, READ TAPER.HLP

*****************************************************************************

WRITTEN BY:  ROGER MATUS, DOUGLAS BOHRER
             PERSONNEL DEPARTMENT, THE FIRST NATIONAL BANK OF CHICAGO
             1 FIRST NATIONAL PLAZA, 22nd FLOOR
             CHICAGO, ILLINOIS  60670

DATE:        11-JUN-80

*****************************************************************************

	TAPER is a general purpose reader of 800 b.p.i. magnetic tapes. Its
specialty is to take character data in an unknown format and, through
interaction with the user, write the data in Digital Equipment format to any
write-enabled disc.  TAPER may be used to read "foreign" tapes.

TECHNICAL INFORMATION

	The user interface and formatting is handled by a program written
in FORTRAN.  The tape handler is written in MACRO-11.  Only the FORTRAN
programs, the EBCDIC collating sequence file, and documentation with the name
TAPER was written by the First National Bank of Chicago. All EXTMT routines
were obtained from the Digital Equipment Computer User's Society. EXTMT was
written by N. A. Bourgeois of Scandia Laboratories and operated there for
the United States Department of Energy.

	The TAPER system was developed on a PDP-11/23 using the following
software:
		RT-11 version 3B operating system
		FORTRAN/RT-11 version 2.1 compiler
		MACRO-11 version 3.2B assembler.

	FORTRAN routines are written to maximize portability between
systems. As such, few system dependent routines are allowed.  Therefore,
it should be usable on other systems. (Note: The user's FORTRAN should allow
for byte variables and the use of the OPEN statement for system devices).

	The MACRO routines are provided for user convenience only. The
supplied documentation, EXTMT.DOC, is also provided.


			*	*	*

	*** NO WARRANTY IS EXPRESSED OR IMPLIED ***  Neither First Chicago
Corporation, the First National Bank of Chicago, nor any of its employees
makes any warranty, either expressed or implied, assumes any legal liability,
nor any responsibility for the accuracy, completeness or usefulness of any
information, product or process disclosed.  Neither does the First Chicago
Corporation, the First National Bank of Chicago, nor any of its employees
represent that use of this material would not infringe privately owned
rights.  No statement found elsewhere in these products shall indicate
otherwise.

			*	*	*

	TAPER.DOC  -- PAGE 2 --


INSTALLATION

	All the code and documentation for TAPER is provided on-line.
These files are as follows: EXTMT.DOC, EXTMT.MAC, EBCDIC.DAT, TAPER.DOC,
TAPER.FOR, TAPER.HLP, and TAPSUB.FOR.


	To compile and link TAPER, use the following RT-11, version 3B,
commands (the . in the first column is a system prompt, the
() indicates a system response):

.FORTRAN /LIST /SHOW:3 /WARNINGS TAPER.FOR
(.MAIN.)

.FORTRAN /LIST /SHOW:3 /WARNINGS TAPSUB.FOR
(SKIP)
(LEOT)
(FORM)

.MACRO /LIST EXTMT.MAC
(ERRORS DETECTED: 0)

.LINK TAPER.OBJ,TAPSUB.OBJ,EXTMT.OBJ



	TAPER is now ready to run by typing  .R TAPER in monitor mode.
Only the files TAPER.SAV, which was created by the linker, and
EBCDIC.DAT are needed for the operation of the program.  All other
files may be removed from the disc if space is at a premium.

SPECIFICATIONS

	1.  The software was operated only on a PDP-11/23 under
		RT-11, version 3B, with FORTRAN/RT-11, version
		2.1.
	2.  Tapes, the tape drive and the controller must be
		for 800 b.p.i. NRZI tapes only (see EXTMT.DOC
		for other formats).
	3.  ASCII or EBCDIC characters are permitted.  Results
		would be unpredictable for numeric or packed
		fields.
	4.  Spanned records on the tape will not be processed
		correctly.  TAPER will issue a record terminator
		at the end of each tape block.  For example, if
		the user specifies an 80-character record, but
		the tape contains an 100-character block, a
		record terminator will appear after characters
		80, 100, 180, 200, and so on.  A warning will be
		issued to the user.
	5.  Records of more than 132 characters may yield
		unpredictable results.  This record size limit
		may be changed at compile time by including the
		/RECORDSIZE:n  switch.  This switch would be used
		with both FORTRAN commands listed above right after
		/SHOW:3.  The "RT-11  System User's Guide" gives more
		detail in section 4 under the FORTRAN command.  TAPER
		will issue a warning to the user any time the selected
		record size contains more than 132 characters.
	6.  Records of more than 1020 characters and blocks of
		more than 10200 characters cannot be processed.
		A fatal system error may occur.
	7.  Data must be entirely on one reel of tape.

	TAPER.DOC  -- PAGE 3 --


OUTPUT

	TAPER produces files in standard RT-11 format when used under
RT-11 version 3B.  This format includes ASCII characters, 512-character
blocks, and the proper directory entry.  Output is handled by the FORTRAN
programs.

EBCDIC TRANSLATION

	EBCDIC, which is the standard collating sequence for many machines,
is not supported by Digital Equipment Corporation.  As such, a special
file, EBCDIC.DAT, was created for use with TAPER.

	Those familiar with EBCDIC will note that the file appears out of
sequence.  This is because EBCDIC on other machines uses the entire 8-bit
word for a range of values from 000 to 256.  Digital Equipment considers
the first bit to be a sign bit and, as such, the word values are -128 to
127.  Adjustments were necessary in order to allow a file to be referenced
by what the PDP-11 would consider to be a negative number.

	The characters <SUB>, decimal 33, and <CR>, decimal 13, are translated
as a <SPACE> on the file.  <SUB> is translated as <CONTROL>Z, which is a
Digital end of file mark.  As such, the user should never write this character
to the disc.  The <CR> is a record terminator and would create problems if
left on file EBCDIC.DAT.  The proper character is inserted into the
collating sequence by the FORTRAN program.  Therefore, <CR> is treated
properly in the program.

	Space could have been saved by writing the sequence as one record,
rather than 256.  However, in an attempt to make the program usable on
smaller systems which may not allow a 256A1 format or EQUIVALENCE
statements, the longer way was elected.

MODIFICATIONS

	The FORTRAN program is extensively documented in the source code.
The writing is somewhat simple to allow for easy understanding by the user.