*






           TSXLIB -- A FORTRAN CALLABLE IMPLEMENTATION
                       OF THE TSX-PLUS EMTS


                       N. A. Bourgeois, Jr.
                   Sandia National Laboratories
                         Albuquerque, NM





             Like RT-11, TSX-Plus offers  the  MACRO  pro-
        grammer a number of system services via programmed
        requests or EMTs.  RT-11 makes its system services
        available  to  the  FORTRAN programmer through the
        system subroutine library, SYSLIB.  TSX-Plus  also
        honors  most  RT-11  programmed  requests.  TSXLIB
        makes the TSX-Plus EMTs available to  the  FORTRAN
        programmer as a library of callable routines.  The
        code in TSXLIB is all reentrant.




                       INTRODUCTION

             The TSX-Plus library routines  provide
        facilities  to  support detached jobs, file
        structured device mounting and dismounting,
        communication   between  running  programs,
        program  performance  analysis,  real  time
        program  execution, shared run time system,
        shared files,  system  status  information,
        communication  between running programs and
        a terminal, program control of  the  termi-
        nal,   ODT  activation  mode,  and  several
        miscellaneous  EMTs.   The  system   status
        information  routines  require  the  use of
        TSX-Plus Version 2.2 [3].  Several  of  the
        real time support routines require TSX-Plus
        Version  3.0  [5].   All   other   routines
        require TSX-Plus Version 2.0 or later.

             TSXLIB  [1]  is  available  from   the
        DECUS/US  Chapter Program Library.  The kit
        includes the MACRO source modules  for  all
        groups of routines, a complete user's manu-
        al, a cross reference  chart,  an  indirect
        command  file to build the library, and the
        implemented library.  The  cross  reference


                                             PAGE 2
        *


        chart  lists  for  each  routine  the  page
        number in the user's manual  and  the  page
        number  in  the "TSX-Plus Reference Manual"
        [2].

             The standard FORTRAN  subroutine  cal-
        ling  sequence  shown  below may be used to
        access all of the routines in TSXLIB.

              CALL SUBRTN ( ARG1, ... ,ARGn )

             Those routines that  return  only  one
        value  are  also  callable as FORTRAN func-
        tions.  This is as follows:

             IRET = RTNAME ( ARG1, ... ,ARGn )

             The   "TSX-Plus   Reference    Manual"
        describes   how  the  EMTs  implemented  in
        TSXLIB are accessed from a  MACRO  program.
        However,    the   FORTRAN/MACRO   interface
        described in the "RT-11 Programmer's Refer-
        ence Manual" [4] may also be used to access
        the routines in the  library.   The  TSXLIB
        (as  well  as  SYSLIB)  routines  are  also
        available to the  "C"  programmer  via  the
        DECUS    "C"    [6]    library    function,
        "call(...)".


                   DETACHED JOB SUPPORT

             Table 1 lists the routines  that  pro-
        vide  detached  job  support from within an
        executing program.

          ISTDJ   Get the status  of  a  detached
                  job.
          KLDTJB  Kill a detached job.
          STDTJB  Start a detached job.

                   Detached Job Support.
                         Table 1.


              DEVICE MOUNTING AND DISMOUNTING

             It is possible to mount and dismount a
        file  structured device for directory cach-
        ing from within  a  running  program.   The
        routines  listed  in  Table 2 provide these
        capabilities.



                                           PAGE 3
        *


          DISMNT  Dismount a file structured dev-
                  ice.
          MOUNT   Mount a file structured device.

             Device Mounting and Dismounting.
                         Table 2.


            INTERPROGRAM MESSAGE COMMUNICATION

             TSX-Plus provides an optional facility
        that allows running programs to communicate
        with  each  other.   Table  3   lists   the
        routines  that  support  this  interprogram
        message communication.

          MSGSND  Send a message to another job.
          RCVMSG  Try to receive a  message  from
                  another job.
          RCVMSW  Wait for a message from another
                  job.

            Interprogram Message Communication.
                         Table 3.

             Messages are transferred between  pro-
        grams  by  using named message channels.  A
        message channel accepts a  message  from  a
        sending  program,  stores  the message in a
        queue  associated  with  the  channel,  and
        delivers the message to a receiving program
        on its request for a message on  the  chan-
        nel.   Message  channels  are separate from
        I/O channels.

             Each active message channel has  asso-
        ciated with it an ASCII character name that
        is used by both the sending  and  receiving
        programs  to  identify  the  channel.   The
        names  associated  with  the  channels  are
        defined  dynamically  by  the  running pro-
        grams.  A message channel  is  active  when
        messages  are being held in the queue asso-
        ciated with the channel or if a program  is
        waiting  for  a  message  from the channel.
        When message channels become inactive  they
        are returned to a free pool and may then be
        reused.

             Once a message is queued on a channel,
        that message will remain in the queue until
        some  program  receives  it.   A  program's
        exiting  to  the  keyboard monitor does not
        remove any pending messages.   This  allows
        one  program to leave a message for another


                                             PAGE 4
        *


        program that will be run at a later time.


               PERFORMANCE ANALYSIS SUPPORT

             For  many  applications  the  keyboard
        monitor  level performance analysis control
        provided by TSX-Plus is adequate.  However,
        in  cases such as analyzing the performance
        of an overlayed program it is necessary  to
        have  control over the performance analysis
        feature  from  the  running  program.   The
        routines  listed  in  Table  4 provide just
        this capability.

          INITPA  Initialize  for  a  performance
                  analysis.
          ISPPA   Stop a performance analysis.
          ISTPA   Start a performance analysis.
          TERMPA  Terminate  from  a  performance
                  analysis.

               Performance Analysis Support.
                         Table 4.


                 REAL TIME PROGRAM SUPPORT

             The real time program support provided
        by  TSX-Plus allows multiple real time pro-
        grams to be run  concurrently  with  normal
        time  sharing  operations.  The basic func-
        tions provided by this facility are  listed
        in Table 5.

             A program must have operator privilege
        to  use any of the real time routines.  The
        real time facilities are available to  both
        normal  jobs  controlled  by  time  sharing
        lines and to detached jobs.  Detached  jobs
        started by time sharing users have operator
        privilege only if the  user  starting  them
        does.

             A basic facility required by many real
        time  programs is the ability to access the
        I/O page which contains the peripheral dev-
        ice  registers.   A normal time sharing job
        does not have this access.  It  is  instead
        mapped  to  a  simulated RMON.  This allows
        programs that directly access offsets  into
        RMON to run correctly.



                                           PAGE 5
        *


          CNVAPA  Convert a virtual address to  a
                  physical address.
          IBICIO  Bit clear a value into the  I/O
                  page.
          IBISIO  Bit set a value  into  the  I/O
                  page.
          ICNINT  Connect an interrupt vector  to
                  a completion routine.
          IPEKIO  Peek at  a  value  in  the  I/O
                  page.
          IPOKIO  Poke a value into the I/O page.
          IRLINT  Release  an  interrupt   vector
                  connection.
          IUNLKM  Unlock a job from memory.
          LKANMY  Lock a job into any memory.
          LKLOMY  Lock a job into low memory.
          MPIOPS  Map the I/O page into the  pro-
                  gram space.
          MPRMPS  Map the simulated RMON into the
                  program space.
          TKCTL   Take exclusive control  of  the
                  system.
          RLCTL   Relinquish exclusive control of
                  the system.
          STPRLV  Set  the  user  mode  processor
                  priority level.

                Real Time Program Support.
                         Table 5.

             A real time program can access the I/O
        page  in  one  of two ways:  it can map the
        I/O page into the program's space;   or  it
        can  leave  the  simulated RMON mapped into
        the program's space and perform peek, poke,
        bit  set, and bit clear operations into the
        I/O page.  It is  much  more  efficient  to
        directly  access  the  device  registers by
        mapping the I/O  page  into  the  program's
        space  than  to use the routines to perform
        each  individual  access.   However,   this
        technique will not work if the program must
        also directly  access  offsets  into  RMON.
        The correct way to access offsets into RMON
        is with the  SYSLIB  routine,  ISPY,  which
        will  work  even  if the I/O page is mapped
        into the program's space.

             The TSX-Plus real time support facili-
        ty  allows a program to connect a real time
        interrupt to a completion routine.  If this
        is done, the completion routine is executed
        each time the specified  interrupt  occurs.
        It  is  possible for several interrupt vec-
        tors to be connected to the same completion


                                             PAGE 6
        *


        routine in a job but it is illegal for more
        than one job to connect to the same  inter-
        rupt vector.

             An execution priority may be specified
        for  each  completion routine.  This is not
        the same as the hardware selected  priority
        of  the interrupt.  All completion routines
        are synchronized with the job  and  run  at
        hardware  priority level zero.  The comple-
        tion routine priority is used  to  schedule
        the completion routines for execution.  The
        available priority levels are zero  through
        seven.   The  execution of a real time com-
        pletion  routine  for  one  job   will   be
        interrupted  and  suspended if an interrupt
        occurs that causes a higher  priority  com-
        pletion  routine  for  another  job  to  be
        queued for execution.  However,  a  comple-
        tion  routine for a given job will never be
        interrupted  to  run   another   completion
        routine  for  the same job even if a higher
        priority completion routine is pending.

             Completion  routine   priorities   one
        through  seven  are  real  time priorities.
        They are higher than the  priorities  given
        to   time  sharing  jobs  and  will  always
        preempt the time sharing jobs.   Completion
        routine  priority  zero  is not a real time
        priority but  rather  a  very  high  normal
        priority.   Such  zero  priority completion
        routines are  time  sliced  in  the  normal
        fashion.   If a completion routine enters a
        wait state it relinquishes  its  real  time
        priority.  Jobs that have real time, inter-
        rupt driven completion routines need not be
        locked in memory.

             In time critical, real  time  applica-
        tions  where  a  program must respond to an
        interrupt with minimum  delay,  it  may  be
        necessary  for  the  job  to lock itself in
        memory to avoid the time consumed  in  pro-
        gram  swapping.   This  facility  should be
        used with caution  since  if  a  number  of
        large  programs  are locked in memory there
        may not be enough space left to  run  other
        programs.

             A running program may  gain  exclusive
        access   to  the  system  to  perform  some
        time-critical task.  The program  may  then
        relinquish this exclusive access when it is
        not needed.


                                             PAGE 7
        *


              SHARED RUN TIME SYSTEM SUPPORT

             TSX-Plus  provides  a  facility   that
        allows  shared  run  time  systems  or data
        areas to be mapped into the address  spaces
        of  multiple  time  sharing  jobs.  Table 6
        lists  the  routines  that   support   this
        feature.

          IASRNT  Associate/disassociate a shared
                  run time system with a job.
          MAPRNT  Map a shared  run  time  system
                  into a job's region.

              Shared Run Time System Support.
                         Table 6.

             Memory space can be conserved by  hav-
        ing  several jobs access a common copy of a
        run time system rather than having to allo-
        cate  space  within  each  job.  Shared run
        time systems are never swapped out of memo-
        ry.   When  a  job is associated with a run
        time system, a portion of the job's virtual
        memory  is  mapped so as to allow access to
        the run time system.


                    SHARED FILE SUPPORT

             Table 7 lists the routines that  offer
        access  to  the  shared file record locking
        facility provided  by  TSX-Plus.   This  is
        useful  in  situations where programs being
        run from several terminals wish to update a
        common  file.   Through  the record locking
        facility  a  program  may  gain   exclusive
        access  to  one  or more blocks in a shared
        file by locking those blocks.  Other  users
        attempting  to lock the same blocks will be
        denied access until the first user releases
        the locked blocks.

          ICKWTS  Check for writes  to  a  shared
                  file.
          IDCLSF  Declare a file to be shared.
          ISVST   Save the  status  of  a  shared
                  file.
          IUALBK  Unlock all locked blocks.
          IUSPBK  Unlock a specific block.
          LKBLK   Try to lock a block.
          LKBLKW  Wait for a block to lock.

                   Shared File Support.
                         Table 7.


                                             PAGE 8
        *


             The recommended procedure for updating
        a  shared  file  being  accessed by several
        users is as follows:

          1.  Open the file.
          2.  Declare the file to be shared.
          3.  Lock all blocks which  contain  the
              desired record.
          4.  Read the locked blocks into memory.
          5.  Update the record.
          6.  Write the  updated  blocks  to  the
              file.
          7.  Unlock the blocks.
          8.  Repeat steps three through seven as
              required.
          9.  Close the file.


                 SYSTEM STATUS INFORMATION

             Information typical of  that  returned
        by  the  SYSTAT  keyboard  command  is made
        available  to  a  running  program  by  the
        routines listed in Table 8.

          ICONTM  Determine the connect time  for
                  a job.
          ICPUTM  Get the CPU time used by a job.
          IEXSTS  Get a job's execution status.
          ILNSTS  Check the status of a line.
          IPGNAM  Get the  name  of  the  program
                  being run by a job.
          IPPNUM  Get   the    project-programmer
                  number for a job.
          MEMPOS  Determine the position of a job
                  in memory.
          MEMUSE  Determine the amount of  memory
                  used by a job.

                System Status Information.
                         Table 8.


              TERMINAL COMMUNICATION SUPPORT

             The routines that allow a running pro-
        gram  to  communicate  with  a terminal are
        listed in Table 9.



                                           PAGE 9
        *


          TRMIN   Accept a string  of  characters
                  from the terminal.
          TRMMSG  Send a message to another  ter-
                  minal.
          TRMOUT  Send a string of characters  to
                  the terminal.

             Terminal Communications Support.
                         Table 9.


                 TERMINAL CONTROL SUPPORT

             The several terminal  control  support
        routines are listed in Table 10.

          BRKCTL  Establish break  sentinal  con-
                  trol.
          HIEFOF  Turn off  the  high  efficiency
                  terminal mode.
          HIEFON  Turn  on  the  high  efficiency
                  terminal mode.
          IACTCH  Check  for  pending  activation
                  characters.
          ITRERR  Check for  terminal  input  er-
                  rors.
          ITRTYP  Determine the terminal type.
          TIMOUT  Set the terminal read time  out
                  value.

                 Terminal Control Support.
                         Table 10.


                 MISCELLANEOUS EMT SUPPORT

             Table 11 lists the routines that  sup-
        port   the   several   miscellaneous   EMTs
        provided by TSX-Plus.

          ISPBLK  Determine the  number  of  free
                  blocks in the spool file.
          ISPY    Return values from  within  the
                  simulated   RMON  (SYSLIB  rou-
                  tine).
          ITSLIC  Determine the TSX-Plus  license
                  number.
          ITSLIN  Determine  the  TSX-Plus   line
                  number.
          MEMSET  Set the memory allocation.

                Miscellaneous EMT Support.
                         Table 11.




                                            PAGE 10
        *


                ODT ACTIVATION MODE SUPPORT

             ODT activation mode may be  turned  on
        and  off  from  within  a  running program.
        Table 12 lists the  routines  that  support
        this  feature.   In this mode TSX-Plus con-
        siders  all  characters  to  be  activation
        characters  except  the  digits, the comma,
        the dollar sign and the semicolon.

          RSRODT  Reset normal activation mode.
          SETODT  Set ODT activation mode.

               ODT Activation Mode Support.
                         Table 12.


                        REFERENCES

        1.  N. A. Bourgeois, Jr.,  "TSXLIB   --   A
            Library  Implementation of the TSX-Plus
            Programmed Requests", 11-490,  DECUS/US
            Chapter  Program Library, Marlboro, MA,
            October 1982.

        2.  S & H Computer Systems, Inc., "TSX-Plus
            Reference   Manual",   Nashville,   TN,
            December 1980.

        3.  S & H Computer Systems, Inc., "TSX-Plus
            Version   2.2  System  Release  Notes",
            Nashville, TN.

        4.  Digital Equipment  Corporation,  "RT-11
            Programmer's     Reference     Manual",
            AA-H378A-TC, Maynard, MA, March 1980.

        5.  S & H Computer Systems, Inc., "TSX-Plus
            Version   3.0  System  Release  Notes",
            Nashville, TN.

        6.  Robert B. Denny,  et  al,  "C  Language
            System  for  RT-11",  11-513,  DECUS/US
            Chapter Program Library, Marlboro,  MA,
            January 1982.