July 14, 1983



         To:      All WP-SATURN users

         From:    R. W. Barnard 
		  Sandia National Laboratories, Div 2565A
		  Albuquerque, NM 87185
		  (505) 844-5115

         Subject: Transfer of .WPS files from RT to RSX (VMS) and back.
                  SATTRN version 1.0



              I have written a program, SATTRN, which will allow the con-
         version and transfer of WP-SATURN* files from RT-11 format to
         FILES-11 (RSX or VMS), format and vice-versa.  SATURN files on RT-
         11 are very straightforward, with no extra carriage returns, or
         extra control characters.  On FILES-11, there are carriage returns
         inserted every 80 characters in wrapped text.  These are necessary
         to make the file readable by the FILES-11 file handlers, but it
         makes RT-11 files not readable on RSX without modification. 
         FILES-11 files used in RT-11 SATURN have unnecessary carriage re-
         turns in wrapped text.

              SATTRN runs on RT-11.  To convert a RT-11 file to FILES-11
         format, the program is run to create a new file; this file is then
         transferred to the RSX or VMS system with the FLX utility.  Trans-
         ferring a file from RSX to RT is done by using FLX to make a RT
         copy and running the program to make a new file reformatted for RT
         SATURN.

              Using the program is simplicity itself.  It has a filespec
         parser in it, so only the minimum information is necessary to
         specify which file is to be converted.  The program expects to
         find a file on device DK: with an extension .WPS.  In this case,
         the user needs only enter the actual file name (e.g., if the file
         in question is DK:REPORT.WPS, the user need type only REPORT). 
         The converted output file will be found on the input device and
         will have an extension .WPX for the conversion RT -> RSX, and .WPT
         for the conversion RSX -> RT.  Both the input device specification
         and extension may be overridden by actually specifying them when
         the program asks (e.g., specifying DY1:REPORT.ABC will produce the
         output file DY1:REPORT.WPn - n=T or X, as above).  The program
         asks which direction the transfer is to be; an unacceptable number
         will cause the program to keep asking until it is satisfied. 
         While the program is doing the converting, it tells the user which
         block it is doing to keep him from wondering if anything is really
         happening.  At the conclusion, it tells him the name of the new,
         converted file.






              When using the FLX utility to transfer the file to or from
         the RSX or VMS system, the /FA (formatted ASCII) switch should be
         used (e.g.  =DX:REPORT.WPX/RT/FA, or DX:/RT/FA=REPORT.WPS).  FLX
         terminates with a warning message that there was a bad ASCII
         record format, but don't fret - the file has been transferred su-
         cessfully.  However, to ensure that the last line really does get
         transferred, the SATTRN program puts in an extra <LF> at the end
         of the file.  The next time you are editing the converted and
         transferred file, go the the bottom and remove the single "%"
         which is there.

	* SATURN is a Registered Trademark of Saturn Systems, Inc.


	 14-Oct-83
	PARSE .OBJ    15  31-Aug-83      SATTRN.FOR     7  11-Jul-83
	SATTRN.DOC     7  14-Oct-83      SATTRN.SAV    29  11-Jul-83
	 4 Files, 58 Blocks