RT-11 Pseudo-Handlers to emulate EIS, FIS, and FPU instructions.

	by Paul Lustgraaf
	   32 Carver Hall
	   Iowa State University
	   Ames, IA  50011
	   515-294-0324

	Adapted from EI.SYS by Dr. P. C. Waggett.

	This is a collection of three pseudo-device handlers for RT-11
	which will enable programs that require certain optional hardware
	to be run on PDP-11's that can not or just do not have that option.
	For example, FORTRAN-77 requires the FPU option, but the PDP-11/03
	does not have that option.  However, by using this package, F77
	CAN be run on an 11/03.

	The handlers included are:

	EI	Supports EIS instructions plus a few others:
		(MUL, DIV, ASH, ASHC, XOR, SXT, SOB)
		Requires 498. words of memory.

	FI	Supports FIS instructions as used on the 11/03 and 11/40:
		(FMUL, FDIV, FSUB, FADD)
		Requires 428. words of memory.

	FP	Supports FPU instructions as used on 11/45, 11/23, etc.
		Requires 1476. words of memory.

	METHOD OF OPERATION


	In order to enable emulation, the appropriate handler(s) must
	be loaded and set ON.  For example:

		LOAD FP: (or EI or FI)
		SET FP ON
		UNLOAD FP:
		LOAD FP:

	This sequence of commands, which may be included in your
	startup command file, loads the handler into memory permanently
	and then steals the interrupt vector at location 10 from the
	monitor.  If you are not intimately familiar with the PDP-11
	architecture, I will explain briefly what is happening here.
	When an illegal instruction is executed, the PDP will trap
	to the address stored at location 10.  The handler will
	intercept any such trap and will inspect the instruction
	causing the trap to see if it is one of the instructions
	the handler is able to emulate.  If so, the operation will
	be done and control will be returned to the program.  If not,
	the handler will pass control to the address previously
	pointed to by location 10.  Since the previous trap address
	is stored inside the handler in memory and RT-11 only changes
	the handlers image on disk, the unload-load sequence must be
	done in order to load the previous trap address in memory.
	Note that this mechanism allows us to have many such handlers
	chained to from location 10.

	If you no longer need to use these pseudo-handlers and you
	wish to remove them from memory, you must first issue the
	command to turn them off, then unload them.

	SET FP OFF
	UNLOAD FP:

	The set OFF command restores the previous trap address to
	location 10.  If you have more than one such pseudo-handler
	in memory, you MUST turn them off in EXACTLY the REVERSE
	order you turned them on.  Any attempt to unload one of
	these handlers before turning it off will probably cause
	the system to crash at some unknown future point.
	DON'T DO IT!

	RESTRICTIONS


	These handlers are intended to allow programs to be run on
	machines which would not otherwise support their execution.
	These handlers will, of course, execute much more slowly
	than the equivalent hardware.  Unlike the original EI.SYS,
	these handlers do not use self-modifying code, so they
	may be used in multi-tasking systems.

	1.  Execution under XM may work, but has not been tested.
	    The problem is that under XM the handler has to run
	    at priority 7 in order to lock out all interrupts and
	    prevent XM from doing a context switch.  Needless to
	    say, the length of a typical fixed or floating point
	    instruction may adversely affect the interrupt
	    response time.  ANYONE CARE TO WORK ON THIS PROBLEM?

	2.  An attempt has been made to emulate the exact behavior
	    of pathological instructions, particularly those which
	    cause some type of trap.  Due to the complexity of this
	    problem, however, some differences may exist with the
	    hardware behavior.  USER BEWARE!

	3.  FP does not implement the interrupt for undefined
	    variables (sometimes referred to as -0).

	4.  The addition/subtraction routine in FI: sometimes
	    differs in the least significant bit from the result
	    given by the hardware.  I believe this is due to some
	    difference in the rounding algorithm.  HELP!

	5.  NO GUARANTEES expressed or implied, etc. etc. etc.

	PERFORMANCE


	Two test programs are included, TESTR4 and TESTR8, which
	are versions of a test program published by Bill Savage
	in the September 1983 issue of Dr. Dobb's Journal.  The
	correct result is exactly 2500 and it is very educational
	to try these programs on different machines.  The following
	results were all obtained using FORTRAN 4 with the indicated
	options:

			Code	Hardware
	Program	Machine	Option	Option		Result		Time(sec)

	TESTR4	11/03	THR	none		2631.716	 145
	TESTR4	11/03 	EIS	none (EI:)	2631.716	 714
	TESTR4	11/03	FIS	none (FI:)	2972.816	 314
	TESTR4	11/03	FPU	none (FP:)	2741.048	1017
	TESTR4	11/03	EIS	EIS		2631.716	 103
	TESTR4	11/03	FIS	FIS		2631.716	  28
	TESTR4	11/23	FPU	FPU		2741.048	  25

	TESTR8	11/03	EIS	EIS		2500.000	 556
	TESTR8	11/03	FIS	FIS		2500.000	 494
	TESTR8	11/03	FPU	none (FP:)	2500.000	1551
	TESTR8	11/23	FPU	FPU		2500.000	  60


		The moral of the story is:
	
	If you have the source and your language gives you the choice,

		RE-COMPILE FOR YOUR OWN HARDWARE!

	Otherwise, you may be able to limp along using these handlers.

			GOOD LUCK!