UU      UU      CCCCCC      LL                      
                UU      UU      CCCCCC      LL                      
                UU      UU    CC      CC    LL                ++    
                UU      UU    CC      CC    LL                ++    
                UU      UU    CC            LL                ++    
                UU      UU    CC            LL                ++    
                UU      UU    CC            LL            ++++++++++
                UU      UU    CC            LL            ++++++++++
                UU      UU    CC            LL                ++    
                UU      UU    CC            LL                ++    
                UU      UU    CC      CC    LL                ++    
                UU      UU    CC      CC    LL                ++    
                  UUUUUU        CCCCCC      LLLLLLLLLL              
                  UUUUUU        CCCCCC      LLLLLLLLLL              










                              USER COMMAND LINKAGE-plus

                                       V07.54a

                                     12 May 1986






                                  William K. Walker

                               Monsanto Research Corp.
                                    P. O. Box 32
                                Miamisburg, OH  45342
                                   (513) 865-3557







                       SPECIAL NOTE TO SCIENTISTS/RESEARCHERS

                                  Read the manual!

                                                                    Page ii



                             TABLE OF CONTENTS



        1.0  ACKNOWLEDGEMENTS . . . . . . . . . . . . . . . . . . . . . . 1

        2.0  IMPORTANT NOTICE . . . . . . . . . . . . . . . . . . . . . . 1

        3.0  BEFORE YOU GET STARTED . . . . . . . . . . . . . . . . . . . 1

        4.0  ABOUT THIS DOCUMENT  . . . . . . . . . . . . . . . . . . . . 2

        5.0  INTRODUCTION . . . . . . . . . . . . . . . . . . . . . . . . 3
        5.1  UCL+ Differences . . . . . . . . . . . . . . . . . . . . . . 3
        5.2  UCL+ Enhancements  . . . . . . . . . . . . . . . . . . . . . 4

        6.0  INSTALLATION . . . . . . . . . . . . . . . . . . . . . . . . 6
        6.1  Installing UCL.SAV . . . . . . . . . . . . . . . . . . . . . 6
        6.1.1  Installing UCL.SAV On RT-11 Systems  . . . . . . . . . . . 6
        6.1.1.1  Installation As A UCL (UCL.SAV)  . . . . . . . . . . . . 6
        6.1.1.2  Installation As A UCF (UCF.SAV)  . . . . . . . . . . . . 7
        6.1.2  Installing UCL.SAV On TSX-Plus Systems . . . . . . . . . . 7
        6.1.2.1  Installation As A UCL (TSXUCL.SAV) . . . . . . . . . . . 8
        6.1.2.2  Installation As A UCI (UKMON.SAV)  . . . . . . . . . . . 8
        6.2  Installing UCLXM.SAV . . . . . . . . . . . . . . . . . . . . 8
        6.2.1  Installing UCLXM.SAV On RT-11 Systems  . . . . . . . . . . 9
        6.2.1.1  Installation As A UCL (UCL.SAV)  . . . . . . . . . . . . 9
        6.2.1.2  Installation As A UCF (UCF.SAV)  . . . . . . . . . . .  10
        6.2.2  Installing UCLXM.SAV On TSX-Plus Systems . . . . . . . .  11
        6.2.2.1  Installation As A UCL (TSXUCL.SAV) . . . . . . . . . .  11
        6.2.2.2  Installation As A UCI (UKMON.SAV)  . . . . . . . . . .  12
        6.3  Installing The CI Handler  . . . . . . . . . . . . . . . .  13
        6.4  Installing UCL+ HELP . . . . . . . . . . . . . . . . . . .  13
        6.5  Installing The UCL+ Distribution Under RTEM  . . . . . . .  14

        7.0  HOW IT WORKS . . . . . . . . . . . . . . . . . . . . . . .  16
        7.1  RT-11 Command Processing With UCL Support  . . . . . . . .  16
        7.2  RT-11 Command Processing With UCF Support  . . . . . . . .  17
        7.3  TSX-Plus Command Processing  . . . . . . . . . . . . . . .  17

        8.0  SYMBOLS  . . . . . . . . . . . . . . . . . . . . . . . . .  19
        8.1  Defining Symbols . . . . . . . . . . . . . . . . . . . . .  19
        8.2  Deleting Symbols . . . . . . . . . . . . . . . . . . . . .  21
        8.3  Running UCL+ Directly  . . . . . . . . . . . . . . . . . .  21
        8.4  Advanced Techniques  . . . . . . . . . . . . . . . . . . .  22
        8.4.1  Using The Quote Character ("|")  . . . . . . . . . . . .  22
        8.4.2  Argument String Parsing ("^n") . . . . . . . . . . . . .  23

        9.0  "HARD-WIRED" COMMANDS  . . . . . . . . . . . . . . . . . .  25
        9.1  CD Command . . . . . . . . . . . . . . . . . . . . . . . .  25
        9.2  CHAIN Command  . . . . . . . . . . . . . . . . . . . . . .  25
        9.3  DISPLAY Command  . . . . . . . . . . . . . . . . . . . . .  26

                                                                   Page iii



        9.4  ERASE Command  . . . . . . . . . . . . . . . . . . . . . .  27
        9.5  LIST Command . . . . . . . . . . . . . . . . . . . . . . .  27
        9.6  NOSL/SLON Command  . . . . . . . . . . . . . . . . . . . .  28
        9.7  PASS_ON Command  . . . . . . . . . . . . . . . . . . . . .  29
        9.8  PATH Command . . . . . . . . . . . . . . . . . . . . . . .  29
        9.9  PROMPT Command . . . . . . . . . . . . . . . . . . . . . .  30
        9.10  RECALL Command  . . . . . . . . . . . . . . . . . . . . .  30
        9.11  RELOAD command  . . . . . . . . . . . . . . . . . . . . .  31
        9.12  RNO Command . . . . . . . . . . . . . . . . . . . . . . .  31
        9.13  STORE Command . . . . . . . . . . . . . . . . . . . . . .  32
        9.14  UCI_MODE Command  . . . . . . . . . . . . . . . . . . . .  33

        10.0  CI HANDLER  . . . . . . . . . . . . . . . . . . . . . . .  34

        11.0  ERROR MESSAGES  . . . . . . . . . . . . . . . . . . . . .  36
        11.1  UCL+ "Warning" Messages (?UCL-W-...)  . . . . . . . . . .  36
        11.2  UCL+ "Fatal" Messages (?UCL-F-...)  . . . . . . . . . . .  36
        11.3  Global Region Loader Errors (?UCLGRL-F-...) . . . . . . .  40
        11.4  CI Handler Errors (?CI-...) . . . . . . . . . . . . . . .  40

        12.0  EXAMPLES  . . . . . . . . . . . . . . . . . . . . . . . .  42

        13.0  V7 RELEASE NOTES  . . . . . . . . . . . . . . . . . . . .  43

        14.0  APPLICATION NOTES . . . . . . . . . . . . . . . . . . . .  45
        14.1  Executing Command/Control Files "By-Name" . . . . . . . .  45
        14.2  Changing The Effect Of RNO/DEFAULTS . . . . . . . . . . .  45
        14.3  Sending Escape Sequences To The Printer . . . . . . . . .  45
        14.4  Moving From UCL+ V6x To UCL+ V7.xx  . . . . . . . . . . .  46
        14.5  Moving From UCL+ V6x Or V7.xx To UCL+ (XM) V7.xx  . . . .  47
        14.6  Disabling Argument Parsing  . . . . . . . . . . . . . . .  47
        14.7  Hints and Kinks: UCF, UCI, And SET UCL FIRST  . . . . . .  48
        14.7.1  Interception Of Monitor Commands  . . . . . . . . . . .  48
        14.7.2  Improper Expansion Of Monitor Commands  . . . . . . . .  49
        14.7.3  Single Key Commands . . . . . . . . . . . . . . . . . .  49
        14.8  UCL+ Assembly Conditionals  . . . . . . . . . . . . . . .  50
        14.9  Modifying RT-11 To Change The UCL/UCF Device/File
              Name  . . . . . . . . . . . . . . . . . . . . . . . . . .  50
        14.10  Modifying TSX-Plus To Change The UCL/UCI Defaults  . . .  52
        14.11  Controlling Command Line Factoring . . . . . . . . . . .  52
        14.12  Patching UCL+ For RT-11 V5.1 . . . . . . . . . . . . . .  54

        15.0  REPORTING PROBLEMS AND SUGGESTIONS  . . . . . . . . . . .  55

        16.0  WISH LIST . . . . . . . . . . . . . . . . . . . . . . . .  56

        17.0  UCL+ COMMAND AND SYNTAX SUMMARY . . . . . . . . . . . . .  57

          UCL+ -- User Command Linkage Program - V07.54a             Page 1
                  Spring 1986 DECUS Release


          1.0  ACKNOWLEDGEMENTS 

          Throughout  this  document,  reference  is  made to the RT-11 and
          TSX-Plus operating systems.  RT-11 is a product of Digital Equip-
          ment  Corporation,  Maynard,  MA;  TSX-Plus is a product of S & H
          Computer Systems, Nashville, TN.  

          The  principal field testers for this version were Rally Barnard,
          John Crowell, Ray Moran, Bob Walraven, and,  of  course,  myself.
          Although  I  get the credit for the most obscure bug, Rally takes
          top field test honors overall for  his  combination  of  quality,
          volume, thoroughness, and tenacity.  


          2.0  IMPORTANT NOTICE 

          IF  YOU ARE GOING TO USE THIS VERSION OF UCL+ UNDER AN RT-11 V5.1
          MONITOR (OR EQUIVALENT RTEM-11 MONITOR), YOU MUST APPLY THE PATCH
          IN  SECTION 14.12 FOR UCL+ TO WORK PROPERLY (IT'S NOT MY FAULT --
          IT'S DEC'S FAULT).  


          3.0  BEFORE YOU GET STARTED 

          Before  you  start  using  UCL+,  there are a few things that you
          should keep in mind.  

               1.  You  don't  have  to get fancy.  With a couple of fairly
                   minor exceptions, you can just  use  UCL+  as  a  direct
                   replacement  for  your  distributed UCL.  Try the sneaky
                   stuff once you get addicted to having it around.  

               2.  If you intend to use the extended features, particularly
                   UCF or UCI_MODE, make sure you read  the  available  do-
                   cumentation.   Note  that  there are a number of goodies
                   contained in the application notes (section 14.0) at the
                   end of this manual.  

               3.  READ  THE  INSTALLATION  INSTRUCTIONS  (section 6.0) for
                   your particular environment.  

               4.  RTEM users can assume that the material concerning RT-11
                   also applies to the RTEM  equivalent  environment.   The
                   significant  exceptions  are the installation procedures
                   and the use of the UCF facility.  


          UCL+ -- User Command Linkage Program - V07.54a             Page 2
                  Spring 1986 DECUS Release


          4.0  ABOUT THIS DOCUMENT 

          A fair amount of effort has gone into this manual to give reason-
          ably comprehensive coverage of the contents of the UCL+ distribu-
          tion  kit.   It  does  not,  however, attempt to include material
          already available in the relevant operating system documentation,
          nor is there extensive coverage of internals.  

          Where  examples  are  felt to be necessary, the following conven-
          tions are followed:  

                o  examples,  unless  otherwise  noted, are for RT-11 V5.0;
                   no "factoring" is used 

                o  in most examples, operator input is underlined 

                o  all  visible lines of input are assumed to be terminated
                   with a carriage return 

                o  "non-printing"  characters  and  control  characters are
                   identified by an abbreviation enclosed by angle brackets
                   ("<>");  e.g., 
                    -  <ret>    = carriage return (CR) 
                    -  <esc>    = escape (ESC) 
                    -  <ctrl/C> = control-C (ETX) 
                    -  <ctrl/Y> = control-Y (EM) 


                o  examples and procedure descriptions, except where noted,
                   assume that all  necessary  files  are  on  the  default
                   device (DK:) 


          UCL+ -- User Command Linkage Program - V07.54a             Page 3
                  Spring 1986 DECUS Release


          5.0  INTRODUCTION 

          UCL+  is  a user command linkage program for use with RT-11 V5 or
          later, RTEM V2.0 or later, and TSX-Plus V4.1 or  later  monitors.
          It contains full support for the user command related features of
          these operating systems.  These include:  

                o  UCL - User Command Linkage (RT-11, RTEM, and TSX-Plus) 

                o  UCI  - User Command Interpreter (TSX-Plus, starting with
                   V5.0) 

                o  UCF - User Commands First (RT-11, starting with V5.2) 

          In  general,  UCL+  can  be  used as a direct replacement for the
          "UCL's" distributed with these operating systems.  There are some
          relatively  minor  incompatibilities between UCL+ and the distri-
          buted versions, as well as a substantial number of  enhancements.
          The remainder of this section summarizes these differences.  


          5.1  UCL+ Differences 

          UCL+  is  upward compatible with the UCL program distributed with
          RT-11 (and the TSX-Plus TSXUCL program) with the following excep-
          tions.  

                o  UCL+  accepts  the  "VMS-like"  symbol definition syntax
                   used by DEC's UCL, but  it  ignores  it.   Instead,  the
                   number  of  characters  that  must be typed to specify a
                   command or symbol unambiguously is a  function  of  con-
                   text.   E.g.,  if  you have defined two symbols starting
                   with "S", "SUPPER"  and  "SUPER",  you  must  type  four
                   characters  to  distinguish  between  them.  However, if
                   they are "SIPPER" and "SUPER", only two  characters  are
                   necessary.  

                o  UCL+  currently  allows symbol names of no more than six
                   characters.  If you use a longer name in  a  definition,
                   UCL+  will  truncate  it  to  six characters and issue a
                   warning message to that effect.  

                o  UCL+  is  different  from the TSX-Plus TSXUCL program in
                   that all commands and symbols are "global", rather  than
                   local  to  a  specific user.  In addition, UCL+ does not
                   "forget" symbol definitions after a user logs off.  


          UCL+ -- User Command Linkage Program - V07.54a             Page 4
                  Spring 1986 DECUS Release


          5.2  UCL+ Enhancements 

          UCL+ contains a number of extensions to the distributed RT-11 and
          TSX-Plus UCL programs.  The following list is a  summary  of  the
          most  important ones.  Refer to the relevant sections of this do-
          cument for further detail.  

                o  UCL+  is  optimized to minimize disk access.  The symbol
                   definitions are contained in internal tables rather than
                   a  separate data file and an "execute-immediate" mode is
                   available for commands that  are  defined  in  terms  of
                   other UCL commands.  

                o  More than one symbol definition can be deleted in a sin-
                   gle command line via the  ERASE  command.   All  current
                   symbol definitions can be removed with ERASE *.  

                o  You can chain to additional "UCL's".  

                o  A  "run-by-name  path"  can be defined which extends the
                   monitor's "run-from-SY:" default.  

                o  You  can  STORE/RECALL  the  program  settings to/from a
                   separate file.  You can do this in  either  "binary"  or
                   "journal" mode.  Journal files can be edited.  

                o  A  PASS_ON  command is included that allows you to force
                   UCL+ to "pass-on" a given command  string  to  the  next
                   program  in the chain (the default mode) or to a program
                   that you specify.  

                o  Symbol  expansions can be DISPLAYed with or without exe-
                   cution.  The DISPLAY command can also be used to  output
                   ASCII  strings  to  the  console  or  printer (handy for
                   sneaky escape sequences).  

                o  Provision   has  been  made  to  make  the  addition  of
                   "hard-wired" commands fairly  easy.   These  are,  typi-
                   cally,  commands  that are too complex to define as sym-
                   bols.   Two  commands  of  this  type  are  included  as
                   examples   (and  because  the  author  finds  them  very
                   handy!):  a CD command which changes the default  device
                   (works  a  lot like the CP/M CD command) and an RNO com-
                   mand which is a DCL-style command  for  use  with  DECUS
                   RUNOFF version M02.4.  

                o  If  you  run  it  directly,  UCL+ will accept lower-case
                   input and most control characters.  

                o  You  may,  in  addition  to the symbol definitions, list
                   other program parameters as well.  List  output  may  be
                   directed to devices/files other than the console.  

          UCL+ -- User Command Linkage Program - V07.54a             Page 5
                  Spring 1986 DECUS Release


                o  UCL+  can  be  employed,  via the UCI_MODE command, as a
                   "User Command Interpreter"  (UCI).   This  functionality
                   was  added  with  UCL+  V7  to take advantage of the UCI
                   facility in TSX-Plus.  

                o  You may dynamically redefine the prompt string issued by
                   UCL+.  

                o  A "quoting" facility is available to override the effect
                   of "operator" characters.  

                o  In order to allow more complex command definitions, UCL+
                   supports the parsing of argument strings into as many as
                   nine sub-strings.  

                o  If you have an RT-11 V5.2 or later monitor, you can take
                   advantage of some additional features:  

                    -  A  CI  "handleroid"  is included which allows you to
                       control and display the action of the  various  Com-
                       mand  Language  Interpreters  (CLI's).  For example,
                       SET CI UCF turns on the User  Commands  First  (UCF)
                       facility.  

                    -  A  special  version  of UCL+ is available for the XM
                       monitor.  Almost the entire program is  continuously
                       resident  in a global region in extended memory.  It
                       is very fast, and uses only 512 (decimal)  words  of
                       low memory.  



          UCL+ -- User Command Linkage Program - V07.54a             Page 6
                  Spring 1986 DECUS Release


          6.0  INSTALLATION 

          This  section of the manual contains information on the installa-
          tion of the major components of the UCL+ distribution.   As  with
          all  sections  of  this  document, a basic familiarity with RT-11
          and, if applicable, TSX-Plus is assumed.  

          In  all of the examples in this section, the UCL+ distribution is
          assumed to be on  the  default  device,  DK:.   Examples,  unless
          otherwise  noted, will work on RT-11 V5.0 or later systems and/or
          the  functionally  equivalent  version  of  TSX-Plus   or   RTEM.
          TSX-Plus  users should also note that the installation procedures
          for TSX assume that the user has sufficient privilege to  execute
          them  --  i.e.,  installation will be probably be accomplished by
          the system manager.  

          The  examples  also  assume that you are going to use the default
          program names when you install the various components.  There are
          cases  where  this  may not be true (for example, if you use both
          the SJ and XM RT-11 monitors).  See the application  notes,  sec-
          tions 14.9 and 14.10, for information on changing these defaults. 

          If  you  are converting from any version of UCL+ prior to V07.50,
          you should also read section 8.4 and the application note in sec-
          tion 14.6.  


          6.1  Installing UCL.SAV 

          UCL.SAV  is  the  "vanilla" UCL+ program.  It will run under ver-
          sions of RT-11 beginning  with  V5.0  (and  the  equivalent  RTEM
          releases)  and  versions  of  TSX-Plus starting with V4.1.  As it
          does a context check on start-up, it is not necessary to generate
          a  special  version  for either operating system.  It is, in fact
          (and by design), possible to use the same copy of  UCL+  in  both
          environments.  The installation procedure may differ, however, in
          some cases.  


          6.1.1  Installing UCL.SAV On RT-11 Systems  - For all versions of
          RT-11, UCL+ serves as a direct replacement  for  the  distributed
          UCL  program  (note  that  the V5.0 distribution contained no UCL
          program).  For those versions of RT-11 supporting  User  Commands
          First (UCF), UCL+ can be used as a UCF also (except RTEM).  


          6.1.1.1  Installation  As  A  UCL (UCL.SAV)  - If you are already
          using a previous version of UCL+, you should first save your cur-
          rent symbol/status data.  For example, 

                    .STORE SY:CURENT                     _______________


          UCL+ -- User Command Linkage Program - V07.54a             Page 7
                  Spring 1986 DECUS Release


          To install UCL.SAV, just copy it to the system device:  

                    .COPY UCL.SAV SY:UCL.SAV                     _______________________

          If you are not a previous UCL+ user, you're done.  Otherwise, the
          next step depends on whether your old UCL+ is V6x or  V7.xx.   If
          it  is  V6x,  apply  the patch described in the application notes
          (section 14.4).  If it is V7.xx, you can skip the patch and type 

                    .RECALL SY:CURENT                     ________________

          to load the symbol/status data into your new copy of UCL+.  

          Note  that  the  above  procedure  is  the same for TSX-Plus V4.1
          users.  


          6.1.1.2  Installation  As A UCF (UCF.SAV)  - Beginning with V5.2,
          RT-11 supports User Commands First (UCF) as well as UCL.  If  you
          wish  to  use  UCL+  as a UCF, you need only make a copy with the
          appropriate name and turn on UCF support in the monitor.   Unless
          you  are doing something sneaky, the installation procedure is as
          follows (note that this command sequence is for RT-11 V5.2):  

                    .copy ucl.sav sy:ucf.sav                     _______________________

                    .r ucf                     _____
                    UCL> prompt "ucf> "                         ______________
                    ucf> <ctrl/C>                         ________

          The  easiest  way to invoke UCF processing is via the CI handler.
          I.e., 

                    .set ci ucf,show                     _______________
                    ?CI-I-CLI's enabled: UCF DCL CCL UCL

          When  UCL+  runs as UCF, it automatically detects this condition,
          and processes commands appropriately.  


          6.1.2  Installing  UCL.SAV On TSX-Plus Systems  - If you are run-
          ning TSX-Plus V4.1, installation is the same as it is  for  RT-11
          (section 6.1.1).  If you are running V5.0 or later, the procedure
          is somewhat different.  

          Note  that  you should make sure that UCL support is enabled when
          you execute your initial TSGEN.  

          Also  note that TSX-Plus users must have read/write access to the
          UCL+ program if they are to be able to define or  erase  symbols.
          The  easiest  way  to  accomplish  this  is  to include an ACCESS
          command in the user's logon command file.  For example:  

          UCL+ -- User Command Linkage Program - V07.54a             Page 8
                  Spring 1986 DECUS Release



                    ACCESS SY:TSXUCL.SAV 


          6.1.2.1  Installation As A UCL (TSXUCL.SAV)  - If you are already
          using a previous version of UCL+, you should first save your cur-
          rent symbol/status data.  For example, 

                    .STORE SY:CURENT                     _______________

          To install UCL.SAV, just copy it to the system device.  Note that
          the default TSX-Plus name for UCL is TSXUCL.SAV.  

                    .COPY UCL.SAV SY:TSXUCL.SAV                     __________________________

          If  you  are  not  a previous UCL+ user, you're done, and you can
          proceed to define the symbols that you intend to use.  Otherwise,
          the  next  step depends on whether your old UCL+ is V6x or V7.xx.
          If it is V6x, apply the patch described in the application  notes
          (section 14.4).  If it is V7.xx, you can skip the patch and type 

                    .RECALL SY:CURENT                     ________________

          to load the symbol/status data into your new copy of UCL+.  


          6.1.2.2  Installation  As  A  UCI (UKMON.SAV)  - UCL+ can also be
          used on a TSX-Plus V5.0 or later system as a User Command  Inter-
          preter  (UCI).   The  following example illustrates a typical in-
          stallation with the default UCI name of UKMON.SAV.  Note that the
          command  prompt  is changed during this procedure to help distin-
          guish the "UCI" copy of UCL+ from other copies that  might  exist
          on the same system as "UCL's".  

                    .COPY UCL.SAV SY:UKMON.SAV                     _________________________
                    .R UKMON                     _______
                    UCL> uci "ukmon> "                         _____________
                    ukmon> <ctrl/C>                           ________

          You would invoke UKMON.SAV as a UCI by typing 

                    .SET KMON UCI                     ____________


          6.2  Installing UCLXM.SAV 

          UCLXM.SAV  is a special version of UCL+ for use with the extended
          memory (XM) monitor on systems running RT-11 V5.2 or  later.   It
          can also be used under TSX-Plus monitors that are compatible with
          RT-11 V5.2 (TSX-Plus V6.0 or later).  


          UCL+ -- User Command Linkage Program - V07.54a             Page 9
                  Spring 1986 DECUS Release


          UCLXM  has  a minimal low memory presence -- typically, about 512
          (decimal) words.  The remainder of the program, about 10K  words,
          resides in a global region in extended memory.  

          In  the RT-11 environment, UCLXM is significantly faster than the
          "vanilla" UCL+ due to the fact that all but a two-block "stub" is
          permanently  memory  resident.   UCLXM  is  a  direct, functional
          replacement  for  the  distributed  UCL  program.   As  with  the
          "vanilla" UCL+ program, UCLXM can also be used as a UCF program. 

          Under TSX-Plus, speed improvement resulting from the use of UCLXM
          instead of the regular UCL+ program will depend on  such  factors
          as  the  amount  of memory available for cache, and the amount of
          swapping normally seen on the system.  It is interesting to note,
          however,  that  the  "low memory" image of UCLXM is less than 512
          bytes (a user job size of 8kb under a V6.01  monitor).   This  is
          due  to the fact that the bulk of the program (20kb) resides in a
          shared global region.  If multiple copies  of  UCL+  are  running
          simultaneously,  they are all sharing the same global region and,
          thus, sharing most of their run-time code.  


                                     WARNING!!!

               Do not attempt to run UCLXM.SAV under a monitor that is
               not compatible with RT-11 V5.2 or later.   The  results
               are unpredictable -- your system may crash.  




          6.2.1  Installing UCLXM.SAV On RT-11 Systems  - Installing the XM
          version of UCL+ under RT-11 is a reasonably straightforward  pro-
          cess,  although  there  may be some special considerations if you
          are "porting" from an earlier, non-XM version of UCL+.  

          All examples in this section are for an RT-11 V5.2 monitor.  


          6.2.1.1  Installation  As  A  UCL (UCL.SAV)  - If you are already
          using a previous version of UCL+, you should first save your cur-
          rent symbol/status data.  For example, 

                    .store sy:curent                     _______________

          If  your  previous  version  of UCL+ was also the XM version, you
          should REMOVE the global region.  

                    .remove ucl                     __________

          To install UCLXM.SAV, copy it to the system device as UCL.SAV.  


          UCL+ -- User Command Linkage Program - V07.54a            Page 10
                  Spring 1986 DECUS Release


                    .copy uclxm.sav sy:ucl.sav                     _________________________

          If  you  are  not  a previous UCL+ user, you're done, and you can
          proceed to define the symbols that you intend to use.  Otherwise,
          the  next  step depends on whether your old UCL+ is an XM version
          or a non-XM version.  If it is a non-XM version of  UCL+,  follow
          the  procedure  described in the application notes (section 14.5)
          to transport your symbol definitions.  If your previous  UCL+  is
          an XM version, you can just type 

                    .recall sy:curent                     ________________

          to load the symbol/status data into your new copy of UCL+.  

          Finally,  it  is  a  good  idea to run UCL and change the command
          prompt.  

                    .r ucl                     _____
                    UCL> prompt "uclxm> "                         ________________
                    uclxm> <ctrl/C>                           ________


          6.2.1.2  Installation  As A UCF (UCF.SAV)  - Beginning with V5.2,
          RT-11 supports User Commands First (UCF) as well as UCL.  If  you
          wish  to  use  UCL+  as  a  UCF, you need to make a copy with the
          appropriate name and turn on UCF support in the monitor.   Unless
          you  plan  to do something sneaky (like letting UCL and UCF share
          the same global region -- risky!), you must also patch  your  UCF
          so  that  it will establish it's own, unique global region in ex-
          tended memory.  The installation procedure is as follows.  

          Remove  the UCF global region and create a new copy of UCF.SAV on
          SY:.  

                    .remove ucf                     __________

                    .copy uclxm.sav sy:ucf.sav                     _________________________

          Next,  apply  the  customization  patch to cause UCF.SAV to use a
          unique global region.  

                    .sipp sy:ucf.sav/a                     _________________
                    Base?    <ret>                             _____
                    Offset?  1024                             ____

                      Base       Offset      Old  New?
                       000000     001024  101704  ;R                                                  __
                       000000     001024   <UCL>  ;RUCF                                                  _____
                       000000     001026   <   >  <ctrl/Y>                                                  ________

          Following this, it is recommended that you run UCF and change the
          command prompt.  

          UCL+ -- User Command Linkage Program - V07.54a            Page 11
                  Spring 1986 DECUS Release


                    .r ucf                      _____
                    UCL> prompt "ucfxm> "                          ________________
                    ucfxm> <ctrl/C>                            ________

          The  easiest  way to invoke UCF processing is via the CI handler.
          I.e., 

                    .set ci ucf,show                     _______________
                    ?CI-I-CLI's enabled: UCF DCL CCL UCL

          When  UCL+  runs as UCF, it automatically detects this condition,
          and processes commands appropriately.  


          6.2.2  Installing UCLXM.SAV On TSX-Plus Systems  - Installing the
          XM version of UCL+ under TSX-Plus is similar to  the  RT-11  pro-
          cedure.   As with RT-11, there may be some special considerations
          if you are "porting" from an earlier, non-XM version of UCL+.  

          In  addition, the XM version of UCL+ must be able to use TSX-Plus
          global region support.   This  can  be  accomplished  by  editing
          TSGEN.MAC  prior  to building TSX-Plus, or through the use of the
          INSTALL command.  PRO/TSX-Plus users must use  the  INSTALL  com-
          mand,  since  TSGEN.MAC  is not included in the PRO distribution.
          For a V6.01 monitor, the command is as follows 

                    install add sy:tsxucl.sav/priv=(nodebug,sysgbl) 

          The  best  place to put this command is in a detached job command
          file that is executed when TSX-Plus is booted.  

          Also  note that TSX-Plus users must have read/write access to the
          UCL+ program if they are to be able to define or  erase  symbols.
          The  easiest  way to accomplish this is to include an ACCESS com-
          mand in the user's logon command file.  For example:  

                    ACCESS SY:TSXUCL.SAV 

          All examples in this section are for a TSX-Plus V6.0 monitor.  


          6.2.2.1  Installation As A UCL (TSXUCL.SAV)  - If you are already
          using a previous version of UCL+, you should first save your cur-
          rent symbol/status data.  For example, 

                    .store sy:curent                     _______________

          If  your  previous  version  of UCL+ was also the XM version, you
          should REMOVE the global region.  

                    .remove ucl                     __________


          UCL+ -- User Command Linkage Program - V07.54a            Page 12
                  Spring 1986 DECUS Release


          To install UCLXM.SAV, copy it to the system device as TSXUCL.SAV. 

                    .copy uclxm.sav sy:tsxucl.sav                     ____________________________

          If  you  are  not  a previous UCL+ user, you're done, and you can
          proceed to define the symbols that you intend to use.  Otherwise,
          the  next  step depends on whether your old UCL+ is an XM version
          or a non-XM version.  If it is a non-XM version of  UCL+,  follow
          the  procedure  described in the application notes (section 14.5)
          to transport your symbol definitions.  If your previous  UCL+  is
          an XM version, you can just type 

                    .recall sy:curent                     ________________

          to load the symbol/status data into your new copy of UCL+.  

          Finally,  it  is a good idea to run TSXUCL and change the command
          prompt.  

                    .r tsxucl                     ________
                    UCL> prompt "tsxucl> "                         _________________
                    tsxucl> <ctrl/C>                            ________


          6.2.2.2  Installation  As  A  UCI  (UKMON.SAV)  - Under TSX-Plus,
          UCL+ can also be used as a User Command Interpreter  (UCI).   The
          following  example  illustrates  a  typical installation with the
          default UCI name of UKMON.SAV.  Note that the name of the  global
          region  used  by  UKMON.SAV  is changed from the default value of
          "UCL".  Note also that the command prompt is changed during  this
          procedure  to  help distinguish the "UCI" copy of UCL+ from other
          copies that might exist on the same system as "UCL's".  

                    .copy uclxm.sav sy:ukmon.sav                     ___________________________
                    .sipp sy:ukmon.sav/a                     ___________________
                    Base?    <ret>                             _____
                    Offset?  1024                             ____

                      Base       Offset      Old  New?
                       000000     001024  101704  ;R                                                  __
                       000000     001024   <UCL>  ;RUKM                                                  _____
                       000000     001026   <   >  ;RON                                                  ____
                       000000     001030   < FP>  <ctrl/Y>                                                  ________
                    .r ukmon                     _______
                    UCL> uci "ukmon> "                         _____________
                    ukmon> <ctrl/C>                           ________

          You would invoke UKMON.SAV as a UCI by typing 

                    .set kmon uci                     ____________

          UCL+ -- User Command Linkage Program - V07.54a            Page 13
                  Spring 1986 DECUS Release


          6.3  Installing The CI Handler 

          The  CI  (Command  line Interpreter) handler can be used on RT-11
          V5.2 or later systems to control the action of the  various  com-
          mand  line  interpreters  (CLI's).   It  contains  no  executable                                                             ______________
          handler code;  all it does is execute SET commands.  Installation          ____________
          is,  therefore,  very  simple.   Just  copy CI.SYS to your system
          device, giving it the name appropriate to your  particular  moni-
          tor.  

          For non-XM versions of the RT-11 monitor:  

                    .copy/sys ci.sys sy:                     ___________________

          For the XM monitor:  

                    .copy/sys ci.sys sy:cix.sys                     __________________________

          See section 10.0 for more information in the CI handler.  


          6.4  Installing UCL+ HELP 

          The UCL+ distribution includes a help-text file named UCLHLP.TXT.
          You can use this file to set up on-line help text for  UCL+  com-
          mands in one of two ways:  

                o  The  most  general,  and most tedious, method is to edit
                   the HELP macros contained in  UCLHLP.TXT  into  HELP.TXT
                   and  then  rebuild  the HELP program.  This technique is
                   described in the RT-11 Installation Guide.  If  you  are
                   using  version  5.1  or later of RT-11, you will have to
                   use SPLIT.SAV to create HELP.EXE and HELP.TXT (see  file
                   UNSUP.TXT  on  the  RT-11  distribution kit).  Note that
                   both the RT-11 and UCL+ help text files contain a  macro
                   named  "HELP."  You  should  retain the RT-11 version of
                   this macro.  

                o  The  second approach involves the creation of a separate
                   HELP program for UCL+.  In this case, you create a macro
                   library from UCLHLP.TXT, build a secondary HELP program,
                   and define a symbol (I like to use HLP)  to  invoke  it.
                   The  following  example  assumes  that  you are using RT
                   V5.1.  All required files  are  assumed  to  be  on  the
                   default device (DK:).  


          UCL+ -- User Command Linkage Program - V07.54a            Page 14
                  Spring 1986 DECUS Release


                      .SPLIT HELP.EXE=HELP.SAV/B:7                        ___________________________

                      .LIB/MAC UCLHLP UCLHLP.TXT                        _________________________

                      .COP HELP.EXE+UCLHLP.MLB UCLHLP.SAV                        __________________________________

                      .COP UCLHLP.SAV SY:                         __________________

                      .HLP==R UCLHLP\^                        _______________



                                        NOTE

               If  you  are using RT-11 V5.2, the SPLIT boundaries are
               different for HELP.SAV.   In  the  above  example,  the
               value  for the "/B" switch in the first line becomes 10
               (octal) instead of 7.  This boundary  may,  of  course,
               change again in later versions of RT-11.  




          6.5  Installing The UCL+ Distribution Under RTEM 

          The  following  special  considerations and restrictions apply to
          using the UCL+ package under the RT-11 Emulator (RTEM):  

                o  The  UCL  program  (UCL.SAV)  should  be  placed in your
                   "private" area.  The distributed UCL program resides  in
                   the read-only portion of the virtual system device.  The
                   system manager should either rename the distributed  UCL
                   program  (if there is one) or delete it.  Otherwise, the
                   installation procedure is the same as for RT-11  systems
                   (section 6.1.1.1).  

                o  If  it is to be used, the CI handler should be placed in
                   the "mark zone" portion of the  virtual  system  device.
                   This  is  normally  done by the system manager.  Section
                   6.3 contains  further  information  on  installing  this
                   handler.  

                o  Later versions of RTEM use the UCF facility to implement
                   specialized commands for this  environment.   Thus,  the
                   UCF facility is not available to RTEM users.  

                o  The  UCL+  help  facility  is  normally installed in the
                   "shared" area of the virtual system device.  See section
                   6.4  for further information on installing the UCL+ help
                   text.  



          UCL+ -- User Command Linkage Program - V07.54a            Page 15
                  Spring 1986 DECUS Release


          In  summary:   the UCL+ program is placed in the user's "private"
          area;  the help program and the CI handler are installed  by  the
          system manager in the "shared" area, with the handler residing in
          the "mark zone." 

          UCL+ -- User Command Linkage Program - V07.54a            Page 16
                  Spring 1986 DECUS Release


          7.0  HOW IT WORKS 

          First,  read  the appropriate sections of the RT-11 Software Sup-
          port Manual (for  version  5.0,  this  is  sections  2.2.4.1  and
          2.2.4.2  --  pages  2-39 through 2-41).  If you are running RT-11
          version 5.2 or later, and you are  interested  in  User  Commands
          First  (UCF),  read  that stuff too.  TSX-Plus users should check
          out the additional material in the TSX manuals  on  User  Command
          Interpreters (UCI's) and the UCL SET commands.  

          OK,  now  that  you've  done your homework (and saved me a lot of
          typing)...  


          7.1  RT-11 Command Processing With UCL Support 

          As  you  will recall, if you are using a version of RT-11 that is
          sysgened to support User Command Linkage, RT goes through a  cer-
          tain  logical  sequence  to  evaluate  a command line.  First, it
          looks at the first word to see if this a valid RT-11 command.  If
          not, it looks on SY:  for a program to run that has the same name
          as this first word (let's call it "word1").  If "SY:word1.SAV" is
          not  found,  it runs SY:UCL.SAV (if it exists) and passes the en-
          tire command line to UCL.  

          UCL+  understands  two  types of commands:  "hard-wired" commands
          (LIST or RECALL, for example),  which  are  "built  in"  to  UCL+
          (hereafter  referred  to  simply  as  "commands"), and "symbols",
          which are commands that you define (or modify or delete) from the
          console.  

          When  UCL+  receives  a  command  line, it first checks to see if
          word1 is a valid  command  and,  if  so,  calls  the  appropriate
          routine.   If  the  command  check  fails, UCL+ looks for a match
          against the currently defined symbols and, if successful, invokes
          the symbol processing stuff.  

          Next,   if   the  PATH  command  is  turned  on,  UCL+  uses  the
          "run-by-name" path to look for a  program  named  "dev:word1.SAV"
          (the  default  is dev=DK) and, if it finds it, runs it by passing
          the command "RUN command-string" to RT-11.  

          Finally,  if  all  else  fails, UCL+ exits with a "?UCL-F-Invalid
          command" error message or, if the CHAIN  command  is  in  effect,
          UCL+  chains to the specified program, and passes it the original
          command line.  


          UCL+ -- User Command Linkage Program - V07.54a            Page 17
                  Spring 1986 DECUS Release


          In summary then, when you enter a command:  

                o  RT-11 tries to execute it, then
                o  RT-11 tries to run it off SY:, then
                o  UCL+ tries to execute it as a command, then
                o  UCL+ tries to execute it as a symbol, then
                o  UCL+ tries to "run-by-name", then
                o  you either get a nasty comment or UCL+ chains to another
                   program.



          7.2  RT-11 Command Processing With UCF Support 

          If your RT-11 is version 5.2 or later, you have support available
          for User Commands First (UCF) processing.  If you turn  UCF  sup-
          port  on  (this  can  be  done  with the CI handler;  see section
          10.0), RT-11 will collect your command line and,  after  checking
          for  IND  syntax, pass it directly to a program named SY:UCF.SAV.
          You can use UCL+ as a "UCF" by making a copy of it named UCF.SAV.
          UCL+  will  now  be intercepting commands before the monitor gets                                                    ______
          them!  This can get really tricky because  UCF  can,  in  effect,
          override normal RT-11 commands.  The implications of all this can
          get pretty complicated and are beyond the scope of  this  manual;
          read the RT-11 documentation and release notes for details.  

          The  main  thing  to remember is that UCL+ processes unrecognized
          commands differently when it is running as UCF than it does  when
          it  is running as UCL.  As UCF, it passes unknown commands to the
          monitor;  as UCL it issues an error message.  This  makes  sense,
          because UCF gets commands first while UCL gets them last.  

          The simplest situation, with UCF support turned on and UCL turned
          off, causes command  lines  to  be  processed  in  the  following
          sequence:  

                o  UCF tries to execute it as a command, then
                o  UCF tries to execute it as a symbol, then
                o  UCF tries to "run-by-name", then
                o  RT-11 tries to execute it, then
                o  RT-11 tries to run it off SY:, then
                o  you get "?KMON-F-Invalid command"



          7.3  TSX-Plus Command Processing 

          If you are using UCL+ with TSX-Plus version 4.1, things work more
          or less the same as they do with RT-11 (see  section  7.1):   TSX
          passes the command string to UCL+ only if KMON fails to recognize
          it.  Things get a little more complicated, however,  if  you  are
          running under a V5.0 or later monitor.  

          UCL+ -- User Command Linkage Program - V07.54a            Page 18
                  Spring 1986 DECUS Release


                o  TSX-Plus  V5.0  looks  for  a "UCL" named SY:TSXUCL.SAV.
                   Version 4.1 uses the same name as RT-11 (SY:UCL.SAV).  

                o  Version  5  implements a UCL "SET option".  SET UCL NONE
                   turns off user command linkage (now who would want to do
                   that?).   SET UCL LAST causes command processing to work
                   like   it   did   under   V4.1   (except   you   get   a
                   "?KMON-F-Unrecognizable  command"  error message instead
                   of "?UCL-F-Invalid command").   SET  UCL  MIDDLE  allows
                   TSXUCL  to  examine  the  command string after it is in-
                   spected for a match against the  monitor  commands,  but
                   before  command  file/run-by-name  processing.   SET UCL
                   FIRST causes TSXUCL to be invoked prior to all KMON pro-
                   cessing  (i.e.,  it works like the RT-11 UCF facility --
                   see section 7.2).  Note that MIDDLE  will  cause  UCL+'s
                   run-by-name  path  to  take  priority over TSX's;  FIRST
                   will, in addition, give priority to UCL+  commands  over
                   KMON  commands  (i.e.,  you can replace monitor commands
                   with UCL+ commands).  

                o  Unless  UCL  is  set  FIRST, the monitor DISPLAY command
                   will preempt the UCL+ DISPLAY command.  This means  that
                   you  will need to define a symbol in order to invoke the
                   UCL+ DISPLAY command properly (for example, DSPLAY==_d). 

                o  UCL+  can also be used, under TSX, as a User Command In-
                   terpreter (UCI).  When UCI support is turned on (via the
                   SET  KMON UCI command), the UCI effectively replaces the                                                               ________
                   keyboard monitor (note that this is different  from  SET
                   UCL  FIRST  where  KMON  collects  the command, and then
                   passes it to UCL).  UCL+ can be used as a UCI by  making
                   a  copy  of it with the appropriate name (the default is
                   SY:UKMON.SAV) and utilizing the UCL+ UCI_MODE command.  


          See the TSX-Plus user documentation for further information.  

          UCL+ -- User Command Linkage Program - V07.54a            Page 19
                  Spring 1986 DECUS Release


          8.0  SYMBOLS 

          This is probably the most important section of this manual.  

          The  main  reason  for  using UCL+ (unless you just don't like to
          have a lot of empty space on your disk) is that it gives you  the
          ability  to  dynamically  define your own commands.  For the pur-
          poses of this  document,  these  user-defined  commands  will  be
          referred  to as "symbols".  The following sections present a sum-
          mary of how to define and manipulate these symbols.  


          8.1  Defining Symbols 

          Symbols  are  defined by entering a "symbol definition string" in
          the format 

                              symbol==definition 

          where  "symbol"  is  the  command  you are defining (6 characters
          max.), "==" is the symbol definition operator,  and  "definition"
          is the character-string (72 characters max.) that will govern the
          way that the symbol is replaced  (expanded)  when  it  is  inter-
          preted.  


                                        NOTE

               DEC's UCL uses a more "VMS-like" structure for defining
               symbols (possible  example:   REB*OOT:==BOOT DL0:   vs.
               REBOOT==BOOT DL0:).  UCL+ will accept the DEC format as
               well as the "normal" one.  


          In  the  simplest  case, suppose you define the symbol "BUILD" by
          entering 

                              BUILD==EX/MAC/NORUN

          If you subsequently enter

                              BUILD MYFILE

          this line is interpreted by UCL+ and passed back to RT-11 as

                              EX/MAC/NORUN MYFILE

          You  may  also  get  multiple-line  definitions via the backslash
          ("\") character.  For example, the symbol "WHEN" defined as 

                              WHEN==DATE\TIME 


          UCL+ -- User Command Linkage Program - V07.54a            Page 20
                  Spring 1986 DECUS Release


          executes as if you had typed 

                              DATE 
                              TIME 

          A "^" character or characters in the definition governs where the
          "argument-part" of the input command string is  inserted  when  a
          symbol is expanded.  Thus, 

                              BUILD==EX/MAC/NORUN 

          and 

                              BUILD==EX/MAC/NORUN ^ 

          are  equivalent  symbol  definitions.  The "^" operator is really
          handy when the "argument-part" is to be embedded in the middle of
          the  expansion  somewhere  rather  than  tacked  on the end.  For
          example:  

                              VERSIO==RESORC SY:^.SAV/V 

          If you type 

                              VERSION PIP 

          this symbol will expand as 

                              RESORC SY:PIP.SAV/V 

          Finally, you may precede the "definition-part" with an underscore
          character ("_").  This will cause UCL+ to process the symbol  ex-
          pansion  in  "execute-immediate"  mode.   In other words, you are
          telling UCL+ that you are defining one symbol in terms of another
          symbol  or hard-wired command.  Thus, the expanded symbol is pro-
          cessed immediately by UCL+ rather than being passed on  to  RT-11
          as  a  command string.  This speeds up command execution substan-
          tially.  

          For example, 

                              SAY==DISPLAY "^"   (example 1) 

          and 

                              SAY==_DISPLAY "^"  (example 2) 

          are equivalent definitions.  If you type 

                              SAY HELLO 

          both will expand (on the first pass through UCL+) as 

          UCL+ -- User Command Linkage Program - V07.54a            Page 21
                  Spring 1986 DECUS Release



                              DISPLAY "HELLO" 

          But,  in  the  first  instance,  the UCL+ program will be invoked          ___
          twice:  once to expand SAY HELLO and  pass  the  string  back  to
          RT-11,  and  a  second  time  to execute DISPLAY "HELLO".  In the
          second example, UCL+ expands the command and then immediately ex-
          ecutes  the  resultant  command string.  Thus, example 2 executes
          much faster, especially on a floppy-based system, because UCL+ is
          only run once to process it, instead of twice.  

          Note  that  you are restricted to using "_" with definitions that
          expand to a single line.  

                              A==_B\C\D 

          will not work correctly (well, not in this version anyways).  


          8.2  Deleting Symbols 

          Individual  symbols can be deleted either by redefining them with
          a null definition or with the ERASE command.  For  example,  sup-
          pose you have defined a symbol TEMP as 

                              TEMP==EDIT MYFILE.MAC\DELETE MYFILE.BAK 

          You can delete this symbol by typing 

                              TEMP== 

          (UCL+  will  display  the message "?UCL-W-Erased symbol TEMP") or
          you can type 

                              ERASE TEMP 

          with  the  same effect.  If you wish to delete more than one sym-
          bol, the ERASE command is more efficient  (see  section  9.4  for
          more details on the ERASE command).  


          8.3  Running UCL+ Directly 

          You  can  also define (or erase) symbols by running UCL+ directly
          and proceeding as described  above  in  response  to  the  "UCL>"
          prompt.   There  is one significant difference, however:  you can
          include almost any character that you wish in a symbol definition
          (upper/lower case, escape, etc.) as long as RT-11 does not inter-
          cept it for it's own purposes (you couldn't  use  control-O,  for
          example).  


          UCL+ -- User Command Linkage Program - V07.54a            Page 22
                  Spring 1986 DECUS Release


          For instance, the escape sequence 

                              <esc>[H<esc>[J 

          can  be  used to clear the screen on a VT100-style terminal.  The
          following dialogue would define a symbol "CLS" to accomplish this
          (items  enclosed  in  angle  brackets  represent  single  control
          characters;  e.g., <esc>):  

                    .UCL
                    UCL> cls==_d "<esc>[H<esc>[J
                    UCL> <ctrl/C>

          Note  that, if the single-line editor was enabled, you would have
          to turn it off before defining the above symbol.  


          8.4  Advanced Techniques 

          This section contains a description of two features that were ad-
          ded to UCL+ beginning with V07.50.  These features,  quoting  and
          argument parsing, are very useful, but they should be used with a
          little care and forethought.  In particular, it is  important  to
          understand  how  they  work (and, perhaps, experiment a bit) when
          defining UCL+ symbols that have nested expansions.  


          8.4.1  Using  The  Quote  Character ("|")  - Quoting is primarily
          used to force  UCL+  to  treat  an  operator  (the  "^"  and  "\"
          characters,  for  example)  as normal text.  This is done by pre-
          ceeding the character to be quoted by the "|" operator.  The most
          common application is to allow characters to be displayed as part
          of a text string that would normally be interpreted as operators.
          For example, the symbol definition:  

                    EXAMPL==_D "|\" 

          Typing EXAMPL would print a "\" at the console.  

          As  a more useful illustration, suppose you wanted to send a line
          of ReGIS graphics instructions to a VT241 (to change  the  screen
          colors,  perhaps).   You will need to preceed the graphics output
          with the text "<esc>Pp" and follow it with "<esc>\" ("<esc>"  in-
          dicates  the  escape  character).   Under TSX-Plus, the following
          symbol definition will do the trick (note the use  of  the  quote
          character to display the "\").  

                    regis==disp "<esc>Pp"\disp "^"\disp "<esc>|\" 

          Refer  to  section 14.11 of the "Application Notes" for a discus-
          sion on implementing this symbol under RT-11.  


          UCL+ -- User Command Linkage Program - V07.54a            Page 23
                  Spring 1986 DECUS Release


          It  is  good  policy, by the way, to use the quote character only
          when it is required.  

          The  other thing to watch out for is nested command expansions (a
          symbol defined in terms of another symbol  defined  in  terms  of
          another...).   Consider,  for  example, the problem of defining a
          symbol to display the quote character itself.  The actual  symbol
          definition is 

                    EXAMPL==_D "||||" 

          Why  four  quote  characters?  Because this definition results in               ____
          two "quoting scans":  once when the EXAMPL  symbol  is  processed
          and  expanded, and once when the resultant D (DISPLAY) command is
          scanned.  In other words, the keyboard command to print a "|" is 

                    DISPLAY "||" 

          In order to define a symbol whose expansion is the above command,
          you must quote both  quotes!   (Typing  DISPLAY  "|"  prints  the
          second quotation mark, not a "|" -- think about it.) 

          Most  situations  are not as messy as this one.  The best rule of
          thumb is to "work from the bottom up." 


          8.4.2  Argument  String Parsing ("^n")  - Argument string parsing
          allows you to extend the function of the "^" operator.  UCL+  can
          break  up the "argument part" of a command string into as many as
          nine sub-strings.  These sub-strings are specified  by  following
          the "^" operator with a number from "1" to "9." UCL+ assumes that
          the sub-strings are separated by spaces.  For example, the phrase
          "this  is  a test" consists of four sub-strings.  As a simple il-
          lustration of how this works in practice, consider the  following
          symbol definition (this is an RT-11 V5.2 example) 

                    exampl==_d "^2 ^1" 

          If you type 

                    exampl you there 

          UCL+ will, in turn, display 

                    there you 

          A more useful example is the "MOVE" command.  

                    move==cop/sys/log ^1 ^2\del/log/sys ^1 

          This command will copy a file from one place to another, and then
          delete the original copy of the file.  Thus, if you type 

          UCL+ -- User Command Linkage Program - V07.54a            Page 24
                  Spring 1986 DECUS Release



                    move shmoo.dat sy:  

          the effect is the same as typing 

                    cop/sys/log shmoo.dat sy:  

                    del/log/sys shmoo.dat 

          Using  argument  parsing is not nearly as tricky as quoting (sec-
          tion 8.4.1, above), but there are a couple  of  basics  that  you
          must keep in mind.  

                o  The  "^"  operator,  unmodified  by  a  trailing numeric
                   value, causes the entire argument string, including  em-
                   bedded  spaces,  to  be inserted into the command expan-
                   sion.  An operator of the form "^n" inserts a sub-string
                   without the "framing" spaces;  i.e., the sub-string will
                   never contain blanks.  

                o  Any  construction of the form "^n" is treated as a pars-
                   ing operator.  However, the sequence "^|n" is  not.   In
                   other  words,  in  an instance where you need to disable
                   parsing, quote the "n".  


          UCL+ -- User Command Linkage Program - V07.54a            Page 25
                  Spring 1986 DECUS Release


          9.0  "HARD-WIRED" COMMANDS 

          The following is a brief description of the commands "hard-wired"
          into UCL+.  Commands such as CHAIN, DISPLAY,  ERASE,  LIST,  etc.
          are  required  to  support  the  various UCL+ functional goodies.
          Others, like CD, RNO, NOSL, and SLON are  included  because  they
          are handy, they are too complex to implement as symbols, and they
          serve as good examples of how to add  your  own  hard-wired  com-
          mands.  

          Note that, as with RT-11 commands, UCL+ commands and symbols need
          not be typed in their entirety to be recognized.  You  need  only
          type enough characters to make a command unambiguous (and to keep
          it from being mistaken as an RT-11 command).  For example,  "LIST
          COMMANDS" can be abbreviated as "LIS CO" ("LI CO" would be inter-
          preted by RT-11 as a "LINK" command).  

          The  commands are listed in alphabetical order.  Underlining with
          "====" is used to highlight the command itself.   Optional  modi-
          fiers,  switches,  and  so forth, are enclosed in square brackets
          ("[]") and these may be nested (for example,  [["]prompt-text["]]
          indicates  that the quotes are optional as well as the entire ar-
          gument).  


          9.1  CD Command

          CD [dev]
          ==

          "Change Device" 

          CD dev    becomes    ASSIGN dev DK:  

          If the device mnemonic, "dev", is omitted you get ASSIGN SY: DK: 

          Note  that the colon (:) at the end of the device mnemonic is not
          required;  "CD DY0" is the same as "CD DY0:".  


          9.2  CHAIN Command

          [NO]CHAIN [file-spec]
              =====

          "Set Up Exit-On-Bad-Command Chain" 

          The  CHAIN  command  allows  you to specify a program for UCL+ to
          chain to if UCL+ is unable to interpret  a  given  command.   The
          original command string is passed to the specified program in the
          same form and in the same fashion that the string  was  given  to
          UCL+.   Issuing  a  CHAIN  command  with  no argument restores or

          UCL+ -- User Command Linkage Program - V07.54a            Page 26
                  Spring 1986 DECUS Release


          retains the most recent CHAIN file specification.  Note that  the
          CHAIN  command will also disable UCI_MODE if it is in effect (see
          also section 9.14).  

          NOCHAIN disables chaining.  


          9.3  DISPLAY Command

          DISPLAY[/switches] command-string
          =======

          or

          DISPLAY "string["]
          =======

          "Display Command Expansion or String"

          The  DISPLAY  command  prints the expansion of the specified UCL+
          command or symbol or, if you enclose the argument with  quotation
          marks, the indicated string is simply printed as is followed by a
          carriage-return/line-feed.  If the trailing quote is omitted,  no
          carriage  control  is  appended (this is the preferred method for
          sending escape sequences).  Output can be directed to the console
          (the default), the printer, or some other specified device/file. 


          Switches:  

          /EXECUTE        prints  the expanded command and then executes it
                          (not valid if DISPLAYing a string).  

          /NOEXECUTE      suppresses command execution (default).  

          /FORM0          allows  the  printer handler to do a formfeed be-
                          fore the first page of output (default;   has  no
                          effect unless SET LP FORM0 command is in effect) 

          /NOFORM0        prevents  the  printer  handler  from executing a
                          formfeed before the first page of output  (recom-
                          mended if you are sending escape sequences to the
                          printer) 

          /PRINTER        directs output to the printer (device LP:).  

          /OUTPUT:file-spec  directs output to the specified device/file.  

          /TERMINAL       directs output to the console (default).  

          Note  that  the  DISPLAY  command is only valid for commands that
          cause a command expansion to be passed to the  keyboard  monitor.

          UCL+ -- User Command Linkage Program - V07.54a            Page 27
                  Spring 1986 DECUS Release


          It  also  does  not work across a CHAIN.  Attempting to DISPLAY a
          "non-expandable" command will cause a "?UCL-F-Invalid DISPLAY ar-
          gument" error message to be issued.  


          9.4  ERASE Command

          ERASE[/switches] symbol1[,symbol2,...]
          =====

          "Erase Symbol(s)"

          The  ERASE  command allows you to delete a symbol or symbols that
          have been previously defined.  If you specify the  entire  symbol
          name,  it  is  deleted  with no verification prompt.  If you only
          type enough of the name to be unambiguous, you will get  an  "Are
          You Sure?" prompt.  

          The command "ERASE *" will delete all of the symbols.  


          Switches:  

          /NOQUERY   omits verification prompt 

          /QUERY     ask  for  operator  verification  (default  if ERASE *
                     used) 


          9.5  LIST Command

          LIST[/switch] thing1[,thing2,...]
          ====

          "List Current Commands/Symbols/Attributes"

          The  LIST  command lists the "hard-wired" commands, currently de-
          fined symbols, CHAIN  assignment/status,  run-by-name  path,  and
          present  release/version to the specified device or file.  If you
          type a LIST command with no arguments, the  symbols  are  listed.
          If  you  omit the output specification, output is directed to the
          console.  


          Switches:  

          /FORM0          allows  the  printer handler to do a formfeed be-
                          fore the first page of output (default;   has  no
                          effect unless SET LP FORM0 command is in effect) 

          /NOFORM0        prevents  the  printer  handler  from executing a
                          formfeed before the first page of output 

          UCL+ -- User Command Linkage Program - V07.54a            Page 28
                  Spring 1986 DECUS Release



          /OUTPUT:file-spec  sends output to the specified device/file 

          /PRINTER        sends output to the printer (LP:) 

          /TERMINAL       sends output to the console (default) 


          Arguments:  

          ALL        list  commands,  symbols,  chain  data, path list, and
                     version.  ("LIST *" has the same effect) 

          CHAIN      list  the  program  to chain to if a command cannot be
                     identified 

          COMMANDS   list the "hard-wired" commands 

          PATH       list the current run-by-name path list 

          SYMBOLS    list the current symbol definitions (default) 

          VERSION    list the program name and version 


                                        NOTE

               If   you   list  a  symbol  whose  definition  contains
               non-printing characters (an escape character, for exam-
               ple),  UCL+  will  indicate  their  presence with a "~"
               character.  E.g., the  "CLS"  example  in  section  8.3
               would list as 

                         CLS   ==_d "~[H~[J 




          9.6  NOSL/SLON Command

          NOSL or SLON
          ====    ====

          "SL editor on/off"

          These commands turn the single-line editor off or on.  

          If  UCL+  is  RUN  directly,  the effect is to toggle SL locally.
          This assumes, of course, that SL  was  installed  and  turned  on
          prior to running UCL+ and that SL is enabled for use by user pro-
          grams.  This  is  particularly  handy  if  you  need  to  include
          characters  in  a  symbol  definition that are intercepted by the

          UCL+ -- User Command Linkage Program - V07.54a            Page 29
                  Spring 1986 DECUS Release


          single-line editor.  For example, if you wished to define a  sym-
          bol that rings the bell on the console, you could use the follow-
          ing sequence of commands:  

                    .UCL
                    UCL> nosl
                    UCL> bell==_d "<ctrl/G>
                    UCL> slon

          If  NOSL  or  SLON  is entered via the monitor, the effect is the
          same as typing, respectively, SET SL OFF or SET SL ON.  


          9.7  PASS_ON Command

          PASS_ON[/TO:program-name] command-string
          =======

          "Pass On Command To Next (or another) Program"

          This  command  tells UCL+ to pass the specified command-string on
          to the program that you specified via the CHAIN command.  If  you
          specify a "program-name", then the command is passed to this pro-
          gram instead.  If CHAINing is not in effect, and  you  failed  to
          specify  a  program  to  chain to, you get your hand slapped with
          "?UCL-F-No CHAIN in effect".  

          Note that the command string is passed "UCL-style" (byte count at
          location 510, string starting at 512) not "run-by-name" style.  


          /TO:program-name   causes  the command-string to be passed to the
                             specified program 


          9.8  PATH Command

          [NO]PATH  [device1[,device2,...]]
              ====

          "Set Up 'Run-by-name' Search Path"

          If  UCL+  does  not "know" a given command, it follows the device
          list set up with the PATH command in attempting a  "run-by-name".
          It uses DK:  by default.  The limit is about 20 device mnemonics.
          Issuing a PATH command without specifying a  device  list  causes
          UCL+ to restore or retain the most recent "run-by-name" path.  

          The NOPATH command disables the "run-by-name" function.  

          UCL+ -- User Command Linkage Program - V07.54a            Page 30
                  Spring 1986 DECUS Release


          9.9  PROMPT Command

          PROMPT [["]prompt-text["]]
          ======

          "Change Prompt String"

          The PROMPT command is used to change the UCL+ input prompt.  This
          command is frequently employed when UCL+ is being  used  in  "UCI
          mode".  The replacement prompt text may optionally be enclosed in
          quotes.  If you issue the PROMPT command with  no  argument,  the
          default prompt ("UCL> ") is restored.  


          9.10  RECALL Command

          RECALL[/switches]  file-spec
          ======

          "Recall Symbol Definition and Status Tables"

          Recalls (loads) the symbol definition and status area from a file
          that has previously been created with  the  STORE  command.   The
          default  device  is  DK:.   The  default  extension  is .UCL (ie,
          DK:filnam.UCL where "filnam" is the file name you specify) if you
          are running the "vanilla" UCL+ program, .UCX if you are using the
          special XM version of UCL+, and .UCJ if the /JOURNAL switch is in
          effect (either version).  


          Switches:  

          /BINARY    this is the default;  loads a file created as a binary
                     image of the UCL+ symbol/status area 

          /JOURNAL   loads  a  "journal" file;  echos the input to the con-
                     sole if /NOQUIET is in effect 

          /NOQUIET   allows echo of commands to console when doing /JOURNAL
                     input;  use this switch with  caution,  especially  if
                     commands may include console escape sequences 

          /QUIET     this is the default;  suppresses echo of commands when
                     doing /JOURNAL input;   invalid  with  /BINARY;   also
                     suppresses    "warning    level"    messages    (e.g.,
                     "?UCL-W-Replaced existing symbol") 

          UCL+ -- User Command Linkage Program - V07.54a            Page 31
                  Spring 1986 DECUS Release


          9.11  RELOAD command

          RELOAD
          ======

          "Reload The UCL+ Global Region"

          When you are using the special XM version of UCL+, almost the en-
          tire program is permanently resident in a global  region  in  ex-
          tended  memory.   The  RELOAD command allows you to force UCL+ to
          reload this memory region from the disk copy of the UCL+  program
          that you are currently running.  


          9.12  RNO Command

          RNO[/switches] file-spec
          ===

          "RUNOFF Command"

          The  RNO command implements a "RUNOFF" command for RT-11.  It re-
          quires a copy of DECUS RUNOFF M02.4 or the equivalent resident on
          the  system device (SY:).  The following information is extracted
          from the comments in the UCL+ sources.  



          RNO/switches MYFILE  becomes  RUNOFF outspec/switches=MYFILE 

          The command switches, and the RUNOFF switches and file specifica-
          tions that they map to, are as follows (consult  the  RUNOFF  do-
          cumentation for detailed information on usage):  

                RNO                             RUNOFF
                ---                             ------
                /BEGIN:n                        /B:n
                /START:n

                /END:n                          /E:n

                /ONLY:n                         /B:n/E:n
                /PAGE:n

                /FORMLENGTH:n                   /F:n

                /HYPHENATION                    /H:YES
                /NOHYPHENATION                  /H:NO

                /HELP                           /I
                /INFORMATION


          UCL+ -- User Command Linkage Program - V07.54a            Page 32
                  Spring 1986 DECUS Release


                /STRIP                          /S
                /NOSTRIP                        ignored

                /UNDERLINE                      /U:L
                /UNDERLINE:BACKSPACE            /U:B
                          :SIMULATED            /U:S
                          :NONE                 /U:N
                /NOUNDERLINE                    /U:N

                /VERSION                        /V

                /WAIT                           /W

           output specifications:

                /OUTPUT:filename                filename...=

                /PRINTER                        LP:...=

                /TERMINAL                       TT:...=

                no output spec. or              LP:...=
                /DEFAULTS


          9.13  STORE Command

          STORE[/switches]  file-spec
          =====

          "Store Current Symbol Definition and Status Tables"

          The  STORE  command causes the symbol/status blocks to be written
          to a specified file.  The default device is DK:.  The default ex-
          tension  is  .UCL  (ie,  DK:filnam.UCL where "filnam" is the file
          name you specify) if you are running the "vanilla" UCL+  program,
          .UCX if you are using the special XM version of UCL+, and .UCJ if
          the /JOURNAL switch is in effect (either version).  

          Switches:  

          /BINARY    this  is the default;  stores a file as a binary image
                     of the UCL+ symbol/status area 

          /JOURNAL   writes  a  "journal"  file;  the file is stored as the
                     series of commands necessary to recreate  the  present
                     UCL+  configuration;   i.e.,  as an "editable" command
                     file 

          UCL+ -- User Command Linkage Program - V07.54a            Page 33
                  Spring 1986 DECUS Release


          9.14  UCI_MODE Command

          [NO]UCI_MODE  [["]prompt-text["]]
              ========

          "Switch 'UCI Mode' On/Off"

          The  UCI_MODE  command  is  employed  to set up UCL+ for use as a
          "User Command Interpreter" (UCI).  TSX-Plus provides  a  facility
          for  designating UCI's.  Typically, a UCI is used to process user
          input either prior to, or instead of, the normal keyboard monitor
          (KMON).  

          Issuing a UCI_MODE command has the following effect on UCL+:  

                o  CHAINing  is  disabled.   Non-UCL+  command  strings are
                   passed to KMON for execution.  

                o  If specified, the "prompt-text" replaces the normal UCL+
                   line prompt;  if  no  "prompt-text"  is  specified,  the
                   default  prompt  ("UCL> ")  is assumed (same effect as a
                   PROMPT command).  

                o  The  names of the hard-wired commands are changed by the                   ________________________________________________________
                   addition of a "prefix character".  Unless you reassemble                   ________________________________
                   UCL+  to change or eliminate it (see section 14.8), this
                   character is a period (".").   Thus,  for  example,  the
                   LIST command becomes ".LIST".  

          NOUCI_MODE acts as follows:  

                o  The  CHAINing  condition in effect prior to the UCI_MODE
                   command is restored.  

                o  If  no prompt-text is specified, the default UCL+ prompt
                   is restored ("UCL> ").  

                o  The normal hard-wired command names are restored.  


          UCL+ -- User Command Linkage Program - V07.54a            Page 34
                  Spring 1986 DECUS Release


          10.0  CI HANDLER 

          This  "handleroid"  allows  you to turn the various RT-11 Command
          Line Interpreters (CLI's) on or off using SET commands.  It  will
          also  show  which  CLI's are enabled.  There are four CLI's:  UCF
          (User  Commands  First),  DCL  (Digital  Command  Language),  CCL
          (Concise  Command  Language),  and  UCL  (User  Command Linkage).
          Refer to the RT-11 documentation for an explanation of each.  The
          possible SET commands for the CI (Command Interpreter) handleroid
          are:  

               SET CI [NO]UCF  --  turn UCF on/off
               SET CI [NO]DCL  --  turn DCL on/off
               SET CI [NO]CCL  --  turn CCL on/off
               SET CI [NO]UCL  --  turn UCL on/off
               SET CI HELP     --  display SET commands
               SET CI RESET    --  same as SET CI NOUCF,DCL,CCL,UCL
               SET CI SHOW     --  display the active CLI's

          By  default,  RT-11  has  all CLI's enabled except UCF.  In other
          words, the normal situation is equivalent to 

                    SET CI NOUCF,DCL,CCL,UCL 

          Thus,  if  you  issued  a  SET CI SHOW command under an unaltered
          monitor, CI would report 

                    ?CI-I-CLI's enabled:  DCL CCL UCL 

          Note  that SET CI RESET restores/insures the above default condi-
          tion.  

          It  is  not  possible to INSTALL CI.  This is because CI contains
          only SET code.  As there is no executable handler code, there  is
          no  reason  why CI should be installable -- it would just waste a
          device slot in the monitor tables that could be  used  for  some-
          thing  else.  The monitor will execute the SET options as long as
          CI has the right name and resides on SY:.  Thus, for the RT-11 SJ
          and  FB monitors, the file should be SY:CI.SYS.  If you are going
          to use it under XM, make a copy named SY:CIX.SYS.  Under RTEM, it
          should reside in the "mark zone" as SY:CIM.SYS.  


                                 NOTE TO RTEM USERS

               RTEM V2.1 uses the UCF facility to implement additional
               monitor commands and options that are specific  to  the
               RTEM environment.  The CI handler automatically adjusts
               to this requirement.   Under  RTEM,  SET  CI  RESET  is
               equivalent  to  SET  CI UCF,DCL,CCL,UCL.  The text dis-
               played by SET CI  HELP  will  reflect  this  difference
               also.  

          UCL+ -- User Command Linkage Program - V07.54a            Page 35
                  Spring 1986 DECUS Release


                                     WARNING!!!

               Turning  off both DCL and CCL effectively turns off the
               monitor.  




                                        NOTE

               CI  will not run under versions of RT-11 prior to V5.2.
               It will not work properly with TSX-Plus V6.0  or  V6.01
               either  -- even though they are "compatible" with RT-11
               V5.2.  



          UCL+ -- User Command Linkage Program - V07.54a            Page 36
                  Spring 1986 DECUS Release


          11.0  ERROR MESSAGES 

          The  following  are the error messages for the current UCL+ pack-
          age.  There are two levels of severity.  "Warning" level messages
          are   preceeded  with  the  prefix  "?program-W-"  (for  example,
          "?UCL-W-Replaced existing symbol"), and they  indicate  that  the
          program  may  have  done  something  that  produced  an erroneous
          result.  Warning level conditions do not cause  program  termina-
          tion.   "Fatal"  messages  are  issued when UCL+ detects an error
          condition that prevents the program from  producing  any  useable
          output.  These messages are preceeded with "?program-F-" (for ex-
          ample, "?UCL-F-Ambiguous command C").  


          11.1  UCL+ "Warning" Messages (?UCL-W-...) 


          Erased symbol A....A

          Issued  when you erase a symbol via the "null definition" method.
          "A....A" is the symbol name.  


          Replaced existing symbol

          Indicates  that  you  have replaced an existing symbol definition
          with another.  


          Truncating symbol definition to 72 characters

          You  have  used  too many characters to describe a symbol defini-
          tion.  UCL+ stores the new symbol, but truncates  the  definition
          part to 72 characters.  


          Truncating symbol name to 6 characters

          You  have used too many characters in a symbol name.  UCL+ stores
          the new symbol, but truncates the name to 6 characters.  


          11.2  UCL+ "Fatal" Messages (?UCL-F-...) 

          If  you are running under a TSX-Plus V5, or later, monitor, those
          messages    flagged    with    "(*)"    will    result    in    a
          "?KMON-F-Unrecognizable command" error message unless UCL+ is run
          directly.  


          Ambiguous command A....A     (*)


          UCL+ -- User Command Linkage Program - V07.54a            Page 37
                  Spring 1986 DECUS Release


          You  have not typed enough characters for UCL+ to determine which
          command or symbol to execute.  "A....A" is the unidentified  com-
          mand.  


          Ambiguous switch A....A

          You  have not typed enough characters for UCL+ to determine which
          command switch to use.  "A....A"  is  the  text  of  the  unknown
          switch.  


          Ambiguous symbol A....A

          You  issued an ERASE command without specifying enough characters
          for UCL+ to determine which symbol to  erase.   "A....A"  is  the
          name of the ambiguous symbol specification.  


          Conflicting switches

          You specified two or more command switches that conflict with one
          another (for example, RNO/TERM/PRINT...).  


          File not found A....A

          The  RECALL  command  was unable to find the file that you speci-
          fied.  "A....A" is the file name causing the error.  


          Illegal file name A....A

          You  specified a file name in an invalid format (for example, too
          many characters, or invalid characters).  "A....A" is the errone-
          ous file name.  


          Invalid argument A....A

          You issued a hard-wired command with an invalid argument (for ex-
          ample, LIST X).  "A....A" is the text of the argument causing the
          error.  


          Invalid device

          You  specified  a device that is unknown to the operating system.
          This error occurs with the RECALL or STORE command.  It may  also
          occur if you make an error when you use LIST/OUT:.  



          UCL+ -- User Command Linkage Program - V07.54a            Page 38
                  Spring 1986 DECUS Release


          Invalid command A....A     (*)

          UCL+  was  unable  to recognize the command string (no match with
          the  hard-wired  commands,  no  match  with  the   symbols,   the
          "run-by-name"  search  failed,  and  no  CHAIN  was  in  effect).
          "A....A" is the unknown command string.  

          Invalid DISPLAY argument A....A

          You attempted to DISPLAY something that is not DISPLAYable (i.e.,
          the input command does not result in a command expansion;  a LIST
          command,  for example), or you tried to DISPLAY a command or sym-
          bol that does not exist.  "A....A" is the  text  of  the  invalid
          DISPLAY target.  


          Invalid or missing option

          You  specified  an  incorrect  option to a command switch, or you
          failed to specify an option value where one was required.  


          Invalid switch A....A

          You  specified an illegal command switch.  "A....A" is the switch
          causing the error.  


          Not enough room for file A....A

          The  STORE  command was unable to find enough room for the output
          file (18 decimal blocks are  required).   "A....A"  is  the  file
          name.  


          Read error A....A

          UCL+  encountered  an error when it attempted to read data from a
          file.  This error is most commonly generated by the  RECALL  com-
          mand.  This may be due to a hard input error, but the usual cause
          is an attempt to RECALL a journal  file  without  specifying  the
          /JOURNAL  switch  to the RECALL command.  "A....A" is the name of
          the file in which the error occurred.  


          RELOAD invalid while journaling

          The  journal  file that you specified in a RECALL/JOURNAL command
          contained a symbol name that UCL+ interpreted as  a  RELOAD  com-
          mand.   Edit  the  journal file to correct this error and try the
          RECALL command again.  

          UCL+ -- User Command Linkage Program - V07.54a            Page 39
                  Spring 1986 DECUS Release




          Symbol definition table full

          You  attempted  to define a new symbol, but UCL+ had no room left
          to store the definition.  


          Symbol not found A....A

          The  ERASE command was unable to find the name of the symbol that
          you specified.  "A....A" is the unknown symbol.  


          UCI_MODE invalid for this monitor

          You  issued  a UCI_MODE command when you were running under RT-11
          or a version of TSX-Plus prior to V5.0.  


          Unable to access LP:

          UCL+  was  unable  to find device LP:, or another job "owns" LP:.
          This error may occur when you use the  /PRINT  option,  and  it's
          most  frequent  cause is the failure to make a logical assignment
          for LP:.  


          Write error A....A

          UCL+  encountered  an  error when it attempted to write data to a
          file.  This error is generated by the STORE command, and  it  im-
          plies  that  the  area  where the ".UCL" file was created is cor-
          rupted.  "A....A" is the name of the  file  in  which  the  error
          occurred.  


          Wrong file format A....A

          You attempted to execute a RECALL/JOURNAL on a binary format file
          or a RECALL/BINARY on a journal file.  "A....A" is  the  name  of
          the file that you attempted to RECALL.  


          Wrong version of UCL A....A

          You  tried  to  RECALL  a  symbol definition/status file that was
          created by a version of UCL+ that is too  old.   For  example,  a
          ".UCL"  file created by a V1 UCL+ would be incompatible with a V7
          series program.  "A....A" is the offending file name.  

          UCL+ -- User Command Linkage Program - V07.54a            Page 40
                  Spring 1986 DECUS Release


          11.3  Global Region Loader Errors (?UCLGRL-F-...) 

          If  you  are running the XM version of UCL+, you may occasionally
          see error messages from the global region loader.  These messages
          are  all  "fatal"  errors  and will be prefixed with "?UCLGRL-F-"
          (for example, "?UCLGRL-F-No room").  


          No room

          You  have  insufficient  memory  for  the loader to run.  This is
          highly unlikely under normal circumstances;  the loader never re-
          quires more than 768 words of low memory.  


          Not XM monitor

          You  attempted to run the XM version of UCL, but you were not us-
          ing the extended memory monitor.  


          PLAS error

          Some  sort  of  memory  management related error occured when the
          loader attempted to create or attach to the global  region.   The
          most likely causes under RT-11 are a shortage of extended memory,
          or an attempt to create too many global regions.  If you are run-
          ning  under a TSX-Plus V6.0 or later monitor, this error can also
          occur if you do not have SYSGBL privilege.  


          I/O error

          The  loader encountered a problem when it attempted to access the
          program image on disk.   Possible  causes  include  a  bad  block
          within  the program disk image, or the program storage device may
          be write protected.  


          11.4  CI Handler Errors (?CI-...) 

          The  CI  handler  generates  messages for two error conditions as
          follows.  


          ?CI-F-Wrong version of RT-11

          You  attempted  you  use  the  CI handler with a version of RT-11
          prior to V5.2.  



          UCL+ -- User Command Linkage Program - V07.54a            Page 41
                  Spring 1986 DECUS Release


          ?CI-W-Disable access to monitor commands/utilities;
                Are you sure?

          You  have  issued a SET command to CI that will result in turning
          off both DCL (Digital Command Language) and CCL (Concise  Command
          Language).   You  are,  in effect, asking to turn off your entire
          RT-11 command interface (except for a few of the UCL+  hard-wired
          commands, assuming that UCF or UCL is still enabled).  In keeping
          with the idea that RT-11 is an "open system", CI  will  go  ahead
          and do this if you respond with "Y" for yes.  

          UCL+ -- User Command Linkage Program - V07.54a            Page 42
                  Spring 1986 DECUS Release


          12.0  EXAMPLES 

          Here  are a few examples of some of the symbol definitions that I
          use frequently.  They are shown below in the  same  fashion  that
          they would be listed via a LIST command.  


          CLS   ==_d "~[H~[J
          BUILD ==delete/info ^.bak\execute/norun ^\delete ^.obj
          DBO   ==dir/brief/order:type
          EXIT  ==\
          HLP   ==r uclhlp\^
          INSPEC==edit/inspect
          MOVE  ==cop/sys/log ^1 ^2\del/sys/log ^1
          NEW   ==dir/new
          PICH10==_d/p/nof "~[1w
          PICH16==_d/p/nof "~[4w
          REBOOT==dup sy:/o/y
          SAY   ==_d "^"
          ULINE ==_d "~[4m^~[0m"
          VERSIO==resorc sy:^.sav/v
          VT100 ==set tt scope,tab,nocrlf
          XM    ==boot sy:rt11xm.sys

          UCL+ -- User Command Linkage Program - V07.54a            Page 43
                  Spring 1986 DECUS Release


          13.0  V7 RELEASE NOTES 

          UCL+ V7 contains a number of extensions to, and minor differences
          from, V6L (the last publicly released version).  

                o  I changed the release/version designation.  V7C was fol-
                   lowed by V07.04.  

                o  UCL+  has  been  updated to work properly under TSX-Plus
                   V5.  

                o  Support has been added to UCL+ to allow it to be used as
                   a User Command Interpreter (UCI).  This was  implemented
                   when  the  author discovered that TSX-Plus version 5 was
                   distributed with a UCI facility (heh, heh, heh)...  

                   As  a  consequence,  the  UCI_MODE/NOUCI_MODE and PROMPT
                   commands were added to  allow  UCL+  to  be  dynamically
                   reconfigured  for use as a UCI.  See section 14.7 in the
                   application notes and the description  of  the  UCI_MODE
                   command  (section  9.14) for further information on this
                   feature.  

                o  CHAIN  and PATH work somewhat differently than in previ-
                   ous versions.   The  /RESET  switch  has  been  removed.
                   NOCHAIN and NOPATH commands have been added.  The effect
                   of these latter commands is to disable their  respective
                   functions.   A  subsequent CHAIN or PATH command with no
                   argument restores the previous condition.  Note  that  a
                   CHAIN command will turn off UCI_MODE if it is in effect. 

                o  The /ALL switch has been removed from the ERASE command.
                   For V7, the equivalent to the old "ERASE/ALL" command is
                   now "ERASE *".  

                o  The  LIST  command has been expanded.  Either "LIST ALL"
                   or "LIST *" will produce a full listing.  "LIST VERSION"
                   has been added.  

                o  A bug has been fixed concerning the way that UCL+ deter-
                   mines command ambiguity.  Formerly, UCL+ would report  a
                   command  as  ambiguous if it detected an ambiguous match
                   within the hard-wired commands.  UCL+ now  searches  the
                   symbols   as   well   before   returning  an  error.   A
                   non-ambiguous match in the hard-wired command list still
                   takes priority over searching the symbol list.  

                o  The  DISPLAY  command has been cleaned up.  UCL+ now re-
                   fuses to DISPLAY "non-expandable" command strings  (most
                   of  the hard-wired commands, insertion or replacement of
                   symbol  definitions,  symbols  defined  in  "chained-to"
                   UCL's).  

          UCL+ -- User Command Linkage Program - V07.54a            Page 44
                  Spring 1986 DECUS Release


                o  A  special  "XM  version" of UCL+ is now included on the
                   distribution kit.  It is intended for use with  monitors
                   having  support  for  global  regions in extended memory
                   (i.e., RT-11 V5.2 or later;  TSX-Plus  V6.0  or  later).
                   Almost all of the "UCLXM" executable code is permanently
                   memory resident.  It is very fast,  and  uses  only  512
                   (decimal) words of low memory.  An additional hard-wired
                   command, "RELOAD", has been added to UCLXM.  

                o  Beginning  with  V07.46,  the  method  that UCL+ uses to
                   search the "run-by-name"  path  list  has  been  changed
                   slightly.  UCL+ no longer exits to the monitor if it en-
                   counters the name of a non-existent device.  Instead, it
                   ignores the error, and trys the next device in the list. 

                o  V07.47  contains code to "work around" some inconsisten-
                   cies in the RT-11 spooler.  If, for example, you issue a
                   DISPLAY/PRINT/NOFORM0  command  with  spooler  flag page
                   support enabled, you will no longer get an unwanted flag
                   page.   UCL+  also avoids the generation of a gratuitous
                   trailing form feed when the SET LP ENDPAG=n option is in
                   effect.  

                o  V07.50  introduces two new advanced features:  "quoting"
                   and argument parsing.  Quoting allows  you  to  use  the
                   quote  character  ("|")  to  force  UCL+  to  treat  the
                   character immediately following it as  text,  regardless
                   of  any  special  meaning that it might normally have to
                   the UCL+ parser.  Argument parsing makes it possible  to
                   indicate  where a specific fragment of the argument text
                   is to be inserted when building a command string.  

                o  With  V07.53,  the  default  mode for RECALL/JOURNAL has
                   been changed from /NOQUIET to /QUIET.  


          UCL+ -- User Command Linkage Program - V07.54a            Page 45
                  Spring 1986 DECUS Release


          14.0  APPLICATION NOTES 

          This  section contains an assortment of hints, restrictions, cus-
          tomization patches, and notes for the current version of UCL+.  


          14.1  Executing Command/Control Files "By-Name" 

          UCL+  can  be used to execute indirect command files and IND con-
          trol files "by-name".  In fact, if you set  things  up  properly,
          you  can  ensure that they are executed in the proper context re-
          gardless of whether SET KMON IND is in effect or not.   The  fol-
          lowing examples illustrate the technique.  Note that you must run
          UCL+ directly to define the necessary symbol for a command file. 

          For command files:

                    .UCL                     ___
                    UCL> zoot==$@sy:zoot                         _______________
                    UCL> <ctrl/C>                         ________

          For control files:

                    .FEEP==IND SY:FEEP                     _________________


          14.2  Changing The Effect Of RNO/DEFAULTS 

          The  effect,  in  the  distributed  version  of  UCL+, of the RNO
          command's /DEFAULT switch is to place the  string  "LP:"  at  the
          beginning  of the CSI command string that is passed to the RUNOFF
          program.  This default text string can be changed by editing  the
          .ASCIZ  string at label DEFTXT in the file UCLHWC.MAC.  For exam-
          ple, if you are directing output to  an  el-cheapo  printer  that
          doesn't do formfeeds, you might want to change DEFTXT to "LP:/F". 


          14.3  Sending Escape Sequences To The Printer 

          Starting  with  V6K,  the  LIST  and  DISPLAY  commands include a
          FORM0/NOFORM0 option.  This option allows you to optionally  dis-
          able  the effect of the "SET LP FORM0" command;  i.e., output can
          be directed to the printer without a  preceding  formfeed.   This
          technique is most useful when you wish to send an escape sequence
          to the printer without triggering a  gratuitous  blank  page.   A
          handy  way  to  accomplish this is to define a generalized symbol
          for doing this sort  of  thing  ("<esc>"  represents  the  escape
          character):  


          UCL+ -- User Command Linkage Program - V07.54a            Page 46
                  Spring 1986 DECUS Release


                    .UCL
                    UCL> nosl
                    UCL> cqwenc==_d/p/nof "<esc>^
                    UCL> <ctrl/C>

          You  can  then  define specific printer-control commands by using
          the general symbol like a "function".   For  example,  to  define
          commands to control the pitch of an LA50/100/120 style printer:  

                    .UCL
                    UCL> pich10==_cqwenc [1w
                    UCL> pich16==_cqwenc [4w
                    UCL> <ctrl/C>


          14.4  Moving From UCL+ V6x To UCL+ V7.xx 

          UCL+  V7 will not allow you to RECALL version 6 or earlier series
          .UCL files.  There is a technique, using the RT-11 utility  SIPP,
          that  will  allow  you  to transfer your symbol definitions, etc.
          without reentering them all.  The patch proceeds as follows:  

                o  Using  SIPP, change the embedded version number at loca-
                   tion 21620 in the old ".UCL" file from 6 to 7.  

                o  RUN  a  V7.xx  copy  of UCL+ and RECALL the patched sym-
                   bol/status file.  

                o  Issue a PROMPT command to restore the "UCL>" prompt.  

                o  Issue a STORE command to write a new ".UCL" file.  

          In  the  example  below,  both the ".UCL" file and the V7 copy of
          UCL.SAV are assumed to be  on  DK:;   "xxxxxx.UCL"  is  your  V6x
          ".UCL"  file.   Note that the SIPP patch is for a V6L file.  Also
          note the use of the /A switch.  

                    .R SIPP                     ______
                    *xxxxxx.UCL/A                     ____________
                    Base?    <ret>                             _____
                    Offset?  21620                             _____

                      Base       Offset      Old  New?
                       000000     021620  006006  \                                                  _

                      Base       Offset      Old  New?
                       000000     021620     006  7                                                  _
                       000000     021621     014  <ctrl/Y>                                                  ________
                    *<ctrl/C>                     ________

          UCL+ -- User Command Linkage Program - V07.54a            Page 47
                  Spring 1986 DECUS Release


                    .RUN UCL                     _______
                    prompt                    ______
                    UCL> recall xxxxxx                         _____________
                    UCL> store xxxxxx                         ____________
                    UCL> <ctrl/C>                         ________

                    .

          Once the above commands have been executed, the resulting V7 copy
          of UCL.SAV will be in the same configuration as your original  V6
          copy.  


                                     WARNING!!!

               The  above  patch  will  not work for the XM version of
               UCL+.  You must apply the method described in the  fol-
               lowing  application  note  if  you intend to run the XM
               version.  




          14.5  Moving From UCL+ V6x Or V7.xx To UCL+ (XM) V7.xx 

          If  you  wish to use the XM version of UCL+, you can transfer the
          symbol/status data from a non-XM version of UCL+ in the following
          fashion:  

                o  If  your  old  ".UCL"  file  is  V6x,  apply  the  patch
                   described  in  the  preceding  application  note  to   a
                   "vanilla" copy (i.e., the non-XM version) of the current
                   UCL+ program.  If your file was  created  with  a  V7.xx
                   UCL+,  just  run the distributed non-XM UCL+ program and
                   execute a RECALL command.  

                o  Run the "vanilla" UCL+ and issue a STORE/JOURNAL command
                   to produce a ".UCJ" file.  

                o  Run the XM version of UCL+ and issue a RECALL/JOURNAL to
                   load the symbol/status data written out in the  previous
                   step.  



          14.6  Disabling Argument Parsing 

          There may be instances where you do not wish the sequence "^n" to                                              ___
          insert an argument sub-string.  This is most likely to  occur  if
          you  are  converting  an  earlier  version of UCL+ to a V07.50 or
          later version and have a symbol definition that  is  supposed  to
          concatenate  the  argument string with a number.  The solution is

          UCL+ -- User Command Linkage Program - V07.54a            Page 48
                  Spring 1986 DECUS Release


          to use the "|" operator to quote the "n".  The easiest way to il-
          lustrate  this  is  with  an example.  Suppose we define a symbol
          named EXAMPL in the following fashion (RT-11 V5.2 syntax):  

                    exampl==_d "^2" 

          If you type 

                    exampl I am R2D 

          UCL+ will display only the word 

                    am 

          because  it  takes the characters "^2" to mean "insert the second
          argument sub-string here." However, if you define EXAMPL as 

                    exampl==_d "^|2" 

          and type 

                    exampl I am R2D 

          UCL+ will then correctly display 

                    I am R2D2 

          Because you have "quoted" the "2", UCL+ interprets the definition
          as "insert the entire argument string ahead of the '2'." 


          14.7  Hints and Kinks:  UCF, UCI, And SET UCL FIRST 

          If  you  are  using UCL+ as a UCI, command lines are inspected by
          UCL+ before they are processed by the operating system's keyboard               ______
          monitor (KMON).  If you are using UCL+ as UCF or, under TSX-Plus,
          with SET UCL FIRST in effect, KMON collects the command line, but
          it is passed to UCL+ without interpretation.  In any of these in-
          stances, the effect is that UCL+ inspects the command before  the
          monitor  does.   Only if UCL+ does not recognize the command will
          the monitor see the command line in unaltered form.   This  occa-
          sions a couple of "gotchas" that you have to watch out for.  


          14.7.1  Interception  Of Monitor Commands  - Some valid KMON com-
          mands may be trapped prematurely by UCL+.  This situation  occurs
          when there is a conflict between a monitor command or normal com-
          mand abbreviation and a symbol name.  For example, the HELP  com-
          mand  under  TSX-Plus  would  normally  be  invoked as "H", "HE",
          "HEL", or "HELP".  If you wish to avoid a conflict with,  say,  a
          symbol  named  "HELLO",  then it would be necessary to define the
          following symbols:  

          UCL+ -- User Command Linkage Program - V07.54a            Page 49
                  Spring 1986 DECUS Release



                    H==HELP
                    HE==HELP
                    HEL==HELP

          Conversly,  the  above  situation  allows you to override monitor
          commands with your own.  E.g., 

                    DELETE==_d "The DELETE command is not allowed!" 


          14.7.2  Improper  Expansion  Of  Monitor  Commands  - This second
          gotcha is a little more subtle.  

          Some  monitor  commands  have the same name as the utilities that
          they invoke.  If you are, for example, running as UCF  with  PATH
          in effect, this can cause invalid command expansions.  

          As  an  illustration,  suppose your run-by-name path is "DK:" and
          DK:  is currently assigned to SY:.  The command  "DUMP/TERM  RUB-
          ISH.DAT"  should be passed to KMON undisturbed (assuming that you
          haven't defined your own DUMP command).  However, UCL+ will  spot
          program  DUMP.SAV  on  "DK:",  and  expand  the  command  as "RUN
          DK:DUMP/TERM  RUBISH.DAT".   DUMP   will   see   something   like
          "RUBISH.DAT=/TERM"  and give you what might seem, at the time, to
          be a mysterious error message.  

          I  normally  avoid this problem by disabling the run-by-name path
          (NOPATH command).  If you have a need to retain  the  run-by-name
          search  path, define some symbols that will cause UCL+ to, in ef-
          fect, pass your command line to the monitor in an unaltered form.
          For the preceeding example, define 

                    DUMP==DUMP


          14.7.3  Single Key Commands  - All is not gotchas...  

          UCL+  is not very picky about the characters that you use in sym-
          bol names.  If you are using UCL+ as a UCI under  TSX-Plus,  then
          you  are running UCL+ directly whenever you input a command line.
          This means that you can define some handy single-key symbols that
          the  monitor  would  strongly  disapprove of under normal circum-
          stances.  For example:  

                    \==edit
                    |==edit/create
                    ??????==help

          One user that I know of (Ray Moran) places his VT100 in alternate
          keypad mode (with a UCL+ command, of course!) and  executes  sym-
          bols  whose names correspond to the escape sequences generated by

          UCL+ -- User Command Linkage Program - V07.54a            Page 50
                  Spring 1986 DECUS Release


          the individual keys.  

          If  you  are  using a VT220, or anything with an LK201 style key-
          board.  You have even more keys that you can define!  


          14.8  UCL+ Assembly Conditionals 

          You  can build a somewhat customized version of UCL+ by modifying
          the conditionals file, UCL.CND, prior to assembly.  

          The prefix conditional, PFX, determines the prefix character used
          by UCL+ when UCI_MODE is in effect.  You can change  this  prefix
          by  changing  the  definition  of PFX from a period (".") to some
          other character.  

          Two  non-essential  hard-wired commands, RNO and CD, are normally
          included when UCL+ is assembled.  If you do not wish  to  include
          the CD command, set conditional CD$C equal to zero;  to eliminate
          the RNO command, set RNO$C equal to zero.  Excluding both the  CD
          and RNO commands decreases the size of UCL+ by 472 decimal words. 

          Use  the  command  file  UCL.COM to build UCL+.  Use UCLXM.COM to
          build the XM version.  


          14.9  Modifying RT-11 To Change The UCL/UCF Device/File Name 

          The  RT-11 monitor can be modified to run UCL.SAV or UCF.SAV from
          some device other than SY:.  The name of the UCL or  UCF  program
          can  also  be  changed.  To accomplish this, you need to know the
          offsets for some  or  all  of  the  following  locations  in  the
          monitor:  

                o  ..UCLD - UCL device name 

                o  ..UCLF - UCL file name 

                o  ..UCFD - UCF device name 

                o  ..UCFF - UCF file name 

          The  values located at the above offsets are all radix-50 and, as
          you might expect, the file name immediately  follows  the  device
          name.   I.e.,  ..UCLF  is  located  at  ..UCLD+2  and  ..UCFF  at
          ..UCFD+2.  

          If  you  are an orderly person, you can find the values for these
          offsets by inspecting the link map for your monitor.  Note  that,
          if  your  monitor version is earlier than V5.2, there will not be
          any ..UCFD/..UCFF values.  


          UCL+ -- User Command Linkage Program - V07.54a            Page 51
                  Spring 1986 DECUS Release


          If you are a somewhat disorderly person (perhaps you are undergo-
          ing TECO withdrawal), you can find ..UCLF and ..UCFF by employing
          the  SIPP  search function and looking for a radix-50 UCL or UCF,
          respectively.  

          In  either case, once you know where these locations are, you can
          use SIPP to patch your monitor to taste.  In the following  exam-
          ple,  the  UCL device is patched from "SY:" to "UCL:".  I usually
          do this because I can then assign some other device  to  be  UCL:
          in  my start-up command file (VM:  is a nice choice).  The labels
          ..UCLD and ..UCLF represent the offsets that were  obtained  from
          the monitor's link map.  

                    .SIPP RT11XM.SYS/A                     _________________
                    Base?    <ret>                             _____
                    Offset?  ..UCLD                             ______

                      Base       Offset      Old  New?
                       000000     ..UCLD  075250  ;R                                                  __
                       000000     ..UCLD   <SY >  ;RUCL                                                  _____
                       000000     ..UCLF   <UCL>  <ctrl/Y>                                                  ________

          If  you  run  more than one type of RT-11 monitor on your system,
          you may wish to use different copies of UCL and/or UCF  depending
          on which monitor is booted.  In the example below, the XM monitor
          is patched to run UCLXM.SAV rather than UCL.SAV.  

                    .SIPP RT11XM.SYS/A                     _________________
                    Base?    <ret>                             _____
                    Offset?  ..UCLF                             ______

                      Base       Offset      Old  New?
                       000000     ..UCLF  101704  ;R                                                  __
                       000000     ..UCLF   <UCL>  <ret>                                                  _____
                       000000     ..UCLF+2 <   >  ;RXM                                                  ____
                       000000     ..UCLF+4 <SAV>  <ctrl/Y>                                                  ________



                                        NOTE

               If  you  install this patch, you should be aware of one
               small catch:  you should use the UCL+ LIST  command  to
               obtain  a  list  of the current symbol definitions.  If
               you type "SHOW COMMANDS", for example, RT-11  will  at-
               tempt  to  run SY:UCL.SAV, even though you have changed
               the name of the "UCL" that it uses for all  other  pur-
               poses.  



          UCL+ -- User Command Linkage Program - V07.54a            Page 52
                  Spring 1986 DECUS Release


          14.10  Modifying TSX-Plus To Change The UCL/UCI Defaults 

          If you select UCL support when you generate TSX-Plus (if not, why
          are  you  reading  this?),  the  default  UCL  program  name   is
          SY:TSXUCL.SAV  (if you are running V5.0 or later).  Likewise, the
          default name for user-written UCI's is SY:UKMON.SAV.  The easiest
          way  to change these names is to edit the TSGEN.MAC file prior to
          building TSX-Plus.  These values are not normally modified by the
          user  and,  thus,  will  not  be  found within the "user area" of
          TSGEN.MAC.  If you hunt around  with  the  editor,  however,  you
          should  be able to find them.  For example, if you have V5.1B and
          want to change the UCL default name, you will discover a line  of
          code that should look like 

                    UCLNAM: .RAD50  /SY TSXUCLSAV/ 

          If  you  are  modifying  the UCI default, you will find something
          like 

                    UKMNAM: .RAD50  /SY UKMON SAV/ 

          To change the defaults, edit the rad50 file names prior to assem-
          bling TSGEN.MAC.  For instance, you could edit the value at label
          "UCLNAM:"   to   change   the  UCL  name  from  SY:TSXUCL.SAV  to
          UCL:TSXUCL.SAV.  Further variations on this theme I leave  as  an
          exercise to the user.  


          14.11  Controlling Command Line Factoring 

          Both RT-11 and TSX-Plus support command line factoring.  However,
          they don't execute it in the same processing sequence.  This  can
          effect the way that you define a symbol that employs factoring as
          part of it's definition.  

          For  example, suppose that you wish to define a symbol, "FTN", to
          invoke the FORTRAN compiler in a specialized  fashion  that  com-
          piles  one  or  more files resident on device "FTN:".  If you are
          using TSX-Plus, you can define the symbol at the monitor level:  

                    .FTN==FORT FTN:(^)                     _________________

          However, the example above will not work properly if you are run-
          ning RT-11.  This is because RT-11 expands the factoring prior to
          passing  the  command line to UCL+.  Thus, RT-11 would remove the
          "unnecessary" parentheses in the preceeding  monitor  level  com-
          mand,  and  UCL+  would  see the definition as "FTN==FORT FTN:^".
          The solution, in this case, is to run UCL+ directly:  

                    .R UCL                     _____
                    UCL> ftn==fort ftn:(^)                         _________________
                    UCL> <ctrl/C>                         ________

          UCL+ -- User Command Linkage Program - V07.54a            Page 53
                  Spring 1986 DECUS Release



          The  tendency  of RT-11 to pass "rare" rather than "raw" commands
          to UCL+ can cause more subtle problems also.  

          Suppose, for example, that you wanted to define a command to send
          a line of ReGIS graphics instructions to a VT241  to  change  the
          screen  colors.   You  must  preceed the graphics output with the
          text "<esc>Pp" and follow it with "<esc>\" ("<esc>" indicates the
          escape  character).  At first glance, it would seem that the fol-
          lowing symbol definition sequence would do the  trick  (note  the
          use of the quote operator to display the "").  

                    .R UCL
                    UCL> regis==disp "<esc>Pp"\disp ^\disp "<esc>|\"
                    UCL> color==_regis S(M0(AH0L50S100)1( etc...
                    UCL> <ctrl/C>

          Unfortunately, since RT-11 is allowed to "touch" the color speci-
          fication string in the above example, it will strip out  most  of
          the  parantheses, and the COLOR command will not work.  One solu-
          tion is to define the REGIS symbol in such a way that it will run
          UCL+  directly (the EXIT symbol is necessary to force a return to
          the monitor).  

                    .R UCL
                    UCL> regis==r ucl\d "<esc>Pp"\d "^"\d "<esc>|\"\exit
                    UCL> exit==\
                    UCL> color==_regis S(M0(AH0L50S100)1( etc...
                    UCL> <ctrl/C>


          UCL+ -- User Command Linkage Program - V07.54a            Page 54
                  Spring 1986 DECUS Release


          14.12  Patching UCL+ For RT-11 V5.1 

          When  you  run the UCL+ program, it executes a "context check" to
          determine which environment it  is  running  in.   Unfortunately,
          there  is  a bug in RT-11 V5.1 which sets some extraneous bits in
          the monitor version code.  This causes the non-XM version of UCL+
          to  behave incorrectly when running under V5.1.  If you are using
          UCL+ with RT-11 V5.1, apply  the  following  patch  to  the  file
          UCL.SAV to force UCL+ to assume that it is running under V5.1.  

          Look  at the link map on the UCL+ distribution (UCL.MAP) and find
          the value of the label "FUDGE" (when this document was  prepared,
          the  value  for "FUDGE" was 025762, but you should check the link
          map just to make sure).  Use SIPP to disable the  release/version
          check  in the context routine ("<ret>" denotes a carriage return,
          "<ctrl/Y>" is a control-Y, operator input is underlined):  

                    .SIPP UCL.SAV/A                     ______________
                    Base?    <ret>                             _____
                    Offset?  FUDGE                             _____

                      Base       Offset      Old  New?
                       000000     FUDGE   002002  240                                                  ___
                       000000     FUDGE+2 005067  <ctrl/Y>                                                  ________

          Note  that it is not necessary to apply this type of patch to the
          XM version of UCL+ (UCLXM.SAV) because it will not run under ver-
          sions of RT-11 prior to V5.2.  

          UCL+ -- User Command Linkage Program - V07.54a            Page 55
                  Spring 1986 DECUS Release


          15.0  REPORTING PROBLEMS AND SUGGESTIONS 


          I want to know about bugs!  

          I am also interested in suggestions for improving UCL+ as well as
          any interesting applications that you may have found for it.  

          I can be contacted at one of the following addresses:  


                    William K. Walker
                    Monsanto Research Corp.
                    P. O. Box 32
                    Miamisburg, OH  45342
                    (513) 865-3557


                    William K. Walker
                    P. 0. Box 149
                    Alpha, OH  45301
                    (513) 426-7094/0344


          If  you are on Compuserve, my ID is 71066,24.  Leave a message in
          EMAIL or in the PDP-11 SIG (within  the  SIG,  address  stuff  to
          "Bill Walker 71066,24").  

          If you discover a genuine bug in the current version of UCL+, and
          you are the first to report it, you get a post-paid copy  of  the
          next release -- you can even keep the floppy.  

          UCL+ -- User Command Linkage Program - V07.54a            Page 56
                  Spring 1986 DECUS Release


          16.0  WISH LIST 

          Aside  from  the  usual fiddling about with the internals, I cur-
          rently plan to make the  following  additions/changes  to  future
          versions of UCL+:  

                o  a  revision  to  the STORE and RECALL commands that will
                   eliminate the  incompatibility  between  .UCL  and  .UCX
                   files, 

                o  a  reasonable way to change the number of characters al-
                   located for symbol names and symbol definitions, 

                o  a  method  to  change the total number of symbol defini-
                   tions allowed in UCL+, and 

                o  some  further  extensions  to  the LIST and DISPLAY com-
                   mands.  

          I  do  NOT intend to implement a "symbol definition editor".  Use
          STORE/JOURNAL and edit the output.  I also don't plan to  add  an
          "F77" command -- I am hoping that the RT-11 people will do this. 

          UCL+ -- User Command Linkage Program - V07.54a            Page 57
                  Spring 1986 DECUS Release


          17.0  UCL+ COMMAND AND SYNTAX SUMMARY 



                              SYMBOL DEFINITION SYNTAX                              ________________________

          name==definition

          where "name"       is a six-character symbol name
                "definition" specifies the symbol expansion


                                      OPERATORS                                      _________

                ==  symbol definition
                \   line separation/termination
                ^n  argument insertion; if "n" used, insert nth part
                _   "execute-immediate" flag
                |   quote flag; treat next character as text only


                                "HARD-WIRED" COMMANDS                                _____________________

          CD        Changes the default device
          CHAIN     Sets up UCL+ exit chaining
          DISPLAY   Displays a string or UCL+ command/symbol expansion
          ERASE     Deletes one or more UCL+ symbols
          LIST      Lists the current UCL+ commands/symbols/status
          NOSL      Turns the single-line editor off
          PASS_ON   Passes a command string to a program "UCL-style"
          PATH      Sets up the UCL+ "run-by-name" path
          PROMPT    Sets the UCL+ command-line prompt string
          RECALL    Loads symbol definition and status tables
          RELOAD    Reloads a UCL+ global region (XM version only)
          RNO       Invokes the RUNOFF program
          SLON      Turns the single-line editor on
          STORE     Saves the UCL+ symbol definition and status tables
          UCI_MODE  Set UCL+ "pass-line-to-KMON" mode (TSX-Plus only)