SAND 80-2464
                                 81h04a




                        A Library Implementation
                                   of
                          Programmed Requests
                                  for
                                TSX-Plus




                          N. A. Bourgeois, Jr.
                   Systems Engineering Division 1738
                      Sandia National Laboratories
                             P. O. Box 5800
                         Albuquerque, NM 87185
                             (505) 844-8088




                                Abstract

                     A  library  of   FORTRAN   callable
                routines that implement the EMTs provid-
                ed    by    TSX-Plus    is    described.
                Descriptions,  calling  sequences, exam-
                ples  of  use,  library  building   pro-
                cedures, and source codes are given.


        TSX-Plus Library                                  PAGE 2



















                This document is issued  by  Sandia  Na-
                tional  Laboratories,  operated  for the
                United States Department  of  Energy  by
                Sandia Corporation.


                                 Notice


                This document was sponsored by the Unit-
                ed States Government.  Neither the Unit-
                ed  States  Government  nor  the  United
                States  Department of Energy, nor any of
                their employees, nor any of  their  con-
                tractors,  subcontractors,  or their em-
                ployees makes any warranty,  express  or
                implied,  or assumes any legal liability
                or responsibility for the accuracy, com-
                pleteness  or usefulness of any informa-
                tion, apparatus, product or process dis-
                closed, or represents that its use would
                not infringe privately owned rights.


                This work was sponsored and funded by:

                    Headquarters, ESD / OCB / Stop 36
                    Hanscom Air Force Base, MA 01731


        TSX-Plus Library                                  PAGE 3



















                            Acknowledgments


                The author wishes to  thank  S & H  Com-
                puter  Systems  Inc.  for its permission
                to  reprint  parts  of  their  "TSX-Plus
                Reference Manual" in this document.

                The author wishes also  to  thank  W. L.
                Jacklin  for his assistance in reviewing
                this document and particularly  for  his
                help  with  the many FORTRAN examples in
                the third chapter.




                              ***********
                              * CAUTION *
                              ***********


                Much of both the MACRO-11  source  codes
                and  the  FORTRAN  examples described in
                this document are as yet untried.

                There  have  been  some   routine   name
                changes   from  prior  releases  of  the
                TSX-Plus library.


        TSX-Plus Library                                  PAGE 4
        Introduction






                            1.  Introduction


             When application programs are executed under a time
        sharing executive such as TSX-Plus * [1,2] certain capa-
        bilities become desirable if not  absolutely  essential.
        These  capabilities  relate  to  requirements  for  such
        things as hardware dependent I/O, shared  files,  inter-
        program  communication, and others.  TSX-Plus provides a
        number of programmed requests or  EMTs  for  these  pur-
        poses.

             This document describes a number of  FORTRAN  call-
        able routines and their calling sequences that implement
        these EMTs.  All of the routines are callable as FORTRAN
        subroutines  and some are also callable as FORTRAN func-
        tions.  The routines are written in MACRO-11  [3].   The
        code  is  completely reentrant and, therefore, shareable
        under TSX-Plus.

             The next section offers a  general  description  of
        the  several  groups of routines.  It describes the pro-
        cess for linking the routines to the FORTRAN application
        program.   The  general  calling sequences are also des-
        cribed.

             The third section gives a detailed  description  of
        each  of  the individual routines.  The descriptions in-
        clude both the calling sequences and, in most cases, ex-
        amples.

             Procedures for constructing the  library  from  the
        several source modules are given in the fourth section.

             Appendix A contains a table of the routines  listed
        in functional groups.

             A description of the distribution kit is  contained
        in Appendix B.












        *   TSX-Plus is a registered trademark of S & H Com-
            puter Systems Inc., Nashville, TN.


        TSX-Plus Library                                  PAGE 5
        General Description






                        2.  General Description


             These TSX-Plus library routines provide  facilities
        to  support detached jobs, file structured device mount-
        ing and dismounting, communication between running  pro-
        grams,  program  performance analysis, real time program
        execution,  shared  run  time  system,   shared   files,
        communication  between  running programs and a terminal,
        program control of the terminal,  ODT  activation  mode,
        and several miscellaneous EMTs.

             The standard FORTRAN  subroutine  calling  sequence
        shown below may be used to access all of the routines in
        the TSX-Plus library.

                      CALL RTNAM ( ARG1,...,ARGn )

             Those routines that return only one value are  also
        callable as FORTRAN functions.  This is as follows:

                     IRET = RTNAM ( ARG1,...,ARGn )

             The application program is first compiled  as  fol-
        lows:

                            .RUN SY:FORTRAN
                            *MYPROG=MYPROG 
                            *^C            

             Then the routines are linked with  the  application
        program as shown below:

                        .RUN SY:LINK           
                        *MYPROG=MYPROG,TSXLIB/F
                        *^C                    
                                   or
                  .RUN SY:LINK                       
                  *MYPROG=MYPROG,TSXLIB,SYSLIB,FPULIB
                  *^C                                

             The application program is now ready for execution.

                             .RUN DK:MYPROG

             The "TSX-Plus Reference Manual" [1]  describes  how
        the  EMTs  implemented  in this TSX-Plus library are ac-
        cessed  from   a   MACRO-11   program.    However,   the
        FORTRAN/MACRO  interface  described  in  the "RT-11 Pro-
        grammer's Reference Manual" [5] may also be used to  ac-
        cess the routines in the library.


        TSX-Plus Library                                  PAGE 6
        General Description


    Detached Job Support

             Table 2-1 lists the routines that provide  detached
        job support from within an executing program.

                ISTDJ   Get the status of a detached job.
                KLDTJB  Kill a detached job.
                STDTJB  Start a detached job.

                         Detached job support.
                               Table 2-1.


    Device Mounting and Dismounting

             It is possible to mount and dismount a file  struc-
        tured device for directory caching from within a running
        program.  The routines listed in Table 2-2 provide these
        capabilities.

                DISMNT  Dismount a file structured device.
                MOUNT   Mount a file structured device.

                    Device mounting and dismounting.
                               Table 2-2.


    Interprogram Message Communication

             TSX-Plus provides an optional facility that  allows
        running  programs to communicate with each other.  Table
        2-3 lists the routines that  support  this  interprogram
        message communication.

                MSGSND  Send a message to another job.
                RCVMSG  Try to receive a  message  from  another
                        job.
                RCVMSW  Wait for a message from another job.

                  Interprogram message ãommunication.
                               Table 2-3.

             Messages are transferred between programs by  using
        named  message  channels.   A  message channel accepts a
        message from a sending program, stores the message in  a
        queue associated with the channel, and delivers the mes-
        sage to a receiving program on its request for a message
        on  the channel.  Message channels are separate from I/O
        channels.

             Each active message channel has associated with  it
        an ASCII character name that is used by both the sending
        and receiving programs to  identify  the  channel.   The
        names   associated   with   the   channels  are  defined
        dynamically by the running programs.  A message  channel


        TSX-Plus Library                                  PAGE 7
        General Description


        is  active when messages are being held in the queue as-
        sociated with the channel or if a program is waiting for
        a  message  from the channel.  When message channels be-
        come inactive they are returned to a free pool  and  may
        then be reused.

             Once a message is queued on a channel, that message
        will remain in the queue until some program receives it.
        A program's exiting to the keyboard monitor does not re-
        move  any  pending messages.  This allows one program to
        leave a message for another program that will be run  at
        a later time.


    Performance Analysis Support

             For many applications the  keyboard  monitor  level
        performance  analysis  control  provided  by TSX-Plus is
        adequate.  However, in cases such as analyzing the  per-
        formance of an overlayed program it is necessary to have
        control over the performance analysis feature  from  the
        running  program.  The routines listed in Table 2-4 pro-
        vide just this capability.

                INITPA  Initialize for a performance analysis.
                ISPPA   Stop a performance analysis.
                ISTPA   Start a performance analysis.
                TERMPA  Terminate from a performance analysis.

                     Performance analysis support.
                               Table 2-4.


    Real Time Program Support

             The real time program support provided by  TSX-Plus
        allows multiple real time programs to be run concurrent-
        ly with normal time sharing operations.  The basic func-
        tions provided by this facility are listed in Table 2-5.

             A program must have operator privilege to  use  any
        of the real time routines.  The real time facilities are
        available to both normal jobs controlled by time sharing
        lines  and  to  detached jobs.  Detached jobs started by
        time sharing users have operator privilege only  if  the
        user starting them does.

             A basic facility required by many  real  time  pro-
        grams  is  the ability to access the I/O page which con-
        tains the peripheral device registers.   A  normal  time
        sharing  job  does  not have this access.  It is instead
        mapped to a simulated RMON.  This allows  programs  that
        directly access offsets into RMON to run correctly.


        TSX-Plus Library                                  PAGE 8
        General Description


                CNVAPA  Convert a virtual address to a  physical
                        address.
                IBICIO  Bit clear a value into the I/O page.
                IBISIO  Bit set a value into the I/O page.
                ICNINT  Connect an interrupt vector to a comple-
                        tion routine.
                IPEKIO  Peek at a value in the I/O page.
                IPOKIO  Poke a value into the I/O page.
                IRLINT  Release an interrupt vector connection.
                ISPY    Return values from within the  simulated
                        RMON (SYSLIB routine).
                IUNLKM  Unlock a job from memory.
                LKANMY  Lock a job into any memory.
                LKLOMY  Lock a job into low memory.
                MPIOPS  Map the I/O page into the program space.
                MPRMPS  Map the simulated RMON into the  program
                        space.

                       Real time program support.
                               Table 2-5.

             A real time program can access the I/O page in  one
        of two ways:  it can map the I/O page into the program's
        space;  or it can leave the simulated RMON  mapped  into
        the program's space and perform peek, poke, bit set, and
        bit clear operations into the I/O page.  It is much more
        efficient  to  directly  access  the device registers by
        mapping the I/O page into the program's  space  than  to
        use  the  routines  to  perform  each individual access.
        However, this technique will not  work  if  the  program
        must  also  directly access offsets into RMON.  The cor-
        rect way to access offsets into RMON is with the  SYSLIB
        routine,  ISPY,  which will work even if the I/O page is
        mapped into the program's space.

             The TSX-Plus real time support  facility  allows  a
        program to connect a real time interrupt to a completion
        routine.  If this is done, the completion routine is ex-
        ecuted  each time the specified interrupt occurs.  It is
        possible for several interrupt vectors to  be  connected
        to  the same completion routine in a job but it is ille-
        gal for more than one job to connect to the same  inter-
        rupt vector.

             An execution priority may  be  specified  for  each
        completion  routine.   This  is  not  the  same  as  the
        hardware selected priority of the interrupt.   All  com-
        pletion  routines  are synchronized with the job and run
        at hardware priority level zero.  The completion routine
        priority is used to schedule the completion routines for
        execution.   The  available  priority  levels  are  zero
        through  seven.  The execution of a real time completion
        routine for one job will be interrupted and suspended if
        an  interrupt  occurs that causes a higher priority com-
        pletion routine for another job to be queued for  execu-


        TSX-Plus Library                                  PAGE 9
        General Description


        tion.   However,  a  completion  routine for a given job
        will never be  interrupted  to  run  another  completion
        routine  for the same job even if a higher priority com-
        pletion routine is pending.

             Completion routine priorities one through seven are
        real  time priorities.  They are higher than the priori-
        ties given to time sharing jobs and will always  preempt
        the time sharing jobs.  Completion routine priority zero
        is not a real time priority but rather a very high  nor-
        mal  priority.   Such  zero priority completion routines
        are time sliced in the normal fashion.  If a  completion
        routine  enters  a  wait  state it relinquishes its real
        time priority.  Jobs  that  have  real  time,  interrupt
        driven completion routines need not be locked in memory.

             In time critical, real time  applications  where  a
        program must respond to an interrupt with minimum delay,
        it may be necessary for the job to lock itself in memory
        to  avoid  the  time consumed in program swapping.  This
        facility should be used with caution since if  a  number
        of  large programs are locked in memory there may not be
        enough space left to run other programs.


    Shared Run Time System Support

             TSX-Plus provides a facility that allows shared run
        time systems or data areas to be mapped into the address
        spaces of multiple time sharing jobs.  Table  2-6  lists
        the routines that support this feature.

                IASRNT  Associate/disassociate a shared run time
                        system with a job.
                MAPRNT  Map a shared  run  time  system  into  a
                        job's region.

                    Shared run time system support.
                               Table 2-6.

             Memory space can be  conserved  by  having  several
        jobs  access  a  common copy of a run time system rather
        than having to allocate space within each  job.   Shared
        run  time systems are never swapped out of memory.  When
        a job is associated with a run time system, a portion of
        the job's virtual memory is mapped so as to allow access
        to the run time system.


    Shared File Support

             Table 2-7 lists the routines that offer  access  to
        the  shared  file  record  locking  facility provided by
        TSX-Plus.  This is useful in situations  where  programs
        being run from several terminals wish to update a common


        TSX-Plus Library                                 PAGE 10
        General Description


        file.  Through the record locking facility a program may
        gain  exclusive access to one or more blocks in a shared
        file by locking those blocks.  Other users attempting to
        lock  the  same  blocks  will be denied access until the
        first user releases the locked blocks.

                ICKWTS  Check for writes to a shared file.
                IDCLSF  Declare a file to be shared.
                ISVST   Save the status of a shared file.
                IUALBK  Unlock all locked blocks.
                IUSPBK  Unlock a specific block.
                LKBLK   Try to lock a block.
                LKBLKW  Wait for a block to lock.

                          Shared file support.
                               Table 2-7.

             The recommended procedure  for  updating  a  shared
        file being accessed by several users is as follows:

            1.  Open the file.
            2.  Declare the file to be shared.
            3.  Lock all blocks which contain  the  desired  re-
                cord.
            4.  Read the locked blocks into memory.
            5.  Update the record.
            6.  Write the updated blocks to the file.
            7.  Unlock the blocks.
            8.  Repeat steps three through seven as required.
            9.  Close the file.


    Terminal Communications Support

             The routines that allow a running program  to  com-
        municate with a terminal are listed in Table 2-8.

                TRMIN   Accept a string of characters  from  the
                        terminal.
                TRMMSG  Send a message to another terminal.
                TRMOUT  Send a string of characters to the  ter-
                        minal.

                    Terminal ãommunications support.
                               Table 2-8.


    Terminal Control Support

             The terminal control support routines are listed in
        Table 2-9.


        TSX-Plus Library                                 PAGE 11
        General Description


                BRKCTL  Establish break sentinal control.
                HIEFOF  Turn off the  high  efficiency  terminal
                        mode.
                HIEFON  Turn on  the  high  efficiency  terminal
                        mode.
                IACTCH  Check for pending activation characters.
                ITRERR  Check for terminal input errors.
                ITRTYP  Determine the terminal type.
                TIMOUT  Set the terminal read time out value.

                       Terminal control support.
                               Table 2-9.


    Miscellaneous EMT Support

             Table 2-10 lists the routines that support the sev-
        eral miscellaneous EMTs provided by TSX-Plus.

                ISPBLK  Determine the number of free  blocks  in
                        the spool file.
                ITSLIC  Determine the TSX-Plus license number.
                ITSLIN  Determine the TSX-Plus line number.
                MEMSET  Set the memory allocation.

                       Miscellaneous EMT support.
                              Table 2-10.


    ODT Activation Mode Support

             ODT activation mode may be turned on and  off  from
        within a running program.  Table 2-11 lists the routines
        that support this feature.  In this mode  TSX-Plus  con-
        siders all characters to be activation characters except
        the digits, the comma, the dollar  sign  and  the  semi-
        colon.

                RSRODT  Reset normal activation mode.
                SETODT  Set ODT activation mode.

                      ODT activation mode support.
                              Table 2-11.


        TSX-Plus Library                                 PAGE 12
        Routine Descriptions






                        3.  Routine Descriptions


             This section presents all of the TSX-Plus  routines
        in  alphabetical  order and provides a detailed descrip-
        tion of each one.   The  FORTRAN  calling  sequence  and
        where  appropriate  an example of each call in a FORTRAN
        program is given.

             The user should be  thoroughly  familiar  with  the
        general  description  of  this TSX-Plus library given in
        the previous section of this document.   Additional  in-
        formation  is available in the "TSX-Plus Reference Manu-
        al" [1] and the "RT-11  Programmer's  Reference  Manual"
        [5].   Some  of  these  TSXLIB routines require calls to
        various SYSLIB routines.

             In the following descriptions,  arguments  enclosed
        in square brackets, [], are optional.


    BRKCTL

             This  routine  is  used  to  declare  a  completion
        routine  that  will be triggered when the BREAK key or a
        declared key on the terminal is  pressed.   The  calling
        sequence is:

                     CALL BRKCTL ( IBRKCH,CPLRTN )

        where:  IBRKCH  is the value of the character that is to
                        be used for the break control.

                CPLRTN  is the name of the completion routine to
                        be  executed when the break character is
                        pressed.

             The specified completion routine  will  be  entered
        when  either  the  BREAK  key  or  the  declared  key is
        pressed.  If no declared key is wanted specify  a  value
        of  zero for IBRKCH.  On some systems the console termi-
        nal BREAK key causes entry into console ODT and for this
        reason requires a declared key value.

             Only one break routine may be specified at  a  time
        for each user.  If a break routine was previously speci-
        fied, it is cancelled when a new break  routine  is  de-
        clared.  If a value of zero is specified for the name of
        the completion routine, CPLRTN, any previously specified
        break routine is cancelled.



        TSX-Plus Library                                 PAGE 13
        Routine Descriptions


             The following example first declares the completion
        routine  as an external, then establishes break sentinel
        control using the letter H, and later cancells the  con-
        trol.

                    EXTERNAL CPLRTN                 
                    IBRKCH = 72                     
                        .                           
                        .                           
                    CALL BRKCTL ( IBRKCH,CPLRTN )   
                        .                           
                        .                           
                    CALL BRKCTL ( 0,0 )             
                        .                           
                        .                           


    CNVAPA

             This routine is used to convert a  virtual  address
        into  a  physical  address.  This is necessary when con-
        trolling devices that do direct memory access transfers.
        The  program  should lock itself into memory before exe-
        cuting  this  routine.   The  calling  sequence  is   as
        follows:

                 CALL CNVAPA ( IVADR,IPADR [ ,IERR ] )

        where:  IVADR   is the virtual address  that  is  to  be
                        converted.

                IPADR   is the name of the  two  element  buffer
                        into which the physical address is to be
                        returned.

                IERR    is negative or the following:

                        0  real time support is not available or
                           this   job  does  not  have  operator
                           privilege.

             The low order sixteen bits of the physical  address
        are  returned in the first element of the buffer, IPADR,
        and the high order two bits of the physical address  are
        returned  in  bit  positions four and five of the second
        element of the buffer.

             The following example first locks itself into memo-
        ry  then  converts  a  virtual address to a physical ad-
        dress.  The program is halted if the error condition  is
        returned.

                   DIMENSION IPADR ( 2 )            
                   CALL LKANMY                      
                   CALL CNVAPA ( "54720,IPADR,IERR )


        TSX-Plus Library                                 PAGE 14
        Routine Descriptions


                   IF ( IERR .EQ. 0 ) STOP          
                       .                            
                       .                            


    DISMNT

             This routine is used to dismount a file  structured
        device.   This  causes  TSX-Plus to stop doing directory
        caching of the device.  The effect of  this  routine  is
        the same as the TSX-Plus DISMOUNT keyboard command.  The
        calling sequence is as follows:

                         CALL DISMNT ( IDVNAM )

        where:  IDVNAM  is the RAD50 value of  the  file  struc-
                        tured device name.

             The following  example  uses  the  SYSLIB  routine,
        IRAD50,  to  convert the ASCII value of the device name,
        DL:, to its RAD50 value.  It then mounts the device  and
        later dismounts it.

                     CALL IRAD50 ( 3,'DL ',IDVNAM )
                     CALL MOUNT ( IDVNAM )         
                         .                         
                         .                         
                     CALL DISMNT ( IDVNAM )        
                         .                         
                         .                         


    HIEFOF

             This routine is used to turn  the  high  efficiency
        terminal mode off.  The calling sequence in as follows:

                              CALL HIEFOF

             The following example first turns  high  efficiency
        terminal mode on and later turns it off.

                              CALL HIEFON
                                  .      
                                  .      
                              CALL HIEFOF
                                  .      
                                  .      


    HIEFON

             This routine is used to turn  the  high  efficiency
        terminal mode on.  The calling sequence is as follows:



        TSX-Plus Library                                 PAGE 15
        Routine Descriptions


                              CALL HIEFON

             TSX-Plus offers a high efficiency mode of  terminal
        operation that eliminates a substantial amount of system
        overhead for terminal character processing  by  reducing
        the amount of processing that is done on each character.
        When  in  high  efficiency  mode,  characters  are  sent
        directly  to  the  terminal  with  minimum  handling  by
        TSX-Plus.  Operations such as expanding tabs  to  spaces
        and  form  feeds  to  line  feeds are omitted as well as
        input processing such as echoing characters  and  recog-
        nizing  control characters such as rubout, control-U and
        control-C.  The only  characters  treated  specially  on
        input  are  user  defined  activation characters and the
        user specified break character.  At least one user spec-
        ified  activation character must be declared if high ef-
        ficiency mode is to be used.  This form of terminal  I/O
        is  designed to facilitate high speed machine to machine
        communication.  It can be used effectively with buffered
        mode terminals.


    IACTCH

             This routine is used to determine if any activation
        characters  have  been  received by the line but not yet
        accepted by the program.  The calling sequences  are  as
        follows:

                          CALL IACTCH ( IRET )
                                   or
                            IRET = IACTCH ()

        where:  IRET    is one of the following:

                        0  no activation character is pending.

                        1  at least one activation character  is
                           pending.


    IASRNT

             This routine is used to associate a shared run time
        system  with a job.  It is also used to disassociate all
        shared run time systems from a  job.   The  calling  se-
        quences are as follows:

                    CALL IASRNT ( IRNTIM [ ,IERR ] )
                                   or
                        IERR = IASRNT ( IRNTIM )

        where:  IRNTIM  is the six character RAD50 value of  the
                        name of the shareable run time system.



        TSX-Plus Library                                 PAGE 16
        Routine Descriptions


                IERR    is one of the following:

                        0  no error.

                        1  run time system name not recognized.

             The effect of this routine is to associate  a  par-
        ticular   shareable   run  time  system  with  the  job.
        However, this routine does not affect the memory mapping
        for  the  job or make the run time system visible to the
        job.  That is  done  by  the  MAPRNT  routine  described
        later.  If some other run time system has been previous-
        ly mapped into the job's region, that mapping  is  unaf-
        fected  by  this  routine.   Thus it is possible to have
        multiple run time systems mapped into the  job's  region
        by  associating and mapping them one at a time into dif-
        ferent regions of the job's virtual memory space.

             If the name pointer, IRNTIM, is set to  zero,  this
        routine causes all run time systems to become disassoci-
        ated from the job and reestablishes normal  memory  map-
        ping for the job.

             The following  example  uses  the  SYSLIB  routine,
        IRAD50,  to  declare the name of the run time system and
        then associates it with the job.  If the error condition
        is returned the program is halted.

                   DIMENSION IRNTIM ( 2 )           
                   CALL IRAD50 ( 6,'TSXLIB',IRNTIM )
                   IERR = IASRNT ( IRNTIM )         
                   IF ( IERR .EQ. 1 ) STOP          
                       .                            
                       .                            


    IBICIO

             This routine is used to perform a bit clear  opera-
        tion  into  a word in the I/O page without requiring the
        job's virtual address region to be  mapped  to  the  I/O
        page.  The calling sequences are as follows:

                  CALL IBICIO ( IADR,IVAL [ ,IERR ] )
                                   or
                      IERR = IBICIO ( IADR,IVAL )

        where:  IADR    is the address of the word  in  the  I/O
                        page to be accessed.

                IVAL    is the value to be bit cleared into  the
                        I/O page.

                IERR    is negative or the following:



        TSX-Plus Library                                 PAGE 17
        Routine Descriptions


                        0  real time support is not available or
                           this   job  does  not  have  operator
                           privilege.

             The following example bit clears  a  value  in  the
        register  at  the  octal address 176500 in the I/O page.
        The program is stopped if the  error  condition  is  re-
        turned.

                     IERR = IBICIO ( "176500,"100 )
                     IF ( IERR .EQ. 0 ) STOP       
                         .                         
                         .                         


    IBISIO

             This routine is used to perform a bit set operation
        into  a word in the I/O page without requiring the job's
        virtual address region to be mapped  to  the  I/O  page.
        The calling sequences are as follows:

                  CALL IBISIO ( IADR,IVAL [ ,IERR ] )
                                   or
                      IERR = IBISIO ( IADR, IVAL )

        where:  IADR    is the address of the word  in  the  I/O
                        page to be accessed.

                IVAL    is the value to be bit set into the  I/O
                        page.

                IERR    is negative or the following:

                        0  real time support is not available or
                           this   job  does  not  have  operator
                           privilege.

             The following example bit sets  a  value  into  the
        register  at  the  octal address 176500 in the I/O page.
        The program is stopped if the error condition returns.

                     IERR = IBISIO ( "176500,"100 )
                     IF ( IERR .EQ. 0 ) STOP       
                         .                         
                         .                         


    ICKWTS

             This routine is used to determine if any other user
        has written to a shared file.  The calling sequences are
        as follows:


        TSX-Plus Library                                 PAGE 18
        Routine Descriptions


                    CALL ICKWTS ( ICHAN [ ,IERR ] )
                                   or
                        IERR = ICKWTS ( ICHAN )

        where:  ICHAN   is the I/O channel open  to  the  shared
                        file.

                IERR    is one of the following:

                        0  no writes have been performed.

                        2  writes have been performed.

             This routine can be used to advantage in  a  situa-
        tion  where  data  from  some block in the file is being
        held in a buffer and it is desired to determine  if  the
        data is valid or if it may be invalid because some other
        user might have altered it by writing to the file.

             The following example opens a  file,  declares  the
        file  to  be  shared  and  then checks for writes to the
        shared file.  If writes have been performed to the  file
        the program is halted.

                   CALL ASSIGN ( 33,'RK3:THIS.DAT' )
                   ICHAN = ( 33 )                   
                   CALL IDCLSF ( ICHAN,5 )          
                       .                            
                       .                            
                   IERR = ICKWTS ( ICHAN )          
                   IF ( IERR .EQ. 2 ) STOP          
                       .                            
                       .                            


    ICNINT

             This  routine  is  used  to  connect  a  completion
        routine  to  an interrupt vector.  The calling sequences
        are as follows:

               CALL ICNINT ( IVEC,CPLRTN,IPRI [ ,IERR ] )
                                   or
                   IERR = ICNINT ( IVEC,CPLRTN,IPRI )

        where:  IVEC    is the interrupt vector address.

                CPLRTN  is the six ASCII character name  of  the
                        completion routine.

                IPRI    is  the  priority  for  the   completion
                        routine in the range of zero to seven.

                IERR    is negative or one of the following:



        TSX-Plus Library                                 PAGE 19
        Routine Descriptions


                        0  real time support is not available or
                           this   job  does  not  have  operator
                           privilege.

                        1  the maximum number of interrupts  are
                           already in use.

                        2  some other job is  already  connected
                           to this interrupt vector.

             The vector  remains  connected  to  the  completion
        routine  until  the  program  terminates  or  until  the
        routine, IRLINT, is executed.

             The  following  example  declares  the   completion
        routine  as an external and connects an interrupt vector
        to the completion routine.  The program is halted if  an
        error condition is returned.

                    EXTERNAL CPLRTN                 
                    IERR = ICNINT ( "320,CPLRTN,3 ) 
                    IF ( IERR .GE. 0 ) STOP         
                        .                           
                        .                           


    IDCLSF

             This routine is used to declare an open file to  be
        shared.  The calling sequences are as follows:

                 CALL IDCLSF ( ICHAN,IACES [ ,IERR ] )
                                   or
                     IERR = IDCLSF ( ICHAN,IACES )

        where:  ICHAN   is the I/O channel number  open  to  the
                        shared file.

                IACES   is     one     of     the      following
                        protection/access codes:

                        0  exclusive/input.

                        1  exclusive/update.

                        2  protected/input.

                        3  protected/update.

                        4  shared/input.

                        5  shared/update.

                IERR    is one of the following:



        TSX-Plus Library                                 PAGE 20
        Routine Descriptions


                        0  no error.

                        1  the I/O channel has not  been  opened
                           to a file.

                        2  attempted to open too  many  channels
                           to shared files.

                        3  attempted to  open  too  many  shared
                           files.

                        4  a file protection/access conflict ex-
                           ists.

             The protection/access code  specifies  two  things,
        the  type  of  protection (exclusive, protected, shared)
        that you are claiming on your use of the  file  and  the
        type of access (input or update) that you intend to make
        to the file.  Exclusive protection means  that  you  re-
        quire  exclusive  access  to  the file and will allow no
        other  users  to  access  the  file  in   any   fashion.
        Protected  protection  means  that  you will allow other
        users to open the file for input but  wish  to  prohibit
        any from opening the file for update.  Shared protection
        means that you are willing to allow other users to  open
        the file for both input and update.

             The following example opens a  file  and  then  de-
        clares  exclusive/update protection/access.  If an error
        condition is returned the program aborts.

                    CALL ASSIGN ( 40,'DK:FILE.DAT' )
                    ICHAN = ILUN ( 40 )             
                    IERR = IDCLSF ( ICHAN,2 )       
                    IF ( IERR .NE. 0 ) STOP         
                        .                           
                        .                           


    INITPA

             This routine is used to set up parameters that will
        control  a  performance  analysis.  It does not actually
        begin the analysis.  The calling sequences are  as  fol-
        lows:

          CALL INITPA ( IBSADR,ITPADR,ICLSZ,IFLAG [ ,IERR ] )
                                   or
              IERR = INITPA ( IBSADR,ITPADR,ICLSZ,IFLAG )

        where:  IBSADR  is the base address of the region to  be
                        monitored.

                ITPADR  is the top address of the region  to  be
                        monitored.


        TSX-Plus Library                                 PAGE 21
        Routine Descriptions


                ICLSZ   is the number of  bytes  to  group  into
                        each histogram cell.

                IFLAG   is one of the following:

                        0  do not include I/O wait time.

                        1  include I/O wait time.

                IERR    is negative or one of the following:

                        0  performance analysis  is  already  in
                           use.

                        1  performance analysis feature  is  not
                           included in this version of TSX-Plus.

             The following example initializes for a performance
        analysis.   The  program aborts if an error condition is
        returned.

                  IERR = INITPA ( "2000,"5400,"100,0 )
                  IF ( IERR .GE. 0 ) STOP             
                      .                               
                      .                               


    IPEKIO

             This routine is used to access or peek at a word in
        the I/O page without requiring the job's virtual address
        region to be mapped to the I/O page.   The  calling  se-
        quence is as follows:

                  CALL IPEKIO ( IADR,IRET [ ,IERR ] )

        where:  IADR    is the address of the word  in  the  I/O
                        page that is to be accessed.

                IRET    is the value returned from the I/O page.

                IERR    is negative or the following:

                        0  real time support is not available or
                           this   job  does  not  have  operator
                           privilege.

             The following example obtains the  value  from  the
        register  at  octal address 176502 in the I/O page.  The
        program is aborted if the error condition is returned.

                   CALL IPEKIO ( "176502,IRET,IERR )
                   IF ( IERR .EQ. 0 ) STOP          
                       .                            
                       .                            


        TSX-Plus Library                                 PAGE 22
        Routine Descriptions


    IPOKIO

             This routine is used to deliver a value into a word
        in  the I/O page without requiring the job's virtual ad-
        dress region to be mapped to the I/O page.  The  calling
        sequences are as follows:

                  CALL IPOKIO ( IADR,IVAL [ ,IERR ] )
                                   or
                      IERR = IPOKIO ( IADR,IVAL )

        where:  IADR    is the address of the word  in  the  I/O
                        page to be accessed.

                IVAL    is the value to be deposited in the  I/O
                        page.

                IERR    is negative or the following:

                        0  real time support is not available or
                           this   job  does  not  have  operator
                           privilege.

             The  following  example  pokes  a  value  into  the
        register  at  octal address 176506 in the I/O page.  The
        program stops if the error condition is returned.

                     IERR = IPOKIO ( "176506,"101 )
                     IF ( IERR .EQ. 0 ) STOP       
                         .                         
                         .                         


    IRLINT

             This routine releases the connection of  an  inter-
        rupt  vector  and  a completion routine.  The connection
        must have been made by previously executing the routine,
        ICNINT.  The calling sequences are as follows:

                      CALL IRLINT ( IVEC [ ,IERR ]
                                   or
                         IERR = IRLINT ( IVEC )

        where:  IVEC    is the interrupt vector address.

                IERR    is negative or the following:

                        0  real time support is not available or
                           this   job  does  not  have  operator
                           privilege.

             The following example first declares the completion
        routine  as  an  external, then connects it to a vector,
        and finally breaks the connection.


        TSX-Plus Library                                 PAGE 23
        Routine Descriptions


                    EXTERNAL CPLRTN                 
                    CALL ICNINT ( "320,CPLRTN,0 )   
                        .                           
                        .                           
                    CALL IRLINT ( "320 )            
                        .                           
                        .                           


    ISPBLK

             This routine is used to  determine  the  number  of
        free  blocks  in  the spool file.  The calling sequences
        are as follows:

                          CALL ISPBLK ( IRET )
                                   or
                            IRET = ISPBLK ()

        where:  IRET    is the number  of  free  blocks  in  the
                        spool file.


    ISPPA

             This routine is used to suspend the  collection  of
        data  for  a  performance analysis.  The data collection
        can be restarted by using the  ISTPA  routine  described
        later.  The calling sequences are as follows:

                          CALL ISPPA [ IERR ]
                                   or
                            IERR = ISPPA ()

        where:  IERR    is negative or the following:

                        0  performance  analysis  has  not  been
                           previously initialized.

             The following example initializes for a performance
        analysis,  then  starts and stops the collection of data
        for the analysis within a loop.

                      CALL INITPA ( "2000,"5400,"100,0 )
                      DO 10 I = 1,53                    
                          CALL ISTPA                    
                              .                         
                              .                         
                          CALL ISPPA                    
                              .                         
                              .                         
                10    CONTINUE                          
                              .                         
                              .                         


        TSX-Plus Library                                 PAGE 24
        Routine Descriptions


    ISPY

             This is a SYSLIB routine that is used to return the
        value  located  at  a specific offset into the simulated
        RMON.   TXS-Plus  has  extended  it  to  return  several
        TSX-Plus  values.   Refer  to  the  "RT-11  Programmer's
        Reference Manual" [5] for information on getting  values
        from within the simulated RMON.  The calling sequence is
        as follows:

                         IRET = ISPY ( IOFFST )

        where:  IRET    is the integer value returned.

                IOFFST  is the offset into the simulated RMON or
                        to return a TSX-Plus value is one of the
                        following:

                        -2  job number.

                        -4  lead-in character used for  terminal
                            controlled options.

                        -6  zero if job is nonprivileged or  one
                            if privileged.

                        -8  zero if PAR 7 is mapped to the simu-
                            lated RMON or one if PAR 7 is mapped
                            to the I/O page.

                        -10 project  number  job  is  logged  on
                            under.

                        -12 programmer number job is  logged  on
                            under.

             The following example aborts  if  the  job  is  not
        privileged.

                        IRET = ISPY ( -6 )     
                        IF ( IRET .EQ. 0 ) STOP
                            .                  
                            .                  


    ISTDJ

             This routine is used to check the status of  a  de-
        tached job.  The calling sequences are as follows:

                      CALL ISTDJ ( JOBNUM,ISTAT )
                                   or
                        ISTAT = ISTDJ ( JOBNUM )

        where:  JOBNUM  is the job number of the detached job.


        TSX-Plus Library                                 PAGE 25
        Routine Descriptions


                ISTAT   is one of the following:

                        0  the job is not active.

                        1  the job is active.

             The following example starts a  detached  job  then
        checks  the  detached job's status until the job becomes
        inactive.

                        CALL STDTJB ( JOBNAM, JOBNUM )
                  10    CONTINUE                      
                        ISTAT = ISTDJ ( JOBNUM )      
                        IF ( ISTAT .NE. 1 ) GO TO 10  
                            .                         
                            .                         


    ISTPA

             This routine is used to begin the actual collection
        of  performance  analysis data.  The INITPA routine must
        have been executed to set up parameters about  the  per-
        formance  analysis  before  this routine is called.  The
        calling sequences are as follows:

                          CALL ISTPA [ IERR ]
                                   or
                            IERR = ISTPA ()

        where:  IERR    is negative or the following:

                        0  performance  analysis  has  not  been
                           initialized.

             The following example initializes for and starts  a
        performance  analysis.   The  program  is  halted if the
        error condition is returned from the call to ISTPA.

                   CALL INITPA ( "2000,"5400,"100,0 )
                   IERR = ISTPA ()                   
                   IF ( IERR .EQ. 0 ) STOP           
                       .                             
                       .                             


    ISVST

             This routine is used to save the status of a shared
        file.  The effect of this routine is to suspend the con-
        nection between the shared file table and the I/O  chan-
        nel.   Any  blocks that are currently locked in the file
        remain locked until the channel is reopened to the  file
        by  using the SYSLIB routine, IREOPN.  After return from
        this routine the channel may be freed by using the  SYS-


        TSX-Plus Library                                 PAGE 26
        Routine Descriptions


        LIB routine, PURGE.  The calling sequence is as follows:

                          CALL ISVST ( ICHAN )

        where:  ICHAN   is the I/O channel number  open  to  the
                        shared file.

             When using a single channel number to access sever-
        al  shared  files it is for each file convenient to ini-
        tially open the file, declare the file to be shared  and
        to  save the status of the file with the SYSLIB routine,
        ISAVES.  The channel being used to  access  the  set  of
        files can then be switched from one file to another with
        the SYSLIB routines, PURGE and IREOPN.  However,  before
        doing  the PURGE, TSX-Plus must be told that you wish to
        save the shared file status of the file  (otherwise  all
        locked  blocks will be unlocked and the file will be re-
        moved from the shared file list).

             The following example opens a file, declares it  to
        be  shared  and  then  saves  the status of the file for
        TSX-Plus.

                    CALL ASSIGN ( 30,'DK:SOME.FIL' )
                    ICHAN = ( 30 )                  
                    CALL IDCLSF ( ICHAN,4 )         
                        .                           
                        .                           
                    CALL ISVST ( ICHAN )            
                        .                           
                        .                           


    ITRERR

             This routine is used to determine if  any  terminal
        input  errors  have occurred.  The calling sequences are
        as follows:

                          CALL ITRERR ( IERR )
                                   or
                            IERR = ITRERR ()

        where:  IERR    is one of the following:

                        0  no errors have occurred.

                        1  an input error has occurred.

             The following example checks for terminal input er-
        rors and aborts the program if one has occurred.

                            .                  
                            .                  
                        IERR = ITRERR ()       


        TSX-Plus Library                                 PAGE 27
        Routine Descriptions


                        IF ( IERR .NE. 0 ) STOP
                            .                  
                            .                  


    ITRTYP

             This routine is used to determine the terminal type
        being  used  on  the time sharing line.  The calling se-
        quences are as follows:

                          CALL ITRTYP ( IRET )
                                   or
                            IRET = ITRTYP ()

        where:  IRET    is one of the following:

                        0  terminal type unknown.

                        1  VT52.

                        2  VT100.

                        3  Hazeltine.

                        4  ADM3A.

                        5  LA36.

                        6  LA120.

                        7  Diablo.

                        8  Qume.


    ITSLIC

             This routine is used to determine the TSX-Plus  li-
        cense number.  The calling sequences are as follows:

                          CALL ITSLIC ( IRET )
                                   or
                            IRET = ITSLIC ()

        where:  IRET    is  the   requested   TSX-Plus   license
                        number.


    ITSLIN

             This routine is used to determine the TSX-Plus time
        sharing  line  number to which the job is attached.  The
        calling sequences are as follows:


        TSX-Plus Library                                 PAGE 28
        Routine Descriptions


                          CALL ITSLIN ( IRET )
                                   or
                            IRET = ITSLIN ()

        where:  IRET    is zero if RT-11 is running or  the  re-
                        quested  line number if TSX-Plus is run-
                        ning.

             The following example aborts if RT-11 is running or
        continues if TSX-Plus is running.

                        IRET = ITSLIN ()       
                        IF ( IRET .EQ. 0 ) STOP
                            .                  
                            .                  


    IUALBK

             This routine is used to unlock all locked blocks in
        a shared file.  The calling sequences are as follows:

                    CALL IUALBK ( ICHAN [ ,IERR ] )
                                   or
                        IERR = IUALBK ( ICHAN )

        where:  ICHAN   is the I/O channel number that  is  open
                        to a shared file.

                IERR    is one of the following:

                        0  no error.

                        1  this channel is not open to a  shared
                           file.

             When this routine is executed all blocks previously
        locked  by  the  user  on  the shared file are unlocked.
        Blocks locked by the user on other  files  are  not  re-
        leased  nor  are blocks of the same file that are locked
        by other users.

             The following example first opens a file,  declares
        it to be shared, locks some blocks, and then unlocks the
        blocks.  The program is stopped if the  error  condition
        is returned.

                       CALL ASSIGN ( 40,'DK:FILE.DAT' )
                       ICHAN = ILUN ( 40 )             
                       CALL IDCLSF ( ICHAN,1 )         
                       DO 10 IBLK = 4,6                
                           CALL LKBLKW ( ICHAN,IBLK )  
                 10    CONTINUE                        
                           .                           
                           .                           


        TSX-Plus Library                                 PAGE 29
        Routine Descriptions


                       IERR = IUALBK ( ICHAN )         
                       IF ( IERR .NE. 0 ) STOP         
                           .                           
                           .                           


    IUNLKM

             This routine is used to unlock a job  from  memory.
        The calling sequences are as follows:

                          CALL IUNLKM [ IERR ]
                                   or
                            IERR = IUNLKM ()

        where:  IERR    is negative or as follows:

                        0  real time support is not available or
                           this   job  does  not  have  operator
                           privilege.

             The following example first locks itself into memo-
        ry and then unlocks itself.

                              CALL LKANMY
                                  .      
                                  .      
                              CALL IUNLKM
                                  .      
                                  .      


    IUSPBK

             This routine is used to unlock  a  specific  locked
        block  in  a  shared file.  The calling sequences are as
        follows:

                 CALL IUSPBK ( ICHAN,IBLOCK [ ,IERR ] )
                                   or
                     IERR = IUSPBK ( ICHAN,IBLOCK )

        where:  ICHAN   is the I/O channel number that  is  open
                        to the shared file.

                IBLOCK  is the number of the  block  to  be  un-
                        locked.

                IERR    is one of the following:

                        0  no error.

                        1  the channel is not open to  a  shared
                           file.



        TSX-Plus Library                                 PAGE 30
        Routine Descriptions


             The following example opens a  file,  declares  the
        file to be shared, locks all blocks in the file and then
        unlocks a specific block in the file.   The  program  is
        stopped if an error condition is returned.

                   CALL ASSIGN ( 30,'DL0:THAT.DAT' )
                   ICHAN = ( 30 )                   
                   CALL IDCLSF ( ICHAN,2 )          
                   CALL LKBLKW ( ICHAN,-1 )         
                   IERR = IUSPBK ( ICHAN,7 )        
                   IF ( IERR .NE. 0 ) STOP          
                       .                            
                       .                            


    KLDTJB

             This routine is used to abort a detached job.   The
        calling sequences are as follows:

                    CALL KLDTJB ( JOBNUM [ ,IERR ] )
                                   or
                        IERR = KLDTJB ( JOBNUM )

        where:  JOBNUM  is the job number of the detached job.

                IERR    is one of the following:

                        0  no error.

                        1  invalid job number.

             The following example first starts a  detached  job
        and then later kills the detached job.  If an error con-
        dition is returned the program is halted.

                     CALL STDTJB ( JOBNAM,JOBNUM )
                         .                        
                         .                        
                     CALL KLDTJB ( JOBNUM,IERR )  
                     IF ( IERR .EQ. 1 ) STOP      
                         .                        
                         .                        


    LKANMY

             This routine is used to lock a job into any memory.
        It causes the job to become locked into the memory space
        it is occupying when this  routine  is  executed.   This
        routine  executes  extremely  fast  as  compared  to the
        routine, LKLOMY, described later.  The calling sequences
        are as follows:


        TSX-Plus Library                                 PAGE 31
        Routine Descriptions


                          CALL LKANMY [ IERR ]
                                   or
                            IERR = LKANMY ()

        where:  IERR    is negative or the following:

                        0  real time support is not available or
                           this   job  does  not  have  operator
                           privilege.

             The job remains locked until the program  exits  or
        the routine, IUNLKM, is executed.

             The following example locks the job into the memory
        space  that  it  currently occupies.  The program termi-
        nates if the error condition is returned.

                        IERR = LKANMY ()       
                        IF ( IERR .EQ. 0 ) STOP
                            .                  
                            .                  


    LKBLK

             This routine is used to  try  to  lock  a  specific
        block  in  a shared file.  If the requested block is not
        available the routine returns immediately with an  error
        code.   If  the  block is available it is locked for the
        requesting user and no error is reported.   The  calling
        sequences are as follows:

                 CALL LKBLK ( ICHAN,IBLOCK [ ,IERR ] )
                                   or
                        IERR = ( ICHAN,IBLOCK )

        where:  ICHAN   is the I/O channel number  open  to  the
                        shared file.

                IBLOCK  is the number of the block to be locked.

                IERR    is one of the following:

                        0  no error.

                        1  this channel is not open to a  shared
                           file.

                        2  request is to lock too many blocks in
                           the file.

                        3  the  requested  block  is  locked  by
                           another user.

             The following example opens a  file,  declares  the


        TSX-Plus Library                                 PAGE 32
        Routine Descriptions


        file to be shared and tries to lock a block in the file.
        If the block is already locked the  program  loops  back
        for  another  try  and if an error condition is returned
        the program halts.

                      CALL ASSIGN ( 40,'DY1:JUNK.DAT' )
                      ICHAN = ( 40 )                   
                      CALL IDCLSF ( ICHAN,2 )          
                10    CONTINUE                         
                      IERR = LKBLK ( ICHAN,3 )         
                      IF ( IERR .EQ. 3 ) GO TO 10      
                      IF ( IERR .NE. 0 ) STOP          
                          .                            
                          .                            


    LKBLKW

             This routine is used to wait for a  specific  block
        to  lock  in  a  shared file.  If the requested block is
        locked by  another  job,  the  requesting  job  will  be
        suspended  until  the  desired  block becomes available.
        The calling sequences are as follows:

                 CALL LKBLKW ( ICHAN,IBLOCK [ ,IERR ] )
                                   or
                     IERR = LKBLKW ( ICHAN,IBLOCK )

        where:  ICHAN   is the I/O channel number  open  to  the
                        shared file.

                IBLOCK  is the number of the block to be locked.

                IERR    is one of the following:

                        0  no error.

                        1  this channel is not open to a  shared
                           file.

                        2  request is to lock too many blocks in
                           the file.

             Other blocks in  the  file  which  were  previously
        locked  remain  locked.  A block number of minus one can
        be used to request  that  all  blocks  in  the  file  be
        locked.  If several users request the same block, access
        will be granted sequentially in the order that  the  re-
        quests are received.

             The following example opens a  file,  declares  the
        file  to  be  shared, and locks all of the blocks in the
        file.  If an error condition  is  returned  the  program
        stops.



        TSX-Plus Library                                 PAGE 33
        Routine Descriptions


                    CALL ASSIGN ( 40,'DK:FILE.DAT' )
                    ICHAN = ( 40 )                  
                    CALL IDCLSF = ( ICHAN,0 )       
                    IERR = LKBLKW ( ICHAN,-1 )      
                    IF ( IERR .NE. 0 ) STOP         
                        .                           
                        .                           


    LKLOMY

             This routine is used to lock a job into low memory.
        It  causes  the  job to be relocated into low memory and
        then to become locked there.  This type of lock is rela-
        tively slow and should be done only if the job is to re-
        main locked for a long period of time.  The calling  se-
        quences are as follows:

                          CALL LKLOMY [ IERR ]
                                   or
                            IERR = LKLOMY ()

        where:  IERR    is negative or the following:

                        0  real time support is not available or
                           this   job  does  not  have  operator
                           privilege.

             The job remains locked in memory until the  program
        terminates or until the routine, IUNLKM, is executed.

             The following example locks the job into low memory
        aborting if the error condition is returned.

                        IERR = LKLOMY ()        
                        IF ( IERR .EQ. 0 ) STOP 
                            .                   
                            .                   


    MAPRNT

             This routine is used to map a  shareable  run  time
        system  into  a  job's region.  The run time system must
        first be associated with the job by executing the IASRNT
        routine described earlier.  The calling sequences are as
        follows:

              CALL MAPRNT ( IPAR,IOFFST,MAPSIZ [ ,IERR ] )
                                   or
                  IERR = MAPRNT ( IPAR,IOFFST,MAPSIZ )

        where:  IPAR    is a number in  the  range  of  zero  to
                        seven  that indicates the job's page ad-
                        dress register (PAR) that is to be  used


        TSX-Plus Library                                 PAGE 34
        Routine Descriptions


                        to  access the run time system.  The PAR
                        number selects  the  region  of  virtual
                        memory in the job that will be mapped to
                        the run time system.  The following cor-
                        respondence  exists  between PAR numbers
                        and virtual octal address regions within
                        the job:

                        0  000000 - 017777
                        1  020000 - 037777
                        2  040000 - 057777
                        3  060000 - 077777
                        4  100000 - 117777
                        5  120000 - 137777
                        6  140000 - 157777
                        7  160000 - 177777

                IOFFST  specifies which portion of the run  time
                        system  is to be mapped into the PAR re-
                        gion.  It specifies the  number  of  the
                        64-byte block within the run time system
                        where mapping is to begin.   This  makes
                        it possible to access different sections
                        of a run time system at different  times
                        or through different regions.

                MAPSIZ  is the number of 64-byte  blocks  to  be
                        mapped.   If  this  value is larger than
                        can be contained within a single PAR re-
                        gion, multiple PAR regions are automati-
                        cally mapped as necessary to contain the
                        entire specified section of the run time
                        system.

                IERR    is one of the following:

                        0  no error.

                        1  there is no run time system associat-
                           ed with this job.

             This routine affects the mapping of  only  the  PAR
        region  specified in IPAR and following PARs if the size
        so requires.  It does not  affect  the  mapping  of  any
        other  PAR  regions that may previously have been mapped
        to a run time system.  Thus a job may have different PAR
        regions  mapped  to  different  sections of the same run
        time system or to different run time systems.  Real time
        programs may map PAR region number seven to the I/O page
        and map other PAR regions to shared run time systems.

             The memory size of a job is not affected by the use
        of  the this routine.  Mapping a portion of a job's vir-
        tual address space to a shared run time  system  neither
        increases  nor  decreases the size of memory occupied by


        TSX-Plus Library                                 PAGE 35
        Routine Descriptions


        the job.  If a job's size is such that a portion of  its
        normal  memory is under a PAR region that is mapped to a
        run time system, that section of its normal  memory  be-
        comes  inaccessible  to  the job as long as the run time
        system mapping is in effect but the memory contents  are
        not lost and may be reaccessed by disassociating all run
        time systems from the job.

             Any of the PAR regions may be mapped to a run  time
        system  including  PAR region number seven which is nor-
        mally not accessible to a job.

             The  following  example  first  uses   the   SYSLIB
        routine, IRAD50, to name the run time system, associates
        the run time system with the job, then maps a PAR region
        to  a section of the run time system, and finally disas-
        sociates the run time system from the job.

                   DIMENSION IRNTIM ( 2 )           
                   CALL IRAD50 ( 6,'TSXLIB',IRNTIM )
                   CALL IASRNT ( IRNTIM )           
                   CALL MAPRNT ( 3,1,4 )            
                       .                            
                       .                            
                   CALL IASRNT ( 0 )                
                       .                            
                       .                            


    MEMSET

             This routine is used to set the  amount  of  memory
        that  will  be  allocated  for the job.  The calling se-
        quences are as follows:

                     CALL MEMSET ( IARG [ ,IRET ] )
                                   or
                         IRET = MEMSET ( IARG )

        where:  IARG    is the top memory address requested.

                IRET    is the top memory address allocated.

             The size allocated to a job  reverts  to  the  size
        specified  by  the  most  recent MEMORY keyboard command
        when the job exits or chains.

             The following example requests a top memory address
        of 120000 (octal).  The program is halted if the alloca-
        tion is less than the request.

                       DATA IARG/"120000/        
                       IRET = MEMSET ( IARG )    
                       IF ( IRET .LT. IARG ) STOP
                           .                     


        TSX-Plus Library                                 PAGE 36
        Routine Descriptions


                           .                     


    MOUNT

             This routine is used to  mount  a  file  structured
        device  for  directory  caching.   The  effect  of  this
        routine is the same as the TSX-Plus MOUNT keyboard  com-
        mand.  The calling sequences are as follows:

                    CALL MOUNT ( IDVNAM [ ,IERR ] )
                                   or
                        IERR = MOUNT ( IDVNAM )

        where:  IDVNAM  is the RAD50 value of the device name.

                IERR    is one of the following:

                        0  no error.

                        1  no room left in the table of  mounted
                           devices.

             The following  example  uses  the  SYSLIB  routine,
        IRAD50,  to  convert  the ASCII device name, DY3, to its
        RAD50 value.  Then the file structured device is  mount-
        ed.   The program is halted if an error condition is re-
        turned.

                     CALL IRAD50 ( 3,'DY3',IDVNAM )
                     IERR = MOUNT ( IDVNAM )       
                     IF ( IERR .EQ. 1 ) STOP       
                         .                         
                         .                         


    MPIOPS

             This routine is used to map the I/O page  into  the
        program  space between the octal addresses of 160000 and
        177777.  The calling sequence is as follows:

                              CALL MPIOPS

             The mapping set up by this routine remains  in  ef-
        fect  until the routine, MPRMPS, is executed or the pro-
        gram terminates.  Operator privilege is required to exe-
        cute this routine.


    MPRMPS

             This routine is used to map a simulated  RMON  into
        the  program space between the octal addresses of 160000
        and 177777.  The calling sequence is as follows:


        TSX-Plus Library                                 PAGE 37
        Routine Descriptions


                              CALL MPRMPS

             Operator privilege  is  required  to  execute  this
        routine.


    MSGSND

             This routine is used  to  queue  up  a  message  to
        another  job  on a named channel.  If other messages are
        already pending on the channel, the new message is added
        to the end of the list of waiting messages.  The sending
        program continues execution and does not  wait  for  the
        message  to  be accepted by a receiving program.  During
        processing the message is copied to an internal  buffer,
        and  the  sending program is free to destroy its message
        on return from this routine.  The calling sequences  are
        as follows:

             CALL MSGSND ( ICHNAM,MSGBUF,MSGSIZ [ ,IERR ] )
                                   or
                 IERR = MSGSND ( ICHNAM,MSGBUF,MSGSIZ )

        where:  ICHNAM  is the six ASCII character name  of  the
                        message channel.

                MSGBUF  is the name of the string array contain-
                        ing the message.

                MSGSIZ  is  the  length  of   the   message   in
                        characters.

                IERR    is one of the following:

                        0  no error.

                        1  all message channels are busy.

                        2  the maximum allowed  number  of  mes-
                           sages  are  being held in the message
                           queues.

                        4  the transmitted message was too  long
                           and  was truncated to the maximum al-
                           lowed length.

             The following  example  uses  the  SYSLIB  routine,
        SCOPY,  to load the string variables, MSGBUF and ICHNAM,
        then sends a message to the named  channel,  JUNK.   The
        program aborts if an error condition is returned.

                LOGICAL*1 MSGBUF ( 14 )                
                LOGICAL*1 ICHNAM ( 8 )                 
                CALL SCOPY ( ' HELLO THERE',MSGBUF,12 )
                CALL SCOPY ( 'JUNK  ',ICHNAM,6 )       


        TSX-Plus Library                                 PAGE 38
        Routine Descriptions


                IERR = MSGSND ( ICHNAM,MSGBUF,12 )     
                IF ( IERR .NE. 0 ) STOP                
                    .                                  
                    .                                  


    RCVMSG

             This routine is used to receive a  message  from  a
        named  channel  if  a message is pending on the channel.
        If no message is pending, an error code is returned, and
        the  calling  program  is allowed to continue execution.
        The calling sequence is as follows:

         CALL RCVMSG ( ICHNAM,MSGBUF,IBUFSZ,MSGSIZ [ ,IERR ] )

        where:  ICHNAM  is the six ASCII character name  of  the
                        message channel.

                MSGBUF  is the  name  of  the  receiving  string
                        array.

                IBUFSZ  is the length of the receiving buffer in
                        characters.

                MSGSIZ  is the length of the received message in
                        characters.

                IERR    is one of the following:

                        0  no error.  A message was received.

                        3  no message was queued  on  the  named
                           channel.

                        4  the message was longer than  the  re-
                           ceiving buffer.

             The following example  sets  up  using  the  SYSLIB
        routine,  SCOPY, to receive a message, and then attempts
        to receive a message on the named  channel,  JUNK.   The
        program is stopped if an error condition is returned.

              LOGICAL*1 ICHNAM ( 8 )                     
              LOGICAL*1 MSGBUF ( 72 )                    
              CALL SCOPY ( 'JUNK  ',ICHNAM,6)            
              CALL RCVMSG ( ICHNAM,MSGBUF,72,MSGSIZ,IERR)
              IF ( IERR .NE. 0 ) STOP                    
                  .                                      
                  .                                      


        TSX-Plus Library                                 PAGE 39
        Routine Descriptions


    RCVMSW

             This routine is used to suspend the execution of  a
        program  until  a  message  becomes available on a named
        channel.  The calling sequence is as follows:

         CALL RCVMSW ( ICHNAM,MSGBUF,IBUFSZ,MSGSIZ [ ,IERR ] )

        where:  ICHNAM  is the six ASCII character name  of  the
                        message channel.

                MSGBUF  is the  name  of  the  receiving  string
                        array.

                IBUFSZ  is the length of the receiving array  in
                        characters.

                MSGSIZ  is the length of the received message in
                        characters.

                IERR    is one of the following:

                        0  a message has been received.

                        1  all message channels are busy.

                        4  the message was longer than  the  re-
                           ceiving buffer.

             The following  example  uses  the  SYSLIB  routine,
        SCOPY,  to  load  the variable, ICHNAM, then waits for a
        message to arrive on the named channel.  The program  is
        stopped if an error condition is returned.

            LOGICAL*1 MSGBUF ( 72 )                        
            LOGICAL*1 ICHNAM ( 8 )                         
            CALL SCOPY ( 'JUNK  ',ICHNAM,6 )               
            CALL RCVMSW ( ICHNAM,MSGBUF,IBUFSZ,MSGSIZ,IERR)
            IF ( IERR .NE. 0 ) STOP                        
                .                                          
                .                                          


    RSTODT

             This routine is used to reset or clear the ODT  ac-
        tivation mode.  The calling sequence is as follows:

                              CALL RSTODT


    SETODT

             This routine is used  to  set  the  ODT  activation
        mode.  The calling sequence is as follows:


        TSX-Plus Library                                 PAGE 40
        Routine Descriptions


                              CALL SETODT

             In this mode TSX-Plus considers all  characters  to
        be  activation  characters except the digits, the comma,
        the dollar sign and the semicolon.


    STDTJB

             This routine is used to start the  execution  of  a
        detached job.  The calling sequence is as follows:

                CALL STDTJB ( JOBNAM,JOBNUM [ ,IERR ] )

        where:  JOBNAM  is  the  ASCII  string,  dev:filnam.ext,
                        terminated by a null byte.

                JOBNUM  is the returned job number.

                IERR    is one of the following:

                        0  no error.

                        1  no detached job line is available.

             If a free detached job line is available, the spec-
        ified  command  file, JOBNAM, is initiated as a detached
        job and the number of the detached job  is  returned  in
        the variable, JOBNUM.

             The following  example  uses  the  SYSLIB  routine,
        SCOPY,  to load the variable, JOBNAM, then initiates the
        detached job, DETJOB.COM, from device, DY2:, storing the
        job number in the variable, JOBNUM.  The program is ter-
        minated if an error condition is returned.

                LOGICAL*1 JOBNAM ( 16 )                 
                CALL SCOPY ( 'DY2:DETJOB.COM',JOBNAM,14)
                CALL STDTJB ( JOBNAM,JOBNUM,IERR )      
                IF ( IERR .EQ. 1 ) STOP                 
                    .                                   
                    .                                   


    TERMPA

             This routine is used to conclude a performance  an-
        alysis.  It has the effect of returning into a user sup-
        plied buffer the results of the analysis and freeing the
        performance  analysis  feature  for  use by other users.
        The calling sequence is as follows:

             CALL TERMPS ( IPARBF,IHSTBF,IHBSIZ [ ,IERR ] )

        where:  IPARBF  is the name of a four element  parameter


        TSX-Plus Library                                 PAGE 41
        Routine Descriptions


                        buffer  with  the  elements  assigned as
                        follows:

                        1  is the base address of the  monitored
                           region.

                        2  is the top address of  the  monitored
                           region.

                        3  is the number of bytes per  histogram
                           cell.

                        4  is a control and status flag with bit
                           assignments as follows:

                           1       I/O wait time was included.

                           100000  at least one of the histogram
                                   cells overflowed.

                IHSTBF  is the name of the histogram buffer.

                IHBSIZ  is the number of elements  or  cells  in
                        the histogram buffer.

                IERR    is negative or one of the following:

                        0  this job is not doing  a  performance
                           analysis.

                        1  area provided for the histogram count
                           vector is too small.

             The histogram data returned consists of a vector of
        16-bit  binary  values,  one  value for each cell in the
        histogram.  The first value corresponds to the histogram
        cell  that starts at the base address of the region that
        was monitored.

             The following example shows  the  complete  perfor-
        mance  analysis from initialization to termination.  The
        program is stopped if an error condition is returned  on
        termination of the analysis.

               DIMENSION IPARBF ( 4 )                   
               DIMENSION IHSTBF ( 16 )                  
               CALL INITPA ( "2000,"4000,"100,0 )       
               CALL ISTPA                               
                   .                                    
                   .                                    
               CALL ISPPA                               
               CALL TERMPA ( IPARBF,IHSTBF,IHBSIZ,IERR )
               IF ( IERR .GE. 0 ) STOP                  
                   .                                    
                   .                                    


        TSX-Plus Library                                 PAGE 42
        Routine Descriptions


    TIMOUT

             This routine is used to set the time out value that
        is  to  be applied to the next terminal input operation.
        The calling sequence is as follows:

                      CALL TIMOUT ( ITIME,IACTCH )

        where:  ITIME   is the time  out  value  in  0.5  second
                        units.

                IACTCH  is the value  of  the  single  character
                        that  is  to  be returned as the last or
                        activation character of the field  if  a
                        time out occurs.

             The value specified with this routine applies  only
        to  the  next  terminal  input field.  The time value is
        reset when the next field is received from the  terminal
        or  the  time  out occurs.  A new time out value must be
        specified for each input field that is to be  time  con-
        trolled.

             The following example uses  a  time  out  value  of
        twenty  seconds  and specifies that a control-X is to be
        returned if the timeout occurs.

                             .                
                             .                
                         CALL TIMOUT ( 40,24 )
                             .                
                             .                


    TRMIN

             This  routine  is  used  to  accept  a  string   of
        characters  from  the terminal.  The calling sequence is
        as follows:

             CALL TRMIN ( ICHBUF,IBFSIZ,ICOUNT [ ,IERR ] )

        where:  ICHBUF  is the name of the buffer that is to re-
                        ceive the string.

                IBFSIZ  is the length of the receiving buffer in
                        characters.

                ICOUNT  is the number of characters actually re-
                        ceived.

                IERR    is one of the following:

                        0  no error.



        TSX-Plus Library                                 PAGE 43
        Routine Descriptions


                        1  the specified buffer overflowed.

             This routine causes a program to wait until an  ac-
        tivation  character  is entered on the terminal and then
        returns all characters received up to and including  the
        last activation character.  This routine is substancial-
        ly more efficient than doing  a  series  of  the  SYSLIB
        routine, ITTINR.  It is particularly well suited for ac-
        cepting input from page buffered terminals.

             The  following  example   accepts   a   string   of
        characters  from the terminal.  The program is halted if
        the error condition is returned.

                  LOGICAL*1 ICHBUF ( 24 )             
                  CALL TRMIN ( ICHBUF,24,ICOUNT,IERR )
                  IF ( IERR .EQ. 1 ) STOP             
                      .                               
                      .                               


    TRMMSG

             This routine is used to send a message  to  another
        line's terminal.  The calling sequence is as follows:

                      CALL TRMMSG ( ILINE,IMSGBF )

        where:  ILINE   is the line number of the terminal  that
                        the message is to be sent.

                IMSGBF  is the name of the buffer that  contains
                        the message.

             The  message  must  be  terminated  with   a   null
        character.

             The following example sends a message to the termi-
        nal connected to line 14.

            LOGICAL*1 IMSGBF ( 30 )                        
            CALL SCOPY ( ' THIS IS THE MESSAGE',IMSGBF,20 )
            CALL TRMMSG ( 14,IMSGBF )                      
                .                                          
                .                                          


    TRMOUT

             This routine is used to send a string of characters
        to the terminal.  The calling sequence is as follows:

                     CALL TRMOUT ( ICHSTR,ICOUNT )

        where:  ICHSTR  is the name of the buffer containing the


        TSX-Plus Library                                 PAGE 44
        Routine Descriptions


                        string of characters.

                ICOUNT  is  the  number  of  characters  in  the
                        string.

             This routine is much more efficient to use  than  a
        series  of  the SYSLIB routine, ITTOUR.  It has the same
        efficiency as the SYSLIB routine, PRINT, but it  uses  a
        count  of  the  number  of characters to send instead of
        having the string terminated with a null character.

             The following example sends a string of  characters
        to the terminal.

             LOGICAL*1 ICHSTR ( 22 )                       
             CALL SCOPY ( ' THIS IS THE STRING.'ICHSTR,20 )
             CALL TRMOUT ( ICHSTR,20 )                     
                 .                                         
                 .                                         


        TSX-Plus Library                                 PAGE 45
        Building the Library






                        4.  Building the Library


             The sources for the TSX-Plus Library consist of the
        eleven  MACRO-11  modules listed in Table 4-1.  The pro-
        cess of constructing the library  file,  TSXLIB.OBJ,  is
        the  same  when  accomplished  under  both RT-11 [4] and
        under TSX-Plus.


                Module  Content

                DETJBS  Detached job support.
                MNTDEV  Device mounting and dismounting.
                MSGCOM  Interjob message communication.
                PRFANL  Performance analysis support.
                RELTIM  Real time program support.
                RUNTIM  Shared run time system support.
                SHRFIL  Shared file system support.
                TRMCOM  Terminal communication.
                TRMCTL  Terminal control.
                TSXMSC  Miscellaneous EMTs.
                TSXODT  ODT activation mode support.

                    TSXLIB MACRO-11 source modules.
                               Table 4-1.


             First  the  MACRO-11  modules  are   assembled   as
        follows:

                             .RUN SY:MACRO 
                             *DETJBS=DETJBS
                             *MNTDEV=MNTDEV
                             *MSGCOM=MSGCOM
                             *PRFANL=PRFANL
                             *RELTIM=RELTIM
                             *RUNTIM=RUNTIM
                             *SHRFIL=SHRFIL
                             *TRMCOM=TRMCOM
                             *TRMCTL=TRMCTL
                             *TSXMSC=TSXMSC
                             *TSXODT=TSXODT
                             *^C           

             Next the library file is constructed as follows:


        TSX-Plus Library                                 PAGE 46
        Building the Library


                     .RUN SY:LIBR                  
                     *TSXLIB=DETJBS,MNTDEV,MSGCOM//
                     *PRFANL,RELTIM,RUNTIM,SHRFIL  
                     *TRMCOM,TRMCTL,TSXMSC,TSXODT  
                     *//                           
                     *^C                           

             The command file, TSXLIB.COM, in  Appendix  B  will
        accomplish   the   construction  of  the  library  file,
        TSXLIB.OBJ.  It will also delete the  several  temporary
        files.


        TSX-Plus Library                                 PAGE 47
        References






                               References


        1.  S & H Computer Systems,  Inc.,  "TSX-Plus  Reference
            Manual", Nashville, TN, December 1980.

        2.  S & H Computer Systems, Inc., "TSX-Plus version  2.0
            System Release Notes", Nashville, TN.

        3.  Digital  Equipment  Corporation,  "PDP-11   MACRO-11
            Language  Reference  Manual",  AA-5075B-TC, Maynard,
            MA, January 1980.

        4.  Digital Equipment Corporation, "RT-11 System  User's
            Guide", AA-5279B-TC, Maynard, MA, March 1980.

        5.  Digital Equipment Corporation,  "RT-11  Programmer's
            Reference  Manual",  AA-H378A-TC, Maynard, MA, March
            1980.


        TSX-Plus Library                                 PAGE 48
        Appendix A






                               Appendix A


             This appendix lists all of the TSXLIB  routines  in
        functional groups.


        Detached Job Support

                ISTDJ   Get the status of a detached job.

                KLDTJB  Kill a detached job.

                STDTJB  Start a detached job.


        Device Mounting and Dismounting

                DISMNT  Dismount a file structured device.

                MOUNT   Mount a file structured device.


        Interprogram Message Communication

                MSGSND  Send a message to another job.

                RCVMSG  Try to receive a  message  from  another
                        job.

                RCVMSW  Wait for a message from another job.


        Performance Analysis Support

                INITPA  Initialize for a performance analysis.

                ISPPA   Stop a performance analysis.

                ISTPA   Start a performance analysis.

                TERMPA  Terminate from a performance analysis.


        Real Time Program Support

                CNVAPA  Convert a virtual address to a  physical
                        address.

                IBICIO  Bit clear a value into the I/O page.



        TSX-Plus Library                                 PAGE 49
        Appendix A


                IBISIO  Bit set a value into the I/O page.

                ICNINT  Connect an interrupt vector to a comple-
                        tion routine.

                IPEKIO  Peek at a value in the I/O page.

                IPOKIO  Poke a value into the I/O page.

                IRLINT  Release an interrupt vector connection.

                IUNLKM  Unlock a job from memory.

                LKANMY  Lock a job into any memory.

                LKLOMY  Lock a job into low memory.

                MPIOPS  Map the I/O page into the program space.

                MPRMPS  Map the simulated RMON into the  program
                        space.


        Shared Run Time System Support

                IASRNT  Associate/disassociate a shared run time
                        system with a job.

                MAPRNT  Map a shared  run  time  system  into  a
                        job's region.


        Shared File Support

                ICKWTS  Check for writes to a shared file.

                IDCLSF  Declare a file to be shared.

                ISVST   Save the status of a shared file.

                IUALBK  Unlock all locked blocks.

                IUSPBK  Unlock a specific block.

                LKBLK   Try to lock a block.

                LKBLKW  Wait for a block to lock.


        Terminal Communications Support

                TRMIN   Accept a string of characters  from  the
                        terminal.

                TRMMSG  Send a message to another terminal.


        TSX-Plus Library                                 PAGE 50
        Appendix A


                TRMOUT  Send a string of characters to the  ter-
                        minal.


        Terminal Control Support

                BRKCTL  Establish break sentinal control.

                HIEFOF  Turn off the  high  efficiency  terminal
                        mode.

                HIEFON  Turn on  the  high  efficiency  terminal
                        mode.

                IACTCH  Check for pending activation characters.

                ITRERR  Check for terminal input errors.

                ITRTYP  Determine the terminal type.

                TIMOUT  Set the terminal read time out value.


        Miscellaneous EMT Support

                ISPBLK  Determine the number of free  blocks  in
                        the spool file.

                ISPY    Return  values  from  within   simulated
                        RMON.

                ITSLIC  Determine the TSX-Plus license number.

                ITSLIN  Determine the TSX-Plus line number.

                MEMSET  Set the memory allocation.


        ODT Activation Mode Support

                RSRODT  Reset normal activation mode.

                SETODT  Set ODT activation mode.


        TSX-Plus Library                                 PAGE 51
        Appendix B






                               Appendix B


             The  TSXLIB  distribution  kit  consists   of   the
        MACRO-11 source modules listed in Table 4-1 and the fol-
        lowing files:

                TSXLIB.COM  TSXLIB builder.

                TSXLIB.CRF  A cross reference chart.

                TSXLIB.DOC  This document.

                TSXLIB.OBJ  The implemented library.