Graphics on the Letterprinter 100
Using "LA100G"










                Graphics on the Letterprinter 100

                         using "LA100G"





                               by

                          Rob Hamilton





                         Multiware, Inc.
                        Davis, California
                            May 1984





1.0  Introduction

LA100G is a program that can read a  file  of  formatted  generic
graphics   instructions,   translate   the  instructions  into  a
disk-based "bitmap" file, and then create a hardcopy image on one
of Digital's Letterprinter or Letterwriter 100 serial printers.

The program features a dot resolution of  up  to  1024  by  1024,
simulated  hardware  character generation, dotted and dashed line
generation, and a flexible means  for  scaling  and  rotating  an
image.

The   input   file   format   is   easily    user-generated    by
"post-processing" device or metafile output from most any popular
graphics package.  It can be read with standard FORTRAN READ  and
FORMAT statements.


Graphics on the Letterprinter 100                          PAGE 2
Using "LA100G"


2.0  How it works

LA100G works in two stages.  In the first stage, the user's input
file   is  read  and  processed.   Vectors  are  "rasterized"  or
converted to "1" dots (bits) in a zeroed background bitmap.  Text
characters  are converted to suitable dot patterns and positioned
in the bitmap.

In the second stage, the bitmap is accessed  in  a  top-to-bottom
direction,  and  rows  of  dots are converted to a format that is
compatible  with  the  LA100  printers.   The  serial  output  is
directed to a logical device called "LA:" until all of the bitmap
has been transferred.



2.1  The Input File

LA100G reads graphics input from  a  user-specified  file.   This
file should be formatted as rows (ASCII records) of three numeric
values each.  The spacing or width of the numeric fields within a
record   is   quite  flexible  because  a  "free-formatted"  READ
statement is used to get the values.

The first number in each record is  an  INTEGER  operation  code.
This  code  defines  the nature of the instruction.  Examples are
"1"  for  MOVE,  "2"  for  DRAW,  "3"  for  TEXT  and   "4"   for
SET_LINE_STYLE.   The  second  and  third  values in a record are
operand arguments, such as X and Y coordinate values  or  a  line
style  code.   A  special  additional record is used to list text
information.

Records are read by LA100G  one-by-one  until  an  END_OF_PICTURE
record or an end-of-file condition is encountered.



2.2  The Raster-Bitmap File

In order to store a rectangular bitmap  with  1024  points  along
each side, it is necessary to maintain an array of 1,048,576 bits
(1MBit)  or  131,072  eight-bit  bytes  (128K-bytes).   This   is
accomplished  by  storing the array on a direct-access disk file.
Only those parts being updated at a particular  moment  are  read
into memory.

Furthermore, it is convenient to divide the bitmap  into  smaller
pieces  or  "cells".  Each cell is designed to occupy exactly one
disk  block,  so  it  can  be  accessed  with  relatively  little
overhead.   Cells  represent square areas of sixty-four bits on a
side.  Thus, there are sixteen cells across the top  and  sixteen
cells down the side of the bitmap, for a total of two-hundred and
fifty-six cells.


Graphics on the Letterprinter 100                          PAGE 3
Using "LA100G"


It is interesting to note that in many instances, only a  portion
of   the   bitmap's  cells  are  actually  filled  with  non-zero
information.  This is because much of the graphics information we
create  contains  large areas of blank space.  LA100G anticipates
this condition by storing a mapped file  of  cells  that  contain
vectors  or  text.   Cells  that are not used in an image are not
represented in the bitmap file.  The first block  of  the  bitmap
file  is  dedicated to holding two-hundred and fifty-six pointers
to respective cells.  A pointer whose  value  is  zero  indicates
that the corresponding cell need not be represented.  



2.3  Disk-Cache of Cells

LA100G maintains a list of bitmap cells  that  are  currently  in
memory.   To  maximize  the  speed  at which vectors and text are
rasterized, the 16-bit versions keep thirty-two cells resident or
"cached." When a new cell is needed and all available cell arrays
are full, the cached cell list is examined, and  the  cell  which
has  been  used  least  recently  is  swapped to the bitmap file.
Thus, cells that are used  most  frequently  are  swapped  least.
Once  the input file has been fully processed, the bitmap file is
closed and saved for future access.  



2.4  Printer Formatting

The LA100 printers utilize a six-hammer  vertical  impact  column
that  moves  horizontally.   For  best scan-to-scan registration,
graphics mode limits actual printing to  print-head  sweeps  from
left-to-right.  A specially defined protocol allows graphics data
to be passed to the printer in dense groups of  six-bit  columns.
The  LA100G program reads the bitmap file blocks (cells) and then
constructs a row of six-bit columns as an array of  ASCII  bytes.
The array is optimized by using the printer's "repeat introducer"
sequence.   Multiple  occurances  of  adjacent   and   equivalent
characters  can  be  replaced  by  the repeat introducer, a count
value, and the character value.

Each six-bit-high row is processed in a different  way  than  the
one  immediately  above  or below it.  This is because the bitmap
file is organized as eight-bit bytes.  Four methods of extracting
six-bits columns are utilized;

      1. Get lowest six bits of cell row
      2. Combine  highest  two  bits of cell row with lowest four
         bits of next cell row
      3. Combine highest four  bits  of cell  row with lowest two
         bits of next cell row
      4. Get highest six bits of cell row



Graphics on the Letterprinter 100                          PAGE 4
Using "LA100G"


A rotation of the four methods is used  to  create  adjacent  and
contiguous six-bit-column rows.

The printer places 132 horizontal dots per inch and 72  dot  rows
per  vertical  inch.   To  best  approximate  a one-to-one aspect
ratio, two horizontal dots are drawn for each  one  specified  in
the  raster  bitmap  file.   Thus, the true aspect ratio of plots
drawn is 66x72 or 0.91667.



3.0  System Requirements

Under the RT-11 operating system,  the  LA100G  program  requires
about  21K  words of memory.  The raster bitmap file (RASFIL.TMP)
is created  with  a  maximum  initial  size  of  two-hundred  and
fifty-eight blocks.  Space for this file must be available on the
default device or directory.  The output file in  LA100  graphics
format  is directed to a logical device called "LA:".  You should
use the ASSIGN command to  connect  this  device  with  either  a
disk/directory or an LA100/LS100 printer.



4.0  Special LA100 Setup Requirements

The Letterprinter 100 should be set up such that its margins  are
at   the   extreme   left   and   right  positions.   Of  course,
communications parameters such as BAUD RATE, PARITY,  and  NUMBER
OF  BITS  must be set in the same manner as for alphanumeric use.
The printer should be ON-LINE and WIDE (14-7/8")  paper  inserted
at the TOP-OF-FORM position.

Keep in mind that once the program has begun to transmit graphics
data  to  the printer, the printer is in its "graphics" mode.  If
the program is aborted prematurely, it will  probably  leave  the
printer  in this mode, causing strange behavior when alphanumeric
data is transmitted.  For this reason, it  is  best  to  let  the
program  finish  normally, whereupon the printer mode is reset to
alphanumeric.  Of course, you can always reset the printer's mode
by turning its power off, and then on again.



5.0  Input File Format

As  discussed  in   section   2.1,   input   files   consist   of
FORTRAN-readable  formatted  records,  with  three numeric values
each.  The first value must be an INTEGER operation code  between
1  and  12.   Each operation code value denotes a unique graphics
function.  The second and third values are used to hold  argument
values.   Note  that some operation codes do not require specific
argument values.  However, dummy arguments must  be  supplied  to


Graphics on the Letterprinter 100                          PAGE 5
Using "LA100G"


satisfy  the  FORTRAN sequential free-format READ.  The value "0"
is usually employed for this purpose.

The following table lists graphics  operation  codes,  and  their
respective operand arguments.


                Input File Op Codes and Operands

  Op Code       Op Code        Argument        Argument
  Function       Value            1               2

   MOVE            1           X value         Y value

   DRAW            2           X value         Y value

   TEXT            3         No. of Chars.        0

  SET_LINE_STYLE   4          Style Code          0

  SET_LIMIT        6           X value         Y value

  SET_OFFSET       7           X value         Y value

  SET_LA100_LIMIT  8           X value         Y value

  END_OF_PICTURE   9              0               0

  SET_TEXT_PATH   10           degrees            0

  SET_TEXT_SIZE   11           X value         Y value

  SET_ROTATE      12           0 or 1             0





5.1  The MOVE command

The  MOVE  command  is   implemented   as   operation   code   1.
Accompanying  X  and  Y  argument  values  direct  a new "current
position" to be established at the coordinate (X,Y).



5.2  The DRAW command

The DRAW command is implemented as operation code 2.  A vector is
drawn  between the previous "current position" and the coordinate
specified by the accompanying arguments.  This coordinate becomes
the new "current position".


Graphics on the Letterprinter 100                          PAGE 6
Using "LA100G"


5.3  The TEXT command

The TEXT command is implemented as operation code 3.   The  first
argument  specifies  the number of characters to be written.  The
text string should be placed in the next input record,  beginning
in column 1.  Text records should not contain any other values or
arguments.



5.4  The SET_LINE_STYLE command

The SET_LINE_STYLE command is implemented as  operation  code  4.
One  of eight different styles (dot-dash patterns) of vectors can
be selected by using this command.   The  first  argument  should
hold  an  INTEGER value between 1 and 8.  Line-style 1 (solid) is
the default.  The others are described here:

                           Line Styles

          1 . . . . . . . . . . Solid Line
          2 . . . . . . . . . . Dot-Dash
          3 . . . . . . . . . . Course Dots
          4 . . . . . . . . . . Fine Dots
          5 . . . . . . . . . . Spaced Dots
          6 . . . . . . . . . . Widely Spaced Dots
          7 . . . . . . . . . . Dash-Dash-Gap
          8 . . . . . . . . . . Dashed Line




5.5  The SET_TEXT_PATH command

The SET_TEXT_PATH command is implemented as  operation  code  10.
Text can be written in one of four directions.  The first operand
argument is used to  select  the  desired  direction  in  angular
degrees:

          0 . . . . . . . . . . left-to-right (default)
         90 . . . . . . . . . . bottom-to-top
        180 . . . . . . . . . . upside-down
        270 . . . . . . . . . . top-to-bottom




5.6  The SET_TEXT_SIZE command

The SET_TEXT_SIZE command is implemented as  operation  code  11.
This  command  allows you to select one of seven character sizes.
An INTEGER character size code is specified in the first argument
position.   The  default size is 2, which creates characters that


Graphics on the Letterprinter 100                          PAGE 7
Using "LA100G"


are fourteen dots high and ten dots wide.  This size  is  closest
in  proportion  to  most popular graphics CRT text sizes.  Size 1
makes the smallest text characters at 5x7  dots,  and  all  other
sizes are integer multiples of size 1.



5.7  The SET_LIMITS command

The SET_LIMITS command is implemented as operation code 6.   This
command  allows  you  to  adjust  the  range  of the input file's
coordinate system.  The maximum expected X and Y values should be
specified  as  the  operand  arguments.   If  this command is not
given, a coordinate system that ranges from 0 to 4095 in X, and 0
to 3071 in Y is assumed.



5.8  The SET_LA100_OFFSETS command

The SET_LA100_OFFSETS command is implemented as operation code 7.
This  command  allows you to displace an image on the page by the
specified number of X and Y LA100 dot units.  Positive  X  and  Y
values  will  cause the image to be placed above and to the right
of the default (0,0) origin.



5.9  The SET_LA100_LIMITS command

The SET_LA100_OFFSETS command is implemented as operation code 8.
This  command  allows  you  to  place an upper limit to the LA100
coordinates to which the input  file  is  scaled.   (Note:   This
feature  implements  a  WINDOW;   not a VIEWPORT.  Information is
scaled and not clipped.) The default LA100 limits are 958 wide by
720 high.



5.10  The SET_ROTATED command

The SET_ROTATED command is  implemented  as  operation  code  12.
Graphics  images  can be rotated 90 degrees by using this command
at the beginning of  the  input  file.   When  a  non-zero  first
argument is passed, graphics will be rotated.  If the argument is
zero, graphics images will be displayed normally.


Graphics on the Letterprinter 100                          PAGE 8
Using "LA100G"


5.11  The END_OF_PICTURE command

The END_OF_PICTURE command is implemented as  operation  code  9.
This  command defines the end of graphics information in an input
file.   No  other  information  in  the  file  will  be  read  or
interpretted.



5.12  Example Input File

Following is a simple  input  file  that  draws  a  rectangle,  a
diagonal  line through the rectangle, the eight line types, and a
text string "Testing ONE TWO".

 12 1 0         ! rotate graphics
  1 10 10
  2 2000, 10
  2 2000, 1000
  2 10, 1000
  2 10 10
  1 1000, 300
  3 15 0
Testing ONE TWO
  4 1 0
  1 100 900
  2 500 900
  4 2 0
  1 100 850
  2 500 850
  4 3 0
  1 100 800
  2 500 800
  4 4 0
  1 100 750
  2 500 750
  4 5 0
  1 100 700
  2 500 700
  4 6 0
  1 100 650
  2 500 650
  4 7 0
  1 100 600
  2 500 600
  4 8 0
  1 100 350
  2 500 350
  4 1 0
  1 10 10
  2 2000, 1000
  9 0 0         ! end picture


Graphics on the Letterprinter 100                          PAGE 9
Using "LA100G"


6.0  Installation of LA100G

The  program  as  distributed  for  RT-11  and  RSX-11M  systems,
consists of six FORTRAN source files:

     LA100G.FOR . . . . Main module
     LA100D.FOR . . . . Input file decoder
     LA100B.FOR . . . . Bitmap Management and Vector Rasterizer
     LA100C.FOR . . . . Dot-Matrix Character Generation
     LA100P.FOR . . . . Bitmap to LA100 conversion
     LA100S.FOR . . . . LA100 format and output processor

Also provided is a command file for  compiling  and  linking  the
program.  This command file is called LA100G.COM.  



7.0  Sample Run

You can run the  LA100G  program  by  typing  your  system's  RUN
command.    The   program   will   ask  you  for  an  input  file
specification.  After the file specification has been typed,  the
bitmap  file  will  be  opened  on  your default device.  If this
fails, an error diagnostic message will be printed.   You  should
make  certain  that  there  is  space available for a file of 258
blocks in length before trying again.

   .RUN LA100G
   Name of input file: TEST1.ARG
   Processing input record  128
   Beginning LA100 Graphics Printing.
   
   Another copy? NO
   .

Note that the program creates but  does  not  delete  the  raster
bitmap file RASFIL.TMP.  This file is kept so that more copies of
the image can be made, without repeating the rasterization  step.
If  it  is  no  longer  needed,  you can use your system's DELETE
command to reclaim the disk space.

To make more copies from an existing raster bitmap file, you  can
simply  press  <RETURN>  in response to the "Name of input file:"
prompt.  A message will appear that says

     Attempt to print from existing bitmap file...



Graphics on the Letterprinter 100                         PAGE 10
Using "LA100G"


7.1  Error Diagnostic Messages


     ?LA100P-F-LA100 output file failed to open

            The  logical  device  "LA:"  does  not
            exist.    Use   your  system's  ASSIGN
            statement  to  connect  a  device   or
            directory with this name.


     ?LA100G-F-Named input file not found.

            The input file you specified does  not
            exist   on  the  directory  or  device
            specified.   Make  certain  that   you
            typed its name correctly.


     ?LA100G-F-Intermediate bitmap file (RASFIL.TMP) not found.

            No input file specification was given,
            so   LA100G   attempted   to  open  an
            existing bitmap file.  This  file  did
            not  exist  or was "locked".  Check to
            see whether the file  is  present  and
            that it is ready for access.


      ?LA100G-F-Raster file failed on open

            The system tried to  open  the  raster
            bitmap file RASFIL.TMP on your default
            directory and failed, probably due  to
            lack  of space.  This file requires an
            initial  allocation  of  258   blocks.
            Once  it  has been created and closed,
            it will probably occupy less space.